INF.47

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods				19 September 2011

Joint Meeting of the RID Committee of Experts and the 
Working Party on the Transport of Dangerous Goods

Geneva, 13–23 September 2011
Item 2 of the provisional agenda
Tanks

Carriage of UN 1075 in tanks

Transmitted by the Government of France

Summary

Executive summary: This document proposes to add UN 1075 in the Table of 4.3.3.2.5. Action to be taken: Modify 4.3.3.2.5 of RID/ADR

1.	UN 1075 PETROLEUM GASES, LIQUEFIED may be carried in RID/ADR tanks with the tank code PxBN in Column (12) in Table A of Chapter 3.2, but is missing in the Table of 4.3.3.2.5.

2.	A definition of LPG including UN 1011, 1075, 1965, 1969 and 1978 will be introduced in the 2013 RID/ADR.

3.	Furthermore the standard EN 12493 used for the design and manufacture of LPG road tankers will include these UN numbers.

4.	To be consistent UN 1075 should be added in the Table of 4.3.3.2.5 with the relevant values.