| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/9 18 December 2008 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-seventh session

Geneva, 10 - 13 March 2009

Item 4.2.30 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 7 to Regulation No. 106

(Pneumatic tyres for agricultural vehicles)

Submitted by the Working Party on Brakes and Running Gear (/

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its sixty-fourth session (ECE/TRANS/WP.29/GRRF/64, para. 39).  It is based on ECE/TRANS/WP.29/GRRF/2007/21/Rev.1, as amended by paragraph 39 of the report.  It is submitted to WP.29 and AC.1 for consideration.

Insert a new paragraph 3.1.8.1., to read:

"3.1.8.1.	The inscription 'I-3' for implement tyres with traction tread as identified in Annex 5, tables 5 and 6."

Insert a new paragraph 6.4.3., to read:

"6.4.3.	However, for the types of tyre for which the size designation is given in the first column of the tables in Annex 5, the allowed percentages are those given in the relevant tables, if any."

Annex 3, part C, amend to read:

"PART C: IMPLEMENT TYRES

Example of the markings to be borne by types of tyres

complying with this Regulation

250/70 R 20 IMP

MINIMUM HEIGHTS OF MARKINGS (mm)

.........

(c)	the symbol "TUBELESS", I-3 if any, the optional word "RADIAL", the optional word "IMPLEMENT" and the date of manufacture may be at a distance from the size designation."

Annex 5

Table 5, the title, amend to read:

"Table 5 Agricultural Implement Tyres – Normal section Sizes"

Table 5, insert the following new tyre size designations:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  | (mm) | (mm) | (mm) |
| 4.10/3.50-4 IMP | 2.10 | 89 | 272 | 101 |
| 190-8 IMP | 5.50 | 182 | 430 | 203 | " |

Table 5, insert a new column for "Overall diameter (D)" identified by (*), and add in the new column the relevant values for the following tyre size designations:

"Table 5 Agricultural Implement Tyres – Normal section Sizes

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 4.00 – 8 IMP | 3 | 112 | 418 | 425 | 203 |
| 4.00 – 9 IMP | 3 | 112 | 443 | 460 | 229 |
| 4.0 – 10 IMP | 3 | 114 | 455 | 465 | 254 |
| 4.00 – 10 IMP | 3 | 114 | 465 | 475 | 254 |
| 4.00 – 12 IMP | 3 | 112 | 519 | 536 | 305 |
| 4.00 – 15 IMP | 3 | 112 | 595 | 612 | 381 |
| 4.00 – 18 IMP | 3 | 112 | 672 | 688 | 457 |
| 4.50 – 19 IMP | 3 | 124 | 720 | 733 | 483 |
| 4.80 – 8 IMP | 3,75 | 121 | 423 | 449 | 203 |
| 5.0 – 10 IMP | 4 | 145 | 505 | 517 | 254 |
| 5.00 – 12 IMP | 4 | 145 | 567 | 580 | 305 |
| 5.00 – 14 IMP | 4 | 145 | 618 | 631 | 356 |
| 5.00 – 15 IMP | 3 | 130 | 639 | 655 | 381 |
| 5.50 – 16 IMP | 4 | 150 | 685 | 703 | 406 |
| 5.90 – 15 IMP | 4 | 150 | 665 | 681 | 381 |
| 6.00 - 9 IMP | 4,5 | 169 | 543 | 556 | 229 |
| 6.00 – 16 IMP | 4 | 158 | 712 | 729 | 406 |
| 6.50 – 16 IMP | 4,5 | 173 | 735 | 754 | 406 |
| 6.70 – 15 IMP | 4,5 | 182 | 704 | 720 | 381 |
| 7.00- 12 IMP | 5 | 187 | 667 | 685 | 305 |
| 7.50 – 10 IMP | 6 | 214 | 634 | 649 | 254 |
| 7.50 – 16 IMP | 5,5 | 202 | 785 | 801 | 406 |
| 7.50 – 18 IMP | 5,5 | 202 | 836 | 852 | 457 |
| 7.50 – 20 IMP | 5,5 | 202 | 887 | 903 | 508 |
| 7.50 – 24 IMP | 5,5 | 202 | 989 | 1013 | 610 |
| 7.60 – 15 IMP | 5,5 | 193 | 734 | 751 | 381 |
| 13.50 – 16.1 IMP | 11 | 353 | 1021 | 1043 | 409 | " |

After table 5 (1 of 2), add the following notes to read:

"Notes:	1.	The suffix "IMP" may be replaced by the wording "IMPLEMENT" on the tyre sidewall.

2.	Tyres of radial structure are identified by means of the letter "R" in place of "-" (e.g. 7.5 L R 15).

3.	Overall diameters (D) in column (*) apply to tyres marked with classification 
code 'I-3' – see paragraph 3.1.8.2."

Table 6 (1 of 2), insert a new column for "Overall diameter (D)" identified by (*), and add in the new column the relevant values for the following tyre size designations:

"Table 6 (1 of 2) Agricultural Implement Tyres – Low Section Sizes

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 8.5L – 14 IMP | 6 | 216 | 721 | 735 | 356 |
| 9.5L – 14 IMP | 7 | 241 | 741 | 757 | 356 |
| 9.5L – 15 IMP | 7 | 241 | 767 | 782 | 381 |
| 11L – 14 IMP | 8 | 279 | 752 | 770 | 356 |
| 11L – 15 IMP | 8 | 279 | 777 | 796 | 381 |
| 11L – 16 IMP | 8 | 279 | 803 | 821 | 406 |
| 12.5L – 15 IMP | 10 | 318 | 823 | 845 | 381 |
| 12.5L – 16 IMP | 10 | 318 | 848 | 870 | 406 |
| 16.5L – 16.1 IMP | 14 | 419 | 1024 | 1046 | 409 | " |

After table 6 (1 of 2), add the following note 3 to read:

"3.	Overall diameters (D) in column (*) apply to tyres marked with classification code 'I-3' – see paragraph 3.1.8.2."

Table 6 (2 of 2), insert a new column for "Overall diameter (D)" identified by (*), and add in the new column the relevant values for the following tyre size designations:

"Table 6 (2 of 2) Agricultural Implement Tyres – Low Section Sizes

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 6.5/80 – 12 IMP | 5 | 163 | 569 | 588 | 305 |
| 6.5/80 – 15 IMP | 5 | 163 | 645 | 663 | 381 |
| 9.0/75 – 16 IMP | 7 | 226 | 749 | 770 | 406 |
| 10.0/80 – 12 IMP | 9 | 264 | 710 | 730 | 305 |
| 11.0/65 - 12 IMP | 9 | 281 | 670 | 692 | 305 |
| 10.0/75 - 15.3 IMP | 9 | 264 | 760 | 780 | 389 |
| 11.5/80 – 15.3 IMP IMP | 9 | 290 | 845 | 867 | 389 |
| 10.5/80 – 18 IMP | 9 | 274 | 885 | 907 | 457 |
| 12.0/75 - 18 IMP | 9 | 299 | 915 | 937 | 457 |
| 12.5/80 - 18 IMP | 9 | 308 | 965 | 987 | 457 |
| 14.5/80 - 18 IMP | 12 | 372 | 1060 | 1082 | 457 |
| 15.0/55 - 17 IMP | 13 | 391 | 850 | 872 | 432 |
| 15.5/80 - 24 IMP | 13 | 394 | 1240 | 1262 | 610 |
| 16.0/70 - 20 IMP | 14 | 418 | 1075 | 1097 | 508 |
| 16.5/85 - 24 IMP | 13 | 417 | 1322 | 1344 | 610 |
| 16.5/85 - 28 IMP | 13 | 417 | 1423 | 1445 | 711 |  |

"

After table 6 (2 of 2), add the following note 3. to read:

"3.	Overall diameters (D) in column (*) apply to tyres marked with classification code 'I-3' – see paragraph 3.1.8.2."

Table 7 (1 of 2), insert the following new tyre size designations:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  | (mm) | (mm) | (mm) |
| 13x6.00-6 | 5 | 154 | 330 | 152 |
| 14x4.50-6 | 3,5 | 113 | 356 | 152 |
| 18x7.50-8 | 6 | 191 | 457 | 203 |
| 19x9.50-8 | 7,5 | 240 | 483 | 203 |
| 20x8.00-8 | 6,5 | 204 | 508 | 203 |
| 20x9.00-8 | 7 | 227 | 508 | 203 |
| 21x7.00-10 | 5,5 | 177 | 533 | 254 |
| 23x9.50-12 | 7 | 235 | 577 | 305 |
| 24x12.00-12 | 9,5 | 304 | 610 | 305 |
| 25x8.00-12 | 6,5 | 203 | 635 | 305 |
| 25x10.00-12 | 8 | 254 | 635 | 305 |
| 25x11.00-12 | 9 | 279 | 635 | 305 |

"

Table 7 (2 of 2), add the following new tyre size designations:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  | (mm) | (mm) | (mm) |
| DH73x50.00-32 | 44 | 1270 | 1880 | 813 |

"

After table 7 (2 of 2), add the following note 4. to read:

"4.	Coefficient "b" for the calculation of the Overall diameter Dmax:

(a)	1.12 for tyres with Nominal rim Diameter (d) less than 380 mm;

(b)	1.10 for tyres with Nominal rim Diameter (d) 381 mm and above."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.