## Slide 1: Behaviour of M2 & M3 general construction in case of Fire Event
IWG - BMFE
Informal document GRSG-116-11
(116th GRSG, 1-5 April 2019, agenda item 2(b))

## Slide 2: IWG BMFE overview
2 meetings on 2018 4th quarter / 2019 1st quarter
  Chair : France (UTAC)
  Secretary : OICA
5th meeting
  2018 November 27th / 28th
  Madrid location (INSIA)
  19 attendees : 3 contracting parties / 7 vehicle manufacturers / 4 automotive suppliers / 5 test centers
6th meeting
  2019 February 27th / 28th
  Oslo location (Norvegian Public Road Administration)
  20 attendees : 4 contracting parties / 5 vehicle manufacturers / 6 automotive suppliers / 5 test centers

## Slide 3: 5th IWG BMFE meeting
UNECE n°118 Contents
  Toxicity and opacity
    Results of the test performed on materials already approved under R118 : most of the tested materials are not compliant with generic protocol coming from railway testing method.
    Need to go further in detail for opacity to focus on testing propotocols adapted to road application (duration, irradiation, …)
    Alternative option : very low flame propagation speed (“non burning materials”) without opacity/toxicity requirement, or higher propagation burning rate with toxicity/opacity requirements.

## Slide 4: 5th IWG BMFE meeting
UNECE n°118 Contents
  Toxicity and opacity
    German proposal : Research study engaged for 10 months starting beginning of 2019 in order to defined a simplified material toxicity test method adapted for road transport.
  Adhesive agent
    Test results on adhesive agent influence : no big gap in terms of inflammability behaviour have been noted. A regulation update is under construction to define the list of agents that can be used without deterioration of the burning behaviour capabilities.

## Slide 5: 5th IWG BMFE meeting
UNECE n°107 Contents
  Automatic exit opening : draft wording proposal
    « § 7.5.1.6. In the case of vehicles of Classes II, III and B, having the engine located to the rear of the driver’s compartment, and in the event of excess temperature in the engine compartment or in any compartment where a combustion heater is located the emergency lighting system according to paragraph 7.8.3. shall automatically activate, and the power-operated service doors situated on the side of the vehicle that is nearer of the side of the road corresponding to the direction of traffic for which the vehicle is designed shall open automatically when the vehicle is stationary or driving at a speed less than or equal to 3 km/h.”

## Slide 6: 5th IWG BMFE meeting
UNECE n°107 Contents
  Safety instructions : draft wording proposal
    “§ 7.19. Safety information: Means to transmit safety information, which permit the operator or the user to easily inform the passengers of the safety instructions as e.g. the location of the emergency exits, the location of the fire extinguishers, safety sign, shall be specified by the manufacturer in the application for approval.
    These means shall be adapted to the design and architecture of the vehicle with the aim of making the safety instructions easily intelligible by the user of any passenger seat.”

## Slide 7: 6th IWG BMFE meeting
Table of accidentology : main crossing factors
  Fires account for between 1.0 and 1.5% of fires in buses and coaches in service.
  Around 10% of buses are involved in fire event during their service lifecycle.
  Fire events are not mainly the result of impacts.
  Fires occur mainly in the engine compartment due to fluid leaks, but in most cases the vehicle does not burn completely.
  Evaluated evacuation times seems to be below 5 minutes

## Slide 8: 5th IWG BMFE meeting
UNECE n°107 Contents
  Full scale test : analyzis of previous tests already performed (RISE) and opportunity to fill in with full scale test leaded by Aguila  fire ignition in engine compartment with 2 setups, emergency exits opened / not opened.
  Main chronology to deal with, according to previous test results :
    Smokes will chronologically appear first, bringing opacity and toxicity effects
    Insulation of engine compartment is such that the thermal effect is not predominant

## Slide 9: 6th IWG BMFE meeting
UNECE n°107 Contents
  Combination of fire detection and fire suppression warnings to the driver : target is to avoid a fire suppression system engagement without alarm to the driver due to a more sensitive detection device included in the fire suppression system. Draft wording proposal :
    “The fire suppression system may alternatively be activated automatically by other means, as long as it activates the alarm system”
  Studies on going trying to define a minimal performance level for fire detection systems (temperature or other means)
  Technical overview on available systems for smoke extraction in other applications

## Slide 10: 6th IWG BMFE meeting
UNECE n°118 Contents
  Opened discussion on the current inflammability requirement relevancy
  Balance between the 3 main parameters has to be defined for road applications : flame spread, smoke toxicity and smoke density (first step of the german toxicity study)
  Opened discussion on a comparison matrix to compare reasons and consequences of requirements per transport mode, including cost rates.

## Slide 11: 6th IWG BMFE meeting
UNECE n°118 Contents
  Adhesive agents : draft wording proposal on annex 2 regarding Information document for component
    “5. Adhesive agents
    5.1. In cases where adhesive agents are used to affix the material to supporting structures or bonding materials together, a list of adhesive agents that can be used without deterioration of the burning behaviour of the material(s): …………………“

## Slide 12: 7th IWG BMFE meeting
Next session
  1 ½ day meeting
  2019, June 25th – 26th
  Location : BASt (Bergisch Gladbach)

## Slide 13: Thanks for your attention.