## Slide 1
Proposal for GTR No. 6 Safety glazing
Submitted by the expert from the Republic of Korea | Informal document GRSG-116-31 (116th GRSG, 1-5 April 2019 agenda item 6(a))

## Slide 2
Purpose
1. In case that open type loadings tray is applied to trucks,
interior mirror application is required to secure rear view.
2. Additionally the many kinds of the truck's efficient safety/convenience
(LDWS, Autonomous sensors, etc.) options are being under development
nowsdays.

## Slide 3
Integrated interior mirror
Purpose
3. If safety/convenience options are fitted to the underside of the windscreen,
it may limit the driver’s direct front of vision.
For the optimization of installation, these options may be integrated
with the interior mirror.

## Slide 4
Purpose
4. However it is difficult for some models to install the interior mirror,
since Area “I” may be intruded.
Mounting part of integrated mirror inside windshield glass
( Intrusion part of Zone ‘I’ )
Zone ‘I’
Space that needs to be allowed
for opaque obscuration
Integrated mirror assembly
Minimum space between headlining
to integrated mirror for installation

## Slide 5
Opaque obscuration of
Zone‘I’ in this Proposal
(The opaque obscuration which is
defined in paragraph 7.1.3.2.4)
Zone ‘I’
P1
P5
P4
P4’
300mm
Proposal
Therefore, the opaque obscuration which is defined in paragraph 7.1.3.2.4.
of Annex is needed to be exempted in Zone I, in order to install integrated
interior mirror.
For reference, the same exemption has been already permitted in the requirement
of light transmittance in 7.1.3.4. of GTR 6.

## Slide 6
Zone ‘I’ (before)
: Not permit opaque obscuration
Zone ‘I’ (after)
: Permit opaque obscuration
6.65˚
10˚
Point ‘O’
The driver’s front vision may be intruded by the opaque obscuration(yellow color),
but most of the opaque obscuration is already obscured by the interior mirror.
▶ Result : There is no problem with Front vision angle
Comparison of front vision
Point ‘O’