| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.15/AC.1/80/Add.6 30 March 2000 Original: ENGLISH |

###### ECONOMIC COMMISSION FOR EUROPE

###### INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and

the Working Party on the Transport of

Dangerous Goods

REPORT OF THE SESSION

Held in Geneva from 13 to 24 March 2000

Addendum 6

Chapter 5.3 of the draft restructured ADR

PLACARDING AND MARKING OF CONTAINERS, MEGCs, TANK-CONTAINERS,

PORTABLE TANKS AND VEHICLES

Text adopted by the Joint Meeting

The secretariat reproduces hereunder the text adopted by the Joint Meeting for Chapter 5.3 of restructured ADR.  The corresponding text of Chapter 5.3 of RID will be reproduced by the Central Office for International Carriage by Rail (OCTI) under the symbol

OCTI/RID/GT-III/2000-A/Add.6.

CHAPTER 5.3

PLACARDING AND MARKING OF CONTAINERS, MEGCs, TANK-CONTAINERS, PORTABLE TANKS AND VEHICLES

NOTE : For marking and placarding of containers, MEGCs, tank-containers and portable tanks for carriage in a transport chain including a maritime journey, see also 1.1.4.2. If the provisions of 1.1.4.2. (c) are applied, only paragraphs 5.3.1.3 and 5.3.2.1.1 of this Chapter are applicable.

5.3.1		Placarding

5.3.1.1		General provisions

5.3.1.1.1	As and when required in this section, placards shall be affixed to the exterior surface of containers, MEGCs, tank-containers, portable tanks and vehicles. Placards shall correspond to the labels required in column (5) and, where appropriate, column (6) of Table A of Chapter 3.2 for the dangerous goods contained in the container, MEGC, tank-container, portable tank or vehicle and shall conform to the specifications given in 5.3.1.7.

5.3.1.1.2	For Class 1, compatibility groups shall not be indicated on placards if the transport unit or container is carrying substances or articles belonging to two or more compatibility groups.  Transport units or containers carrying substances or articles of different divisions shall bear only placards conforming to the model of the most dangerous division in the order:

1.1 (most dangerous), 1.5, 1.2, 1.3, 1.6, 1.4 (least dangerous).

When 1.5 D substances are carried with substances or articles of Division 1.2, the transport unit or container shall be placarded as Division 1.1.

5.3.1.1.3.	For Class 7, the primary risk placard shall conform to model No.7D as specified in 5.3.1.7.2.  This placard is not required for vehicles or containers carrying excepted packages and for small containers.

Where both class 7 labels and placards would be required to be affixed to vehicles, containers, MEGCs, tank-containers or portable tanks, an enlarged label corresponding to the label required may be displayed instead of placard No.7D to serve both purposes.

        - Containers, MEGCs, tank-containers, portable tanks or vehicles containing goods of more than one class need not bear a subsidiary risk placard if the hazard represented by that placard is already indicated by a primary or subsidiary risk placard.

5.3.1.1.5	Placards which do not relate to the dangerous goods being carried, or residues thereof, shall be removed or covered.

5.3.1.2		Placarding of containers, MEGCs, tank-containers and portable tanks

[NOTE: This sub-section does not apply to swap-bodies, except tank swap bodies.]

The placards shall be affixed to both sides and at each end of the container, MEGC,tank-container or portable tank.

5.3.1.3		Placarding of vehicles carrying containers, MEGCs, tank-containers or portable tanks

[NOTE: This sub-section does not apply to the placarding of vehicles carrying swap-bodies other than tank swap-bodies; for such vehicles, see 5.3.1.5]

If the placards affixed to the containers or tank-containers are not visible from outside the carrying vehicles, the same placards shall also be affixed to both sides and at the rear of the vehicle.  Otherwise, no placard need be affixed on the carrying vehicle.

5.3.1.4		Placarding of vehicles for carriage in bulk, tank-vehicles, battery vehicles and vehicles with demountable tanks

Placards shall be affixed to both sides and at the rear of the vehicle.

[NOTE: When, in the course of an ADR journey or at the end of an ADR journey, a tank semi-trailer is separated from its tractor to be loaded on board a ship or an inland navigation vessel, placards shall also be displayed at the front of the semi-trailer.]

5.3.1.5		Placarding of vehicles carrying packages only

[NOTE: This sub-section applies also to vehicles carrying swap-bodies loaded with packages]

5.3.1.5.1	For transport units carrying packages containing substances or articles of Class 1, placards shall be affixed to both sides and at the rear of the transport unit.

5.3.1.5.2	For vehicles carrying radioactive material of Class 7 in packagings or IBCs (other than excepted packages), placards shall be affixed to both sides and at the rear of the vehicle.

[NOTE: If, during an ADR journey, a vehicle carrying packages containing dangerous goods of classes other than Classes 1 and 7 is loaded on board a ship for sea transport or if the ADR journey precedes a voyage by sea, placards shall be affixed to both sides and at the rear of the vehicle. Placards may remain affixed to both sides and at the rear of the vehicle after a sea voyage.]

5.3.1.6		Placarding of empty, tank-vehicles, battery vehicles, tank-containers, MEGCs and portable tanks

5.3.1.6.1	Empty tank-vehicles, vehicles with demountable tanks, battery-vehicles,tank-containers, MEGCs and portable tanks uncleaned and not degassed, and empty vehicles and containers for carriage in bulk, uncleaned, shall continue to display the placards required for the previous load.

5.3.1.7		Specifications for placards

5.3.1.7.1	Except as provided in 5.3.1.7.2 for the Class 7 placard, a placard shall:

(a) Be not less than 250 mm by 250 mm, with a line of the same colour as the symbol running 12.5mm inside the edge and parallel with it;

(b) Correspond to the label required for the dangerous goods in question with respect to colour and symbol (see 5.2.2.2); and

(c) Display the numbers(and for goods of Class 1, the compatibility group letter) prescribed for the dangerous goods in question in 5.2.2.2 for the corresponding label, in digits not less than 25 mm high.

        - The Class 7 placard shall be not less than 250 mm by 250 mm with a black line running 5 mm inside the edge and parallel with it and is otherwise as shown below.(Model No. 7D). The number "7" shall not be less than 25 mm high.  The background colour of the upper half of the placard shall be yellow and of the lower half white, the colour of the trefoil and the printing shall be black.  The use of the word "RADIOACTIVE" in the bottom half is optional to allow the use of this placard to display the appropriate United Nations number for the consignment.

Placard for radioactive material of Class 7

(No.7D)

Symbol (trefoil): black; Background: upper half yellow with

white border, lower half white;

The lower half shall show the word RADIOACTIVE or alternatively, when required, the appropriate UN Number (see 5.3.2.1.2)

and the figure ‘7'in the bottom corner.

5.3.1.7.3	For tanks with a capacity of not more than 3 m3 and for small containers, placards may be replaced by labels conforming to 5.2.2.2.

5.3.2		Orange-coloured plate marking

5.3.2.1		General orange-coloured plate marking provisions

5.3.2.1.1	Transport units carrying dangerous goods shall display two rectangular reflectorized orange-coloured plates conforming to 5.3.2.2.1, set in a vertical plane.  They shall be affixed one at the front and the other at the rear of the transport unit, both perpendicular to the longitudinal axis of the transport unit.  They shall be clearly visible.

5.3.2.1.2	When a hazard identification number is indicated in column (20) of table A of Chapter 3.2, tank-vehicles or transport units having one or more tanks carrying dangerous goods shall in addition display on the sides of each tank or tank compartment, clearly visible and parallel to the longitudinal axis of the vehicle, orange-coloured plates identical with those prescribed in 5.3.2.1.1.  These orange-coloured plates shall bear the hazard identification number and the UN number prescribed respectively in columns (20) and (1) of table A of chapter 3.2 for each of the substances carried in the tank or in a compartment of the tank.

5.3.2.1.3	For tank-vehicles or transport units having one or more tanks carrying substances with UN Nos. 1202, 1203 or 1223, or aviation fuel classed under UN Nos. 1268 or 1863, but no other dangerous substance, the orange-coloured plates prescribed in 5.3.2.1.2 need not be affixed if the plates affixed to the front and rear in accordance with 5.3.2.1.1. bear the hazard identification number and the UN number prescribed for the most hazardous substance carried, i.e. the substance with the lowest flash-point.

5.3.2.1.4	When a hazard identification number is indicated in column (20) of Table A of chapter 3.2, transport units and containers carrying dangerous solid substances in bulk shall in addition display on the sides of each transport unit or container, clearly visible and parallel to the longitudinal axis of the vehicle, orange-coloured plates identical with those prescribed in 5.3.2.1.1. These orange-coloured plates shall bear the hazard identification number and the UN number prescribed respectively in columns (20) and (1) of table A of Chapter 3.2 for each of the substances carried in bulk in the transport unit or in the container.

5.3.2.1.5	For containers carrying dangerous solid substances in bulk and for tanks-containers, the plates prescribed in 5.3.2.2 and 5.3.2.3 may be replaced by a self-adhesive sheet, by paint or by any other equivalent process, provided the material used for this purpose is weather-resistant and ensures durable marking.  In this case, the provisions of the last sentences of 5.3.2.2.2, concerning resistance to fire, shall not apply.

5.3.2.1.6	For transport units carrying only one substance, the orange-coloured plates prescribed in 5.3.2.1.2 and 5.3.2.1.3 shall not be necessary provided that those displayed at the front and rear in accordance with 5.3.2.1.1 bear the hazard identification number and the UN number prescribed respectively in columns (20) and (1) of Table A of Chapter 3.2

5.3.2.1.7	The above requirements are also applicable to empty fixed or demountable tanks, tank-containers and battery-vehicles, uncleaned and not degassed and empty vehicles and empty containers for carriage in bulk, uncleaned.

5.3.2.1.8	Orange-coloured plates which do not relate to dangerous goods carried, or residues thereof, shall be removed or covered.  If plates are covered, the covering shall be total and remain effective after 15 minute’ engulfment in fire.

5.3.2.2		Specifications for the orange-coloured plates

5.3.2.2.1	The reflectorized orange-coloured plates shall be of 40 cm base and not less than 30 cm high; they shall have a black border not more than 15 mm wide. They shall be clearly visible. If the size and construction of the vehicle are such that the available surface area is insufficient to affix these orange-coloured plates, their dimensions may be reduced to 300 mm for the base, 120 mm for the height and 10 mm for the black border.

NOTE: The colour of the orange plates in conditions of normal use should have chromaticity co-ordinates lying within the area on the chromaticity diagram formed by joining the following co-ordinates

| Chromaticity co-ordinates of points at the corners of the area on the chromaticity diagram |  |  |  |  |
| --- | --- | --- | --- | --- |
| x y | 0.52 0.38 | 0.52 0.40 | 0.578 0.422 | 0.618 0.38 |

Luminance factor of reflectorized colour:  ( > 0.12.

Reference centre E, standard illuminant C, normal incidence 45°, viewed at 0°.

Co-efficient of reflex luminous intensity at an angle of illumination of 5°, viewed at 0.2°: not less than 20 candelas per lux per m2.

5.3.2.2.2	The hazard identification number and the UN number shall consist of black digits 100 mm high and of 15 mm stroke thickness.  The UN number shall be inscribed in the lower part of the plate and the hazard-identification number in the upper part ; they shall be separated by a horizontal black line, 15 mm in stroke width, extending from side to side of the plate at mid-height (see 5.3.2.2.3).  The hazard identification number and the UN number shall be indelible and shall remain legible after 15 minutes’ engulfment in fire.

5.3.2.2.3	Exemple of orange-coloured plate with hazard identification number and UN number

Hazard

Identification number

(2 or 3 figures)

UN number

(4 figures)

Background orange.

Border, horizontal line and figure black,

15 mm thickness.

5.3.2.3		Meaning of hazard identification numbers

5.3.2.3.1	The hazard identification number consists of two or three figures. In general, the figures indicate the following hazards:

2		Emission of gas due to pressure or to chemical reaction

3			Flammability of liquids (vapours) and gases or self-heating liquid

4	        	Flammability of solids or self-heating solid

5	   Oxidizing (fire-intensifying) effect

6	   Toxicity or risk of infection

7	   Radioactivity

8	   Corrosivity

9	   Risk of spontaneous violent reaction

NOTE: The risk of spontaneous violent reaction within the meaning of figure 9 include the possibility following from the nature of a substance of a risk of explosion, disintegration and polymerization reaction following the release of considerable heat or flammable and/or toxic gases.

Doubling of a figure indicates an intensification of that particular hazard.

Where the hazard associated with a substance can be adequately indicated by a single figure, this is followed by zero.

The following combinations of figures, however, have a special meaning: 22, 323, 333, 362, 382, 423, 44, 446, 462, 482, 539, 606, 623, 642, 823, 842 and 90, see 5.2.3.3.2 below.

If a hazard identification number is prefixed by the letter "X", this indicates that the substance will react dangerously with water. For such substances, water may only be used by approval of experts.

        - The hazard identification numbers listed in column (20) of table A of chapter

3.2 have the following meanings:

20	asphyxiant gas or gas with no subsidiary risk

22	refrigerated liquefied gas, asphyxiant

223	refrigerated liquefied gas, flammable

225	refrigerated liquefied gas, oxidizing (fire-intensifying)

23	flammable gas

239		flammable gas, which can spontaneously lead to violent reaction

25	oxidizing (fire-intensifying) gas

26	toxic gas

263		toxic gas, flammable

265	toxic gas, oxidizing (fire-intensifying)

268	toxic gas, corrosive

30		flammable liquid (flash-point between 23 °C and 61 °C, inclusive) or	flammable liquid or solid in the molten state with a flash-point above	61 °C, heated to a temperature equal to or above its flash-point, or

self-heating liquid

323		flammable liquid which reacts with water, emitting flammable gases

X323	flammable liquid which reacts dangerously with water, emitting flammable gases 1/

33	highly flammable liquid (flash-point below 23 °C)

333	pyrophoric liquid

333	pyrophoric liquid which reacts dangerously with water 1/

336	highly flammable liquid, toxic

338	highly flammable liquid, corrosive

X338		highly flammable liquid, corrosive, which reacts dangerously with

water 1/

- highly flammable liquid which can spontaneously lead to violent

reaction

36	flammable liquid (flash-point between 23 °C and 61 °C inclusive), slightly toxic, or self-heating liquid, toxic

- flammable liquid, toxic, which reacts with water, emitting flammable

gases

X362	flammable liquid toxic, which reacts dangerously with water, emitting flammable gases 1/

368	flammable liquid, toxic, corrosive

- flammable liquid (flash-point between 23 °C and 61 °C, inclusive),

corrosive

382		flammable liquid, corrosive, which reacts with water,

emitting flammable gases

X382	flammable liquid, corrosive, which reacts dangerously with water, emitting flammable gases 1/

- flammable liquid, which can spontaneously lead to violent reaction

40	flammable solid, or self-reactive substance, or self-heating substance

423	solid which reacts with water, emitting flammable gases

X423	flammable solid which reacts dangerously with water, emitting flammable gases 1/

43	spontaneously flammable (pyrophoric) solid

44		flammable solid, in the molten state at an elevated temperature

446		flammable solid, toxic, in the molten state, at an elevated temperature

46	flammable or self-heating solid, toxic

462		toxic solid which reacts with water, emitting flammable gases

X462	solid which, reacts dangerously with water, emitting toxic gases 1/

48	flammable or self-heating solid, corrosive

- corrosive solid which reacts with water, emitting flammable gases 1/

X482	solid which, reacts dangerously with water, emitting corrosive gases 1/

_________

1/	Water not to be used except by approval of experts.

50	oxidizing (fire-intensifying) substance

539	flammable organic peroxide

55	strongly oxidizing (fire-intensifying) substance

556	strongly oxidizing (fire-intensifying) substance, toxic

558		strongly oxidizing (fire-intensifying) substance, corrosive

- strongly oxidizing (fire-intensifying) substance, which can spontaneously lead

- to violent reaction

56	oxidizing substance (fire-intensifying), toxic

568	oxidizing substance (fire-intensifying), toxic, corrosive

58	oxidizing substance (fire-intensifying), corrosive

59	oxidizing substance (fire-intensifying) which can spontaneously lead to violent reaction

60	toxic or slightly toxic substance

606	infectious substance

623		toxic liquid, which reacts with water, emitting flammable gases

63	toxic substance, flammable (flash-point between 23 °C and 61 °C inclusive)

638	toxic substance, flammable (flash-point between 23 °C and 61 °C inclusive), corrosive

639	toxic substance, flammable (flash-point not above 61 °C) which can spontaneously lead to violent reaction

64	toxic solid, flammable or self-heating

642		toxic solid, which reacts with water, emitting flammable gases

65	toxic substance, oxidizing (fire-intensifying)

66	highly toxic substance

663		highly toxic substance, flammable (flash-point not above 61 °C)

664	highly toxic solid, flammable or self-heating

665	highly toxic substance, oxidizing (fire-intensifying)

668	highly toxic substance, corrosive

669		highly toxic substance which can spontaneously lead to violent reaction

68	toxic substance, corrosive

- toxic or slightly toxic substance, which can spontaneously lead to violent reaction

70	radioactive material

72	radioactive gas

723	radioactive gas, flammable

- radioactive liquid, flammable (flash-point not above 61 °C)

74	radioactive solid, flammable

75	radioactive material, oxidizing (fire-intensifying)

76	radioactive material, toxic

78	radioactive material, corrosive

80	corrosive or slightly corrosive substance

X80	corrosive or slightly corrosive substance, which reacts dangerously with 	water 1/

823		corrosive liquid which reacts with water, emitting flammable gases

- corrosive or slightly corrosive substance, flammable (flash-point

between 23 °C and 61 °C inclusive)

X83		corrosive or slightly corrosive substance, flammable, (flash-point

between 23 °C and 61 °C inclusive), which reacts dangerously with

water 1/

- corrosive or slightly corrosive substance, flammable (flash-point between 23 °C and 61 °C inclusive) which can spontaneously lead to violent reaction 1/

X839	corrosive or slightly corrosive substance, flammable (flash-point between 23 °C and 61 °C inclusive), which can spontaneously lead to violent reaction and which reacts dangerously with water 1/

84	corrosive solid, flammable or self-heating

842		corrosive solid which reacts with water, emitting flammable gases

85		corrosive or slightly corrosive substance, oxidizing (fire-intensifying)

- corrosive or slightly corrosive substance, oxidizing (fire-intensifying) and toxic

86	corrosive or slightly corrosive substance, toxic

88	highly corrosive substance

X88		highly corrosive substance, which reacts dangerously with water 1/

883	highly corrosive substance, flammable (flash-point between 23 °C and 61 °C inclusive)

884	highly corrosive solid, flammable or self-heating

885	highly corrosive substance, oxidizing (fire-intensifying)

886	highly corrosive substance, toxic

X886		highly corrosive substance, toxic, which reacts dangerously with

water 1/

- corrosive or slightly corrosive substance, which can spontaneously lead to violent reaction

90	environmentally hazardous substance; miscellaneous dangerous substances

99	miscellaneous dangerous substance carried at an elevated temperature.

_________

1/	Water not to be used except by approval of experts.

5.3.3		Mark for elevated temperature substances

Tank-vehicles, tank-containers, special vehicles or especially equipped

vehicles for which a mark for elevated temperature substances is

required according to special provision 580 in column (6) of Table A of

Chapter 3.2 shall bear on both sides and at the rear a triangular shaped mark

with sides of at least 250 mm, to be shown in red, as reproduced below.

_______________________