## INF. 8

# ADR

# Part 5

Chapter 5.3  and 5.4

5.3.2 Orange coloured plate marking

5.4.1.2 Additional information required for certain classes

Executive summary:

Add 5.4.1.1 with an new provision , because the regulation existe in ADR 1999 under marginal number 2314 and 31 500 (2).

# Introduction

In 5.3.2.1.3 we have the regulation to affixed orange plates to the front and rear of tank-vehicles and transport units with the UN-number prescribed the lowest flashpoint.

For using this regulation in the transport document must be a information, which compartment contained the substances.

Proposal

New 5.4.1.1. 11

By using 5.3.2.1.3 , a multi-compartment tank-vehicule or transport-unit  ist marked according to 5.3.2.1.3 the substances contained in each compartment shall be specified in the transport document.

Justification

The same regulation existe in ADR 1999 Marginal number 2314 and 31500 (2).

_______