ECONOMIC COMMISSION FOR EUROPE	INF.4E

###### INLAND TRANSPORT COMMITTEE

Working Party on the Transport

of Dangerous Goods

(Seventy-second session,

Geneva, 13-17 May 2002)

## LIST OF PROPOSED CORRECTIONS TO THE 2001 VERSION OF ADR,

N:B: 	Corrections appearing in bold have not been submitted to the Joint Meeting (18-22 March 2002) but have been checked, if needed, with the OCTI Secretariat.

1.1.3.6.3	(Does not apply to the English version)

1.2.1	(Does not apply to the English version)

2.1.3.8	In the second sentence, replace "(see definition in 2.3.4.7)" with "(see definition in 2.3.5.1)".

2.2.3.1.1	Under NOTE 1, for "under the sustained combustibility test conditions given in sub-section 32.5.2 of Part III of the Manual of Tests and Criteria do not sustain combustion" read "do not sustain combustion according to the criteria of 32.2.5 of Part III of the Manual of Tests and Criteria".

Under NOTE 6, insert the words "highly corrosive and having a boiling point or an initial boiling point exceeding 35 (C" between "UN No. 2920 CORROSIVE LIQUID, FLAMMABLE, N.O.S." and "are substances of Class 8 (see 2.2.8.1).".

2.2.41.4	(Does not apply to the English version)

2.2.51.1.8	(Does not apply to the English version)

2.2.52.4	(Does not apply to the English version)

3.2.1	Under the explanatory text for Column (10) amend last sentence of the first paragraph to read: " If no code is given, carriage in portable tanks is not permitted unless a competent authority approval is granted as detailed in 6.7.1.3.".

Table A of Chapter 3.2

In column (18) delete "CV28" for all the entries for which a label conforming to model No. 2.3 is prescribed in Column (5).

| UN No. | Column No. | Corrections |
| --- | --- | --- |
| 1040 ethylene oxide (without nitrogen), 1363, 1364, 1365, 1373, 1379, 1386, 1442, 1805 solid entry, 2217, 2858 and 3175 | 14 | Delete the contents of the cell |
| 1040 ethylene oxide with nitrogen and 2481 | 14 | Insert "FL" |
| 1396 packing group III, 1418 packing group III, 1458 packing group III, 1459 packing group III, 1481 packing group III, 1482 packing group III, 1483 packing group III, 1503, 2870 (not in devices), 3119, 3120, 3229, 3230, 3239 and 3240 | 14 | Insert "AT" |
| 1598, 2077, 2250 and 2516 | 12 | Insert "SGAH" before "L4BH" |
| 1600, 2312, 2447 and 3250 | 18 | Delete "CV28/CW28" |
| 1790, packing group I, entry with more than 60% but not more than 85% hydrofluoric acid | 13 | Insert "TE1" |
| 1805, solid entry | 20 | Insert "80" |
| 2073, 2672 and 3318 | 2 | (Does not apply to the English version) |
| 2250 | 7 | Replace "LQ17" with "LQ18" |
| 2315 and 3151 | 7 | Replace "LQ29" with "LQ26 LQ29" |
| 2431, 2432 and 2433 liquid entry | 7 | Replace "LQ9" with "LQ19" |
| 2623 | 8 | Replace "LP01" with "LP02" |
| 3152 | 7 | Replace "LQ29" with "LQ25" |
| 3224 | 19 | Insert "S18" |
| 3244 | 17 | Replace "VV9" with "VV10" |
| 3207, packing group II | 9a | Delete "B2" |
| 3207, packing group III | 9a | Delete "B4" |
| 3354 | 19 | Delete "S7" |

3.4.5	(Does not apply to the English version)

4.1.4.1	R001	Delete special packing provision RR3.

4.1.4.2	IBC02	Delete special packing provision B11.

4.2.4.2.5 T50,

and 4.3.3.2.5	(Does not apply to the English version)

5.1.5.4	In the table, for special form radioactive material replace in the references column "1.6.5.4" with "1.6.6.3"; for packages containing 0.1 kg or more of uranium hexafluoride replace in the references column "6.4.22.3" with "6.4.22.1"; for approved packages design subjected to transitional measures replace in the columns for the competent authority approval "1.6.5" with "1.6.6" and "1.6.5.2, 1.6.5.3" with "1.6.6.2" in the references column.

In the table, in the references column, for Type B(U) packages add "6.4.22.2", forType B(M) packages add "6.4.22.3", for Type C packages add "6.4.22.2" and for special form radioactive material add "6.4.22.5".

5.4.1.1.6	Insert ", "EMPTY LARGE PACKAGING"" after "EMPTY IBC"

6.1.6.2	In the table for Class 8, before the entry for "Hydrazine, aqueous solutions with not more than 64% hydrazine by mass (UN No. 2030)" insert the following title "Corrosive liquids toxic (classification code CT1)"

6.4.22.7	Replace "1.6.5" with "1.6.6".

6.10.2.1	(Does not apply to the English version)

7.2.4	V8 (1)	Replace "2.2.41.19" with "2.2.41.1.17".

7.3.3	VV10	Insert ", as a full load," after "carriage in bulk is permitted".

7.4.1	In the first sentence, replace "Columns (12) and (13)" with "Columns (10) or (12)" and at the end of the sentence add "unless a competent authority approval is granted as detailed in 6.7.1.3".

7.5.4	Delete "2.3," in the second paragraph and in sub-paragraph (b) of the third paragraph.

7.5.11	(Does not apply to the English version)

______________________