|  | EU N.A. draft 1stPhase | Japan MLIT proposal（ 17 July） | Remarks |
| --- | --- | --- | --- |
| Vehicle Categoly | GVM < 2.5ton of ① M1 and ② N1 derived from M1 | ①Passenger Car ≦10 persons and ②Commercial vehicle with GVW≦2.5ton derived from Passenger Car |  |
| Effective Date | New Type from 10/'05 All type 7/'10 80% 12/'11 90% 12/'12 100% | A)Vehicles exept B New Type： 9/'05 All Type： 9/'10 [ B ) Vehicle listed in box will be ] [ New Type： 9/'07 ] [ All Type： 9/'12 ] | . |
| Impactor & Area | Child Impactor 3.5Kg for WAD 1000- (82.5mm forword from bonnet rear referrence line ) | Child Impactor 3.5Kg for WAD 1000-1700 Adult Impactor 4.5Kg for WAD1700－2100mm |  |
| Velocity & Angle | 35Km/h 50deg. | 32Km/h Angle shown in this table |  |
| Criteria & Area | Area≧2/3, HIC≦1000 Remaining Area, HIC≦2000 | ( |  |

＊EU N.A has leg impact test requirement which is not  shown in this table.

# Text boxes

2002.7.18  JAMA

"Pedestrian Protection"     Comparison of Draft Regulations

@very low vehicle

（ with Hpt hight ≦ 450mm（JAMA)）

＠vehicle with high durability（SUV or CV）

＠Full cab-over    @Hybrid Powered Car

| Classification of Vehicle Type | Child | Adult |
| --- | --- | --- |
| Veh. w/ BLE < 835mm (Sedan) | 65 | 65 |
| Veh. w/ BLE ≧ 835mm (SUV) | 60 | 90 |
| Veh. w/ Bonnet Angle ≧ 30degree (Cab over) | 25 | 50 |