UK proposal for amendments to Regulation No. 48, paragraph 6.20.6.

The UK offers the following proposal, in order to:

1)	reflect more precisely the outcome of the third ad-hoc AFS meeting which agreed to mandate automatic headlamp levelling for AFS, and

2)	align more closely with the existing Regulation No. 48 text.

Paragraphs 6.20.6.1.2. to 6.20.6.2.2., amend to read:

"6.20.6.1.2.	The downward inclination of the horizontal part of the "cut-off" of the basic passing beam shall remain between the limits indicated in paragraph 6.2.6.1.2. of this Regulation under all the static loading conditions of the vehicle of annex 5 of this Regulation and the initial aiming shall be within the specified values;

6.20.6.1.2.1.	In case the basic passing beam is generated by several beams from different lighting units, the provisions according to paragraph 6.20.6.1.2. above apply to each said beam's "cut-off" (if any), which is designed to project into the angular zone, as indicated under item 9.4.1. of the communication form conforming to the model in annex 1 to Regulation No. xxx.

6.20.6.2.	Headlamp levelling device

6.20.6.2.1.	In the case where a headlamp levelling device is necessary to satisfy the requirements of paragraph 6.20.6.1.2., the device shall be automatic.

6.20.6.2.2.	In the event of a failure of this device, the passing beam shall not assume a position in which the dip is less than it was at the time when the failure of the device occurred."

___________________