UN/SCETDG/30/INF.73

# COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

## HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirtieth session

# Geneva, 4-12 (a.m.) December 2006

Item 2(a)(ii) of the provisional agenda

PROPOSALS OF AMENDMENT TO THE RECOMMANDATIONS

ON THE TRANSPORT OF DANGEROUS GOOD

Amendments to ST/SG/AC.10/C.3/2006/93

### Transmitted by the expert from the United States of America

Based on comments received from the Sub-Committee at the present meeting, the following amendments are made to the proposals presented in ST/SG/AC.10/C.3/2006/93:

- The proposals to amend tank instructions for substances for which specific data is not available are withdrawn.

- The proposals to amend tank instructions for materials of Classes other than Division 6.1 Packing Group I are withdrawn.

- The proposal relative to Bromoacetone is withdrawn as the Sub-Committee has already agreed to amend the tank provisions consistent with the guiding principles previously in the biennium.

A revised annex is provided which includes the toxicity and vapour pressure data for all substances whose tank instructions are proposed to be amended. The Sub-Committee is invited to take a decision only on substances of Division 6.1 PG I for which data has been presented. The remainder of the entries are retained in struck-out text for the information of the Sub-Committee as they may be the subject of future work.

Proposed Revised Tank Instructions for Toxic by Inhalation Liquids

| Liquids with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50: |
| --- |
|  |  |  |  |  | Current | Proposed | Liquid |
| UN # | Name | Class | SR | PG | Instruction | Special Provisions | Instruction | Special Provisions | LC50 (ml/m3) | SVC | 500 LC50 |
| 1092 | ACROLEIN, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP7 TP13 | T22 | TP2, TP7, TP13 | 25 | 28900 | 12500 |
| 1185 | ETHYLENEIMINE, STABILIZED | 6.1 | 3 | I |  |  | T22 | TP2, TP13 | 76 | 217000 | 38000 |
| 1238 | METHYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 | 88 | 135000 | 44000 |
| 1239 | METHYL CHLOROMETHYL ETHER | 6.1 | 3 | I | T14 | TP2 | T22 | TP2, TP13 | 160 | 210000 | 80000 |
| 1244 | METHYLHYDRAZINE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 | 68 | 50300 | 34000 |
| 1251 | METHYL VINYL KETONE, STABILIZED | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 | 5 | 93400 | 2500 |
| 1994 | IRON PENTACARBONYL | 6.1 | 3 | I |  |  | T22 | TP2, TP13 | 6 | 30300 | 3000 |
| 2480 | METHYL ISOCYANATE | 6.1 | 3 | I |  |  | T22 | TP2, TP13 | 22 | 458000 | 11000 |
| 2482 | n-PROPYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T22 | TP2, TP13 | 44 | 69700 | 22000 |
| 2484 | tert-BUTYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T22 | TP2, TP13 | 22 | 19700 | 11000 |
| Liquids with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 |
|  |  |  |  |  | Current | Proposed | Liquid |  |  |  |  |
| UN # | Name | Class | SR | PG | Instruction | Special Provisions | Instruction | Special Provisions | LC50 | SVC | 10 LC50 |
| 1098 | ALLYL ALCOHOL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 253 | 26000 | 2530 |
| 1135 | ETHYLENE CHLOROHYDRIN | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 74 | 6450 | 740 |
| 1143 | CROTONALDEHYDE or CROTONALDEHYDE, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 93 | 42100 | 930 |
| 1163 | DIMETHYLHYDRAZINE, UNSYMMETRICAL | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 504 | 206000 | 5040 |
| 1182 | ETHYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 145 | 55300 | 1450 |
| 1595 | DIMETHYL SULPHATE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 17 | 1000 | 170 |
| 1605 | ETHYLENE DIBROMIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 650 | 11300 | 6500 |
| 1647 | METHYL BROMIDE AND ETHYLENE DIBROMIDE MIXTURE, LIQUID | 6.1 |  | I |  |  | T20 | TP2, TP13 | -- | -- | -- |
| 1670 | PERCHLOROMETHYL MERCAPTAN | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 | -- | 32900 | -- |
| 1695 | CHLOROACETONE, STABILIZED | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 262 | 41900 | 2620 |
| 1722 | ALLYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 61 | 20400 | 610 |
| 1752 | CHLOROACETYL CHLORIDE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 660 | 24600 | 6600 |
| 1809 | PHOSPHORUS TRICHLORIDE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 208 | 125000 | 2080 |
| 1892 | ETHYLDICHLOROARSINE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 36 | 2800 | 360 |
| 2232 | 2-CHLOROETHANAL | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 160 | 24300 | 1600 |
| 2334 | ALLYLAMINE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 590 | 261000 | 5900 |
| 2337 | PHENYL MERCAPTAN | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 66 | 1450 | 660 |
| 2382 | DIMETHYLHYDRAZINE, SYMMETRICAL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 680 | 92000 | 6800 |
| 2407 | ISOPROPYL CHLOROFORMATE | 6.1 | 3 8 | I |  |  | T20 | TP2, TP13 | 299 | 36800 | 2990 |
| 2438 | TRIMETHYL-ACETYL CHLORIDE | 6.1 | 3 8 | I | T14 |  | T20 | TP2, TP13 | 507 | 35500 | 5070 |
| 2477 | METHYL ISOTHIOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 635 | 27400 | 6350 |
| 2485 | n-BUTYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 105 | 13900 | 1050 |
| 2487 | PHENYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 16 | 2470 | 160 |
| 2488 | CYCLOHEXYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 15 | 2170 | 150 |
| 2521 | DIKETENE, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 551 | 10500 | 5510 |
| 2606 | METHYL ORTHOSILICATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 200 | 13300 | 2000 |
| 2644 | METHYL IODIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 448 | 414000 | 4480 |
| 2646 | HEXACHLOROCYCLO-PENTADIENE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 | 3 | 100 | 30 |
| 3023 | 2-METHYL-2-HEPTANETHIOL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |  |  | 1020 |
| 3246 | METHANESULPHONYL CHLORIDE | 6.1 | 8 | I | T14 | TP2 TP12 TP13 | T20 | TP2, TP12, TP13 | 205 | 2760 | 2050 |

# Footnotes

While no data can be provided on the mixture as compositions will vary, data has been provided for both methyl bromide and ethylene dibromide.