RDW TEST CENTRUM Lelystad

TEST PLAN MCGTR	MEETBLAD nr 2

| Driver | 2 |
| --- | --- |
| Place | Lelystad |
| Vehicle make/type | Triumph |
| VIN | ND03CTI.5?? |
| Tires; tyre pressure | front: Bridgestone Battax B1020 120/70ZR17 M/C 58W; press. 2,5 bar rear: Bridgestone Battax B1020 180/55ZR17 M/C 78W; press. 2,9 bar |
| Test weights | Front 161 kg Rear 224 kg |
| Date | 11-05-2006 |
| Road-surface | Asphalt/basalt | Weather conditions | Dry |
| Wind force | 1 | m/s | Wind direction | N-NW |
| Barometric pressure | 1015 | mbar | Temperature | 19 | ˚C |
| Humidity | 50 | % | Remarks | - |

4.9.3 Stops on high friction surface (Vehicle lightly loaded )

|  | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Actual speed [km/h] | 57,8 | 58,5 | 62,5 | 62,4 | 61,3 | 63,4 |
| Deceleration [m/sec2] | 8,03 | 8,97 | 7,69 | 9,03 | 8,42 | 7,94 |
| Brake distance [m] | 19,24 | 17,74 | 22,15 | 21,32 | 20,80 | 24,00 |
| Controlforce front [daN] | 25 | 27,5 | 23 | 21 | 24,5 | 17 |
| Controlforce rear [daN] | 31 | 25,5 | 28 | 30 | 32 | 28,5 |
| t 40 – 20 [s] | 0.5800 | 0.6300 | 0.8400 | 0.5900 | 0.6400 | 0.6800 |
| Z | 0.9655 | 0.8889 | 0.6667 | 0.9492 | 0.8750 | 0.8235 |
| Diagram number | - | - | - | - | - | - |
| Document name: RKhoogb _ - | 001 | 003 | 011 | 012 | 013 | 015 |

4.9.4. Stops on low friction  (Vehicle lightly loaded )

|  | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Actual speed [km/h] | 56,8 | 62,8 | 58,6 | 60,6 | 59,7 | 60,1 |
| Deceleration [m/sec2] | 2,27 | 2,40 | 2,31 | 2,56 | 2,36 | 2,51 |
| Brake distance [m] | - | - | - | - | - | - |
| Controlforce front [daN] | 19 | 17,5 | 16,5 | 19,5 | 17,5 | 17,5 |
| Controlforce rear [daN] | 30 | 32 | 32,5 | 33,5 | 36,5 | 34,0 |
| t 40 – 20 [s] | 2.5300 | 2.1600 | 2.4000 | 2.1000 | 2.4400 | 2.1900 |
| Z | 0.2213 | 0.2593 | 0.2333 | 0.2667 | 0.2295 | 0.2557 |
| Diagram number | - | - | - | - | - | - |
| Document name: Rklaag _ - | 013 | 014 | 016 | 018 | 020 | 021 |

4.9.7. Wheel lock check –low to hight surface transition  (Vehicle lightly loaded )

|  | 1 | 2 | 3 |
| --- | --- | --- | --- |
| Actual speed [km/h] | 56,7 | 58,0 | 57,3 |
| Speed low-high [km/h] | 48,4 | 50,7 | 49,7 |
| Response time transition | 0.30 | 0.31 | 0.29 |
| Controlforce front [daN] | 23 | 20,5 | 18 |
| Controlforce rear [daN] | 33 | 42 | 35,5 |
| Diagram number |  |  |  |
| Document name: Rovergang _- | 002 | 004 | 006 |

RDW TEST CENTRUM Lelystad

TEST PLAN MCGTR	MEETBLAD nr 2

4. K measurement test – ECE R78 ABS Annex 4

Test results Wet Low Friction Surface

| Vstart [km/h] | Control force front [daN] | Control force rear [daN] | t40-20 [s] | Z | diagram number |
| --- | --- | --- | --- | --- | --- |
| 46,6 | ? | 3,5 | 2,35 | 0.238 | RKLnoABS_006 |
| 47,3 | ? | 5 | 2,32 | 0.241 | RKLnoABS_013 |
| 47,8 | ? | 5 | 2,23 | 0.251 | RKLnoABS_015 |
| 47,0 | ? | 4 | 2,27 | 0.247 | RKLnoABS_029 |
| 46,8 | ? | 3,5 | 2,29 | 0.245 | RKLnoABS_030 |

Test results Wet High Friction Surface

| Vstart [km/h] | Control force front [daN] | Control force rear [daN] | t40-20 [s] | Z | diagram number |
| --- | --- | --- | --- | --- | --- |
| 61,3 | 9 | ? | 0,69 | 0.812 | RKHnoABS_010 |
| 61,4 | 8,5 | ? | 0,72 | 0.778 | RKHnoABS_012 |
| 60,2 | 8 | ? | 0,74 | 0.757 | RKHnoABS_016 |
| 60,7 | 10,5 | ? | 0,71 | 0.789 | RKHnoABS_020 |
| 59,9 | 8,5 | ? | 0,76 | 0.737 | RKHnoABS_024 |

Test results Dry High Friction Surface

| Vstart [km/h] | Control force front [daN] | Control force rear [daN] | t40-20 [s] | Z | diagram number |
| --- | --- | --- | --- | --- | --- |