27-GTRBR-06

06/06/09

6th Informal meeting: GTR motorcycle braking – 06/06/06-07

Participants:

Canada		: Mr Brault

USA		: Mr Wondimneh, Soodoo

Japan, JASIC	: Messrs Hoshi, Hayashi, Hibara, Kiuchi, Sahashi

IMMA		: Messrs  Cart, Dutrieux, Honda, Rogers, Stocker, Twining

India		: Badusha, Ramiah

UK		: Thatcher

1.	Minutes

1.1 	Minutes of 5/GTRBR

Agreed	: The minutes of 5/MCGTR (27-GTRBR-05 of 05/11/26)

1.2	Documents issued since the last agenda

The documents 19-GTRBR-06 to 26-GTRBR-06

2.	Discussion of the results of the ABS test plan

Documents : 11-GTRBR-06, plan for action

: 18-GTRBR-06, project progress

: 10-GTRBR-06-rev1, revised test plan

Noted	 : The remaining issues (as discussed during the pilots tests) were related to the ABS testing:

- Surface measurement of friction methods/comparison between K-method – ASTM

- Performance requirements: low µ and high µ, low-high µ jump;

- ABS cycling with a certain input brake force;

: The presentation of the testing results from the NHTSA contractor

: The main conclusions from the ABS testing were:

- The K-method and the ASTM method had showed comparable results.

- Performance requirements for low µ and high µ could be met easily.

(However the low µ surface was slightly above 0,45)

- The low-high µ jump test had showed that it was difficult to determine a specific time

to identify the low to high µ transition.

: USA’s suggestion to only look at the point of rise of deceleration value.

- During tests, some motorcycles had experienced a rear wheel lift : did this event mean

a failure of meeting the performance requirements ?

: The test results from UK:

- low µ test done on a surface slightly less than 0.3; high µ test done at (approx) 0,75

- low to high µ jump test done for brake controls actuated simultaneously and

separately.

: The test results from NL:

- Test done on asphalt and basalt; low µ test done on a surface slightly less than 0,3

- It was not clear if only 6 stops had been made.

- It was not clear where the response transition time of the low to high µ stop came

from.

- Need to check in ”MEETBLAD nr 1” if the test results of the Wet, High Friction

Surface were actually not the test results of the Dry High Friction Surface.

: The test results from Harley-Davidson:

- The test had been done one bike with one rider.

- Tests done with both brake controls applied simultaneously.

- Test track of asphalt (0,98) and basalt (less or equal to 0,3).

- A test bike weight of 760 pounds (including test equipment and rider).

: The following paragraphs of the GTR text had been agreed without change:

    - Paragraph 4.9.1 `General Information`

    - Paragraph 4.9.3.2 `Performance Requirements/high friction surface`

: For Paragraph 4.9.3.1 `Test conditions and procedure`, IMMA proposed to use a maximum

brake actuation value.

: Harley-Davidson did not see the need for a value as the only issue to consider was to confirm

the ABS cycling.

: Harley-Davidson proposed a wider range/tolerance.

: Two possibilities/options for the “brake actuation force” section of Paragraph 4.9.3:

  - the force applied shall be that which is necessary to ensure that the ABS is cycling fully from the test speed to 10 km/h (thus no forces specified)

  - to have a max. brake actuation force of 250 N for hand control and 400 N for foot control (from § 4.4) and link it to a note which states that the ABS must be cycling throughout the stop)

: USA preferred option 2 but IMMA and Japan wanted to have option 1.

: TransportCanada preferred possibility 2, but as it was not a requirement in any existing

regulation, could accept option 1.

: IMMA reasoning was that there was no justification based on long time testing.

: IMMA though that the basic (foundation) brake test already covered the general braking

capability of the motorcycle.

: USA needed for compliance reason to include an upper limit and therefore could not accept

option 1.

: For Paragraph 4.9.7.2 `Performance Requirements/low to high friction surface transition`:

: UK was not completely satisfied as they would like to have the same text as in R78.

: IMMA noted that not enough data was yet available in order to include specific

values.

: A proper justification, if any, should be prepared for GRRF when possible.

: A presentation from US with counter proposal which would require meeting a specified

deceleration over a length of track which includes the transition point (low to high) in the

middle.

: IMMA commented that this would need time to be verified and would also require the test

conditions to be specified.

: USA stated that the low-high mu jump test was not necessary, and then could accept only a

stability test instead.

: Harley-Davidson using a procedure based on a % of the average deceleration of the high µ test,

which must be attained within a certain response time after the low to high transition point.

: Japan stated that the USA counter proposal would require additional testing.

: The Harley-Davidson procedure could be checked with the current available test data but more

detailed investigation would be necessary.

: UK stated that there was not enough time but was in favour of the premise behind the

Harley-Davidson procedure.

: IMMA would consider the various options.

: No specific text had been included as it was agreed that not enough data was available and

that IMMA’s concerns had been addressed by allowing lower control forces.

Agreed: The main issue was to confirm the ABS functioning;

: No final decision was achieved for Paragraph 4.9.3.1.

: It was decided to keep both possibilities in the draft GTR text with arguments for both in the

Preamble.

: The GTRBR Group would have to reach an agreement before the extra GRRF session of June.

: For Paragraph 4.9.4.2 `Test conditions and procedure/low friction surface`, it was agreed to use

0.7 times (70%) of the actual test surface coefficient with a maximum of 0.45 PBC, which

would mean that manufacturers could do their test on lower then 0.45 PBC but (for US) would

have to verify also a test on 0.45 PBC as this would be the compliance value

to be checked by NHTSA

: The following text:

(a) the stopping distance (S) shall be  ≤ 0.0056V2/P  (where V is the specified test speed in km/h, P is the peak braking coefficient and S is the required stopping distance in meters) or the MFDD shall be ≥ 6.87P m/s2

: The following text for Paragraph 4.9.7.2 `Performance Requirements/low to high friction

surface transition` had been confirmed

After passing over the transition point between the low and high friction surfaces, the vehicle deceleration shall increase.

3.	Discussion of the Indian questions

Documents: 15-GTRBR-06, the Indian comments

Noted	: The Indian presentation								(Annex1.ppt)

: India made a presentation which contains a counter proposal to §4.4.3, that was less stringent,

because of certain types of small motorcycles which had difficulty meeting the proposed

requirements.

: There were no such issues for other Members of the GTRBR Group.

: Some mechanisms in the 1998 Global Agreement would allow the Indian issue to be solved at

the national level, and this would be the best solution at this time.

Agreed	: The points listed as replies to the comments 					(Annex2.doc)

4.	Next steps

Agreed	: The following timetable

- by 9th of June, the pro’s/con’s on the outstanding item (ABS brake actuation

force) would be circulated by the Chairman to the GTRBR Members

- By the 14th of June, GTRBR Members would indicate their preference to the

Chairman

- The Chairman would revise the Preamble text and the GTR text as agreed 			during the meeting and circulate them by 12th of June

- Comments would be forwarded by GTRBR Members to the Chairman

by 14th June

- The final revised draft GTR text would be forwarded to the UN Secretariat as

an informal document to GRRF

5.	Future meetings

Agreed	: A date for 7/MCGTR would be defined if necessary