# UN/SCEGHS/17/INF.14

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the Globally

# Harmonized System of Classification

# and Labelling of Chemicals

# Seventeenth session,

# Geneva, 29 June – 1 July 2009

# Item 2 (d) of the provisional agenda

UPDATING OF THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Revision of Annexes 1, 2 and 3 of the GHS – Precautionary Statements

Transmitted by the expert from the United Kingdom on behalf of

the informal correspondence group

Introduction

1.	At its sixteenth session (December 2008), the Subcommittee approved the continuing work plan for the informal correspondence group (CG) on the improvement of Annexes 1, 2, and 3 of the GHS (see document ST/SG/AC.10/C.4/2008/CRP.3/Add.5).  This stated that the group would:

“Pursue work to further improve Annexes 1, 2 and 3 of the GHS.  The correspondence group will work on the following work streams, with the first given priority:

Workstream 1:  to develop proposals to rationalize and improve the usability of hazard and precautionary statements, including proposals to eliminate redundancies among these statements

Workstream 2: to improve the presentation of Annexes 1 to 3 of the GHS, taking into account the intended audiences, uses and purposes of the GHS.”

2.	This information document aims to make progress within workstream 1 by presenting a number of suggestions to edit and rationalise the current list of GHS precautionary statements (PS).

3.	The paper also sets out proposals for some changes to the PS for physical hazards which have been put forward by CEFIC.  The two sets of suggested changes are presented together with a view to ensuring that the overall set of amendments agreed to the PS are consistent and complementary.

4.	An earlier version of these proposals (not including the CEFIC proposals) was presented to the Subcommittee in information document UN/SCEGHS/15/INF.26.  The proposals have since been discussed within the informal CG by email and at the break-out meetings of the group at the 15th and 16th sessions.  Most recently comments have been received from the CG on a draft of this document circulated in May 2009, which included the CEFIC proposals.  The present document has been revised to take into account the comments and feedback received during these discussions, however the proposals remain in development and are subject to further discussion and agreement within the informal CG prior to submission of a formal proposal.  The purpose of this information document is therefore to give an update to the Subcommittee on the work being carried out by the CG and, acknowledging the limited time for scrutiny before the plenary meeting of the Subcommittee, to seek its feedback on the proposals in their current form.

5.	Subject to the subcommittee’s views, the informal CG will continue work on the proposals with a view to submitting a working document for the December 2009 meeting.

Proposals for rationalisation of GHS precautionary statements

6.	Presently there are a number of factors limiting the usability of the GHS PS:

(a)	A high number of PS may be triggered for a substance or mixture, even with a relatively simple classification.  Including all the statements triggered for a given chemical would arguably confuse the user and reduce the effectiveness of hazard and safety communication.

(b)	Selection of appropriate PS by manufacturers and suppliers can be difficult when a large number are triggered.

(c)	Different hazard classifications trigger similar but different PS, leading to arguably unnecessary small differences between precautionary measures recommended in different circumstances.

7.	Given the number and relatively unstructured nature of the existing PS, there is substantial scope for reducing both the overall number of PS and the amount of precautionary “wordage” that must appear on labels, without reducing the essential precautionary information given on labels.

8.	This paper includes proposals which aim to achieve this through making editorial amendments to the current list of PS.  Proposals are also included to rephrase statements where they are currently unclear or confusing.

Example 1

9.	Currently there are a few cases where very similar precautionary statements are given within the Prevention and Storage categories.  For example, the following statements appear:

P220 Keep/store away from clothing/…/combustible materials

P420 Store aware from other materials

10.	The precautionary behaviour prescribed by these two statements is essentially the same (to keep the chemical in question away from various other materials).  Therefore, the statements could be replaced with one single statement without loss of protection:

P220  Keep/Store away from clothing/…/combustible materials/other materials

11.	This statement gives the manufacturer/supplier or competent authority the flexibility to specify, as appropriate, the materials that the chemical needs to be kept away from.

12.	It is also proposed to include some additional guidance in the ‘conditions for use’ column to clarify the use of the words ‘keep’ and ‘store’.  It is suggested that ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used only when this precaution applies to storage.

Example 2

13.	Currently the Prevention category contains the following two statements:

P280 Wear protective gloves/protective clothing/eye protection/face protection.

P281 Use personal protective equipment as required

14.	P280 applies to several hazard categories, and for each of these guidance is given in the ‘conditions for use’ column as to which specific type of equipment should be specified by the manufacturer/supplier or competent authority (e.g. ‘specify face protection’ for Explosives, divisions 1.1-1.5).  No further guidance is given for application of P281, which applies to unstable explosives and CMR categories 1A, 1B and 2.

15.	Given the similarity between these statements, rationalisation could be achieved by replacing them with a single statement:

P280 Wear protective gloves/protective clothing/eye protection/face protection/…

16.	Where specific guidance is currently given as to the type of equipment to be specified in P280 this should be retained in its current form for the relevant hazard categories.  In the case of the categories to which P281 applies, it is proposed that the general direction ‘manufacturer/supplier or the competent authority to specify type of equipment’ should be added to retain the current flexibility of this statement.  Adding the ellipsis ‘…’ to this statement would also indicate that further types of personal protective equipment may be required for these hazard categories other than those specifically mentioned.

Example 3

17.	The current list of PS includes six statements recommending that a user seek medical attention in different circumstances:

|  | Current precautionary statements |  | Suggested precautionary statements |
| --- | --- | --- | --- |
| P310 | Immediately call a POISON CENTER or doctor/physician | P310* | Immediately call a POISON CENTER/ or doctor/physician/… |
| P311 | Call a POISON CENTER or doctor/physician | P311* | Call a POISON CENTER/ or doctor/physician/... |
| P312 | Call a POISON CENTER or doctor/physician if you feel unwell | P312* | Call a POISON CENTER/ or doctor/physician/… if you feel unwell |
| P313 | Get medical advice/attention |  |  |
| P314 | Get medical advice/attention if you feel unwell |  |  |
| P315 | Get immediate medical advice/attention |  |  |

18.	Although phrased slightly differently, the basic advice being given here – to seek medical attention from an appropriate source – is the same in relation to P310-P312 and P313-P315, with differences within these two groups of statements indicating different degrees of urgency.  This suggests that a single set of three statements could be used instead of the current six.

19.	It is also necessary to take into account that the appropriate source of ‘front line’ medical advice will differ in different jurisdictions.  In some regions and countries Poison Centers or Poison Control Centers will be the appropriate first point of contact for workers or consumers, whereas in others Poison Centers only provide advice to medical professionals, and consumers and workers should seek advice from a different source.  Therefore, while there is scope for reducing the number of PS of this type, adequate flexibility is needed to take into account different arrangements for seeking medical advice or attention which may be in place.

20.	It is therefore suggested that three statements, P310*-P312* are used as listed in the right hand column above.  These statements would apply to all the categories to which P310-P312 and P313-P315 currently apply – P310* would take over the hazard categories to which P310 and P313 currently applies, and so on.  They would also replace P310-P312 and P313-P315 in combined PS, as appropriate.  Use of the slash ‘/’ indicates that the manufacturer/supplier or competent authority should specify the appropriate source of first line medical advice, depending on the nature of the hazard and the way that the relevant services are organised locally.

21.	It is also suggested that text be placed in the column (5) where these statements apply stating that ‘manufacturer/supplier or the competent authority to specify the appropriate source of medical advice’.

22.	However it is recognised that in some cases more than one possible source of medical attention may be appropriate in relation to a single product or chemical.  In this case, the generic statement ‘Get medical advice/attention’ or ‘get immediate medical advice/attention’ may be appropriate.  These statements are therefore mentioned as options in the ‘conditions for use’ column.

23.	The advantages of this rationalisation would be three-fold: first to reduce the overall number of PS; second, to avoid any confusion which could arise from differences in instructions about the type of medical attention to be obtained in different situations; and third to give flexibility for statements which reflect the arrangements in any country or region to be selected as appropriate.

Amendments to physical precautionary statements

24.	In addition some amendments are proposed to the precautionary statements for physical hazards with a view to rationalising and clarifying the conditions of application for these statements.

Organic Peroxides and Self-reactive substances

25.	The hazardous properties of organic peroxides and self-reactive substances are more or less the same.  In GHS the classification principles, classification flow-chart and tests to be executed are also identical as well as the breakdown of Types A-G.  Furthermore, types A-G of organic peroxides and self-reactive substances have the same hazardous properties description. Therefore it is proposed to harmonise the precautionary statements for these two hazard classes.

26.	To achieve this it is proposed to apply the following additional precautionary statements to Organic peroxides:

P370 + P380 + P375: In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. (types A and B only)

P403: Store in a well-ventilated place. (types A, B, C, D, E, F)

27.	The following precautionary statement would also apply in addition to Self-reactive substances and mixtures (Types A, B, C, D, E, F).

P410: Protect from sunlight

28.	Finally, the statement P370 + P378: In case of fire: Use … for extinction, has been removed from the precautionary statements for self-reactive substances together with the note, “Manufacturer /supplier of the competent authority to specify appropriate media. – if water increases risk’.  This is because water can always be used for extinction with chemicals within these hazard classes since in no case do they react with water.   Moreover, water would in all cases be the recommended means to extinguish such fires because of its cooling capacity and ability to significantly reduce the effect of the decomposition of the materials.

Gases under pressure

29.	Precautionary statement P410, “Protect from sunlight” is currently assigned to compressed gases, liquefied gases and dissolved gases within hazard class 2.5.

30.	The risk of increasing the internal pressure of a gas receptacle up to its test pressure or of having it liquid full because of its exposure to sunshine does not exist at certain latitudes but may exist at others.  This requirement may be completely irrelevant in northern countries but could make sense in certain southern countries.

31.	Therefore it is proposed to add the following note under ‘conditions of use’ for this statement: “- To be used in countries where the likelihood exists for the content of the receptacle to exceed 60°C if the receptacle is not protected from sunshine.”

32.	The criterion of 60°C is taken from the criteria to determine the maximum filling ratio for liquefied gases in P200 (3)(c) of the UNRTDG (the Orange Book): “.....in addition the liquid phase shall not fill the pressure receptacles at any temperature up to 60°C."  This criterion gives a safety margin versus the other criteria of P200 that limits the internal pressure at 65°C below the test pressure of the receptacle.

Flammable liquids/gases, explosives, organic peroxides

33.	Amendments as shown in Annex 2 are proposed for the following reasons:

34.	In some cases the list of hazard classes or categories to which a precautionary statement has to be applied was incomplete (e.g. explosives are not mentioned for P234 "Keep only in original container" although their classification is linked to a certain packaging through the division assignment procedure).

35.	In some cases conditions for use are added or further refined, respectively.

Numbering issues

36.	In light of the proposed changes to PS, a decision is needed on how the alphanumeric coding of PS should be adapted to take these into account.  Three options for this have been considered:

Option 1:  Re-order numbering after changes so that the numbering remains sequential within each group of PS (groups being P20X, P21X, etc.).  For example, if P307 is deleted as suggested above, the current P308 (IF exposed or concerned:) would be renumbered P307, and the current P309 (IF exposed or if you feel unwell:) would be renumbered P308.  Aside from this, edited PS retain their existing numbering.

Option 2: Edited PS retain their existing numbering, and other statements retain the same numbering as they currently have where possible.  However, entirely new PS would be given a new number.

Option 3: Unchanged PS retain the same numbering, but any changed statements are given a new number.

37.	The advantages and disadvantages of each option are summarised below.

| Option | Advantages | Disadvantages |
| --- | --- | --- |
| 1 | There will be no gaps in numbering after the PS have been edited – numbering remains sequential within each group of PS. | Many statements may need to be given a new number to retain sequential numbering, even though they have not changed in any way. Users may find this confusing. |
| 2 | Numbering of statements can stay in the same grouped format provided the number of new statements does not increase substantially (since little need for new numbers) Statements for which there are only minor editorial changes retain the same numbers, facilitating cross-referencing between versions of the GHS. | Some gaps will appear in numbering where statements have been removed. Some statements will change in wording while retaining the same number, which could cause confusion where there is use of different editions of the GHS. |
| 3 | Statements which retain the same numbering will have exactly the same wording in different editions of the GHS. | There will now be numerous gaps in the numbering as any statement that is edited will require an entirely new number. Continued use of the existing numbering groups may not be possible, since a large number of new numbers will be needed, especially in future if further editorial amendments are made to the PS. |

38.	In view of the above considerations, option 2 is recommended as involving the best combination of maintaining existing numbering where possible while avoiding confusion due to the same numbers being assigned to different statements.  However, the views of the subcommittee are welcomed on this issue.

Summary of annexes

39.	A summary of the Annexes to this document is given below:

Annex 1 – 	List of suggested editorial changes to precautionary statements with brief explanations

Annex 2 – 	List of suggested changes to physical precautionary statements

Annex 3 – 	Suggested changes to tables A3.2.1, A3.2.2, A3.2.3, A3.2.4 (markup showing changes)

Annex 4 – 	‘Clean’ copy of tables A3.2.1, A3.2.2, A3.2.3, A3.2.4, incorporating all proposed changes

Annex 5 – 	Suggested changes to the tables in A3.3.5 (marked up)

Next steps

40.	Information document UN/SCEGHS/16/INF.24 informed the subcommittee that the informal correspondence group are considering, in addition to editorial changes to the PS, a number of further approaches to rationalising the PS in Annex 3 of the Purple Book.  These include:

(a)	Combination of precautionary statements;

(b)	Re-grouping of precautionary statements;

(c)	Guidance for selection of precautionary statements;

(d)	An ‘order of preference’ for precautionary statements;

(e)	Use of ‘signpost’ statements which refer to more detailed precautionary information located other than on the label;

41.	Taking into account document UN/SCEGHS/16/INF.20 (Canada) the informal correspondence group informally agreed to consider the above approaches in the order listed above.  Other approaches to rationalisation of the precautionary statements will also be considered as appropriate and suggestions from the subcommittee are welcomed.  The informal correspondence group aims to bring forward further proposals based on these approaches at subsequent Subcommittee meetings.

42.	It was agreed at the December 2008 meeting of the Subcommittee that the correspondence group should also take forward work on Workstream 2, to improve the presentation of Annexes 1 to 3 of the GHS, although Workstream 1 (rationalisation/reduction in redundancy of PS) should be given priority.  It is therefore the intention of the correspondence group to take forward work on Workstream 2 once satisfactory progress has been made within Workstream 1.

Action requested of the subcommittee

43.	The Subcommittee is invited to:

(a)	Comment on the proposals to rationalise precautionary statements given in paragraphs 5. – 22. and Annex 1, 3, 4 and 5;

(b)	Comment on the proposals to rationalise and amend the physical precautionary statements given in paragraphs 23. – 34. and Annex 2, 3, 4 and 5;

(c)	Comment on the proposal for re-numbering the PS in light of the changes, given in paragraphs 35.- 37.

| Annex 1: List of suggested changes to precautionary statements with brief explanations (Rationalisation) |
| --- |
| Code | Statement | Issue | Suggested change |
| P101 | If medical advice is needed, have product container or label at hand | None | None |
| P102 | Keep out of reach of children | None | None |
| P103 | Read label before use | Redundant – odd advice | Replace with: Read entire label before use |
| P201 P202 | Obtain special instructions before use Do not handle until all safety precautions have been read and understood. | P201 not clear, and seems to be redundancy between the statements. | Replace with: Do not handle until all safety precautions have been read and understood |
| P210 | Keep away from heat/sparks/open flames/hot surfaces. – No smoking. | None | None |
| P211 | Do not spray on an open flame or other ignition source | None | None |
| P220 P420 | Keep/store away from clothing/…/combustible materials Store away from other materials | Apparent redundancy, though P220 is prevention, and P420 Storage at present. | Replace by single statement: Keep/Store away from clothing/…/other materials/combustible materials. Manufacturer to specify incompatible materials and whether ‘keep’ or ‘store’. - ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used when this precaution only applies to storage |
| P221 | Take any precaution to avoid mixing with combustibles/… | ‘any precaution’ is not clear and seems redundant. | Replace with: Do not mix with combustibles |
| P222 | Do not allow contact with air | None | None |
| P223 | Keep away from any possible contact with water, because of violent reaction and possible flash fire | None | None |
| P230 | Keep wetted with… | None | None |
| P231 | Handle under inert gas | None | None |
| P422 | Store contents under… | None | None |
| P232 | Protect from moisture | None | None |

| Annex 1: List of suggested changes to precautionary statements with brief explanations (Rationalisation) (cont’d) |
| --- |
| Code | Statement | Issue | Suggested change |
| P233 P404 | Keep container tightly closed Store in a closed container | Redundancy, though P233 is prevention and P404 is storage. In some cases, (e.g. Acute toxicity, inhalation cat 1) P233 comes under storage as combination statement P403+P233 | Delete P404 and replace with modified P233, ‘Keep container in a tightly closed container’. This covers relevant precaution for substances and mixtures which, in contact with water, emit hazardous gases, which is the only hazard category to which P404 applies. |
| P234 | Keep only in original container | None | None |
| P235 | Keep cool | None | None |
| P240 | Ground/bond container and receiving equipment | None | None |
| P241 | Use explosion-proof electrical/ventilating/lighting/…/equipment | Any equipment used (electrical or non-electrical) should be explosion proof, so could be shorter | Instead use ‘Use explosion proof … equipment’. May also specify that manufacturer/supplier or the competent authority to specify equipment. |
| P242 | Use only non-sparking tools | None | None |
| P243 | Take precautionary measures against static discharge | None | None |
| P244 | Keep reduction valves free from grease and oil. | Reduction valves‘: it is not clear and this statement should apply to all equipment that comes into contact with oxidizing gases | Replace with: Keep cylinder valves and pressure regulators free from grease and oil. |
| P250 | Do not subject to grinding/shock/friction | None | None |
| P260 P261 | Do not breathe dust/fume/gas/mist/ vapours/spray Avoid breathing dust/fume/gas/mist/ vapours/spray | Redundancy – same action required. ‘Do not create dust’ etc. would also be more appropriate than ‘do not breathe…’ in some situations, where this is practicable. | Delete P261 – replace with single statement, Do not create/ breathe dust/fume/gas/mist/vapours/ spray. Manufacturer supplier should specify practicable precaution as well as applicable conditions. |
| P262 | Do not get in eyes, on skin, or on clothing | None | None |
| P263 | Avoid contact during pregnancy/ while nursing | None | None |
| P264 | Wash… thoroughly after handling | None | None |
| P270 | Do not eat/drink or smoke when using this product | None | None |
| P271 | Use only outdoors in a well-ventilated area | None | None |
| P272 | Contaminated work clothing should not be allowed out of the workplace. | None | None |
| P273 | Avoid release to the environment | None | None |
| P280 P281 | Wear protective gloves/protective clothing/eye protection/face protection Use personal protective equipment as required | Redundancy | Replace with one statement: Wear protective gloves/protective clothing/face protection… Manufacturer/supplier or the competent authority to specify appropriate personal protective equipment. |
| P282 | Wear cold insulating gloves/face shield/eye protection | No change | No change |
| P283 | Wear fire/flame resistant/retardant clothing | No change | No change |
| P284 P285 | Wear respiratory protection In case of inadequate ventilation wear respiratory protection | Redundancy. Also, not clear why P285 appropriate for respiratory sensitisers only rather than P284 – it is also a lot less simple than P284 and it may be difficult for users to judge whether there is ‘adequate’ ventilation. | Replace P285 with P284: Wear respiratory protection. |
| P301 P302 P303 P304 P305 P306 | IF SWALLOWED: IF ON SKIN: IF ON SKIN (or hair): IF INHALED: IF IN EYES: IF ON CLOTHING: | Some redundancy between P302 and P303 | Delete P302 (use P303 instead). |
| P307 P308 P309 | IF exposed: IF exposed or concerned: IF exposed or if you feel unwell: | Some redundancy. However may want to retain P308 for CMRs and separate PS for cat 1 and 2 STOT. | Replace P309 with IF you feel unwell: |
| P310 P311 P312 P313 P314 P315 | Immediately call a POISON CENTER or doctor/physician Call a POISON CENTER or doctor/physician Call a POISON CENTER or doctor/physician if you feel unwell Get medical advice/attention Get medical advice/attention if you feel unwell Get immediate medical advice/attention | Redundancy, esp. as regards 310-312 and 313-315. Not all jurisdictions have Poison Centres which can be called by workers/ members of the public. Need flexibility for manufacturers/suppliers to specify source of first line medical advice. | Use only: P310 Immediately call a POISON CENTER/ or doctor/physician/…,, P311 Call a POISON CENTER/ or doctor/physician/... and Call a POISON CENTER/ or doctor/physician/… if you feel unwell. Add note in column 5, “manufacturer/supplier or the competent authority to specify the appropriate source of medical advice.” Also add note in column 5 that ‘The statement “Get immediate medical advice/attention” may be used on labels where more than one possible source of medical attention is available’. |
| P320 P321 P322 | Specific treatment is urgent (see … on this label) Specific treatment (see … on this label) Specific measures (see … on this label) | Redundancy. Urgency will be indicated by P310 and P311 – i.e. P320 only applies to acute tox cat 1,2 – this is also given P310. No real difference between ‘treatment’ and ‘measures’. | Replace with specific treatment (see … on this label). |
| P330 | Rinse mouth | None | None |
| P331 | Do NOT induce vomiting | None | None |
| P332 P333 | If skin irritation occurs If skin irritation or rash occurs | P332 is redundant | Replace with: P333 If skin irritation or rash occurs |
| P334 | Immerse in cool water/wrap in wet bandages | None | None |
| P335 | Brush off loose particles from skin | None | None |
| P336 | Thaw frosted parts with lukewarm water. Do not rub affected area. | None | None |
| P337 | If eye irritation persists: | None | None |
| P338 | Remove contact lenses, if present and easy to do. Continue rinsing. | None | None |
| P340 P341 P342 | Remove victim to fresh air and keep at rest in a position comfortable for breathing If breathing is difficult, remove victim to fresh air and keep at rest in a position comfortable for breathing. If experiencing respiratory symptoms: | P341 and P342 only apply to respiratory sensitisation cat 1, and the content can better be expressed in a combined precautionary statement which doesn’t use P342. The word ‘victim’ is not ideal in this context – ‘individual’ is better. | Delete P342. Replace P341 with If breathing is difficult, remove victim individual to fresh air and keep at rest in a position comfortable for breathing. Instead of P342+P311, add P311 to combined statement P304+341 to form a single statement: IF INHALED: If breathing is difficult, remove victim to fresh air and keep at rest in a position comfortable for breathing. Call a POISON CENTER/doctor/physician/… |
| P350 P351 P352 P353 | Gently wash with plenty of soap and water. Rinse cautiously with water for several minutes. Wash with plenty of soap and water Rinse skin with water/shower | Redundancy – though P351 should be kept separate as applies specifically to eyes. Soap may not always be available. Encouraging people to use “soap and water” could discourage quick action. Therefore, the PS should be modified to focus on using water. | Replace P350, P352 and P353 with: P352 wash skin with plenty of water. |
| P360 | Rinse immediately contaminated clothing and skin with plenty of water before removing clothes | None | None |
| P361 P362 P363 | Remove/take off immediately all contaminated clothing Take off contaminated clothing and wash before reuse. Wash contaminated clothing before reuse. | Redundancy, same can be accomplished with fewer statements. Removing contaminated clothing and washing before re-use go together (one action doesn’t make sense without the other). No need to have both ‘remove’ and ‘take off’. | Replace P361-P363 with: P361: Remove/Immediately take off immediately all contaminated clothing. Wash before reuse P362: Take off contaminated clothing. Wash before re-use. |
| P370 | In case of fire: | None | None |
| P371 | In case of major fire and large quantities | None | None |
| P372 | Explosion risk in case of fire | None | None |
| P373 | DO NOT fight fire when fire reaches explosives | None | None |
| P374 | Fight fire with normal precautions from a reasonable distance. | None | None |
| P375 | Fight fire remotely due to risk of explosion | None | None |
| P376 | Stop leak if safe to do so | None | None |
| P377 | Leaking gas fire: Do not extinguish, unless leak can be stopped safely | None | None |
| P378 | Use… for extinction | ‘Extinction’ not the clearest phrase here | Replace with P378: Use … to extinguish |
| P380 | Evacuate area | None | None |
| P381 | Eliminate all ignition sources if safe to do so | None | None |
| P390 | Absorb spillage to prevent material-damage | None | None |
| P391 | Collect spillage | None | None |
| P401 | Store… | None | None |
| P402 | Store in a dry place | None | None |
| P403 | Store in a well-ventilated place | None | None |
| P404 | Store in a closed container | Redundancy with P233 | Delete – see P233. |
| P405 | Store locked up | None | None. |
| P406 | Store in corrosive resistant/…container with a resistant inner liner. | None | None |
| P407 | Maintain air gap between pallets | None | None |
| P410 | Protect from sunlight | None | None |
| P411 | Store at temperatures not exceeding …°C/…°F | None | None |
| P412 | Do not expose to temperatures exceeding 50°C/122°F | None | None |
| P413 | Store bulk masses greater than …kg/…lbs at temperatures not exceeding …°C/…°F | None | None |
| P420 | Store away from other materials | Redundancy (P220) | Delete – see P220 |
| P422 | Store contents under… | Redundancy (P231) | Delete – see P422 |
| P501 | Dispose of contents/container to… | None | None |

| Annex 2: Suggested changes to precautionary statements (amendments to physical hazard statements) |
| --- |
| Code | Prevention precautionary statements | Hazard class | Hazard category | Conditions for use |
| P234 | Keep only in original container | Explosives (chapter 2.1) | Unstable explosives and Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | For explosives, self-reactive substances and organic peroxides repackaging may result in a different hazard category |
|  |  | Self reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
|  |  | Substances and mixtures corrosive to metals (2.16) | 1 |  |
| P240 | Ground/bond container and receiving equipment | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - if the explosive is electrostatically sensitive. |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3 | - if electrostatically sensitive material is for reloading - if product is volatile so as to generate hazardous atmosphere |
|  |  | Flammable solids (chapter 2.7) | 1, 2 | - if electrostatically sensitive material is for reloading. |
| P241 | Use explosion-proof electrical/ventilating/lighting... equipment | Flammable liquids (chapter 2.6) | 1, 2 | …manufacturer/supplier or the competent authority to specify equipment |
|  |  | Flammable liquids (chapter 2.6) | 3 | …manufacturer/supplier or the competent authority to specify equipment - if product is volatile so as to generate hazardous atmosphere. |
|  |  | Flammable solids (chapter 2.7) | 1, 2 | …manufacturer/supplier or the competent authority to specify equipment - if dust clouds can occur |
| P242 | Use only non-sparking tools | Flammable gases (chapter 2.6) | 1, 2 | - if product is sensitive to mechanical sparks |
|  |  | Flammable liquids (chapter 2.6) | 1, 2 |  |
|  |  | Flammable liquids (chapter 2.6) | 3 | - if product is volatile so as to generate hazardous atmosphere and sensitive to mechanical sparks |

| Annex 2: Suggested changes to precautionary statements (amendments to physical hazard statements) (cont’d) |
| --- |
| Code | Prevention precautionary statements | Hazard class | Hazard category | Conditions for use |
| P243 | Take precautionary measures against static discharge | Flammable liquids (chapter 2.6) | 1, 2 | - if material is electrostatically sensitive |
|  |  | Flammable liquids (chapter 2.6) | 3 | - if product is volatile so as to generate hazardous atmosphere and electrostatically sensitive |
| P370 | In case of fire: | Explosives (chapter 2.1) | Divisions1.1, 1.2, 1.3, 1.4, 1.5 |  |
|  |  | Oxidizing gases (chapter 2.4) | 1 |  |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P372 | Explosion risk in case of fire | Explosives (chapter 2.1) | Unstable explosives and Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4S AMMUNITION OR COMPONENTS THEREOF |
| P373 | DO NOT fight fire when fire reaches explosives | Explosives (chapter 2.1) | Unstable explosives and Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4S |
| P374 | Fight fire with normal precautions from a reasonable distance | Explosives (chapter 2.1) | Division 1.4 | - except if explosives are 1.4S AMMUNITION OR COMPONENTS THEREOF |
| P375 | Fight fire remotely due to risk of explosion | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1 |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B |  |
| P378 | Use … for extinction to extinguish | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 | Manufacturer/supplier or the competent authority to specify appropriate media - if water increases risk |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |  |
| P380 | Evacuate area | Explosives (chapter 2.1) | Unstable explosives |  |
|  |  | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4 S |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Oxidising liquids (chapter 2.13) | 1 |  |
|  |  | Oxidising solids (chapter 2.14) | 1 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B |  |
| P370 + P378 | In case of fire: Use … for extinction to extinguish | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 | … Manufacturer/supplier to specify appropriate media. - if water increases risk |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidising liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidising solids (chapter 2.14) | 1, 2, 3 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P370 + P380 | In case of fire: Evacuate area | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4 S |
| P370 + P380 + P375 | In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B |  |
| P403 | Store in a well-ventilated place | Flammable gases (chapter 2.2) | 1, 2 |  |
|  |  | Oxidising gases (chapter 2.4) | 1 |  |
|  |  | Gases under pressure (chapter 2.5) | Compressed gas |  |
|  |  |  | Liquefied gas |  |
|  |  |  | Refrigerated liquefied gas |  |
|  |  |  | Dissolved gas |  |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Tyeps A, B, C, D, E, F |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1, 2, 3 | - if product is volatile so as to generate a hazardous atmosphere |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
| P410 | Protect from sunlight | Flammable aerosols (chapter 2.3) | 1, 2 |  |
|  |  | Gases under pressure (chapter 2.5) | Compressed gas | - To be used in countries where the likelihood exists for the content of the receptacle to exceed 60°C if the receptacle is not protected from sunshine |
|  |  |  | Liquefied gas |  |
|  |  |  | Dissolved gas |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P403 + P235 | Store in a well-ventilated place. Keep cool | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |

Annex 3:

Tables A3.2.1, A3.2.2, A3.2.3, A3.2.4 incorporating all proposed changes (marked up)

Table A3.2.1	Codification of general precautionary statements

| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| --- | --- | --- | --- | --- |
| P101 | If medical advice is needed, have product container or label at hand. | As appropriate |  | Consumer products |
| P102 | Keep out of reach of children | As appropriate |  | Consumer products |
| P103 | Read entire label before use | As appropriate |  | Consumer products, and others as appropriate |
| P104 | Do not use until all safety precautions have been read and understood. | As appropriate |  | Consumer products, and others as appropriate |

| Table A3.2.2: Codification of prevention precautionary statements |
| --- |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P201 | Obtain special instructions before use |  |  |  |
| P202 | Do not handle until all safety precautions have been read and understood | Explosives (chapter 2.1) | Unstable explosive |  |
|  |  | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 |  |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity, effects on or via lactation (chapter 3.7) | Additional category |  |
| P210 | Keep away from heat/sparks/open flames/hot surfaces. – No smoking. | No change |  |  |
| P211 | Do not spray on an open flame or other ignition source | No change |  |  |

| Annex 3 (cont’d) |
| --- |
| Table A3.2.2: Codification of prevention precautionary statements (cont’d) |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P220 | Keep/store away from clothing/…/other materials/combustible materials. | Oxidizing gases (chapter 2.4) | 1 | Manufacturer/supplier or the competent authority to specify other incompatible materials. - ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used when this precaution only applies to storage |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 2,3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 2,3 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1 | Specify to keep away from clothing and other combustible materials. |
|  |  | Oxidizing solids (chapter 2.14) | 1 |  |
| P221 | Take any precaution to avoid mixing with combustibles Do not mix with combustibles/… | Oxidizing liquids (chapter 2.13) | 1, 2, 3 | Manufacturer/supplier or the competent authority to specify other incompatible materials. |
|  |  | Oxidising solids (chapter 2.14) | 1, 2, 3 |  |
| P222 | Do not allow contact with air | No change |  |  |
| P223 | Keep away from any possible contact with water, because of violent reaction and possible flash fire | No change |  |  |
| P230 | Keep wetted with… | No change |  |  |
| P231 | Handle under inert gas | No change |  |  |
| P232 | Protect from moisture | No change |  |  |
| P233 | Keep in a container tightly closed container | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1,2,3 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1,2,3 | -if product is volatile so as to generate hazardous atmosphere |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
| P234 | Keep only in original container | Explosives (chapter 2.1) | Unstable explosives and Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | For explosives, self-reactive substances and organic peroxides repackaging may result in a different hazard category |
|  |  | Self reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
|  |  | Substances and mixtures corrosive to metals (2.16) | 1 |  |
| P235 | Keep cool | No change |  |  |
| P240 | Ground/bond container and receiving equipment | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - if the explosive is electrostatically sensitive. |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3 | - if electrostatically sensitive material is for reloading - if product is volatile so as to generate hazardous atmosphere |
|  |  | Flammable solids (chapter 2.7) | 1, 2 | - if electrostatically sensitive material is for reloading. |
| P241 | Use explosion-proof electrical/ventilating/lighting/…/ ... equipment | Flammable liquids (chapter 2.6) | 1, 2 | …manufacturer/supplier or the competent authority to specify equipment |
|  |  | Flammable liquids (chapter 2.6) | 3 | …manufacturer/supplier or the competent authority to specify equipment - if product is volatile so as to generate hazardous atmosphere. |
|  |  | Flammable solids (chapter 2.7) | 1, 2 | …manufacturer/supplier or the competent authority to specify equipment - if dust clouds can occur |
| P242 | Use only non-sparking tools | Flammable gases (chapter 2.2) | 1, 2 | - if product is sensitive to mechanical sparks |
|  |  | Flammable liquids (chapter 2.6) | 1, 2 |  |
|  |  | Flammable liquids (chapter 2.6) | 3 | - if product is volatile so as to generate hazardous atmosphere and sensitive to mechanical sparks |
| P243 | Take precautionary measures against static discharge | Flammable liquids (chapter 2.6) | 1, 2 | - if material is electrostatically sensitive |
|  |  | Flammable liquids (chapter 2.6) | 3 | - if product is volatile so as to generate hazardous atmosphere and electrostatically sensitive |
| P244 | Keep cylinder valves and pressure regulators free from grease and oil. | Oxidizing gases (chapter 2.4) | 1 |  |
| P250 | Do not subject to grinding/shock/friction | No change |  |  |
| P251 | Pressurized container: Do not pierce or burn, even after use. | No change |  |  |
| P260 | Do not create/ breathe dust/fume/gas/mist/vapours/spray | Acute toxicity – inhalation (chapter 3.1) | 1,2,3,4 | Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C | - specify do not breathe dusts or mists - if inhalable particles of dusts or mists may occur during use. |
|  |  | Respiratory sensitization (chapter 3.4) | 1 | Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
|  |  | Reproductive toxicity – effects on or via lactation (chapter 3.7) | Additional category | - specify do not breathe dusts or mists - if inhalable particles of dusts or mists may occur during use |
|  |  | Specific target organ toxicity, single exposure (chapter 3.8) | 1,2 | Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, repeated exposure (chapter 3.9) | 1,2 |  |
| P261 | Avoid breathing dust/fume/gas/mist/vapours/spray |  |  |  |
| P262 | Do not get in eyes, on skin, or on clothing | No change |  |  |
| P263 | Avoid contact during pregnancy/ while nursing | No change |  |  |
| P264 | Wash … thoroughly after handling | No change |  |  |
| P270 | Do not eat/drink or smoke when using this product | No change |  |  |
| P271 | Use only outdoors in a well-ventilated area | No change |  |  |
| P272 | Contaminated work clothing should not be allowed out of the workplace. | No change |  |  |
| P273 | Avoid release to the environment | No change |  |  |
| P280 | Wear protective gloves/protective clothing/eye protection/face protection/… | Explosives (chapter 2.1) | Unstable explosives, Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - specify face protection Manufacturer/supplier or the competent authority to specify type of equipment. |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 | - specify protective gloves and eye/face protection Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F | - specify protective gloves and eye/face protection Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Acute toxicity – dermal (chapter 3.1) | 1, 2, 3, 4 | - specify protective gloves/clothing |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C | Specify protective gloves/ clothing and eye/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. |
|  |  | Skin irritation (chapter 3.2) | 2 | Specify protective gloves Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
|  |  | Severe eye damage (chapter 3.3) | 1 | specify eye/face protection Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Eye irritation (chapter 3.3) | 2A | specify eye/face protection Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 | Manufacturer/supplier or the competent authority to specify appropriate personal protective equipment. |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
| P281 | Use personal protective equipment as required |  |  |  |
| P282 | Wear cold insulating gloves/face shield/eye protection | No change |  |  |
| P283 | Wear fire/flame resistant/retardant clothing | No change |  |  |
| P284 | Wear respiratory protection | Acute toxicity, inhalation (chapter 3.1) | 1,2 | Manufacturer/supplier or the competent authority to specify equipment |
|  |  | Respiratory sensitization (chapter 3.4) | 1 |  |
| P285 | In case of inadequate ventilation wear respiratory protection |  |  |  |

| Annex 3 (cont’d) |
| --- |
| Table A3.2.3 Codification of response precautionary statements |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P301 | IF SWALLOWED: | No change |  |  |
| P302 | IF ON SKIN: |  |  |  |
| P303 | IF ON SKIN (or hair): | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2,3,4 |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
| P304 | IF INHALED: | No change |  |  |
| P305: | IF IN EYES: | No change |  |  |
| P306: | IF ON CLOTHING: | No change |  |  |
| P307 | IF exposed: | No change |  |  |
| P308: | IF exposed or concerned: | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 |  |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity, effects on or via lactation (chapter 3.7 | Additional category |  |
| P309 | IF exposed or if you feel unwell: | Specific target organ toxicity, single exposure (chapter 3.8) | 2 |  |
| P310 | Immediately call a POISON CENTER/doctor/physician/… | Gases under pressure (chapter 2.5) | Refrigerated liquefied gas | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Acute toxicity, oral (chapter 3.1) | 1,2,3 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1,2 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Severe eye damage (chapter 3.3) | 1 |  |
|  |  | Aspiration hazard (chapter 3.10) | 1,2 |  |
| P311 | Call a POISON CENTER/doctor/physician/… | Acute toxicity, inhalation (chapter 3.1) | 3 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Skin irritation (chapter 3.2) | 2, 3 |  |
|  |  | Eye irritation (chapter 3.3) | 2A, 2B |  |
|  |  | Respiratory sensitisation (chapter 3.4) | 1 |  |
|  |  | Skin sensitisation (chapter 3.4) | 1 |  |
|  |  | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 |  |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity, effects on or via lactation (chapter 3.7) | 1A, 1B, 2 |  |
|  |  | Specific target organ toxicity, single exposure (chapter 3.8) | 1, 2 |  |
| P312 | Call a POISON CENTER/doctor/physician/… if you feel unwell | Acute toxicity, oral (chapter 3.1) | 4 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Acute toxicity, oral (chapter 3.1) | 5 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 3, 4, 5 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 4 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 5 |  |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, repeated exposure (chapter 3.9) | 1,2 |  |
| P313 | Get medical advice/attention |  |  |  |
| P314 | Get medical advice/attention if you feel unwell |  |  |  |
| P315 | Get immediate medical advice/attention |  |  |  |
| P320 | Specific treatment is urgent (see … on this label) |  |  |  |
| P321 | Specific treatment (see … on this label) | Acute toxicity, oral (chapter 3.1) | 1,2,3 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2,3,4 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1,2,3 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
|  |  | Specific target organ toxicity, single exposure (chapter 3.8) | 1 |  |
| P322 | Specific measures (see … on this label) |  |  |  |
| P330 | Rinse mouth | No change |  |  |
| P331 | Do NOT induce vomiting | No change |  |  |
| P332 | If skin irritation occurs: |  |  |  |
| P333 | If skin irritation or rash occurs: | Skin irritation (chapter 3.2) | 2,3 |  |
|  |  | Skin sensitisation (chapter 3.4) | 1 |  |
| P334 | Immerse in cool water/wrap in wet bandages | No change |  |  |
| P335 | Brush off loose particles from skin | No change |  |  |
| P336 | Thaw frosted parts with lukewarm water. Do not rub affected area | No change |  |  |
| P337 | If eye irritation persists: | No change |  |  |
| P338 | Remove contact lenses, if present and easy to do. Continue rinsing. | No change |  |  |
| P340 | Remove victim individual to fresh air and keep at rest in a position comfortable for breathing | Acute toxicity, inhalation (chapter 3.1) | 1,2,3,4 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
| P341 | If breathing is difficult, remove victim individual to fresh air and keep at rest in a position comfortable for breathing | Respiratory sensitization (chapter 3.4) | 1 |  |
| P342 | If experiencing respiratory symptoms |  |  |  |
| P350 | Gently wash with plenty of soap and water |  |  |  |
| P351 | Rinse cautiously with water for several minutes. | No change |  |  |
| P352 | Wash skin with plenty of soap and water | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2,3,4 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
| P353 | Rinse skin with water/shower |  |  |  |
| P360 | Rinse immediately contaminated clothing and skin with plenty of water before removing clothes. | Oxidizing liquids (chapter 2.13) | 1 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1 |  |
| P361 | Remove Immediately Ttake off immediately all contaminated clothing . Wash before reuse | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2,3 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B. 1C |  |
| P362 | Take off all contaminated clothing. Wash before re-use | Acute toxicity, dermal (chapter 3.1) | 4 |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
| P363 | Wash contaminated clothing before re-use |  |  |  |
| P370 | In case of fire: | Explosives (chapter 2.1) | Divisions1.1, 1.2, 1.3, 1.4, 1.5 |  |
|  |  | Oxidizing gases (chapter 2.4) | 1 |  |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P370 | In case of fire: | No change |  |  |
| P371 | In case of major fire and large quantities | No change |  |  |
| P372 | Explosion risk in case of fire | Explosives (chapter 2.1) | Unstable explosives and divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4S AMMUNITION OR COMPONENTS THEREOF |
| P373 | DO NOT fight fire when fire reaches explosives | Explosives (chapter 2.1) | Unstable explosives and divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4S |
| P374 | Fight fire with normal precautions from a reasonable distance. | Explosives (chapter 2.1) | Division 1.4 | - except if explosives are 1.4S AMMUNITION OR COMPONENTS THEREOF |
| P375 | Fight fire remotely due to risk of explosion | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B |  |
| P376 | Stop leak if safe to do so | No change |  |  |
| P377 | Leaking gas fire: Do not extinguish, unless leak can be stopped safely | No change |  |  |
| P378 | Use … for extinction to extinguish | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 | Manufacturer/supplier or the competent authority to specify appropriate media - if water increases risk |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |  |
| P380 | Evacuate area | Explosives (chapter 2.1) | Unstable explosives |  |
|  |  | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4 S |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Oxidising liquids (chapter 2.13) | 1 |  |
|  |  | Oxidising solids (chapter 2.14) | 1 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B |  |
| P381 | Eliminate all ignition sources if safe to do so | No change |  |  |
| P390 | Absorb spillage to prevent material-damage | No change |  |  |
| P391 | Collect spillage | No change |  |  |
| P301+ P310 | IF SWALLOWED: Immediately call a POISON CENTER or/doctor/physician… | Acute toxicity, oral (chapter 3.1) | 1,2,3 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Aspiration hazard (chapter 3.10) | 1,2 |  |
| P301+ P312 | IF SWALLOWED: call a POISON CENTER/or doctor/physician if you feel unwell. | Acute toxicity, oral (chapter 3.1) | 4 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
| P301 + P330 + P331 | IF SWALLOWED: Rinse mouth. Do NOT induce vomiting | No change |  |  |
| P302 P303+ P334 | IF ON SKIN (or hair): Immerse in cool water/wrap in wet bandages. | No change |  |  |
| P302 P303+ P350 P352 | IF ON SKIN (or hair): Gently wash skin with plenty of water/soap and water…. | Acute toxicity, dermal (chapter 3.1) | 1,2 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 3,4 |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
| P303 + P361 + P353 P352 | IF ON SKIN (or hair): Remove/ Take off immediately all contaminated clothing. Rinse skin with water/shower. Wash skin with plenty of water… | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
| P304 + P312 | IF INHALED: Call a POISON CENTER/or doctor/physician if you feel unwell. | Acute toxicity, inhalation (chapter 3.1) | 5 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
| P304 + P340 | IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. | No change |  |  |
| P304 + P341 + P311 | IF INHALED: If breathing is difficult, remove victim to fresh air and keep at rest in a position comfortable for breathing. Call a POISON CENTER/doctor/physician/… | Respiratory sensitisation (chapter 3.4) | 1 |  |
| P305 + P351 + P338 | IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. | No change. |  |  |
| P306 + P360 | IF ON CLOTHING: Rinse immediately contaminated clothing and skin with plenty of water before removing clothes. | No change. |  |  |
| P307 + P311 | If exposed: call a POISON CENTRE or doctor/physician |  |  |  |
| P308 + P313 | If exposed or concerned: get medical advice/attention call a POISON CENTRE/doctor/physician/… | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 1 |  |
|  |  | Reproductive toxicity, effects on or via lactation (chapter 3.7) | Additional category |  |
| P309 + P311 | If exposed or you feel unwell: call a POISON CENTER or doctor/physician. | Specific target organ toxicity, single exposure (chapter 3.8) | 1, 2 |  |
| P332 + P313 | If skin irritation occurs: Get medical advice/attention |  |  |  |
| P333 + P313 | If skin irritation or rash occurs: get medical advice/attention Call a POISON CENTER/doctor/physician… | Skin irritation (chapter 3.2) | 2,3 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Skin sensitisation (chapter 3.4) | 1 |  |
| P335 + P334 | Brush off loose particles from skin. Immerse in cool water/wrap in wet bandages. | No change. |  |  |
| P337 + P313 | If eye irritation persists: Get medical advice/attention Call a POISON CENTER/doctor/physician… | Eye irritation (chapter 3.3) | 2A, 2B | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
| P342 + P311 | If experiencing respiratory symptoms: get medical advice/attention |  |  |  |
| P370 + P376 | In case of fire: Stop leak if safe to do so. | No change |  |  |
| P370 + P378 | In case of fire: Use … for extinction | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 | … Manufacturer/supplier to specify appropriate media. - if water increases risk |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidising liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidising solids (chapter 2.14) | 1, 2, 3 |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P370 + P380 | In case of fire: Evacuate area | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4 S |
| P370 + P380 + P375 | In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B |  |
| P371 + P380 + P375 | In case of major fire and large quantities: Evacuate area. Fight fire remotely due to the risk of explosion. | No change. |  |  |

| Annex 3 (cont’d) |
| --- |
| Table A3.2.4: Codification of storage precautionary statements |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P401 | Store… | No change |  |  |
| P402 | Store in a dry place | No change |  |  |
| P403 | Store in a well-ventilated place | Flammable gases (chapter 2.2) | 1, 2 |  |
|  |  | Oxidising gases (chapter 2.4) | 1 |  |
|  |  | Gases under pressure (chapter 2.5) | Compressed gas |  |
|  |  |  | Liquefied gas |  |
|  |  |  | Refrigerated liquefied gas |  |
|  |  |  | Dissolved gas |  |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Tyeps A, B, C, D, E, F |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1, 2, 3 | - if product is volatile so as to generate a hazardous atmosphere |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
| P404 | Store in a closed container |  |  |  |
| P405 | Store locked up | No change |  |  |
| P406 | Store in corrosive resistant/…container with a resistant inner liner. | No change |  |  |
| P407 | Maintain air gap between pallets | No change |  |  |
| P410 | Protect from sunlight | Flammable aerosols (chapter 2.3) | 1, 2 |  |
|  |  | Gases under pressure (chapter 2.5) | Compressed gas | - To be used in countries where the likelihood exists for the content of the receptacle to exceed 60°C if the receptacle is not protected from sunshine |
|  |  |  | Liquefied gas |  |
|  |  |  | Dissolved gas |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P411 | Store at temperatures not exceeding …°C/…°F | No change |  |  |
| P412 | Do not expose to temperatures exceeding 50°C/122°F | No change |  |  |
| P413 | Store bulk masses greater than …kg/…lbs at temperatures not exceeding …°C/…°F | No change |  |  |
| P420 | Store away from other materials |  |  |  |
| P422 | Store contents under… | No change |  |  |
| P402 + P404 P233 | Store in a dry place. Keep in a container tightly closed container | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1,2,3 |  |
| P403 + P233 | Store in a well-ventilated place. Keep in a container tightly closed container. | No change |  |  |
| P403 + P235 | Store in a well-ventilated place. Keep cool | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P410 + P403 | Protect from sunlight. Store in a well-ventilated place. | Gases under pressure (chapter 2.5) | Compressed gas | - To be used in countries where the likelihood exists for the content of the receptacle to exceed 60°C if the receptacle is not protected from sunshine |
|  |  |  | Liquefied gas |  |
|  |  |  | Dissolved gas |  |
| P410 + P412 | Protect from sunlight. Do not expose to temperatures exceeding 50°C/122°F | No change |  |  |
| P411 + P235 | Store at temperatures not exceeding …°C/…°F. Keep cool. | No change |  |  |

Table A3.2.5 Codification of disposal precautionary statements

| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| --- | --- | --- | --- | --- |
| P501 | Dispose of contents/container to… | No change |  |  |

Annex 4:

Suggested changes to tables A3.2.1, A3.2.2, A3.2.3, A3.2.4 (clean copy)

| Table A3.2.1 |
| --- |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P101 | If medical advice is needed, have product container or label at hand. | As appropriate |  | Consumer products |
| P102 | Keep out of reach of children | As appropriate |  | Consumer products |
| P103 | Read entire label before use | As appropriate |  | Consumer products, and others as appropriate |
| P104 | Do not use until all safety precautions have been read and understood. | As appropriate |  | Consumer products, and others as appropriate |

| Annex 4 (cont’d) |
| --- |
| Table A3.2.2 Codification of prevention precautionary statements |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P202 | Do not handle until all safety precautions have been read and understood | Explosives (chapter 2.1) | Unstable explosive |  |
|  |  | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 |  |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity, effects on or via lactation (chapter 3.7) | Additional category |  |
| P210 | Keep away from heat/sparks/open flames/hot surfaces. – No smoking. | No change |  |  |
| P211 | Do not spray on an open flame or other ignition source | No change |  |  |
| P220 | Keep/store away from clothing/…/other materials/combustible materials. | Oxidizing gases (chapter 2.4) | 1 | Manufacturer/supplier or the competent authority to specify other incompatible materials. - ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used when this precaution only applies to storage |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 2,3 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1 | Specify to keep away from clothing and other combustible materials. |
|  |  | Oxidizing solids (chapter 2.14) | 1 |  |
| P221 | Do not mix with combustibles/… | Oxidizing liquids (chapter 2.13) | 1, 2, 3 | Manufacturer/supplier or the competent authority to specify other incompatible materials. |
|  |  | Oxidising solids (chapter 2.14) | 1, 2, 3 |  |
| P222 | Do not allow contact with air | No change |  |  |
| P223 | Keep away from any possible contact with water, because of violent reaction and possible flash fire | No change |  |  |

| Annex 4 (cont’d) |
| --- |
| Table A3.2.2 Codification of prevention precautionary statements (cont’d) |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P230 | Keep wetted with… | No change |  |  |
| P231 | Handle under inert gas | no change |  |  |
| P232 | Protect from moisture | No change |  |  |
| P233 | Keep in a tightly closed container | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1,2,3 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1,2,3 | -if product is volatile so as to generate hazardous atmosphere |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
| P234 | Keep only in original container | Explosives (chapter 2.1) | Unstable explosives and Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | For explosives, self-reactive substances and organic peroxides repackaging may result in a different hazard category |
|  |  | Self reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
|  |  | Substances and mixtures corrosive to metals (2.16) | 1 |  |
| P235 | Keep cool | No change |  |  |
| P240 | Ground/bond container and receiving equipment | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - if the explosive is electrostatically sensitive. |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3 |  |
|  |  | Flammable solids (chapter 2.7) | 1, 2 | - if electrostatically sensitive material is for reloading. |
| P241 | Use explosion-proof ... equipment | Flammable liquids (chapter 2.6) | 1, 2 | …manufacturer/supplier or the competent authority to specify equipment |
|  |  | Flammable liquids (chapter 2.6) | 3 | …manufacturer/supplier or the competent authority to specify equipment - if product is volatile so as to generate hazardous atmosphere. |
|  |  | Flammable solids (chapter 2.7) | 1, 2 | …manufacturer/supplier or the competent authority to specify equipment - if dust clouds can occur |
| P242 | Use only non-sparking tools | Flammable gases (chapter 2.6) | 1, 2 | - if product is sensitive to mechanical sparks |
|  |  | Flammable liquids (chapter 2.6) | 1, 2 |  |
|  |  | Flammable liquids (chapter 2.6) | 3 | - if product is volatile so as to generate hazardous atmosphere and sensitive to mechanical sparks |
| P243 | Take precautionary measures against static discharge | Flammable liquids (chapter 2.6) | 1, 2 | - if material is electrostatically sensitive |
|  |  | Flammable liquids (chapter 2.6) | 3 | - if product is volatile so as to generate hazardous atmosphere and electrostatically sensitive |
| P244 | Keep cylinder valves and pressure regulators free from grease and oil. | Oxidizing gases (chapter 2.4) | 1 |  |
| P250 | Do not subject to grinding/shock/friction | No change |  |  |
| P251 | Pressurized container: Do not pierce or burn, even after use. | No change |  |  |
| P260 | Do not create/ breathe dust/fume/gas/mist/vapours/spray | Acute toxicity – inhalation (chapter 3.1) | 1,2,3,4 | Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C | - specify do not breathe dusts or mists - if inhalable particles of dusts or mists may occur during use. |
|  |  | Respiratory sensitization (chapter 3.4) | 1 | Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
|  |  | Reproductive toxicity – effects on or via lactation (chapter 3.7) | Additional category | - specify do not breathe dusts or mists - if inhalable particles of dusts or mists may occur during use |
|  |  | Specific target organ toxicity, single exposure (chapter 3.8) | 1,2 | Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, repeated exposure (chapter 3.9) | 1,2 |  |
| P262 | Do not get in eyes, on skin, or on clothing | No change |  |  |
| P263 | Avoid contact during pregnancy/ while nursing | No change |  |  |
| P264 | Wash … thoroughly after handling | No change |  |  |
| P270 | Do not eat/drink or smoke when using this product | No change |  |  |
| P271 | Use only outdoors in a well-ventilated area | No change |  |  |
| P272 | Contaminated work clothing should not be allowed out of the workplace. | No change |  |  |
| P273 | Avoid release to the environment | No change |  |  |
| P280 | Wear protective gloves/protective clothing/eye protection/face protection/… | Explosives (chapter 2.1) | Unstable explosives, Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - specify face protection Manufacturer/supplier or the competent authority to specify type of equipment. |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 | - specify protective gloves and eye/face protection Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F | - specify protective gloves and eye/face protection Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Acute toxicity – dermal (chapter 3.1) | 1, 2, 3, 4 | - specify protective gloves/clothing |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C | Specify protective gloves/ clothing and eye/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. |
|  |  | Skin irritation (chapter 3.2) | 2 | Specify protective gloves Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
|  |  | Severe eye damage (chapter 3.3) | 1 | specify eye/face protection Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Eye irritation (chapter 3.3) | 2A | specify eye/face protection Manufacturer/supplier or the competent authority to specify type of equipment |
|  |  | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 | Manufacturer/supplier or the competent authority to specify appropriate personal protective equipment. |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
| P282 | Wear cold insulating gloves/face shield/eye protection. | No change |  |  |
| P283 | Wear fire/flame resistant/retardant clothing | No change |  |  |
| P284 | Wear respiratory protection | Acute toxicity, inhalation (chapter 3.1) | 1,2 | Manufacturer/supplier or the competent authority to specify equipment |
|  |  | Respiratory sensitization (chapter 3.4) | 1 |  |

| Annex 4 (cont’d) |
| --- |
| Table A3.2.3 Codification of response precautionary statements |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P301 | IF SWALLOWED: | No change |  |  |
| P303 | IF ON SKIN (or hair): | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2,3,4 |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
| P304 | IF INHALED: | No change |  |  |
| P305: | IF IN EYES: | No change |  |  |
| P306: | IF ON CLOTHING: | No change |  |  |
| P307 | IF exposed: | No change |  |  |
| P308: | IF exposed or concerned: | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 |  |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity, effects on or via lactation (chapter 3.7 | Additional category |  |
| P309 | IF you feel unwell: | Specific target organ toxicity, single exposure (chapter 3.8) | 1, 2 |  |
| P310 | Immediately call a POISON CENTER/doctor/physician/… | Gases under pressure (chapter 2.5) | Refrigerated liquefied gas | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Acute toxicity, oral (chapter 3.1) | 1,2,3 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1,2 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Severe eye damage (chapter 3.3) | 1 |  |
|  |  | Aspiration hazard (chapter 3.10) | 1,2 |  |

| Annex 4 (cont’d) |
| --- |
| Table A3.2.3 Codification of response precautionary statements (cont’d) |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P311 | Call a POISON CENTER/doctor/physician/… | Acute toxicity, inhalation (chapter 3.1) | 3 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Skin irritation (chapter 3.2) | 2, 3 |  |
|  |  | Eye irritation (chapter 3.3) | 2A, 2B |  |
|  |  | Respiratory sensitisation (chapter 3.4) | 1 |  |
|  |  | Skin sensitisation (chapter 3.4) | 1 |  |
|  |  | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 |  |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity, effects on or via lactation (chapter 3.7) | 1A, 1B, 2 |  |
|  |  | Specific target organ toxicity, single exposure (chapter 3.8) | 1, 2 |  |
| P312 | Call a POISON CENTER/doctor/physician/… if you feel unwell | Acute toxicity, oral (chapter 3.1) | 4 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Acute toxicity, oral (chapter 3.1) | 5 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 3, 4, 5 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 4 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 5 |  |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) |  |  |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) |  |  |
|  |  | Specific target organ toxicity, repeated exposure (chapter 3.9) | 1,2 |  |
| P321 | Specific treatment (see … on this label) | Acute toxicity, oral (chapter 3.1) | 1,2,3 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2,3,4 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1,2,3 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
|  |  | Specific target organ toxicity, single exposure (chapter 3.8) | 1 |  |
| P330 | Rinse mouth | No change |  |  |
| P331 | Do NOT induce vomiting | No change |  |  |
| P333 | If skin irritation or rash occurs: | Skin irritation (chapter 3.2) | 2,3 |  |
|  |  | Skin sensitisation (chapter 3.4) | 1 |  |
| P334 | Immerse in cool water/wrap in wet bandages | No change |  |  |
| P335 | Brush off loose particles from skin | No change |  |  |
| P336 | Thaw frosted parts with lukewarm water. Do not rub affected area | No change |  |  |
| P337 | If eye irritation persists: | No change |  |  |
| P338 | Remove contact lenses, if present and easy to do. Continue rinsing. | No change |  |  |
| P340 | Remove individual to fresh air and keep at rest in a position comfortable for breathing | Acute toxicity, inhalation (chapter 3.1) | 1,2,3,4 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
| P341 | If breathing is difficult, remove individual to fresh air and keep at rest in a position comfortable for breathing | Respiratory sensitization (chapter 3.4) | 1 |  |
| P351 | Rinse cautiously with water for several minutes. | No change |  |  |
| P352 | Wash skin with plenty of water | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2,3,4 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
| P360 | Rinse immediately contaminated clothing and skin with plenty of water before removing clothes. | Oxidizing liquids (chapter 2.13) | 1 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1 |  |
| P361 | Immediately take off all contaminated clothing . Wash before reuse | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 1,2,3 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B. 1C |  |
| P362 | Take off contaminated clothing. Wash before re-use | Acute toxicity, dermal (chapter 3.1) | 4 |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
| P370 | In case of fire: | Explosives (chapter 2.1) | Divisions1.1, 1.2, 1.3, 1.4, 1.5 |  |
|  |  | Oxidizing gases (chapter 2.4) | 1 |  |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P370 | In case of fire: | No change |  |  |
| P371 | In case of major fire and large quantities | No change |  |  |
| P372 | Explosion risk in case of fire | Explosives (chapter 2.1) | Unstable explosives and divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4S |
| P373 | DO NOT fight fire when fire reaches explosives | Explosives (chapter 2.1) | Unstable explosives and divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4S |
| P374 | Fight fire with normal precautions from a reasonable distance. | Explosives (chapter 2.1) | Division 1.4 | - except if explosives are 1.4S |
| P375 | Fight fire remotely due to risk of explosion | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1 |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B |  |
| P376 | Stop leak if safe to do so | No change |  |  |
| P377 | Leaking gas fire: Do not extinguish, unless leak can be stopped safely | No change |  |  |
| P378 | Use … to extinguish | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 | Manufacturer/supplier or the competent authority to specify appropriate media - if water increases risk |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |  |
| P380 | Evacuate area | Explosives (chapter 2.1) | Unstable explosives |  |
|  |  | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4 S |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Oxidising liquids (chapter 2.13) | 1 |  |
|  |  | Oxidising solids (chapter 2.14) | 1 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B |  |
| P381 | Eliminate all ignition sources if safe to do so | No change |  |  |
| P390 | Absorb spillage to prevent material-damage | No change |  |  |
| P391 | Collect spillage | No change |  |  |
| P301+P310 | IF SWALLOWED: Immediately call a POISON CENTER /doctor/physician… | Acute toxicity, oral (chapter 3.1) | 1,2,3 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Aspiration hazard (chapter 3.10) | 1,2 |  |
| P301+P312 | IF SWALLOWED: call a POISON CENTER/ doctor/physician if you feel unwell. | Acute toxicity, oral (chapter 3.1) | 4 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
| P301 + P330 + P331 | IF SWALLOWED: Rinse mouth. Do NOT induce vomiting | No change |  |  |
| P303+ P334 | IF ON SKIN (or hair): Immerse in cool water/wrap in wet bandages. | No change |  |  |
| P303+ P352 | IF ON SKIN (or hair): wash skin with plenty of water…. | Acute toxicity, dermal (chapter 3.1) | 1,2 |  |
|  |  | Acute toxicity, dermal (chapter 3.1) | 3,4 |  |
|  |  | Skin irritation (chapter 3.2) | 2 |  |
|  |  | Skin sensitization (chapter 3.4) | 1 |  |
| P303 + P361 + P352 | IF ON SKIN (or hair): Take off immediately all contaminated clothing. . Wash skin with plenty of water … | Flammable liquids (chapter 2.6) | 1,2,3 |  |
|  |  | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |  |
| P304 + P312 | IF INHALED: Call a POISON CENTER/doctor/physician if you feel unwell. | Acute toxicity, inhalation (chapter 3.1) | 5 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
| P304 + P340 | IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. | No change |  |  |
| P304 + P341 + P311 | IF INHALED: If breathing is difficult, remove victim to fresh air and keep at rest in a position comfortable for breathing. Call a POISON CENTER/doctor/physician/… | Respiratory sensitisation (chapter 3.4) | 1 |  |
| P305 + P351 + P338 | IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. | No change. |  |  |
| P306 + P360 | IF ON CLOTHING: Rinse immediately contaminated clothing and skin with plenty of water before removing clothes. | No change. |  |  |
| P308 + P313 | If exposed or concerned: call a POISON CENTRE/doctor/physician/… | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 1 |  |
|  |  | Reproductive toxicity, effects on or via lactation (chapter 3.7) | Additional category |  |
| P309 + P311 | If exposed or you feel unwell: call a POISON CENTER or doctor/physician. | Specific target organ toxicity, single exposure (chapter 3.8) | 1, 2 |  |
| P333 + P313 | If skin irritation or rash occurs: Call a POISON CENTER/doctor/physician… | Skin irritation (chapter 3.2) | 2,3 | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
|  |  | Skin sensitisation (chapter 3.4) | 1 |  |
| P335 + P334 | Brush off loose particles from skin. Immerse in cool water/wrap in wet bandages. | No change. |  |  |
| P337 + P313 | If eye irritation persists: Call a POISON CENTER/doctor/physician… | Eye irritation (chapter 3.3) | 2A, 2B | Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |
| P370 + P376 | In case of fire: Stop leak if safe to do so. | No change |  |  |
| P370 + P378 | In case of fire: Use … for extinction | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 | … Manufacturer/supplier to specify appropriate media. - if water increases risk |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  |  | Oxidising liquids (chapter 2.13) | 1, 2, 3 |  |
|  |  | Oxidising solids (chapter 2.14) | 1, 2, 3 |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P370 + P380 | In case of fire: Evacuate area | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | - except if explosives are 1.4 S |
| P370 + P380 + P375 | In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B |  |
| P371 + P380 + P375 | In case of major fire and large quantities: Evacuate area. Fight fire remotely due to the risk of explosion. | No change. |  |  |

| Annex 4 (cont’d) |
| --- |
| Table A3.2.4 Codification of Storage precautionary statements |
| Code | Precautionary statement | Hazard class | Hazard category | Conditions for use |
| P401 | Store… | No change |  |  |
| P402 | Store in a dry place | No change |  |  |
| P403 | Store in a well-ventilated place | Flammable gases (chapter 2.2) | 1, 2 |  |
|  |  | Oxidising gases (chapter 2.4) | 1 |  |
|  |  | Gases under pressure (chapter 2.5) | Compressed gas |  |
|  |  |  | Liquefied gas |  |
|  |  |  | Refrigerated liquefied gas |  |
|  |  |  | Dissolved gas |  |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Tyeps A, B, C, D, E, F |  |
|  |  | Organic Peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1, 2, 3 | - if product is volatile so as to generate a hazardous atmosphere |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
|  |  | Specific target organ toxicity, single exposure; narcotic effects (chapter 3.8) | 3 |  |
| P403 | Store in a well-ventilated place | No change |  |  |
| P405 | Store locked up | No change |  |  |
| P406 | Store in corrosive resistant/…container with a resistant inner liner. | No change |  |  |
| P407 | Maintain air gap between pallets | No change |  |  |
| P410 | Protect from sunlight | Flammable aerosols (chapter 2.3) | 1, 2 |  |
|  |  | Gases under pressure (chapter 2.5) | Compressed gas | - To be used in countries where the likelihood exists for the content of the receptacle to exceed 60°C if the receptacle is not protected from sunshine |
|  |  |  | Liquefied gas |  |
|  |  |  | Dissolved gas |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P411 | Store at temperatures not exceeding …°C/…°F |  |  |  |
| P413 | Store bulk masses greater than …kg/…lbs at temperatures not exceeding …°C/…°F | No change |  |  |
| P422 | Store contents under… | No change |  |  |
| P402 + P233 | Store in a dry place. Keep in a tightly closed container | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1,2,3 |  |
| P403 + P233 | Store in a well-ventilated place. Keep in a tightly closed container. | No change |  |  |
| P403 + P235 | Store in a well-ventilated place. Keep cool | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |  |
| P410 + P403 | Protect from sunlight. Store in a well-ventilated place. | Gases under pressure (chapter 2.5) | Compressed gas | - To be used in countries where the likelihood exists for the content of the receptacle to exceed 60°C if the receptacle is not protected from sunshine |
|  |  |  | Liquefied gas |  |
|  |  |  | Dissolved gas |  |
| P410 + P412 | Protect from sunlight. Do not expose to temperatures exceeding 50°C/122°F | No change |  |  |
| P411 + P235 | Store at temperatures not exceeding …°C/…°F Keep cool. | No change |  |  |

Table A3.2.5 Codification of disposal precautionary statements

| P501 | Dispose of contents/container to… | No change |  |  |
| --- | --- | --- | --- | --- |

Annex 5:

Changes to A3.3.5 tables – marked up

| EXPLOSIVES (Chapter 2.1) |
| --- |
|  |  |  | Symbol Exploding bomb |
| Hazard category | Signal word | Hazard statement |  |
| Unstable explosive | Danger | H200 | Unstable explosive |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P234 Keep only in original container - repackaging may result in a different hazard category P281 Use personal protective equipment as required. P280 Wear face protection Manufacturer/supplier or the competent authority to specify type of equipment. | P372 Explosion risk in case of fire. - except if explosives are 1.4S P373 DO NOT fight fire when fire reaches explosives. - except if explosives are 1.4S P380 Evacuate area. | P401 Store ... …in accordance with local/regional/ national/international regulations (to be specified). | P501 Dispose of contents/container to ... …in accordance with local/regional/ national/international regulations (to be specified). |

| EXPLOSIVES (Chapter 2.1) |
| --- |
|  |  |  | Symbol Exploding bomb |
| Hazard category | Signal word | Hazard statement |  |
| Division 1.1 | Danger | H201 | Explosive; mass explosion hazard |  |
| Division 1.2 | Danger | H202 | Explosive; severe projection hazard |  |
| Division 1.3 | Danger | H203 | Explosive; fire, blast or projection hazard |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P230 Keep wetted with... … Manufacturer/supplier or the competent authority to specify appropriate material. if drying out increases explosion hazard, except as needed for manufacturing or operating processes (e.g. nitrocellulose). P234 Keep only in original container - repackaging may result in a different hazard category P240 Ground/bond container and receiving equipment. - if the explosive is electrostatically sensitive. P250 Do not subject to grinding/shock/…/friction. …Manufacturer/supplier or the competent authority to specify applicable rough handling. P280 Wear face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P380 In case of fire: evacuate area. - except if explosives are 1.4S P372 Explosion risk in case of fire. - except if explosives are 1.4S P373 DO NOT fight fire when fire reaches explosives. - except if explosives are 1.4S | P401 Store ... …in accordance with local/regional/national/international regulations (to be specified). | P501 Dispose of contents/container to ... … in accordance with local/ regional/national/international regulations (to be specified). |

| EXPLOSIVES (Chapter 2.1) |
| --- |
|  |  |  |  | Symbol Exploding bomb |
| Hazard category | Signal word | Hazard statement |  |
| Division 1.4 | Warning | H204 | Fire or projection hazard |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P234 Keep only in original container - repackaging may result in a different hazard category P240 Ground/bond container and receiving equipment. - if the explosive is electrostatically sensitive. P250 Do not subject to grinding/shock/…/friction. Manufacturer/supplier or the competent authority to specify applicable rough handling. P280 Wear face protection. Manufacturer/supplier or competent authority to specify type of equipment. | P370+P380 In case of fire: Evacuate area. - except if explosives are 1.4S P372 Explosion risk in case of fire. - except if explosives are 1.4S AMMUNITION AND COMPONENTS THEREOF. P373 DO NOT fight fire when fire reaches explosives. - except if explosives are 1.4S P374 Fight fire with normal precautions from a reasonable distance. - Except if explosives are 1.4S AMMUNITION AND COMPONENTS THEREOF. | P401 Store ... …in accordance with local/regional/ national/international regulations (to be specified). | P501 Dispose of contents/container to... … in accordance with local/regional/national/international regulations (to be specified). |

| EXPLOSIVES (Chapter 2.1) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| Division 1.5 | Danger | H205 | May mass explode in fire |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P230 Keep wetted with... … Manufacturer/supplier or the competent authority to specify appropriate material. - if drying out increases explosion hazard, except as needed for manufacturing or operating processes (e.g. nitrocellulose). P234 Keep only in original container - repackaging may result in a different hazard category P240 Ground/bond container and receiving equipment - if the explosive is electrostatically sensitive. P250 Do not subject to grinding/shock/…/friction. …Manufacturer/supplier or the competent authority to specify applicable rough handling. P280 Wear face protection. Manufacturer/supplier or competent authority to specify type of equipment. | P370 + P380 In case of fire: Evacuate area. - except if explosives are 1.4S P372 Explosion risk in case of fire. - except if explosives are 1.4S P373 DO NOT fight fire when fire reaches explosives. - except if explosives are 1.4S | P401 Store ... …in accordance with local/regional/ national/international regulations (to be specified). | P501 Dispose of contents/container to ... … in accordance with local/regional/ national/international regulations (to be specified). |

| FLAMMABLE GASES (Chapter 2.2) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H220 | Extremely flammable gas |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. -No smoking. Manufacturer/supplier or competent authority to specify applicable ignition source(s). P242 Use only non-sparking tools - if product is sensitive to mechanical sparks | P377 Leaking gas fire: Do not extinguish, unless leak can be stopped safely. P381 Eliminate all ignition sources if safe to do so. | P403 Store in well-ventilated place. |  |

| FLAMMABLE GASES (Chapter 2.2) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 2 | Warning | H221 | Flammable gas |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. -No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition sources(s). P242 Use only non-sparking tools - if product is sensitive to mechanical sparks | P377 Leaking gas fire: Do not extinguish, unless leak can be stopped safely. P381 Eliminate all ignition sources if safe to do so. | P403 Store in well-ventilated place. |  |

| FLAMMABLE AEROSOLS (Chapter 2.3) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H222 | Extremely flammable aerosol |  |
| 2 | Warning | H223 | Flammable aerosol |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. -No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition sources(s). P211 Do not spray on an open flame or other ignition source. P251 Pressurized container: Do not pierce or burn, even after use. |  | P410 + P412 Protect from sunlight. Keep/store at temperatures not exceeding 50 ºC/122 ºF. |  |

| OXIDIZING GASES (Chapter 2.4) |
| --- |
|  |  |  | Symbol Flame over circle |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H270 | May cause or intensify fire; oxidizer |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P220 Keep/Store away from clothing/…/combustible materials. …Manufacturer/supplier or the competent authority to specify other incompatible materials. - ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used when this precaution only applies to storage P244 Keep cylinder valves and pressure regulators free from grease and oil. | P370 + P376 In case of fire: Stop leak if safe to do so. | P403 Store in well-ventilated place. |  |

| GASES UNDER PRESSURE (Chapter 2.5) |
| --- |
|  |  |  | Symbol Gas cylinder |
| Hazard category | Signal word | Hazard statement |  |
| Compressed gas | Warning | H280 | Contains gas under pressure; may explode if heated |  |
| Liquefied gas | Warning | H280 | Contains gas under pressure; may explode if heated |  |
| Dissolved gas | Warning | H280 | Contains gas under pressure; may explode if heated |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
|  |  | P410 + P403 Protect from sunlight. Store in a well-ventilated place. - To be used in countries where the likelihood exists for the content of the receptacle to exceed 60°C if the receptacle is not protected from sunshine |  |

| GASES UNDER PRESSURE (Chapter 2.5) |
| --- |
|  |  |  | Symbol Gas cylinder |
| Hazard category | Signal word | Hazard statement |  |
| Refrigerated liquefied gas | Warning | H281 | Contains refrigerated gas; may cause cryogenic burns or injury |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P282 Wear cold insulating gloves/face shield/eye protection. | P336 Thaw frosted parts with lukewarm water. Do not rub affected area. P315 Get immediate medical advice/attention P310 Immediately call a POISON CENTER/doctor/physician Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. | P403 Store in well-ventilated place. |  |

| FLAMMABLE LIQUIDS (Chapter 2.6) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H224 | Extremely flammable liquid and vapour |  |
| 2 | Danger | H225 | Highly flammable liquid and vapour |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces.– No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P233 Keep in a container tightly closed container. P240 Ground/Bond container and receiving equipment - if electrostatically sensitive material is for reloading. - if product is volatile so as to generate hazardous atmosphere. P241 Use explosion-proof electrical/ventilating/ lighting/.../ ... equipment. ... Manufacturer/supplier or the competent authority to specify equipment. P242 Use only non-sparking tools - if product is sensitive to mechanical sparks P243 Take precautionary measures against static discharge. - if material is electrostatically sensitive P280 Wear protective gloves/eye protection/face protection Manufacturer/supplier or the competent authority to specify type of equipment. | P303 + P361 + P353 P352 IF ON SKIN (or hair): Remove/Immediately Ttake off immediately all contaminated clothing . Wash before reuse. Rinse skin with water/shower. Wash skin with plenty of soap and water P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P403 + P235 Store in a well-ventilated place. Keep cool. | P501 Dispose of contents/container to... … in accordance with local/regional/national/international regulations (to be specified). |

| FLAMMABLE LIQUIDS (Chapter 2.6) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 3 | Warning | H226 | Flammable liquid and vapour |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces.– No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P233 Keep in a container tightly closed container. P240 Ground/Bond container and receiving equipment - if electrostatically sensitive material is for reloading. - if product is volatile so as to generate hazardous atmosphere. P241 Use explosion-proof electrical/ventilating/ lighting/.../ ... equipment. ... Manufacturer/supplier or the competent authority to specify equipment. - if product is volatile so as to generate hazardous atmosphere P242 Use only non-sparking tools. - if product is volatile so as to generate hazardous atmosphere and sensitive to mechanical sparks P243 Take precautionary measures against static discharge. - if product is volatile so as to generate hazardous atmosphere and electrostatically sensitive P280 Wear protective gloves/eye protection/face protection Manufacturer/supplier or the competent authority to specify type of equipment. | P303 + P361 + P353 P352 IF ON SKIN (or hair): Remove/Immediately Ttake off immediately all contaminated clothing . Wash before reuse. Rinse skin with water/shower. Wash skin with plenty of soap and water P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P403 + P235 Store in a well-ventilated place. Keep cool. | P501 Dispose of contents/container to... … in accordance with local/regional/national/ international regulations (to be specified). |
| FLAMMABLE LIQUIDS (Chapter 2.6) |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 4 | Warning | H227 | Combustible liquid |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from flames and hot surfaces. – No smoking. P280 Wear protective gloves/eye protection/face protection Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P403 + P235 Store in a well-ventilated place. Keep cool. | P501 Dispose of contents/container to... in accordance with local/regional/ national/international regulations (to be specified). |
| FLAMMABLE LIQUIDS (Chapter 2.6) |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 4 | Warning | H227 | Combustible liquid |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from flames and hot surfaces. – No smoking. P280 Wear protective gloves/eye protection/face protection Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P403 + P235 Store in a well-ventilated place. Keep cool. | P501 Dispose of contents/container to... in accordance with local/regional/ national/international regulations (to be specified). |

| FLAMMABLE SOLIDS (Chapter 2.7) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H228 | Flammable solid |  |
| 2 | Warning | H228 | Flammable solid |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P240 Ground/Bond container and receiving equipment. - if electrostatically sensitive material is for reloading. P241 Use explosion-proof electrical/ventilating/lighting/…/ ... equipment ... Manufacturer/supplier or the competent authority to specify equipment. - if dust clouds can occur. P280 Wear protective gloves/eye protection/face protection Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use ... for extinction ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. |  |  |

| SELF-REACTIVE SUBSTANCES AND MIXTURES (Chapter 2.8) |
| --- |
|  |  |  | Symbol Exploding bomb |
| Hazard category | Signal word | Hazard statement |  |
| Type A | Danger | H240 | Heating may cause an explosion |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P220 Keep/Store away from clothing/…/combustible materials. ... Manufacturer/supplier or the competent authority to specify other incompatible materials. - ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used when this precaution only applies to storage . P234 Keep only in original container. - repackaging may result in a different hazard category P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use ... for extinction ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. P370 + P380 + P375 In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. | P403 + P235 Store in a well-ventilated place. Keep cool. P410 Protect from sunlight P411 Store at temperatures not exceeding …°C/…°F. ... Manufacturer/supplier or the competent authority to specify temperature. P420 Store away from other materials. | P501 Dispose of contents/container to... … in accordance with local/regional/national/international regulations (to be specified). |

| SELF-REACTIVE substances and mixtures (Chapter 2.8) |
| --- |
|  |  |  | Symbol Exploding bomb and flame |
| Hazard category | Signal word | Hazard statement |  |  |
| Type B | Danger | H241 | Heating may cause a fire or explosion |  |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P220 Keep/Store away from clothing/.../combustible materials. ... Manufacturer/supplier or the competent authority to specify other incompatible materials. P234 Keep only in original container. - repackaging may result in a different hazard category P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk P370 + P380 + P375 In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. | P403 + P235 Store in a well-ventilated place. Keep cool. P410 Protect from sunlight P411 Store at temperatures not exceeding …°C/…°F. ... Manufacturer/supplier or the competent authority to specify temperature. P420 Store away from other materials. | P501 Dispose of contents/container to... …in accordance with local/regional/national/international regulations (to be specified). |

| SELF-REACTIVE substances and mixtures (Chapter 2.8) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| Type C | Danger | H242 | Heating may cause a fire |  |
| Type D | Danger | H242 | Heating may cause a fire |  |
| Type E | Warning | H242 | Heating may cause a fire |  |
| Type F | Warning | H242 | Heating may cause a fire |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P220 Keep/Store away from clothing/…/combustible materials. …Manufacturer/supplier or the competent authority to specify other incompatible materials. P234 Keep only in original container. - repackaging may result in a different hazard category P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use ... for extinction ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P403 + P235 Store in a well-ventilated place. Keep cool. P410 Protect from sunlight P411 Store at temperatures not exceeding …°C/…°F. ...Manufacturer/supplier or the competent authority to specify temperature. P420 Store away from other materials. | P501 Dispose of contents/container to... …in accordance with local/regional/national/international regulations (to be specified). |

| PYROPHORIC LIQUIDS (Chapter 2.9) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H250 | Catches fire spontaneously if exposed to air |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition sources(s). P222 Do not allow contact with air. P422 Store contents under… …Manufacturer/supplier or the competent authority to specify appropriate liquid or inert gas. P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P302 + P334 IF ON SKIN (or hair): Immerse in cool water/wrap with wet bandages P370 + P378 In case of fire: Use ... for extinction ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P422 Store contents under ... ... Manufacturer/supplier or the competent authority to specify appropriate liquid or inert gas. |  |

| PYROPHORIC SOLIDS (Chapter 2.10) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H250 | Catches fire spontaneously if exposed to air |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P222 Do not allow contact with air. P422 Store contents under… …Manufacturer/supplier or the competent authority to specify appropriate liquid or inert gas. P280 Wear protective gloves/eye protection/face protection Manufacturer/supplier or the competent authority to specify type of equipment. | P335 + P334 Brush off loose particles from skin. Immerse in cool water/wrap in wet bandages. P370 + P378 In case of fire: Use ... for extinction ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P422 Store contents under ... …Manufacturer/supplier or the competent authority to specify appropriate liquid or inert gas. |  |

| SELF-HEATING SUBSTANCES AND MIXTURES (Chapter 2.11) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H251 | Self-heating; may catch fire |  |
| 2 | Warning | H252 | Self-heating in large quantities; may catch fire |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P235 + P410 Keep cool. Protect from sunlight. P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. P220 Keep/store away from clothing/…/other materials/combustible materials. Manufacturer/supplier or the competent authority to specify other incompatible materials. - ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used when this precaution applies to storage |  | P407 Maintain air gap between stacks/pallets. P413 Store bulk masses greater than … kg/…lbs at temperatures not exceeding …°C/…°F. ... Manufacturer/supplier or the competent authority to specify mass and temperature. P420 Store away from other materials. |  |

| substances and mixtures WHICH, IN CONTACT WITH WATER, EMIT FLAMMABLE GASES (Chapter 2.12) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H260 | In contact with water releases flammable gases, which may ignite spontaneously |  |
| 2 | Danger | H261 | In contact with water releases flammable gas |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P223 Keep away from any possible contact with water, because of violent reaction and possible flash fire. P231 + P232 Handle under inert gas. Protect from moisture. P233 Keep in a container tightly closed container P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P335 + P334 Brush off loose particles from skin and immerse in cool water/wrap in wet bandages. P370 + P378 In case of fire: Use ... for extinction ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P402 + P404 P233 Store in a dry place. Store in a closed container. Keep in a tightly closed container. | P501 Dispose of contents/container to... …in accordance with local/regional/national/ international regulations (to be specified). |

| substances and mixtures WHICH, IN CONTACT WITH WATER, EMIT FLAMMABLE GASES (Chapter 2.12) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 3 | Warning | H261 | In contact with water releases flammable gas |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P231 + P232 Handle under inert gas. Protect from moisture. P233 Keep in a container tightly closed container P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. | P402 + P404 P233 Store in a dry place. Store in a closed container. Keep in a tightly closed container. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| OXIDIZING LIQUIDS (Chapter 2.13) |
| --- |
|  |  |  | Symbol Flame over circle |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H271 | May cause fire or explosion; strong oxidizer |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat. P220 Keep/Store away from clothing and other combustible materials. P221 Take any precaution to avoid mixing with combustibles/... Do not mix with combustibles/… ... Manufacturer/supplier or the competent authority to specify other incompatible materials. P280 Wear protective gloves /eye protection/face protection/… - specify fire/ flame resistant/retardant clothing P283 Wear fire/flame resistant/retardant clothing. | P306 + P360 IF ON CLOTHING: Rinse immediately contaminated clothing and skin with plenty of water before removing clothes. P371 + P380 + P375 In case of major fire and large quantities: Evacuate area. Fight fire remotely due to the risk of explosion. P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. |  | P501 Dispose of contents/container to... …in accordance with local/regional/ national/international regulations (to be specified). |

| OXIDIZING LIQUIDS (Chapter 2.13) |
| --- |
|  |  |  | Symbol Flame over circle |
| Hazard category | Signal word | Hazard statement |  |
| 2 | Danger | H272 | May intensify fire; oxidizer |  |
| 3 | Warning | H272 | May intensify fire; oxidizer |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat. P220 Keep/Store away from clothing/…/combustible materials. …Manufacturer/supplier or the competent authority to specify other incompatible materials. - ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used only when this precaution only applies to storage P221 Take any precaution to avoid mixing with combustibles/... Do not mix with combustibles/… ... Manufacturer/supplier or the competent authority to specify other incompatible materials. P280 Wear protective gloves /eye protection/face protection/… - specify fire/ flame resistant/retardant clothing | P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. |  | P501 Dispose of contents/container to... …in accordance with local/regional/ national/international regulations (to be specified). |

| OXIDIZING SOLIDS (Chapter 2.14) |
| --- |
|  |  |  | Symbol Flame over circle |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H271 | May cause fire or explosion; strong oxidizer |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat. P220 Keep away from clothing and other combustible materials. P221 Take any precaution to avoid mixing with combustibles/... Do not mix with combustibles/… …Manufacturer/supplier or the competent authority to specify other incompatible materials. P280 Wear protective gloves /eye protection/face protection/… - specify fire/ flame resistant/retardant clothing P283 Wear fire/flame resistant/retardant clothing. | P306 + P360 IF ON CLOTHING: Rinse immediately contaminated clothing and skin with plenty of water before removing clothes. P371 + P380 + P375 In case of major fire and large quantities: Evacuate area. Fight fire remotely due to the risk of explosion. P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. |  | P501 Dispose of contents/container to... …in accordance with local/regional/ national/international regulations (to be specified). |

| OXIDIZING SOLIDS (Chapter 2.14) |
| --- |
|  |  |  | Symbol Flame over circle |
| Hazard category | Signal word | Hazard statement |  |
| 2 | Danger | H272 | May intensify fire; oxidizer |  |
| 3 | Warning | H272 | May intensify fire; oxidizer |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat. P220 Keep/Store away from clothing/…/ combustible materials. … Manufacturer/supplier or the competent authority to specify incompatible materials. P221 Take any precaution to avoid mixing with combustibles/... Do not mix with combustibles/… …Manufacturer/supplier or the competent authority to specify other incompatible materials. - ‘keep’ should be used where temperature should never be exceeded - ‘store’ should be used where temperature should only not be exceeded in storage. P280 Wear protective gloves /eye protection/face protection/… - specify fire/ flame resistant/retardant clothing | P370 + P378 In case of fire: Use ... for extinction. ... Manufacturer/supplier or the competent authority to specify appropriate media. - if water increases risk. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ORGANIC PEROXIDES (Chapter 2.15) |
| --- |
|  |  |  | Symbol Exploding bomb |
| Hazard category | Signal word | Hazard statement |  |
| Type A | Danger | H240 | Heating may cause an explosion |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces.- No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P220 Keep/Store away from clothing/…/combustible materials. ... Manufacturer/supplier or the competent authority to specify incompatible materials. - ‘keep’ should be used when the chemical should be kept away from the specified materials at all times, whereas ‘store’ should be used when this precaution only applies to storage P234 Keep only in original container. - repackaging may result in a different hazard category P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use … for extinction … Manufacturer/supplier to specify appropriate media. if water increases risk P370 + P380 + P375 In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. | P411 + P235 Store at temperatures not exceeding …°C/…°F. Keep cool. ... Manufacturer/supplier or the competent authority to specify temperature. P403 + P235 Store in a well-ventilated place. Keep cool P410 Protect from sunlight. P420 Store away from other materials. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ORGANIC PEROXIDES (Chapter 2.15) |
| --- |
|  |  |  | Symbol Exploding bomb and flame |
| Hazard category | Signal word | Hazard statement |  |  |
| Type B | Danger | H241 | Heating may cause a fire or explosion |  |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P220 Keep /Store away from clothing/.../combustible materials. ... Manufacturer/supplier or the competent authority to specify incompatible materials. P234 Keep only in original container. - repackaging may result in a different hazard category P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use … for extinction … Manufacturer/supplier to specify appropriate media. if water increases risk P370 + P380 + P375 In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. | P411 + P235 Store at temperatures not exceeding …°C/…°F. Keep cool. Manufacturer/supplier or the competent authority to specify temperature. P403 + P235 Store in a well-ventilated place. Keep cool P410 Protect from sunlight. P420 Store away from other materials. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ORGANIC PEROXIDES (Chapter 2.15) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| Type C | Danger | H242 | Heating may cause a fire |  |
| Type D | Danger | H242 | Heating may cause a fire |  |
| Type E | Warning | H242 | Heating may cause a fire |  |
| Type F | Warning | H242 | Heating may cause a fire |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Manufacturer/supplier or the competent authority to specify applicable ignition source(s). P220 Keep/Store away from clothing/.../ combustible materials ... Manufacturer/supplier or the competent authority to specify incompatible materials. P234 Keep only in original container. - repackaging may result in a different hazard category P280 Wear protective gloves/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P370 + P378 In case of fire: Use … for extinction … Manufacturer/supplier to specify appropriate media. if water increases risk | P411 + P235 Store at temperatures not exceeding …°C/…°F. Keep cool. ... Manufacturer/supplier or the competent authority to specify temperature. P403 + P235 Store in a well-ventilated place. Keep cool P410 Protect from sunlight. P420 Store away from other materials. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| CORROSIVE TO METALS (Chapter 2.16) |
| --- |
|  |  |  | Symbol Corrosion |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Warning | H290 | May be corrosive to metals |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P234 Keep only in original container. | P390 Absorb spillage to prevent material damage. | P406 Store in corrosive resistant/... container with a resistant inner liner. ... Manufacturer/supplier or the competent authority to specify other compatible materials. |  |

| ACUTE TOXICITY - ORAL (Chapter 3.1) |
| --- |
|  |  |  | Symbol Skull and crossbones |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H300 | Fatal if swallowed |  |
| 2 | Danger | H300 | Fatal if swallowed |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P264 Wash …thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P270 Do not eat, drink or smoke when using this product. | P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER/or doctor/physician/…. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P321 Specific treatment (see ... on this label) ... Reference to supplemental first aid instruction. - if immediate administration of antidote is required. P330 Rinse mouth. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ACUTE TOXICITY - ORAL (Chapter 3.1) |
| --- |
|  |  |  | Symbol Skull and crossbones |
| Hazard category | Signal word | Hazard statement |  |
| 3 | Danger | H301 | Toxic if swallowed |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P264 Wash … thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P270 Do not eat, drink or smoke when using this product. | P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER/or doctor/physician/…. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P321 Specific treatment (see ... on this label) ... Reference to supplemental first aid instruction. - if immediate administration of antidote is required. P330 Rinse mouth. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ACUTE TOXICITY - ORAL (Chapter 3.1) |
| --- |
|  |  |  | Symbol Exclamation mark |
| Hazard category | Signal word | Hazard statement |  |
| 4 | Warning | H302 | Harmful if swallowed |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P264 Wash … thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P270 Do not eat, drink or smoke when using this product. | P301 + P312 IF SWALLOWED: Call a POISON CENTER or/doctor/physician/… if you feel unwell. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. P330 Rinse mouth. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ACUTE TOXICITY - ORAL (Chapter 3.1) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 5 | Warning | H303 | May be harmful if swallowed |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
|  | P312 Call a POISON CENTER/doctor/physician/… if you feel unwell. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. |  |  |

| ACUTE TOXICITY - DERMAL (Chapter 3.1) |
| --- |
|  |  |  | Symbol Skull and crossbones |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H310 | Fatal in contact with skin |  |
| 2 | Danger | H310 | Fatal in contact with skin |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P262 Do not get in eyes, on skin, or on clothing. P264 Wash … thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P270 Do not eat, drink or smoke when using this product. P280 Wear protective gloves/protective clothing. Manufacturer/supplier or the competent authority to specify type of equipment. | P302 + P350 + P352 IF ON SKIN (or hair): Gently wash with plenty of soap and water. Wash skin with plenty of soap and water. P310 Immediately call a POISON CENTER/or doctor/physician/…. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P322 Specific measures (see ... on this label) P321 Specific treatment (see … on this label) ... Reference to supplemental first aid instruction. - if immediate measures such as specific cleansing agent is advised. P361 Remove Immediately Ttake off immediately all contaminated clothing . Wash before reuse. P363 Wash contaminated clothing before reuse. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ACUTE TOXICITY - DERMAL (Chapter 3.1) |
| --- |
|  |  |  | Symbol Skull and crossbones |
| Hazard category | Signal word | Hazard statement |  |
| 3 | Danger | H311 | Toxic in contact with skin |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P280 Wear protective gloves/protective clothing. Manufacturer/supplier or the competent authority to specify type of equipment. | P302 + P352 IF ON SKIN (or hair): Wash skin with plenty of soap and water. P312 Call a POISON CENTRE/or doctor/physician/… if you feel unwell. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. P322 Specific measures (see ... on this label) P321 Specific treatment (see … on this label) ... Reference to supplemental first aid instruction. - if measures such as specific cleansing agent is advised. P361 Remove Immediately Ttake off immediately all contaminated clothing . Wash before reuse. P363 Wash contaminated clothing before reuse. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ACUTE TOXICITY - DERMAL (Chapter 3.1) |
| --- |
|  |  |  | Symbol Exclamation mark |
| Hazard category | Signal word | Hazard statement |  |
| 4 | Warning | H312 | Harmful in contact with skin |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P280 Wear protective gloves/protective clothing Manufacturer/supplier or the competent authority to specify type of equipment. | P302 + P352 IF ON SKIN (or hair): Wash skin with plenty of soap and water. P312 Call a POISON CENTER/or doctor/physician/… if you feel unwell. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. P322 Specific measures (see ... on this label) P321 Specific treatment (see … on this label) ... Reference to supplemental first aid instruction. - if measures such as specific cleansing agent is advised. P362 Take off all contaminated clothing. Wash before re-use P363 Wash contaminated clothing before reuse. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ACUTE TOXICITY - DERMAL (Chapter 3.1) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 5 | Warning | H313 | May be harmful in contact with skin |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
|  | P312 Call a POISON CENTER/or doctor/physician/… if you feel unwell. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. |  |  |

| ACUTE TOXICITY - INHALATION (Chapter 3.1) |
| --- |
|  |  |  | Symbol Skull and crossbones |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H330 | Fatal if inhaled |  |
| 2 | Danger | H330 | Fatal if inhaled |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P260 Do not create/breathe dust/fume/gas/mist/ vapours/spray. Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. P271 Use only outdoors or in a well-ventilated area. P284 Wear respiratory protection. Manufacturer/supplier or the competent authority to specify equipment. | P304 + P340 IF INHALED: Remove victim individual to fresh air and keep at rest in a position comfortable for breathing. P310 Immediately call a POISON CENTER/or doctor/physician/…. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P320 Specific treatment is urgent (see ... on this label) P321 Specific treatment (see … on this label) ... Reference to supplemental first aid instruction. - if immediate administration of antidote is required. | P403 + P233 Store in a well-ventilated place. Keep in a container tightly closed container. - if product is volatile as to generate hazardous atmosphere. P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ACUTE TOXICITY - INHALATION (Chapter 3.1) |
| --- |
|  |  |  | Symbol Skull and crossbones |
| Hazard category | Signal word | Hazard statement |  |
| 3 | Danger | H331 | Toxic if inhaled |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P261 Avoid breathing dust/fume/gas/mist/ vapours/spray. P260 Do not create/breathe dust/fume gas/mist/vapours/spray Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. P271 Use only outdoors or in a well-ventilated area. | P304 + P340 IF INHALED: Remove victim individual to fresh air and keep at rest in a position comfortable for breathing. P311 Call a POISON CENTER/or doctor/physician. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P321 Specific treatment (see ... on this label) P321 Specific treatment (see … on this label) ... Reference to supplemental first aid instruction. - if immediate specific measures are required. | P403 + P233 Store in a well-ventilated place. Keep in a container tightly closed container. - if product is volatile so as to generate hazardous atmosphere. P405 Store locked up. | P501 Dispose of content/container to… … in accordance with local/regional/national/international regulations (to be specified). |

| ACUTE TOXICITY - INHALATION (Chapter 3.1) |
| --- |
|  |  |  | Symbol Exclamation mark |
| Hazard category | Signal word | Hazard statement |  |
| 4 | Warning | H332 | Harmful if inhaled |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P261 Avoid breathing dust/fume/gas/mist/ vapours/spray. P260 Do not create/breathe dust/fume gas/mist/vapours/spray Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. P271 Use only outdoors or in a well-ventilated area. | P304 + P340 IF INHALED: Remove victim individual to fresh air and keep at rest in a position comfortable for breathing. P312 Call a POISON CENTER/or doctor/physician/… if you feel unwell. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. |  |  |

| ACUTE TOXICITY - INHALATION (Chapter 3.1) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 5 | Warning | H333 | May be harmful if inhaled |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
|  | P304 + P312 IF INHALED: Call a POISON CENTER/or doctor/physician/… if you feel unwell. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. |  |  |

| SKIN CORROSION/IRRITATION (Chapter 3.2) |
| --- |
|  |  |  | Symbol Corrosion |
| Hazard category | Signal word | Hazard statement |  |
| 1A to 1C | Danger | H314 | Causes severe skin burns and eye damage |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P260 Do not breathe dusts or mists. - if inhalable particles of dusts or mists may occur during use. P264 Wash …thoroughly after handling. …Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P280 Wear protective gloves/protective clothing/eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P301 + P330 + P331 IF SWALLOWED: Rinse mouth. Do NOT induce vomiting. P303 + P361 + P353 P352 IF ON SKIN (or hair): Remove Immediately Ttake off immediately all contaminated clothing . Wash before reuse. Rinse skin with water/shower. Wash skin with plenty of soap and water. P363 Wash contaminated clothing before reuse. P304 + P340 IF INHALED: Remove victim individual to fresh air and keep at rest in a position comfortable for breathing. P310 Immediately call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P321 Specific treatment (see ... on this label) ... Reference to supplemental first aid instruction. - Manufacturer/supplier or the competent authority may specify a cleansing agent if appropriate. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |
| SKIN CORROSION/IRRITATION (Chapter 3.2) |
|  |  |  | Symbol Exclamation mark |
| Hazard category | Signal word | Hazard statement |  |
| 2 | Warning | H315 | Causes skin irritation |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P264 Wash … thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P280 Wear protective gloves. Manufacturer/supplier or the competent authority to specify type of equipment. | P302 + P352 IF ON SKIN (or hair): Wash skin with plenty of soap and water. P321 Specific treatment (see ... on this label) ... Reference to supplemental first aid instruction. - Manufacturer/supplier or the competent authority may specify a cleansing agent if appropriate. P332 + P313 If skin irritation occurs: Get medical advice/attention. P333 + P311 If skin irritation or rash occurs: Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P362 Take off contaminated clothing . Wash before reuse. |  |  |
| SKIN CORROSION/IRRITATION (Chapter 3.2) |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 3 | Warning | H316 | Causes mild skin irritation |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
|  | P332 + P313 If skin irritation occurs: Get medical advice/attention. P333 + P311 If skin irritation or rash occurs: Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |  |  |

| EYE DAMAGE/IRRITATION (Chapter 3.3) |
| --- |
|  |  |  | Symbol Corrosion |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H318 | Causes serious eye damage |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P280 Wear eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P310 Immediately call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |  |  |

| EYE DAMAGE/IRRITATION (Chapter 3.3) |
| --- |
|  |  |  | Symbol Exclamation mark |
| Hazard category | Signal word | Hazard statement |  |
| 2A | Warning | H319 | Causes serious eye irritation |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P264 Wash … thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P280 Wear eye protection/face protection. Manufacturer/supplier or the competent authority to specify type of equipment. | P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P337 + P313 If eye irritation persists: Get medical advice/attention. Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |  |  |

| EYE DAMAGE/IRRITATION (Chapter 3.3) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 2B | Warning | H320 | Causes eye irritation |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P264 Wash … thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. | P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P337 + P313 If eye irritation persists: Get medical advice/attention. Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |  |  |

| SENSITIZATION - RESPIRATORY (Chapter 3.4) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 1, 1A, 1B | Danger | H334 | May cause allergy or asthma symptoms or breathing difficulties if inhaled |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P261 Avoid breathing dust/fume/gas/mist/ vapours/spray. P260 Do not create/breathe dust/fume gas/mist/vapours/spray Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. P284 Wear respiratory protection Manufacturer/supplier or the competent authority to specify equipment P285 In case of inadequate ventilation wear respiratory protection. Manufacturer/supplier or the competent authority to specify equipment | P304 + P341 IF INHALED: If breathing is difficult, remove victim individual to fresh air and keep at rest in a position comfortable for breathing. P342 + P311 If experiencing respiratory symptoms: Call a POISON CENTER/or doctor/physician. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| SENSITIZATION - SKIN (Chapter 3.4) |
| --- |
|  |  |  | Symbol Exclamation mark |
| Hazard category | Signal word | Hazard statement |  |
| 1, 1A, 1B | Warning | H317 | May cause an allergic skin reaction |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P261 Avoid breathing dust/fume/gas/mist/ vapours/spray. P260 Do not create/breathe dust/fume gas/mist/vapours/spray Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. P272 Contaminated work clothing should not be allowed out of the workplace. P280 Wear protective gloves. Manufacturer/supplier or the competent authority to specify type of equipment. | P302 + P352 IF ON SKIN (or hair): Wash skin with plenty of soap and water. P333 + P313 +P311 If skin irritation or rash occurs: Get medical advice/attention. Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P321 Specific treatment (see ... on this label) ... Reference to supplemental first aid instruction. - Manufacturer/supplier or the competent authority may specify a cleansing agent if appropriate. P362 Take off all contaminated clothing. Wash before re-use P363 Wash contaminated clothing before reuse. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| GERM CELL MUTAGENICITY (Chapter 3.5) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H340 | May cause genetic defects <...> |  |
| 2 | Warning | H341 | Suspected of causing genetic defects <...> |  |
|  |  | <...> (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P280 Wear protective gloves/protective clothing/eye protection/face protection Manufacturer/supplier or the competent authority to specify appropriate personal protective equipment. P281 Use personal protective equipment as required. | P308 + P313 + P311 IF exposed or concerned: Get medical advice/attention. Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| CARCINOGENICITY (Chapter 3.6) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H350 | May cause cancer <...> |  |
| 2 | Warning | H351 | Suspected of causing cancer <...> |  |
|  |  | <...> (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard). |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P280 Wear protective gloves/protective clothing/eye protection/face protection Manufacturer/supplier or the competent authority to specify appropriate personal protective equipment. P281 Use personal protective equipment as required. | P308 + P313 + P311 IF exposed or concerned: Get medical advice/attention. Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| TOXIC TO REPRODUCTION (Chapter 3.7) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H360 | May damage fertility or the unborn child <...> <<...>> |  |
| 2 | Warning | H361 | Suspected of damaging fertility or the unborn child <...> <<...>> |  |
|  |  | <...> (state specific effect if known) |  |
|  |  | <<...>> (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P280 Wear protective gloves/protective clothing/eye protection/face protection Manufacturer/supplier or the competent authority to specify appropriate personal protective equipment. P281 Use personal protective equipment as required. | P308 + P313 + P311 IF exposed or concerned: Get medical advice/attention. Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| TOXIC TO REPRODUCTION (Chapter 3.7) (effects on or via lactation) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| (additional) | No signal word | H362 | May cause harm to breast-fed children |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood P260 Do not breathe dusts or mists. - if inhalable particles of dusts or mists may occur during use. P263 Avoid contact during pregnancy/while nursing. P264 Wash … thoroughly after handling. …Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P270 Do not eat, drink or smoke when using this product. | P308 + P313 + P311 IF exposed or concerned: Get medical advice/attention. Call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. |  |  |

| SPECIFIC TARGET ORGAN TOXICITY (Single Exposure) (Chapter 3.8) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H370 | Causes damage to organs <...> <<...>> |  |
|  |  | <...> (or state all organs affected if known) |  |
|  |  | <<...>> (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P260 Do not breathe dust/fume/gas/mist/ vapours/spray. Manufacturer/supplier or the competent authority to specify applicable conditions. P264 Wash …thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P270 Do not eat, drink or smoke when using this product. | P307 + P311 If exposed: call a POISON CENTER or doctor/physician. P307 + P311 IF exposed: Call a POISON CENTER/or doctor/physician… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P321 Specific treatment (see ... on this label) ... Reference to supplemental first aid instruction. - if immediate measures are required. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| SPECIFIC TARGET ORGAN TOXICITY (Single Exposure) (Chapter 3.8) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 2 | Warning | H371 | May cause damage to organs <...> <<...>> |  |
|  |  | <...> (or state all organs affected, if known) |  |
|  |  | <<...>> (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P260 Do not create/breathe dust/fume/gas/mist/ vapours/spray. Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. P264 Wash … thoroughly after handling. … Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P270 Do not eat, drink or smoke when using this product. | P309 + P311 IF exposed or if you feel unwell: Call a POISON CENTER or doctor/physician. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| SPECIFIC TARGET ORGAN TOXICITY (Single Exposure) (Chapter 3.8) |
| --- |
|  |  |  | Symbol Exclamation mark |
| Hazard category | Signal word | Hazard statement |  |
| 3 | Warning | H335 | May cause respiratory irritation; or |  |
|  |  | H336 | May cause drowsiness or dizziness |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P261 Avoid breathing dust/fume/gas/mist/ vapours/spray. P260 Do not create/breathe dust/fume gas/mist/vapours/spray Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. P271 Use only outdoors or in a well-ventilated area. | P304 + P340 IF INHALED: Remove victim individual to fresh air and keep at rest in a position comfortable for breathing. P312 Call a POISON CENTER/or doctor/physician/… if you feel unwell. Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. | P403 + P233 Store in a well-ventilated place. Keep in a container tightly closed container. - if product is volatile so as to generate hazardous atmosphere. P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| SPECIFIC TARGET ORGAN TOXICITY (Repeated Exposure) (Chapter 3.9) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H372 | Causes damage to organs <...> through prolonged or repeated exposure <<...>> |  |
|  |  | <...> (state all organs affected, if known) |  |
|  |  | <<...>> (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P260 Do not create/breathe dust/fume/gas/mist/ vapours/spray. Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. P264 Wash … thoroughly after handling. …Manufacturer/supplier or the competent authority to specify parts of the body to be washed after handling. P270 Do not eat, drink or smoke when using this product. | P314 Get medical advice/attention if you feel unwell. P312 Call a POISON CENTER/doctor/physician… if you feel unwell Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| SPECIFIC TARGET ORGAN TOXICITY (Repeated Exposure) (Chapter 3.9) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 2 | Warning | H373 | May cause damage to organs <...> through prolonged or repeated exposure <<...>> |  |
|  |  | <...> | (state all organs affected, if known) |  |
|  |  | <<...>> | (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P260 Do not create/breathe dust/fume/gas/mist/ vapours/spray. Manufacturer/supplier or the competent authority to specify practicable precaution and applicable conditions. | P314 Get medical advice/attention if you feel unwell. P312 Call a POISON CENTER/doctor/physician… if you feel unwell Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get medical advice/attention if you feel unwell" may be used on labels where more than one possible source of medical attention is available. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| ASPIRATION HAZARD (Chapter 3.10) |
| --- |
|  |  |  | Symbol Health hazard |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H304 | May be fatal if swallowed and enters airways |  |
| 2 | Warning | H305 | May be harmful if swallowed and enters airways |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
|  | P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER/doctor/physician/… Manufacturer/supplier or the competent authority to specify the appropriate source of medical attention. The statement "Get immediate medical advice/attention" may be used on labels where more than one possible source of medical attention is available. P331 Do NOT induce vomiting. | P405 Store locked up. | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| HAZARDOUS TO THE AQUATIC ENVIRONMENT - ACUTE HAZARD (Chapter 4.1) |
| --- |
|  |  |  | Symbol Environment |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Warning | H400 | Very toxic to aquatic life |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P273 Avoid release to the environment. - if this is not the intended use. | P391 Collect spillage. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| HAZARDOUS TO THE AQUATIC ENVIRONMENT - ACUTE HAZARD (Chapter 4.1) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 2 | No signal word | H401 | Toxic to aquatic life |  |
| 3 | No signal word | H402 | Harmful to aquatic life |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P273 Avoid release to the environment. - if this is not the intended use. |  |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| HAZARDOUS TO THE AQUATIC ENVIRONMENT - LONG-TERM HAZARD (Chapter 4.1) |
| --- |
|  |  |  | Symbol Environment |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Warning | H410 | Very toxic to aquatic life with long lasting effects |  |
| 2 | No signal word | H411 | Toxic to aquatic life with long lasting effects |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P273 Avoid release to the environment. - if this is not the intended use. | P391 Collect spillage. |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| HAZARDOUS TO THE AQUATIC ENVIRONMENT - LONG-TERM HAZARD (Chapter 4.1) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 3 | No signal word | H412 | Harmful to aquatic life with long lasting effects |  |
| 4 | No signal word | H413 | May cause long lasting harmful effects to aquatic life |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P273 Avoid release to the environment. - if this is not the intended use. |  |  | P501 Dispose of contents/container to... ... in accordance with local/regional/national/international regulations (to be specified). |

| HAZARDOUS TO THE OZONE LAYER (Chapter 4.2) |
| --- |
|  |  |  | Symbol Exclamation mark |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Warning | H420 | Harms public health and the environment by destroying ozone in the upper atmosphere |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
|  |  |  | P502 Refer to manufacturer/supplier for information on recovery/recycling |

-------------------

# Footnotes

Throughout, additions are indicated in bold underlined text, and deletions in strikethrough.