| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/34 17 December 2008 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-seventh session

Geneva, 10 - 13 March 2009

Item 4.2.40 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 2 to Regulation No. 123

(Adaptive front-lighting systems (AFS))

Submitted by the Working Party on Lighting and Light-Signalling (GRE) (/

The text reproduced below was adopted by GRE at its sixtieth session.  It is based on ECE/TRANS/WP.29/GRE/2008/38, not amended.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRE/60, para. 29).

Paragraphs 5.8.2. and 5.8.2.1., amend to read:

"5.8.2.	provide means to achieve a traffic-change function, meeting the values shown in the following table when tested according to paragraph 6.2. below with the adjustment left unchanged compared to that for the original traffic direction;

5.8.2.1.	Passing beam designed for right-hand traffic and adapted to left-hand traffic:

at 0.86D-1.72L	at least 3 lux

at 0.57U-3.43R	not more than 1.0 lux"

Insert a new paragraph 5.8.2.2., to read:

"5.8.2.2.	Passing beam designed for left-hand traffic and adapted to right-hand traffic:

at 0.86D-1.72R	at least 3 lux

at 0.57U-3.43L	not more than 1.0 lux "

Paragraph 5.8.2.1. (former), renumber as paragraph 5.8.2.3.

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.