| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/41 17 December 2008 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-seventh session

Geneva, 10-13 March 2009

Item 4.2.39 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 3 to the Regulation No. 121

(Hand controls, tell tales and indicators)

Submitted by the Working Party on General Safety Provisions (/

The text reproduced below was adopted by the Working Party on General Safety Provisions (GRSG) at its ninety-fifth session (ECE/TRANS/WP.29/GRSG/74, para. 38).  It is based on ECE/TRANS/WP.29/GRSG/2008/27, as amended by para. 38 of the report.  It is submitted to WP.29 and AC.1 for consideration.

Table 1, items 35. and 36., amend to read:

"

| No | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | Item | symbol 2/ | Function | Illumination | Colour |
| … | … | … | … | … | … |
| 35. | Engine Start | 11/, 19/ | Control | No |  |
| 36. | Engine Stop | 11/, 19/ | Control | Yes |  |
| … | … | … | … | … | … |

"

Table 1, add a new footnote 19, to read:

"19/	The functions "start" and "stop" may be combined in one control.  As an alternative to the prescribed symbol(s) it is allowed to use the text "START" and/or "STOP" or a combination of symbols and text.  Text can be displayed in uppercase and/or lowercase letters."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.