| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/48 23 December 2008 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

# One-hundred-and-forty-seventh session

Geneva, 10-13 March 2009

Item 16.2 of the provisional agenda

PROGRESS ON THE DEVELOPMENT OF NEW GLOBAL TECHNICAL REGULATIONS OR ON THE AMENDMENTS OF GLOBAL TECHNICAL REGULATIONS

Gtr No. 7 (Head restraints)

Amendments to the proposal to develop Phase II of gtr No. 7 
and to establish an informal group for its development

Submitted by the representative of the United States of America (/

The text reproduced below was submitted by the representative of the United States of America and proposes amendments to the proposal to develop amendments to global technical regulation (gtr) No. 7 (ECE/TRANS/WP.29/2008/115).  The proposed amendments are marked in bold and in strikethrough characters.

A.	PROPOSAL

Paragraph 4., amend to read (footnote 2/ remains):

"4.	At higher speed rear impact crashes (∆V ≥ 18 km/h), there are as many minor whiplash injuries as recorded in the low speed crashes and there are a significant number of more severe whiplash injuries (MAIS 2 and MAIS 3) occurring./.  The United States of America is currently evaluating several dummies and a dynamic test that could address these injuries."

B.	JUSTIFICATION

These amendments are clarification to the text to better reflect the evaluations being conducted by the United States.

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.

/ <http://www.sae.org/events/gim/presentations/2008moorhouse1.pdf>