| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/86 29 July 2009 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-ninth session

Geneva, 10 - 13 November 2009

Item 4.2.8 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 1 to Revision 5 to Regulation No. 37

(Filament lamps of power-driven vehicles and their trailers)

Submitted by the Working Party on Lighting and Light-Signalling (/

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-first session.  It is based on ECE/TRANS/WP.29/GRE/2009/11, as amended by para. 7 of the report and on ECE/TRANS/WP.29/GRE/2009/12, not amended.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/61, para.7).

Paragraphs 2.1.1., amend to read:

"2.1.1. 	Definition of "category"

The term "category" is used in this Regulation to describe different basic design of standardised filament lamps. Each category has a specific designation, as for example: "H4", "P21W", "T4W", "PY21W"or "RR10W"."

Paragraph 2.1.2., insert a reference to footnote 1/ and footnote 1/, to read:

"2.1.2. 	Definition of "type"

Filament lamps of different 1/ "types" are filament lamps within the same category which differ in such essential respects as:

_____________

1/	A selective-yellow bulb or an additional selective-yellow outer bulb, solely intended to change the colour but not the other characteristics of a filament lamp emitting white light, does not constitute a change of type of the filament lamp."

Paragraph 2.1.2.1., amend to read (including the deletion of footnote 1/ and the reference 1/):

"2.1.2.1. 	trade name or mark (Filament lamps bearing the same trade name or mark but produced by different manufacturers are considered as being of different types. Filament lamps produced by the same manufacturer differing only by the trade name or mark may be considered to be of the same type);"

Paragraph 2.1.2.2., amend to read:

"2.1.2.2. 	bulb design and/or cap design, in so far as these differences affect the optical results;"

Paragraph 2.1.2.3., shall be deleted

Paragraphs 2.1.2.4. and 2.1.2.5., renumber as paragraphs 2.1.2.3. and 2.1.2.4.

Annex 1, Sheet P19W/2, footnote 4, amend to read:

"4/	For categories PS19W, PSY19W and PSR19W, dimensions may be checked with O-ring removed to assure the correct mounting during testing."

Annex 1, Sheet P24W/2, footnote 4, amend to read:

"4/	For categories PS24W, PSX24W, PSY24W and PSR24W, dimensions may be checked with O-ring removed to assure the correct mounting during testing."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.