| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRE/2009/49 16 July 2009 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-second session

Geneva, 6 - 9 October 2009

Item 15(c) of the provisional agenda

OTHER BUSINESS

Regulation No. 27

(Advance warning triangle)

Proposal for draft Corrigendum 1 to Revision 1 to Regulation No. 27

Submitted by the expert from Poland (/

The text reproduced below was prepared by the expert from Poland in order to update the reference to the ISO standard in the text of Annex 5 of the Regulation.  The modifications to the current text of the Regulation No. 27 are marked in bold characters.

# A.	PROPOSAL

# Annex 5, paragraph. 12.1., amend to read:

"12.1.	One of the samples of the fluorescent material submitted according to paragraph 3.5. of this Regulation shall be subjected to a temperature and irradiation test described in ISO 105-B02:1994/Amd.2:2000, par. 7.2.4 Method 4, until the contrast No. 4 of the grey scale has been reached for the reference sample No. 5."

# B.	JUSTIFICATION

In paragraph 12.1. of Annex 5 of Regulation No. 27, it is referred generally to the outdated 1978 ISO Standard that is no longer available.  Since ISO 105 contains many test methods covered by several parts of the Regulation, the proposition updates this standard and quotes precise reference and method of measurement.

- - - -

# Footnotes

(/  In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.