|  | .15/88/INF.3 | INF.20E |
| --- | --- | --- |
|  | Economic Commission for Europe Inland Transport Committee Working Party on the Transport of Dangerous Goods Eighty-eighth session Geneva, 3–7 May 2010 Item 5 of the provisional agenda Work of the RID/ADR/ADN Joint Meeting Tran | 28 April 2010 |

Texts adopted by the Joint Meeting: amendments to RID, ADR and ADN for entry into force on 1 January 2011

Note by the secretariat

The secretariat reproduces hereafter the amendments to RID/ADR/ADN for entry into force on 1 January 2011 as adopted by the Joint Meeting at its March 2010 session (ECE/TRANS/WP.15/AC.1/118, annex II).

Part 1

Chapter 1.2

1.2.1	In the definition for "applicant", at the beginning of the second sentence, replace "In the case of periodic testing and exceptional checks" with "In the case of periodic inspections, intermediate inspections and exceptional checks".

(Reference documents: ECE/TRANS/WP.15/AC.1/2010/28 and informal document INF.21)

In the definition for "EN (standard)", replace "(CEN, 36 rue de Stassart, B-1050 Brussels)" with "(CEN, Avenue Marnix 17, B-1000 Brussels)".

Chapter 1.6

1.6.1		Add the following new transitional measure:

"1.6.1.22	Inner receptacles of composite IBCs manufactured before 1 July 2011 and marked in accordance with the requirements of 6.5.2.2.4 in force up to 31 December 2010 may still be used.".

(Reference document: ECE/TRANS/WP.15/AC.1/2010/35)

1.6.3.18	(RID:) Amend the second and the third sub-paragraphs to read as follows:

"However, they shall be marked with the relevant tank code and if applicable the relevant alphanumeric codes of special provisions TC and TE in accordance with 6.8.4.".

(ADR:) At the end, add "provided that the assignment to the relevant tank code and the relevant marking have been carried out".

(Reference document: informal document INF.42)

1.6.4.12	Add the following new paragraph at the end:

"However, they shall be marked with the relevant tank code and if applicable the relevant alphanumeric codes of special provisions TC and TE in accordance with 6.8.4.".

(Reference document: informal document INF.42)

Chapter 1.8

1.8.7.1.2 (c) and 1.8.7.5 (heading)	After "periodic inspection", insert ", intermediate inspection".

1.8.7.7.4	In the heading, after "periodic inspections", insert ", intermediate inspections".

(Reference document: ECE/TRANS/WP.15/AC.1/2010/28)

Part 3

Chapter 3.2

3.2.1, Table A

For UN 1704, in column (3b), replace "T2" with "T1". In column (9b), replace "MP10" with "MP15". In column (12), delete "SGAH". In column (16), delete "W11/V11". (RID only:) In column (19), replace "CE9" with "CE5".

(Reference document: informal document INF.28)

3.2.1, Table A, column (7a)

Informal document INF.23 adopted (for ADR, ECE/TRANS/WP.15/204, confirmed) with the following amendments:

In the ninth indent under "Replace the alphanumeric code LQ with "0" for:", insert at the beginning "(ADR only:)".

In the seventeenth indent under "Replace the alphanumeric code LQ with "0" for:", insert at the beginning "(ADR only:)".

In the twenty-third under "Replace the alphanumeric code LQ with "0" for:", replace "3257 (twice)" with "3257 (ADR only: twice)".

In the first indent under "Replace the alphanumeric code LQ with "120 ml" for:", replace "except for UN Nos. 2668 and 2857" with "except for UN 2857".

Chapter 3.3

3.3.1	SP 251	In the first paragraph, replace "the code "LQ0"" with "the quantity "0"". In the last paragraph, delete "in accordance with the LQ code defined in 3.4.6".

Part 4

Chapter 4.3

4.3.4.1.2	In the table, against "L10CH", in column "Class", insert a reference to tablenote * after "6.1". The tablenote reads as follows:

"*	Substances with an LC50 lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 shall be assigned to tank code L15CH.".

(ADR only:) Under "L10CH", in the columns "Classification code" and "Packing group", after T4, insert a new row with the following information: "T5	I".

Under "L10CH", in the columns "Classification code" and "Packing group", at the end, insert a new row with the following information: "TFW	I".

Amend the entry for "L15CH" to read as follows:

| L15CH | 3 | FT1 | I |
| --- | --- | --- | --- |
|  | 6.1** | T1 | I |
|  |  | T4 | I |
|  |  | TF1 | I |
|  |  | TW1 | I |
|  |  | TO1 | I |
|  |  | TC1 | I |
|  |  | TC3 | I |
|  |  | TFC | I |
|  |  | TFW | I |
|  | and groups of permitted substances for tank codes LGAV, LGBV, LGBF, L1.5BN, L4BN, L4BH, L10BH and L10CH ** Substances with an LC50 lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 shall be assigned to this tank code. |

(Reference document: ECE/TRANS/WP.15/AC.1/2010/18 and informal document INF.42)

Part 5

Chapter 5.4

5.4.1.1.4	Amend to read as follows:

"5.4.1.1.4	(Deleted)".

(Reference document: ECE/TRANS/WP.15/AC.1/2009/20)

Part 6

Chapter 6.2

6.2.6.4		In the first indent, replace "as amended by Commission Directive 94/1/EC5" with "as amended and applicable at the date of manufacture" and delete footnote 5.

(Reference document: ECE/TRANS/WP.15/AC.1/2010/8)

Part 7

Chapter 7.1

7.1.3	Replace "591 (status at 01.01.1998, 2nd edition)" with "591 (status at 01.10.2007, 3rd edition)" and replace "592-4 (status at 01.09.2004, 2nd edition)" with "592-4 (status at 01.05.2007, 3rd edition)".

(Reference document: informal document INF.27)

Amendments to document ECE/TRANS/WP.15/204 – OTIF/RID/CE/2009/11

Part 1

Chapter 1.6

1.6.1.19	Amend to read as follows:

"1.6.1.19	The provisions of 2.2.9.1.10.3 and 2.2.9.1.10.4 concerning the classification of environmentally hazardous substances applicable until 31 December 2010 may be applied until 31 December 2013.".

(Reference document: informal document INF.47)

Chapter 1.8

1.8.6 (heading), 1.8.6.1 and 1.8.6.2.1	After "periodic inspections", insert ", intermediate inspections".

1.8.6.4.1 and 1.8.6.4.3	After "periodic inspection", insert ", intermediate inspection".

(Reference document: ECE/TRANS/WP.15/AC.1/2010/28)

1.8.7.2.4	In the second paragraph after the Note, replace "the use and periodic inspection" with "the use, periodic inspection and intermediate inspection".

(Reference document: ECE/TRANS/WP.15/AC.1/2010/28 and informal document INF.21)

Part 2

Chapter 2.2

2.2.9.1.10.5.2	Replace the amendment with the following new amendment:

"2.2.9.1.10.5	Replace with the following two paragraphs:

"2.2.9.1.10.5	Substances or mixtures classified as environmentally hazardous substances (aquatic environment) on the basis of Regulation 1272/2008/EC*

If data for classification according to the criteria of 2.2.9.1.10.3 and 2.2.9.1.10.4 are not available yet, the classification as environmentally hazardous substances (aquatic environment) shall be adopted either according to Directives 67/548/EEC** and 1999/45/EC*** (risk phrases R50; R50/53; R51/53) or according to Regulation 1272/2008/EC* (category Acute1, Chronic1 or Chronic 2). This means:

a)	If a substance or mixture has been allocated such risk phrase(s) or category, it shall be classified as an environmentally hazardous substance (aquatic environment).

b)	If a substance or mixture has not been allocated such risk phrase(s) or category, it shall not be classified as an environmentally hazardous substance (aquatic environment).

(Note by the secretariat: during the report reading, some editorial issues were identified and the secretariat was invited to submit a proposal for improved text to the Working Party on the Transport of Dangerous Goods and the RID Committee of Experts.)

2.2.9.1.10.6	Assignment of substances or mixtures classified as environmentally hazardous substances (aquatic environment) according to the provisions in 2.2.9.1.10.3, 2.2.9.1.10.4 or 2.2.9.1.10.5

Substances or mixtures classified as environmentally hazardous substances (aquatic environment), not otherwise classified under RID/ADR shall be designated:

UN No. 3077 ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S.; or

UN No. 3082 ENVIRONMENTALLY HAZARDOUS SUBSTANCE, LIQUID, N.O.S.

They shall be assigned to packing group III.".".

(Reference documents: ECE/TRANS/WP.15/AC.1/2010/30 and informal documents INF.15 and INF.44)

Part 6

Chapter 6.8

6.8.2.3.3	In the second paragraph after the Note, replace "the use and periodic inspection" with "the use, periodic inspection and intermediate inspection".

(Reference documents: ECE/TRANS/WP.15/AC.1/2010/28 and informal document INF.21)

# Footnotes

* 	Regulation 1272/2008/EC of the European Parliament and of the Council of 16 December 2008 on classification, labelling and packaging of substances and mixtures (Official Journal of the European Union No. L 353 of 30 December 2008).

** 	Council Directive 67/548/EEC of 27 June 1967 on the approximation of laws, regulations and administrative provisions relating to the classification, packaging and labelling of dangerous substances (Official Journal of the European Communities No. 196 of 16 August 1967, pp. 1 – 5).

*** 	Directive 1999/45/EC of the European Parliament and of the Council of 31 May 1999 concerning the approximation of the laws, regulations and administrative provisions of the Member States relating to the classification, packaging and labelling of dangerous preparations (Official Journal of the European Communities No. L 200, of 30 July 1999, pp. 1 – 68).