Proposal for amendments to ECE/TRANS/WP.29/GRE/2010/10

Note:	The proposal is based on the text of ECE/TRANS/WP.29/GRE/2010/10.  The changes to ECE/TRANS/WP.29/GRE/2010/10 are marked in strikethrough and bold characters.

A.	PROPOSAL

Paragraph 7.1., amend to read:

"7.1.	All measurements shall be carried out with uncoloured standard filament lamps of the types prescribed at 13.2V for the device, adjusted to produce the reference luminous flux prescribed for those types of filament lamps at 13.2 V for light sources as listed in Regulation No. 37, Annex 1 under the group 1 and at 13.5 V for the light sources as listed in Regulation No. 37, Annex 1 under the group 2, when not supplied by an electronic light source control gear."

B.	JUSTIFICATION

The proposed amendment to paragraph 7.1 in ECE/TRANS/WP.29/GRE/2010/10 can be interpreted as requiring all measurements to be performed at the constant voltage of 13.2V or 13.5V. For this reason, the wording about the voltage should be changed to “... produce the reference luminous flux ....”