| Transmitted by the expert from India | Informal document No. GRE-63-14 (63rd GRE, 29-31 March 2010, agenda item 16) |
| --- | --- |

Proposal for draft Supplement 12 to the 01 series of amendments to Regulation No. 53

(Installation of lighting and light-signalling devices for L3 category of vehicles)

The text reproduced below was prepared by the expert from India to introduce modifications in the current text of the Regulation No. 53. The modifications to the current text of the Regulation are marked in bold or strikethrough characters.

A. 	PROPOSAL

“6.4.7. 	"Circuit-closed" “Tell-tale”

Prohibited. Tell-tale optional; where fitted, this tell-tale must be an operating tell-tale consisting of a non-flashing warning light which comes on in the event of the malfunctioning of the stop lamps.”

B.	Justification

Presently, Regulation No. 53 prohibits fitment of “circuit closed tell-tale” for Stop lamp. ECE R 48 permits operating tell-tale as optional for four wheelers. India suggest that similar option may also be provided for two wheelers in ECE R53.