Proposal of Corrigendum 6 to the 03 series of amendments to Regulation No. 19

Paragraph 6.4.3., amend to read:

"6.4.3.	Photometric requirements

When so adjusted, the front fog lamp shall meet the photometric requirements in the table below (refer also to Annex 4, paragraph 2.2. of this Regulation):

| Designated lines or zones | Vertical position */ above h + below h - | Horizontal position */ left of v: - right of v: + | Luminous intensity (in cd) | To comply |
| --- | --- | --- | --- | --- |
| Point 1, 2 **/ | + 60° | ± 45° | 60 max | All points |
| Point 3, 4 **/ | + 40° | ± 30° |  |  |
| Point 5, 6 **/ | + 30° | ± 60° |  |  |
| Point 7, 10 **/ | + 20° | ± 40° |  |  |
| Point 8, 9 **/ | + 20° | ± 15° |  |  |
| Line 1 **/ | + 8° | - 26° to + 26° | 90 max | All line |
| Line 2 **/ | + 4° | - 26° to + 26° | 105 max | All line |
| Line 3 | + 2° | - 26° to + 26° | 170 max | All line |
| Line 4 | + 1° | - 26° to + 26° | 250 max | All line |
| Line 5 | 0° | - 10° to + 10° | 340 max | All line |
| Line 6 ***/ | - 2.5° | 5° inwards to 10° outwards - 10° to + 10° | 2,000 min | All line |
| Line 7 ***/ | - 6.0° | 5° inwards to 10° outwards - 10° to + 10° | < 50 per cent of max. on line 6 | All line |
| Line 8L and R ***/ | -1.5° to - 3.5° | - 22° and + 22° | 800 min | One or more points |
| Line 9L and R ***/ | -1.5° to - 4.5° | - 35° and + 35° | 320 min | One or more points |
| Zone D ***/ | - 1.5° to - 3.5° | - 10° to + 10° | 8,400 max | Whole zone |
| */ The co-ordinates are specified in degrees for an angular web with a vertical polar axis. **/ See paragraph 6.4.3.4. ***/ See paragraph 6.4.3.2. |

"

Paragraph 6.4.3.2., amend to read:

"6.4.3.2. 	At the request of the applicant, two front fog lamps constituting a matched pair corresponding to paragraph 4.2.2.5. may be tested separately. In this case the specified requirements for lines 6, 7, 8, 9 and the Zone D in the table in paragraph 6.4.3. apply to half the sum of readings of the right-hand and left-hand side front fog lamp. However each of the two front fog lamps shall meet at least 50 per cent of the minimum value required for line 6. Additionally, each of the two front fog lamps that constitute the matched pair corresponding to paragraph 4.2.2.5. are only required to meet the requirements of line 6 and line 7 from 5° inwards to 10° outwards.”

Justification

Revision 5, Corrigendum 3 of Regulation 19 has inadvertently introduced a conflict between the horizontal position specified for lines 6 and 7 in paragraph 6.4.3. and the diagram in Annex 4, paragraph 2.2.

The horizontal position specified for lines 6 and 7 in paragraph 6.4.3. (5° inwards to 10° outwards) should only apply to the special case of a matched pair of front foglamps and therefore paragraph 6.4.3.2 should have been amended instead of the table in paragraph 6.4.3.

As the horizontal position requirement of - 10° to + 10° applies in the general case of a front foglamp type approved as a single device, the diagram in Annex 4, paragraph 2.2 is correct.