|  | United Nations | ST/SG/AC.10/C.3/2012/20 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 4 April 2012 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-first session

Geneva, 25 June – 4 July 2012

Item 2 (f) of the provisional agenda

Explosives and related matters: miscellaneous

Classification of ammonium nitrate

Transmitted by the Australian Explosives Industry Safety Group (AEISG)

Introduction

- The purpose of this paper is to ensure ammonium nitrate, which does not meet one or more of the existing classification criteria, is covered by the Model Regulations on the Transport of Dangerous Goods, and handled accordingly.

- There are two entries for ammonium nitrate in the Dangerous Goods List in Chapter 3.2 of the Model Regulations, namely,

| UN No. | Name and description | Class or division | Subsidiary risk | UN packing group | Special provisons | Limited and excepted quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Instructions | Special provisions |
| 1942 | AMMONIUM NITRATE, with not more than 0.2% total combustible material, including any organic substance, calculated as carbon to the exclusion of any other added substance | 5.1 |  | III | 306 | 5 Kg | EI | P002 IBC08 LP02 | B3 | TI BK1 BK2 BK3 | TP33 |
| 0222 | AMMONIUM NITRATE with more than 0.2% combustible substances, including any organic substance calculated as carbon, to the exclusion of any other added substance | 1.1D |  |  |  | 0 | E0 | P112(b) P112(c) | PP47 |  |  |

- As defined above, UN1942 is used for Ammonium Nitrate with not more than 0.2% carbon, and which does not exhibit explosive properties when tested in accordance with Test Series 1 and 2 (refer SP306).

- UN0222 is used for Ammonium Nitrate with more than 0.2% carbon, regardless of its behaviour in Test Series 1 and 2.

Discussion

- While the determining factor for classification with entry UN0222 is the carbon content alone, there are two factors for the entry UN1942 - both the carbon content and the satisfactory performance in Test Series 2.

- This raises a potential, and not unlikely, situation where Ammonium Nitrate, with not more than 0.2% carbon, does not satisfy Test Series 2 and therefore cannot be accommodated within existing entries (refer table below).

| Ammonium Nitrate carbon content | UN TEST SERIES 2 |
| --- | --- |
|  | SATISFY | NOT SATISFY |
| Not more than 0.2% C | UN1942 | ???? |
| More than 0.2% C | UN0222 | UN0222 |

- The potential for  Ammonium Nitrate, of various types or from various sources, to fail Test Series 2 is not unlikely as shown by example results in Test Series 2 of the Manual of Tests and Criteria (e.g low density).

- Should manufactured or imported Ammonium Nitrate not satisfy Test Series 2, but contain not more than 0.2% carbon as confirmed by analysis, there would remain a need to classify and appropriately handle such material.

Proposal

- It is proposed to amend the entry for Ammonium Nitrate, UN0222, in Column 2 of the Dangerous Goods List to read:

“AMMONIUM NITRATE with more than 0.2% combustible substances, including any organic substance calculated as carbon, to the exclusion of any other added substance

or

AMMONIUM NITRATE which has not satisfied Test Series 2”.

Alternative proposal

- Alternatively, a Special Provision SPXXX could be added to Column 6 of the entry for UN0222. Such Special Provision to be added to Chapter 3.3 would read:

“This entry may also be used for Ammonium Nitrate which has not satisfied Test Series 2, regardless of carbon content.”

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2011-2012 approved by the Committee at its fifth session (refer to ST/SG/AC.10/C.3/76, para. 116 and ST/SG/AC.10/38, para. 16).