|  | United Nations | ST/SG/AC.10/C.3/2012/63 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 23 August 2012 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-second session

Geneva, 3–11 December 2012
Item 7 of the provisional agenda

New proposals for amendments to the Model Regulations 
on the Transport of Dangerous Goods

Amendments regarding lithium batteries

Transmitted by the expert from Germany

Introduction

1.	In the penultimate sentence of special provision 188 as well as in the definition of lithium content in 38.3.2.3 in the Manual of Tests and Criteria fifth revised edition amendment 1 it says that “lithium content” means the mass of lithium in the anode of a lithium metal or lithium alloy cell” respectively “Lithium content is applied to lithium metal and lithium alloy cells and batteries, and for a cell means the mass of lithium in the anode of a lithium metal or lithium alloy cell”.

2.	With regard to the applicability of the provisions referred to, the question was raised whether lithium batteries whose lithium content is not located at the anode but at the cathode are at all subject to the provisions of the UN Model Regulations. Germany is of the opinion that all lithium batteries are subject to these provisions, irrespective of whether the lithium content is located at the anode or at the cathode.

3.	For the purpose of adapting the provisions of the UN Model Regulations and of the Manual of Tests and Criteria to the stage of development of lithium batteries, it is proposed to replace the specific term “anode” with the more general term “electrode”.

Proposal:

The penultimate sentence of special provision 188 should be amended to read as follows:

“As used above and elsewhere in these Regulations, “lithium content” means the mass of lithium in one of the electrodes the anode of a lithium metal or lithium alloy cell.”

Moreover, the first sentence of the definition in 38.3.2.3 in the Manual of Tests and Criteria fifth revised edition amendment 1 should be worded as follows:

“Lithium content is applied to lithium metal and lithium alloy cells and batteries, and for a cell means the mass of lithium in one of the electrodes the anode of a lithium metal or lithium alloy cell, which for a primary cell is measured when the cell is in an undischarged state and for a rechargeable cell is measured when the cell is fully charged.”

The first sentence of  38.3.3 (f) should be worded as follows::

„When testing a battery assembly in which the aggregate lithium content of all anodes, when fully charged, is not more than 500 g, or in the case of a lithium ion battery, with a Watt-hour rating of not more than 6 200 Watt-hours, that is assembled from cells or batteries that have passed all applicable tests, one battery assembly in a fully charged state shall be tested under tests 3, 4 and 5, and, in addition, test 7 in the case of a rechargeable battery assembly.“

The last sentence of  38.3.3 should be worded as follows:

„When batteries that have passed all applicable tests are electrically connected to form a battery assembly in which the aggregate lithium content of all anodes, when fully charged, is more than 500 g, or in the case of a lithium ion battery, with a Watt-hour rating of more than 6 200 Watt-hours, that battery assembly does not need to be tested if it is equipped with a system capable of monitoring the battery assembly and preventing short circuits, or over discharge between the batteries in the assembly and any overheat or overcharge of the battery assembly.“

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2011-2012 approved by the Committee at its fifth session (refer to ST/SG/AC.10/C.3/76, para. 116 and ST/SG/AC.10/38, para. 16).