UN/SCETDG/41/INF.38 UN/SCEGHS/23/INF.12

| Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification 15 June 2012 and Labelling of Chemicals |
| --- |
| Sub-Committee of Experts on the Transport of Dangerous Goods Forty-first session Geneva, 25 June - 04 July 2012 Item 2 (c) of the provisional agenda: Explosives and related matters: Desensitized explosives | Sub-Committee of Experts on the Globally Harmonized System of Classification and Labelling of Chemicals Twenty-third session Geneva, 04 July – 06 July 2012 Item 2 (a) of the provisional agenda Updating the Globally Harmonized System of Classification and Labelling of Chemicals: Physical hazards |

Test Results on typical desensitized explosives and other energetic materials

Transmitted by the Expert from Germany

Introduction

- In document ST/SG/AC.10/C.3/2012/28-ST/SG/AC.10/C.4/2012/1 the International Council of Chemical Associations (ICCA) presents test results for industrial nitrocellulose according to the test method prescribed in the German “Guideline for the assignment of substances which may show explosive properties to storage groups (SprengLR011)” (“Determination of 10.000 kg scale burning rate”) used by the German competent authority (BAM Federal Institute for Materials Research and Testing) to assign energetic substances  to storage groups.

- In the past BAM has tested also other typical desensitized explosives according to this test method.

- For supply and use the test method is also generally used to determine storage groups for other energetic substances, e.g., organic peroxides and self-reactive substances (see literature list, too).

- The expert from Germany would like to present the following test results:

Test results

| No | UN No | Substance/formulation | Packaging(s), net mass per packaging | Storage group |
| --- | --- | --- | --- | --- |
| 1 | 3474 | 1-Hydroxybenzotriazole Monohydrate | 1(G), 1(H2), 50 kg/20 kg | Ib |
| 2 | 1344 | Trinitrophenol (Picric Acid), wetted with not less than 30 % water, by mass | 1(G), 35 kg | Ia |
| 3 | 1356 | Trinitrotoluene (TNT), wetted with not less than 30 % water, by mass | 1(G), 50 kg | Ia |
| No | UN No | Substance/formulation | Packaging(s), net mass per packaging | Storage group |
| 4 | 1336 | Nitroguanidine (Picrite), wetted with not less than 20 % water, by mass | IBC 13H2, 580 kg | III |
| 5 | 3380 | Propatyl Nitrate 20 %, by mass, with not less than 80 % Lactose Monohydrate, by mass | 1(G), 35 kg | III |
| 6 | 3319 | Nitroglycerin mixture, desensitized, solid, n.o.s. with more than 2 % but not more than 10 % nitroglycerin, by mass | 1(G), 50 kg | III |

| No | UN No | Substance/formulation | Packaging instruction, -method, net mass per packaging | Storage group |
| --- | --- | --- | --- | --- |
| 7 | 3104 | Dibenzoyl peroxide 68 % - 77 %, water 23 % - 31 % | P520, OP6, 25 kg | II |
| 8 | 3101 | 2,5-Dimethyl-2,5-di-(tert-butylperoxy) hexyne -3, technically pure | P520, OP5, 25 kg | Ib |
| 9 | 3113 | tert-Butyl peroxy-2-ethylhexanoate, technically pure | P520, OP6, 25 kg | Ib |
| 10 | 3111 | tert-Butyl peroxyisobutyrate 75 % - 77 %, Diluent type A 23 % - 25 % | P520, OP5, 25 kg | Ib |
| 11 | 3103 | tert-Butyl peroxyisopropylcarbonate 75 % - 77 %, diluent type A 23 % - 27 % | P520, OP5, 25 kg | II |
| 12 | 3101 | tert-Butyl peroxydiethylacetate, technically pure | P520, OP5, 25 kg | Ib |
| 13 | 3104 | Cyclohexanone peroxide 85 % - 91 %, water 9 % - 15 % | P520, OP6, 25 kg | II |
| 14 | 3113 | tert-Butyl peroxypivalate 73 % - 77 %, diluent type A 23 % - 27 % | P520, OP5, 25 kg | Ib |
| 15 | 3103 | tert-Butyl hydroperoxide 77 % - 81 %, Di-tert-butyl peroxide 8 % - 10 %, water 7 % - 12 % | P520, OP5, 25 kg | Ia |
| 16 | 3112 | Di(-2-methylbenzoyl) peroxide 67 % - 85 %, water 15 % - 33 % | P520, OP5, 25 kg | Ib |
| 17 | 3234 | Azodi(isobutyronitrile), technically pure | P520, OP6, 25 kg | Ia |
| 18 | 3236 | 2,2’-Azodi(2-methylbutyronitrile) | P520, OP7, 25 kg | Ia |

Remarks

Assignment to storage groups:

Ia:	 The AC is equal or more than 300 kg/min.

Ib:	 The AC is equal or more than 140 kg/min but less than 300 kg/min.

II: 	 The AC is equal or more than 60 kg/min but less than 140 kg/min.

III: The AC is less 60 kg/min.

Ac is the corrected burning rate for an extrapolated mass of 10.000 kg.

- If a desensitized explosive or another energetic substance as packed for use and supply fulfils the criteria for a mass explosion effect it has to be classified as an explosive or as a type A substance if it fulfils the criteria for an assignment to the hazard classes organic peroxide or a self-reactive substance, respectively.  Such substances are not under discussion here.

Consideration

- The test method [1] can be used to determine the different hazards (mass burning rate, heat radiation, fire) of desensitized explosives and other reactive substances for supply and use according to the GHS. The experts are invited to discuss this paper together with document ST/SG/AC.10/C.3/2012/28-ST/SG/AC.10/C.4/2012/1.

Literature

[1]	German “Guideline for the assignment of substances which may show explosive properties to Storage Groups (SprengLR011)”

[2]	Thermal radiation hazards from organic peroxides, Roberts, T.A. and Merrifield, R., J. Loss. Prev. Process Ind. 1990, 3, 244.

[3]	Thermal radiation hazard and separation distances for industrial cellulose nitrate, Roberts, T.A. and Merrifield, R., J. Loss. Prev. Process Ind. 1992, 5,311.

[4]	Storage of Organic Peroxides, Publication Series on Dangerous Substances 8 (PGS 8), Ministries of Social Affairs and of the Interior, The State Secretary of Housing, Spatial Planning and Environment (VROM), The Netherlands 2006.

[5]	The storage and handling of organic peroxides, Guidance Note CS21, Health and Safety Executive, 1998, United Kingdom