Proposal for Supplement [42] to the 03 series of amendments of Regulation No. 37

I.	Proposal

Paragraph 2.4.2., amend to read:

"2.4.2. … 	This will be followed by an identification code comprising not more than three characters. Only the Arabic numerals and capital letters listed in footnote 3 ( 3 ) shall be used .."

Annex 3, amend to read:

"ANNEX 3

EXAMPLE OF THE ARRANGEMENT OF THE APPROVAL MARK

(see paragraph 2.4.3)

The above approval mark affixed to a filament lamp indicates that the lamp has been approved in the United Kingdom (E11) under the approval code A01.

The first character of the approval code indicates that the approval was granted in accordance with the requirements of Regulation No 37 as amended by the 02 and 03 (*) series of amendments."

II.	Justification

The German Type Approval Authority uses the same pool of code combinations for all light sources according to Regulations Nos.37, 99 and 128. This pool will be exhausted in the near future. It is therefore necessary to extend the range of possible combinations.