## Slide 1: R55: Performance vs. Requirements
Submitted by the experts from the informal working group on R-55
Informal document GRRF-79-03
(79th GRRF, 16 – 20 February 2015,
agenda item 4)
The informal working group on regulation 55 (R55) is asking GRRF for comments and guidance on a principle and structural matter with the R55.
This presentation will show the issue and give a proposal for some structural changes.

## Slide 2: R55: Performance vs. Requirements
At type approval regulation 55 applies to a single vehicle or a single component
  It then governs what performance will be certified
  The requirements to be fulfilled in terms of geometry and load carrying capacity are given in annex 5, 6 and 7.

## Slide 3: R55: Performance vs. Requirements
  A process to develop a new coupling may be seen as a number of steps
    Decide what class of coupling
      main text of R55
    Decide capacity, i.e. D, Dc, V, U, S and Av
      For some classes consult annex 5
    Check test force requirement, i.e. design/test loads
      Annex 6
    Check any standardized dimensions, articulations angle, installation limitation, … requirements
      Annex 5 and 7
    Design and test
    Certify performance

## Slide 4: R55: Performance vs. Requirements
In operation two or more vehicles controls the performance needed, i.e. requirements.
To know the performance needed is the same as to say what force will in operation appear in the couplings.
In order to have safe and common utilization of the certified performance we need to have an agreed way to estimate forces in operation.
  This agreed way is the D- and V-value formulas in the main text of R55
    Those are valid for combinations of two vehicle
    A combination of rigid truck + dolly + semi-trailer is not covered.

## Slide 5: R55: Performance vs. Requirements
New transport systems are developed and new multi-vehicle combinations are put into operation.
  One example is the European Modular System, EMS
In order to correctly utilize and not to overstress the coupling equipment additional agreed formulas need to be added to R55.

## Slide 6: R55: Performance vs. Requirements
This procedure to agree:
  How performance is verified and certified
  How performance may be utilized
  … has been and is sound and common practice in many areas of industry
I.e. R55 is form this perspective sound
But it needs to be augmented.

## Slide 7: R55: Performance vs. Requirements
A proposal is made to group all those agreed formulas in a new Annex.
The content of that Annex is needed to set the boundary for utilization of certified performance.
At operation it is a prerequisite that this Annex is observed and applied.
  The new annex defines how the certified performances may be utilized.
  The formulas shall reflect the envelop of the force generation mechanisms at operation.

## Slide 8: R55: Performance vs. Requirements
Adding the new formulas enables the legislator to keep in control of the safety level as new vehicle combinations are introduced.
The new annex brings a clean and comprehensible structure to the regulation from this perspective.
  An answer to the question “How may I use this installed coupling?” is found in the new annex.
  There is no need to look everywhere in the regulation.

## Slide 9: R55: Performance vs. Requirements
Main text
Annex 1
Annex 2
Annex 3
Annex 4
Annex 6
Annex 5
Annex 7
Type Approval
Operation
As is
Performance
Requirements

## Slide 10: R55: Performance vs. Requirements
Main text
Annex 1
Annex 2
Annex 3
Annex 4
Annex 6
Annex 5
Annex 7
New
Annex x
Type Approval
Operation
As proposed
Performance
Requirements

## Slide 11: R55: Performance vs. Requirements
The proposed structure will give an opening for the legislator to stay in control of the boundary conditions of utilization in many respects
  New combination types
  Extreme transports
  Performance validity
  Speed restrictions
  …

## Slide 12: R55: Performance vs. Requirements
Thank you for the attention!