Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods	14 September 2016

Joint Meeting of the RID Committee of Experts and the 
Working Party on the Transport of Dangerous Goods

Geneva, 19–23 September 2016
Item 5 (b) of the provisional agenda

Proposals for amendments to RID/ADR/ADN:

new proposals

The inclusion of additional substances to UN1202

Transmitted by the Government of the Russian Federation

Introduction

1.	In practice, rail, water, road and sea transport occupies a significant share of Petroleum fuel - fuel oil (mazut). In the Russian Federation and other CIS countries, the product of oil refining produced according to requirements of Interstate standard GOST 10585-2013 [8]. Petroleum fuel. Mazut. Specifications. (Petroleum fuel. Mazut. Specifications).

2.	Depending on the application, set the following brands of oil:

- Naval F5 (Ф5);

- Flue 40;

- Flue 100.

3.	Fuel Naval F5 is obtained from the direct product of oil refining with the addition of up to 22% kerosene-gas oil fractions of a catalytic or thermal cracking. On physical and chemical parameters of Petroleum fuel - fuel oil (mazut) must meet the requirements set out in Annex 1 and 2. The temperature of the Petroleum fuel flash - oil closed cup can reach more than 60 ° C and not more than 100 ° C.

Sentence

4.	Based on the physicochemical properties of the Petroleum fuel - oil (flash point in closed cup 60 ° C and not more than 100 ° C, fractional composition) and shipped at elevated temperatures (70 - 120 ° C), the Russian Federation considers advisable complement UN1202 position new substance Fuel oil (flashpoint more than 60 ° C and not more than 100 ° C).

5.	If approved by the Sub-Committee on proposals of the Russian Federation, it will also be advisable to amend the Rules of RID/ADR/ADN/SMGS.

- Supplement Note 2 paragraph 2.2.3.1.1 as follows:

“2: By derogation from paragraph 2.2.3.1.1 above, diesel fuel, gasoil, heating oil (light), mazut including synthetically manufactured products having a flash-point above that  60 ° C and not more that 100 ° C shall be deemed substance of Class 3, UN No 1202.”

- Change the position of the 3rd UN 1202 in Table A of Chapter 3.2 as follows:

"GAS OIL or DIESEL FUEL or HEATING OIL,  LIGHT (flash-point  more  than 60 ° C and not more than 100 ° C) or MAZUT (flash-point more than 60 ° C and not more than 100 ° C).";

- Include in alphabetical order a new position in the table B of Chapter 3.2:

"MAZUT (flash-point more than 60 ° C and not more than 100 ° C)."

Rationale

According to experts of the Russian Federation complement positions UN1202 substance MASUT (flash-point is more than 60 ° C and not more than 100 ° C) will more accurately define the conditions for the transport of dangerous goods, which occupies a significant share in the volume of vehicle traffic.

List of sources used

| 1. | ASTM D 93-13 | The standard method for determining the flash point in closed crucible Penski- Martens. |
| --- | --- | --- |
|  | (ASTM D 93-13) | (Standard test method for flash point by Pensky-Martens closed cup tester). |
| 2. | 2 STB 1651-2006 | Petroleum products. Determination of flash point and ignition device in an open crucible for Cleveland method. |
| 3. | STB ISO 2592-2010 | Petroleum products. Determination of flash point and ignition device in an open crucible for Cleveland method. |
| 4. | ISO 2592: 2000 | Petroleum products. Determination of flash point and ignition. Method Cleveland Open Cup. |
|  | (ISO 2592: 2000) | (Petroleum products - Determination of flash and fire points - Cleveland open cup method). |
| 5. | ASTM D 92-12 | The standard method for determining the flash point and ignition COC Cleveland. |
|  | (ASTM D 92-12) | (Standard test method for flash and fire points by Cleveland open cup). |
| 6. | ASTM D 240-09 | The standard method for determining the heat of combustion of liquid hydrocarbon fuels in a bomb calorimeter. |
|  | (ASTM D 240-09) | (Standard test method for heat of combustion of liquid hydrocarbon fuels by bomb calorimeter). |
| 7. | GOST P 51069-97 | Petroleum and petroleum products. Method for determination of density, relative density and API Gravity hydrometer. |
| 8. | GOST 10585-2013 | Petroleum fuel. Mazut. Specifications |

Annex 1

Physical and chemical indicators of Petroleum fuel – mazut according by GOST 10585-2013 [8]

| Indicator | The value of the brand | Test method |
| --- | --- | --- |
|  | Navy F5 | Heating 40 | Heating 100 |  |
| 1 Kinematic viscosity, mm2/s, not more: |  |  |  | GOST 33 GOST 31391, |
| at 50 ° C | 36,20 | - | - |  |
| at 80 ° C | - | 59,00 | - |  |
| at 100 ° C | - | - | 50,00 |  |
| or conditional viscosity at 100 ° C, TA degrees, not more than | - | - | 6.80 | GOST 6258 |
| 2. Flash Point, ° C, min: |  |  |  |  |
| Closed Cup | 80 | - | - | GOST ISO 2719, GOST 6356 standard [2] |
| Open Cup | - | 90 | 110 | GOST 4333 standards [2] - [5] |
| 3. Pour Point, ° C, max | Minus 5 | 10 | 25 | In accordance with GOST 20287 (method B) |
| for fuel oil from the oil with a high paraffin content | - | 25 | 42 |  |
| 4. The heat of combustion (lower) based on the dry fuel, kJ / kg, at least for the fuel oil with sulfur content,% |  |  |  | In accordance with GOST 21261, the standard [6] |
| 0.50, 1.00, 1.50, 2, 00 | 41454 | 40740 | 40530 |  |
| 2.50, 3.00, 3.50 | - | 39900 | 39900 |  |
| 5. Density at 15 ° C, kg / m 3, more | 958.3 | Not regulated. certain mandatory | According to the standard [7], GOST 31072, GOST 31392 |

Appendix 2

Quality passports (certificates) for fuel oil – mazut