## Slide 1: ASEP IWG Report to GRB 65th
ASEP, from 2005 to 2019 :
Background informations
Detailed elaborated work plan and timeline of future works
Transmitted by the IWG ASEP
Informal document GRB-65-24
(65th GRB, 15-17 February 2017,
agenda item 4 (b))

## Slide 2: ASEP, the origin
“The sound emission of the vehicle under normal driving conditions different from the conditions of the type approval test in Annex 3 shall not differ considerably from what can be expected from the type approval test result”

## Slide 3: ASEP, background Information, 2005
The GRB, in 2005, approved the adoption of the revised International Organization for Standardization (ISO) 362 test procedure (TRANS/WP.29/GRB/40) as the technical basis for future versions of Regulation No. 51 and Regulation No. 41 on vehicle noise.
As a consequence of the change in technical testing methods, a number of contracting parties expressed concern regarding :
  the change in vehicle engine speed (r.p.m.) used during the certification test.
  the desire to prohibit “cheating”,
  a desire to check for ‘nonlinear’ behaviour,
  a desire for an additional, independent, set of noise emission stringency tests for the approval of motor vehicles.
As a result of these concerns, GRB established (TRANS/WP.29/GRB/40) an informal group on Additional Sound Emission Provisions (ASEP) for the incorporation of additional specifications for Regulation No. 51

## Slide 4: ASEP, background Information, 2005-2010
19 meeting from Novembre 2005 to december 2009
At the September 2009 session of GRB, the Chairman of the informal group reported to GRB that a consensus recommendation to GRB on Regulation No. 51 ASEP was not possible
At the February 2010 meeting, while there was no further progress on a single consensus proposal, there was, however, an strong opinion expressed by contracting parties and accredited NGOs that a prompt resolution of this issue was necessary
In september 2010, A proposal to address the concerns expressed has been provided by GRB Chairman that reaches the goals set forth by GRB for the purpose of ASEP in a sufficient manner to provide a basis for agreement by GRB and subsequent adoption by WP.29. (ECE/TRANS/WP.29/GRB/2010/9)
As with any compromise proposal, no one will be completely satisfied, but each expressed policy goal of GRB can be shown to have been satisfied

## Slide 5: ASEP, background Information, 2015-2016
Within the working group for future work for GRB 62, 63 and 64th session, several concerns about ASEP have been presented :
Update the text to improve clarity and simplification in short term
Add missing sound limit values for N1 and Off-road in Annex7 para. 5.3 to be added.
Series hybrid vehicles are excluded from the ASEP until 30 June 2019; new test methods will be necessary in R51.
ASEP as a part of type approval (not as a manufacturer declaration)
More general technical review in cooperation with ISO (Improvement of methods)
It was proposed to create an IWG for ASEP starting on 2016.

## Slide 6: ASEP, background Information, 2015-2016
The expert from France presented the results of a survey on additional sound emission provisions (ASEP) (GRB-64-16). According the expert, the survey had identified a lot of issues in the application of ASEP of the 03 series of amendments to Regulation No. 51 and the need for further work on this subject. He further reported that this view was also shared by ISO, which proposed to revise the ASEP provisions (GRB-64-04).
To make progress in this area, GRB decided, subject to WP.29 consent, to establish an IWG on ASEP and adopted its Terms of Reference (ToR) (GRB-64-23 and Rev.1).
The aim of the group is to propose improvement of this regulation.

## Slide 7: ASEP, future works , 2016-2017 TOR 2016
For primary objective of IWG for ASEP shall :
On a short term :
  continue work done by ISO to update the text to improve clarity and simplification;
  propose missing limits for e.g. N1 from UN R51.02 in reference sound assessment;
  re-structure the text or better understanding
The aim of IWG is to present
  a working document for consideration during the 65th GRB in February 2017 for clarification on ASEP
  a detailed elaborated work plan and timeline

## Slide 8: ASEP, future works , 2016-2019 TOR 2016
Objective of IWG on mid/long term
  review and improve test procedure for automatic transmission in non-locked Transmission condition;
  propose a test procedures for hybrid vehicles and new technologies of vehicle.
  propose a simplified test procedure and/or alternative test (such as in-door testing) to save time and to enable direct application of ASEP during type approval
The group will present a progress report including already achieved further results by September 2018 and a comprehensive proposal by September 2019

## Slide 9: ASEP, future works , 2016-2019 TOR 2016
In addition, the IWG for ASEP might also propose a general principle for revision of ASEP regarding :
  Consideration of scope and target to elaborate on sound behaviours subject to criticism;
  Improve the effectiveness of the method regarding off-cycle tests, …)
  Field of application
  Control range (method to be more representative for urban driving behavior)
  Consider harmonization with ASEP UN R41 - if possible

## Slide 10: Current situation Slope-Assement
Strengths | Weaknesses
Prevents excessively loud noise emission in the ASEP control range. | Limits designed with assumption sound emission is correlated to throttle – does not account for loud partial throttle situations
Identifies and prohibits “test detection” strategies used in R51.02 | Not all gears are in the scope of ASEP
Easily understood RPM vs. sound limits | RPM based limits not applicable for all products.
 | Require a lot of tests and time

## Slide 11: Current situation Lurban-Assement
Strengths | Weaknesses
Prevents excessively loud noise emission in the ASEP control range. | Not applicable for accelerations lower than aurban
Identifies and prohibits “test detection” strategies used in R51.02 | Simple speed compensation
Assessment is sensitive to actual measured acceleration – if you don’t make acceleration, but only make sound, you get a high result. | Assessment is sensitive to actual acceleration measured – acceleration measured may not be actual vehicle performance
Performance based and design neutral | 
Applicable to vehicles with no combustion engine RPM. | Limitation concept more difficult to understand
 | Require a lot of tests and time

## Slide 12: Current situation Reference Sound Assessment
Reference Sound-Assessment was introduced to simulate regulation UN51.02 on vehicle approved on UN51.03.
IWG for ASEP consider that this method
  is not efficient to address current concern of ASEP
  is not representative to UN51.02. Uncertainties necessary for simulation are bigger than the restrictions applied already by the other assessment methods.
IWG for ASEP recommends to consider the deletion of Reference Sound Assessment after revision of ASEP.

## Slide 13: Considerations of IWG about Goals for ASEP
The primary consideration for ASEP :
UN R51.03 ASEP is already a big improvement compared to UN Regulation R51.02, but:
  The UN Regulation R51.03 has just started; thus products approved according to R51.03 have not yet arrived to the market on a large scale.
  Many manufacturers, and especially aftermarket, will use the old R51.02 approvals up to the maximum possible application date in 2022.

## Slide 14: Considerations of IWG about goals for ASEP
The primary consideration for ASEP :
In general, IWG for ASEP recommends to increase the effectiveness of Regulation R51 – ASEP by addressing real world concerns as perceived by public. This will support the trust from all involved parties
IWG for ASEP recommends to address undesired effects when reducing limits in future phases of R51.03 (cycle detection, manipulation, aftermaket, …)
Increasing market penetration of electronically controlled technologies (soundbox, variable exhaust systems, …) must carefully be watched and be reliably protected against manipulation

## Slide 15: Concerns and elaborated work plan and timeline
Extreme driving behaviour (starting highest RPM, extreme acceleration, non compliant speed ) ?
IWG for ASEP acknowledges that this concern is not subject to be solved by vehicle regulations.
IWG for ASEP recommends to not consider such extreme behaviour for ASEP while real driving happens at much lower performance.

## Slide 16: Concerns and elaborated work plan and timeline
Manipulation, Aftermaket and maintenance (racing-silencer, dB-Eaters, additional control units, illegal flap system/steering, …)
IWG for ASEP recommends to insert additionnal requirements comparable to UN-R41.04 point 6.5 in UN-R51
IWG for ASEP recommends to consider controls and roadside checking when developing new methods.
IWG for ASEP proposes to work on these concerns in a mid term perspective.

## Slide 17: Concerns and elaborated work plan and timeline
UN non compliant (ASEP-Declaration non ok, deviation of vehicle to approval, …)
IWG for ASEP recommends to include ASEP as part of type approval testing
 IWG for ASEP proposes to work on an more efficient way to include it in TA testing (complete tests by Technical Service (TS), minimum number of points by TS, simplified method, …) in a short term

## Slide 18: Concerns and elaborated work plan and timeline
Vehicle extremely loud outside ASEP-Range/gear and grey areas of the regulation (racing mode, Use of dB-Eater, …)
IWG for ASEP proposes to consider the extension of ASEP-range (<20 km/h, > 80 km/h, > nBB_ASEP, all gears …) during revision of ASEP
IWG proposes to consider new concepts when defining future control range (e.g. v*a concept, …)
IWG for ASEP proposes to consider impact on available test facilities to perform testing exceeding the current control range
IWG proposes to work on this concern in a short term

## Slide 19: Concerns and elaborated work plan and timeline
Weakness of current ASEP methods :
IWG recommends to consider only one test procedure instead of three for mandatory application
IWG proposes to work on short term on a new concept based on :
  strenghts and weaknesses of current methods
  real driving performance
  technological neutrality (automatic transmission, hybrid vehicle, …)
  Criteria given for the determination of the term “vehicle of concern” (e.g. evidence of cycle beating and/or cycle detection, unexpected vehicle noise behaviour based on the individual vehicle’s technical capability, …)

## Slide 20: Concerns and elaborated work plan and timeline
Weakness of current ASEP methods :
  IWG proposes improvement of current methods taking into consideration new concepts :
    v*a concept
    Real Driving Noise (RDN)
    Partial throttle, cruise, …
  IWG for ASEP proposes to work on simplified test procedure and/or alternative test (such as in-door testing) to save time and to enable direct application of ASEP during type approval

## Slide 21: Concerns and elaborated work plan and timeline
IWG for ASEP
  will present a progress report each GRB session
  will propose, as appropriate, to update the text to improve clarity and simplification each GRB session
  will develop project plan incl. milestones for Q2 2017
  targets a comprehensive final report by September 2019.
  proposes to consult with ISO as appropriate
  proposes to hold Task Force meetings with limited number of participants as appropriate

## Slide 22: Concerns and elaborated work plan and timeline
IWG for ASEP proposes four meetings per year
Upcoming meetings
  May 10th morning to 12th noon, Brussels (Scope, review of new concept, continued discussion on pros and cons of existing methtods, project plan)
  July , 1st half, J or US, possibly combined with QRTV GTR meeting
  November, 2nd week, US or J