## Slide 1: Proposals from the Informal Working Group on AEBS
Informal Working Group on AEBS for Light Vehicles
New Regulation
Informal document GRVA-01-10
1st GRVA, 25-28 September 2018
Agenda item 7
To construct
New UN Regulation
Chair and Secretary IWG AEBS – GRVA 01
Short Version

## Slide 2
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
New Regulation
This presentation show the draft proposal for a new UN Regulation on AEBS (GRVA-01-02)
Especially the red frame in this ppt shows that guidance from GRVA is necessary.
Guidance from GRVA

## Slide 3
Informal Working Group on AEBS for Light Vehicles
Activities based on TOR (GRRF-84-03)
Chair and Secretary IWG AEBS – GRVA 01
IWG meetings 3rd meeting in Brussels (19-20 February 2018)
4th meeting in Tokyo (16-17 May 2018)
5th meeting in London (26-27 June 2018)
Draft proposal for 1st GRVA in September 2018
(Informal document GRVA-01-02)
IWG meetings 6th meeting in Paris (1-2 October 2018)
7th meeting in Brussels (1st week of December 2018)
7th meeting in Geneva or Brussels (12-13 November 2018)
Draft proposal for 2nd GRVA in January 2019 as Working document
EC and Japan propose an amendment of TOR (Informal document GRVA-01-09)

## Slide 4
Informal Working Group on AEBS for Light Vehicles
GRVA-01-02 - Draft Proposal for a new UN Regulation on AEBS (M1/N1)
Chair and Secretary IWG AEBS – GRVA 01
Scope
Definitions
Specifications
General
Warnings, Emergency braking, False reaction avoidance
Car to Car (C2C) scenario
Car to Pedestrian (C2P) scenario
Car to Bicycle (C2B) scenario
Interruption by the Driver
Manual deactivation
Warning Indication
Provisions for the Periodic Technical Inspection
Remaining open issues (including Test Procedure)
Green means common specifications in each scenario

## Slide 5
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to car scenario – Rear-end collision
Collision warning:
At the latest 0,8 seconds before the start of emergency braking
Emergency Braking:
Average braking demand of at least [3.8 m/s² deceleration, with at least a peak at 6.43 m/s² or fully cycling ABS,]
Damage Mitigation or Collision Avoidance
1st Stage
Collision Warning
2nd Stage
Emergency Braking
z
z
z
Activation Speed:
The system shall be active at least within the vehicle speed range between 10 km/h and 60 km/h and at all vehicle load conditions
Moving and Stationary targets

## Slide 6
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to car scenario - Speed reduction by braking demand
The table show the speed reduction in each relative speed for M1 vehicle.
About N1 vehicle, IWG still need further discussion.
The speed reduction shall be demonstrated according to the test procedure.
Based on discussion of last point to steer and last point to brake

## Slide 7
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to pedestrian scenario – Crossing collision
Chair and Secretary IWG AEBS – GRVA 01
Walking speed: 5 km/h
Collision Warning:
When the AEBS has detected the possibility of a collision with a pedestrian crossing the road, a collision warning shall be provided, and shall be provided no later than the start of emergency braking intervention.
Emergency Braking:
When the system has detected the possibility of an imminent collision, an emergency braking shall emit an average braking demand of at least [3.8 m/s² deceleration, with at least a peak at 6.43 m/s² or fully cycling ABS].
Activation Speed:
The system shall be active at least within the vehicle speed range between [20] km/h and 60 km/h and at all vehicle load conditions

## Slide 8
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to pedestrian scenario - Speed reduction by braking demand
2020
2023
1st step
2nd step
1st step(2020) is Collision avoidance until 30 km/h.
2nd step(2023) is Collision avoidance until 42 km/h.
IWG discussed step approach for the speed reduction of M1 vehicle.
About N1 vehicle, IWG still need further discussion.
30km/h
42km/h

## Slide 9
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to pedestrian scenario - Speed reduction by braking demand
The speed reduction shall be demonstrated according to the test procedure. Based on same approach of Car to Car scenario

## Slide 10
The phases of implementation would also need guidance from GRVA. In particular it is proposed that car to car requirements (42 km/h collision avoidance) as well as car to pedestrian with reduced performance (collision avoidance at 30 km/h only) would apply from the date of entry into force (original version of the regulation from 2020 for new types) whereas the car to pedestrian with higher speed (42 km/h) would apply in a second step (2023 for new types). The introduction phase for car to bicycle could then come later.
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to pedestrian scenario - Speed reduction by braking demand
Guidance from GRVA

## Slide 11
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to bicycle scenario – Crossing and Same direction
Speed of bicycle: [15 km/h]
Activation Speed:
The system shall be active at least within the vehicle speed range between 10 km/h and [30 km/h] and at all vehicle load conditions
Crossing
Same direction

## Slide 12
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to bicycle scenario - Crossing and Same direction
For car to cyclist, the group agreed from accident data that the two most relevant scenarios are a cyclist crossing (similar to pedestrian scenario) and a cyclist driving in the same direction as the car (similar to car to car scenario). However, for the latter, it seems that steering is much more efficient than braking, so the usefulness of such a braking test needs to be checked again.
The group still faces difficulty in agreeing on performance requirements for the car to bicycle collision given the lack of vehicles with this technology on the market (only one vehicle was tested under EuroNcap in 2018). One alternative would be to require simply a warning in a first step or to discuss this issue again after the finalization of the discussion on cars and pedestrians.
Guidance from GRVA

## Slide 13
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Manual deactivation
The group also discussed the possibility of a manual deactivation of the AEBS function. The compromise reached was that such a switch could be allowed but switching off the AEBS should not be too easy. However this compromise was not unanimously supported by all Contracting parties.
Guidance from GRVA

## Slide 14
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Remaining open issues (including Test Procedure)
Remaining open issues are indicated in square brackets in the document. One major issue is the minimum requirements that shall be required when the vehicle is outside test conditions (e.g. different mass, different road conditions). In addition for both car to car and car to pedestrian, few issues remain opened for some particular cases (e.g. for vans derived from trucks approved under Regulation R 13).
IWG still need further discussion for these issues.

## Slide 15
Summary of this report
Chair and Secretary IWG AEBS – GRVA 01
Explanation of C2C and C2P requirements
(Page 5 - 9)
2. Implementation of AEBS (Step approach)
(Page 8 and 10)
3. Car to Bicycle scenario (Page 11 - 12)
4. Manual deactivation (Page 13)

## Slide 16
Informal Working Group on AEBS for Light Vehicles
Thank you
for your attention
IWG meetings 6th meeting in Paris (OICA office)
(1-2 October 2018: Next week of this GRVA)
Chair and Secretary IWG AEBS – GRVA 01

## Slide 17: Proposals from the Informal Working Group on AEBS
Informal Working Group on AEBS for Light Vehicles
New Regulation
Informal document GRVA-01-XX
1st GRVA, 25-28 September 2018
Agenda item 7
To construct
New UN Regulation
Chair and Secretary IWG AEBS – GRVA 01
Full Version
Appendix

## Slide 18
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
New Regulation
This presentation show the draft proposal for a new UN Regulation on AEBS (GRVA-01-02)
Especially the red frame in this ppt shows that guidance from GRVA is necessary.
Guidance from GRVA

## Slide 19
Informal Working Group on AEBS for Light Vehicles
Activities based on TOR (GRRF-84-03)
Chair and Secretary IWG AEBS – GRVA 01
IWG meetings 3rd meeting in Brussels (19-20 February 2018)
4th meeting in Tokyo (16-17 May 2018)
5th meeting in London (26-27 June 2018)
Draft proposal for 1st GRVA in September 2018
(Informal document GRVA-01-02)
IWG meetings 6th meeting in Paris (1-2 October 2018)
7th meeting in Brussels (1st week of December 2018)
Draft proposal for 2nd GRVA in February 2019 as Working document
EC and Japan propose an amendment of TOR (Informal document GRVA-01-XX)

## Slide 20
Informal Working Group on AEBS for Light Vehicles
GRVA-01-02 - Draft Proposal for a new UN Regulation on AEBS (M1/N1)
Chair and Secretary IWG AEBS – GRVA 01
Scope
Definitions
Specifications
General
Warnings, Emergency braking, False reaction avoidance
Car to Car (C2C) scenario
Car to Pedestrian (C2P) scenario
Car to Bicycle (C2B) scenario
Interruption by the Driver
Manual deactivation
Warning Indication
Provisions for the Periodic Technical Inspection
Remaining open issues (including Test Procedure)
Green means common specifications in each scenario

## Slide 21
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Scope
Category M1 and N1
Scenarios:
Car to Car (C2C) scenario
Vulnerable road user:
Car to Pedestrian (C2P) scenario
Car to Bicycle (C2B) scenario

## Slide 22
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Definitions
Other definitions:
"Emergency Braking "Collision Warning”
"Vehicle Type with Regard to its Advanced Emergency Braking System”
"Subject Vehicle“ "Soft Target (Vehicle Target, Pedestrian Target and Cyclist Target)“
"Common Space” "Self-Check” "Time to Collision (TTC)"

## Slide 23
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - General
Reference of other regulations:
ABS(R13H and R13), EMC(R10), Annex CEL

## Slide 24
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - General
Reference of other regulations:
The group would also need guidance on the way to refer to the latest version of UN Regulation No. 10 and to targets (ISO standard or copy/paste requirements) to ensure a coherent practice across the different GRs (e.g. target used for cyclist detection by trucks currently discussed in GRSG).
Guidance from GRVA

## Slide 25
Informal Working Group on AEBS for Light Vehicles
Specifications - Warnings
Chair and Secretary IWG AEBS – GRVA 01
Failure warning (inc. self-check)
Deactivation warning

## Slide 26
Informal Working Group on AEBS for Light Vehicles
Specifications - Emergency braking, False reaction avoidance
Chair and Secretary IWG AEBS – GRVA 01
Emergency braking
The requirements follow each scenario
False reaction avoidance
Para. 6.10. False Reaction Avoidance Test

## Slide 27
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to car scenario – Rear-end collision
Collision warning:
At the latest 0,8 seconds before the start of emergency braking
Emergency Braking:
Average braking demand of at least [3.8 m/s² deceleration, with at least a peak at 6.43 m/s² or fully cycling ABS,]
Damage Mitigation or Collision Avoidance
1st Stage
Collision Warning
2nd Stage
Emergency Braking
z
z
z
Activation Speed:
The system shall be active at least within the vehicle speed range between 10 km/h and 60 km/h and at all vehicle load conditions
Moving and Stationary targets

## Slide 28
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to car scenario - Speed reduction by braking demand
The table show the speed reduction in each relative speed for M1 vehicle.
About N1 vehicle, IWG still need further discussion.
The speed reduction shall be demonstrated according to the test procedure.
Based on discussion of last point to steer and last point to brake

## Slide 29
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to pedestrian scenario – Crossing collision
Chair and Secretary IWG AEBS – GRVA 01
Walking speed: 5 km/h
Collision Warning:
When the AEBS has detected the possibility of a collision with a pedestrian crossing the road, a collision warning shall be provided, and shall be provided no later than the start of emergency braking intervention.
Emergency Braking:
When the system has detected the possibility of an imminent collision, an emergency braking shall emit an average braking demand of at least [3.8 m/s² deceleration, with at least a peak at 6.43 m/s² or fully cycling ABS].
Activation Speed:
The system shall be active at least within the vehicle speed range between [20] km/h and 60 km/h and at all vehicle load conditions

## Slide 30
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to pedestrian scenario - Speed reduction by braking demand
2020
2023
1st step
2nd step
1st step(2020) is Collision avoidance until 30 km/h.
2nd step(2023) is Collision avoidance until 42 km/h.
IWG discussed step approach for the speed reduction of M1 vehicle.
About N1 vehicle, IWG still need further discussion.
30km/h
42km/h

## Slide 31
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to pedestrian scenario - Speed reduction by braking demand
The speed reduction shall be demonstrated according to the test procedure. Based on same approach of Car to Car scenario

## Slide 32
The phases of implementation would also need guidance from GRVA. In particular it is proposed that car to car requirements (42 km/h collision avoidance) as well as car to pedestrian with reduced performance (collision avoidance at 30 km/h only) would apply from the date of entry into force (original version of the regulation from 2020 for new types) whereas the car to pedestrian with higher speed (42 km/h) would apply in a second step (2023 for new types). The introduction phase for car to bicycle could then come later.
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to pedestrian scenario - Speed reduction by braking demand
Guidance from GRVA

## Slide 33
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to bicycle scenario – Crossing and Same direction
Speed of bicycle: [15 km/h]
Activation Speed:
The system shall be active at least within the vehicle speed range between 10 km/h and [30 km/h] and at all vehicle load conditions
Crossing
Same direction

## Slide 34
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to bicycle scenario - Crossing and Same direction
For car to cyclist, the group agreed from accident data that the two most relevant scenarios are a cyclist crossing (similar to pedestrian scenario) and a cyclist driving in the same direction as the car (similar to car to car scenario). However, for the latter, it seems that steering is much more efficient than braking, so the usefulness of such a braking test needs to be checked again.
The group still faces difficulty in agreeing on performance requirements for the car to bicycle collision given the lack of vehicles with this technology on the market (only one vehicle was tested under EuroNcap in 2018). One alternative would be to require simply a warning in a first step or to discuss this issue again after the finalization of the discussion on cars and pedestrians.
Guidance from GRVA

## Slide 35
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Interruption by the Driver
This requirement based on the requirement of AEBS for large tracks (R131).

## Slide 36
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications - Manual deactivation
The group also discussed the possibility of a manual deactivation of the AEBS function. The compromise reached was that such a switch could be allowed but switching off the AEBS should not be too easy. However this compromise was not unanimously supported by all Contracting parties.
Guidance from GRVA

## Slide 37
Informal Working Group on AEBS for Light Vehicles
Specifications – Warning Indicator
This paragraph descried about Collision warning, Failure warning. These requirement based on the requirement of AEBS for large tracks (R131).

## Slide 38
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Specifications – Provisions for the Periodic Technical Inspection
This requirement based on existing the regulation of AEBS for large tracks (R131).

## Slide 39
Chair and Secretary IWG AEBS – GRVA 01
Informal Working Group on AEBS for Light Vehicles
Remaining open issues (including Test Procedure)
Remaining open issues are indicated in square brackets in the document. One major issue is the minimum requirements that shall be required when the vehicle is outside test conditions (e.g. different mass, different road conditions). In addition for both car to car and car to pedestrian, few issues remain opened for some particular cases (e.g. for vans derived from trucks approved under Regulation R 13).
IWG still need further discussion for these issues.

## Slide 40
Informal Working Group on AEBS for Light Vehicles
Thank you
for your attention
IWG meetings 6th meeting in Paris (OICA office)
(1-2 October 2018: Next week of this GRVA)
Chair and Secretary IWG AEBS – GRVA 01