SGS 6 - 08

Action Items for SGS VI

- OICA will discuss with BMW the possibility of submission of a proposal for LH2 that mimics the structure and detail of the OICA CH2 proposal

- China will provide details of the tests performed on the tank and on the fuel cell

- Korea will provide test report in English at the next meeting

- All should provide comments on Part A to Secretary as soon as possible

- Glenn Scheffler will suggest simplified diagrams and a section on LH2 for Part A

- ISO will provide descriptions of existing standards for the list of regulations (Part A Section 4)

- Korea will provide information on regulation for inclusion in the list (Part A Section 4)

- Secretary will distribute table with assignments for contributions to the Technical Rationale section

- US (DOT) will develop a proposal for a telltale warning

- US (DOE/Glenn) will provide justification for increased time interval for measurement of vehicle exhaust

- OICA will provide justification for 3-second interval for concentrations exceeding 4%

- US/Secretary will develop a draft of the sunlight protection requirement for consideration

- US (DOE/Chris) will provide text describing the risk-based assessment in support of sunlight protection for hydrogen tank but not gasoline tank (1.2.2)

- OICA will discuss issue, consider the proposal for multiple shutoff valves (1.3.1) and provide justifications why one valve would be enough; Japan to provide justification why one shut-off valve is not enough for Part A

- TUV to provide technical justification for overpressure protection of the low-pressure section (1.4.1)

- Germany will check with the EC representative to see if the EC will present the overpressure protection issue to WP.29 (1.4.1)

- OICA/SAE/TUV to provide proposed language on hydrogen detection in enclosed spaces (1.5.1) – (draft language provided at the 6th meeting)

- Japan and TUV will prepare rationale and submit an objective test procedure for compliance for air-tightness test (2.2.1) at vehicle level

- OICA to modify the text on the test conditions and procedures, to be consistent with current requirements so that the procedures can be modified

- ISO will provide presentation slides for posting

- US (DOE) will distribute pneumatic performance testing document (OICA proposal)

- OICA to discuss removal of the temperature range specification provision from the OICA proposal in response to Canada and US comments.

- China will check into getting the Tsinghua University presentation from 27 May

- US (DOE) will get information from ‘first responders’ regarding the direction of PRD discharge valve

- Germany and OICA work together on simplifying language for 5.2.2.3.3.

- Canada and US provide testing results on the localized fire project

- US (DOE/Chris) will provide suggestion for heading for 5.2.2.3.4.

- US will check on implementation of information collection for H storage container

- ISO and OICA/SAE work together on developing paper for the Task Force meeting

- ALL provide comments by June 30 on OICA and ISO proposals