## Slide 1
UNFC based reporting – Coal and CBM Resources
Application of UNFC for
Integrated and Unified Reporting
of Coal and CBM Resources
– An Approach.
Binay Dayal,
Director (Tech/Planning and Design)
CMPDI
Notes: 1

## Slide 2
United Nation Framework Classification
(UNFC)
United Nation Framework Classification (UNFC) is a system classifying the estimations based on three digit codes representing Geological Certainty, Feasibility, and Economic viability.
In the UNFC System, Reserve/Resources are represented by following three digits codes:
Economic (E) - Represented by first digit.
Feasibility (F) - Represented by second digit.
Geological (G) - Represented by third digit.
Notes: 2

## Slide 3: UNFC – 2009 SYSTEM: CATEGORIES
E = Economic Viability
E1‐Extraction and sale has been confirmed to be economically viable.
E2‐Extraction and sale is expected to become economically viable in the foreseeable future.
E3‐Extraction and sale is not expected to become economically viable in the foreseeable future or evaluation is at too early a stage to determine economic viability.
F = Feasibility Study
F1‐Feasibility of extraction by a defined development project or mining operation has been confirmed.
F2‐ Feasibility of extraction by a defined development project or mining operation is subject to further evaluation.
F3‐Feasibility of extraction by a defined development project or mining operation cannot be evaluated due to limited technical data.
F4‐No development project or mining operation has been identified.

## Slide 4: UNFC – 2009 SYSTEM: CATEGORIES
G = Geological Assessment
G1‐Quantities associated with a known deposit that can be estimated with a high level of confidence.
G2‐Quantities associated with a known deposit that can be estimated with a moderate level of confidence.
G3‐ Quantities associated with a known deposit that can be estimated with a low level of confidence.
G4‐ Estimated quantities associated with a potential deposit, based primarily on indirect evidence.

## Slide 5: UNFC – 2009 SYSTEM: SUB-CATEGORIES
E 1
E 1.1 Extraction and sale is economic on the basis of current market conditions and realistic assumptions of future market conditions.
E 1.2 Extraction and sale is not economic on the basis of current market conditions and realistic assumptions of future market conditions, but is made viable through government subsidies and/or other considerations.
E 3
E 3.1 Quantities that are forecast to be extracted, but which will not be available for sale.
E 3.2 Economic viability of extraction cannot yet be determined due to insufficient information (e.g. during the exploration phase).
E 3.3 On the basis of realistic assumptions of future market conditions, it is currently considered that there are not reasonable prospects for economic extraction and sale in the foreseeable future.

## Slide 6: UNFC – 2009 SYSTEM: SUB-CATEGORIES
F 1
F 1.1 Extraction is currently taking place.
F 1.2 Capital funds have been committed and implementation of the development project or mining operation is underway.
F 1.3 Sufficiently detailed studies have been completed to demonstrate the feasibility of extraction by implementing a defined development project or mining operation.
F 2
F 2.1 Project activities are ongoing to justify development in the foreseeable future.
F 2.2 Project activities are on hold and/or where justification as a commercial development may be subject to significant delay.
F 2.3 There are no current plans to develop or to acquire additional data at the time due to limited potential.

## Slide 7: UNFC - COAL INDIA LTD (CIL) BLOCKS
Utilizing the detailed guidelines to correlate the ISP (Indian Standard Procedure) classification to UNFC 2004 system available from Indian Bureau of Mines (IBM), the UNFC classification of the coal resources (as on 01.04.2013) in blocks of CIL were done on the UNFC-2004 system.
Based on available guidelines, the E, F and G categories were mapped with the ISP as well as the prevalent practice in CIL for feasibility studies and economic viability assessments.
The interpretations of E, F, G axes for CIL Blocks, developed accordingly, are given below:

## Slide 8
Geological Assessment (G)
Geological assessment is categorized into the following 4 sub-groups:
  Detailed Exploration or Proved Reserves (- (G1)
  General Exploration or Indicated Reserves - (G2)
  Prospecting or Inferred Reserves - (G3)
  Reconnaissance or Prognosticated Resources - (G4)
[ Inferred reserves: occurring in the area between radii of 1 km and 2 km from an exploratory borehole
Indicated reserves: occurring in the area between radii of 200 m and 1 km from an exploratory borehole
Proved reserves: occurring in the area within 200 m radius from an exploratory borehole. Mining projects are planned on the basis of this ]
Notes: 8

## Slide 9: Feasibility Assessment (F)
Feasibility assessment is represented by the following 3 sub-groups:
  Feasibility i.e. Project Report Prepared - (F1)
  Pre-Feasibility with economics prepared - (F2)
  No PR or Pre-Feasibility with economics prepared – (F3)
Economic assessment is represented by the following sub-groups:
    Economic – (E1)
    Potentially Economic or not economic – (E2)
    Economics not determined – (E3)

## Slide 10: UNFC 2009 SYSTEM IN CIL BLOCKS
The UNFC Classification of coal resources in CIL blocks is being updated. Upgradation to UNFC 2009 system will be attempted.
Data for environmental and social constraints is also being generated.
Draft guidelines for conversion of ISP classification to UNFC 2009 system (categories and sub-categories) was circulated by Indian Bureau of Mines (IBM) in Aug 2014. CMPDI has submitted its suggestions to IBM for finalizing the guidelines.
Finalized guidelines from IBM would help in UNFC classification in CIL on the 2009 system.

## Slide 11: UNFC APPLICATION TO CBM RESOURCES
Application of UNFC to CBM Resources:
Uniformly applicable criteria to be developed primarily for the G-Axis;
Guiding principle remains the same – confidence level of information about the Gas Content and Permeability factors primarily;
These two factors would in turn help in fixing the requisite borehole density i.e. the sampling/observation points for Gas studies and reservoir characteristics tests
G-Axes criteria therefore depends upon borehole density, gas content, permeability etc;

## Slide 12: UNFC APPLICATION TO CBM RESOURCES
CBM resource studies may generally involve:
Desorption studies – using core samples; estimation of gas content, and resource assessment vis-à-vis coal volume i.e. Resource modeling.
Geo-engineering tests – Reservoir characteristics,
Adsorption studies – Adsorption Isotherm parameters for reservoir modeling;
Feasibility Studies

## Slide 13: UNFC APPLICATION TO CBM RESOURCES
Prognosticates estimates through indirect methods based on empirical studies and theoretical methods, to compute the gas volume – may form the G4 category of UNFC.
Estimates through experimental methods using Adsorption Isotherm analyses – may form G3 category
Estimates through direct methods involving boreholes say 2-3 km apart with proximate analyses – may form G2 category
Reasonably firm estimates through direct methods involving borehole density of 150-650 sq. m per borehole, with coal characterizations and its analysis – may form G1 category
For each of these categories, the criteria depends upon borehole density, coal characteristics, gas content, permeability etc. To enhance confidence level for lower gas content seams may require higher borehole density for reservoir characterization for reservoir modeling and feasibility studies etc.

## Slide 14: UNFC APPLICATION TO CBM RESOURCES
Unified or integrated reporting of coal and CBM resources would require correlation between at least one factor common to both.
Borehole density may be a possible factor to link the resources.
However, variations in G category for CBM resources depend not only on borehole density but also upon gas content, permeability, etc.
Linking coal and CBM through E and F axes appears unlikely due to variability in extraction-feasibility, technology, commercial considerations, market availability, economics, etc.
Focus may therefore be kept on the possibility of linking the G-axes criteria for coal and CBM through at least one factor, for unified reporting of these two resources.

## Slide 15
THANK YOU

## Slide 16
Coal Resources & Reserves under CIL
as per UNFC Classification
CIL Subsidiary-wise UNFC Classification as on 01.04.2013 (excluding 119 assigned blocks) |  |  |  |  |  |  |  |  |  | 
Company | Coal Resource (Mt) |  |  |  |  |  |  | Coal Reserve (Mt) |  | 
 | U N F C Code |  |  |  |  |  |  |  |  | 
 | 3,3,3 | 3,3,2 | 3,3,1 | 2,2,2 | 2,2,1 | 2,1,1 | Total Resource | 1,2,2 1,2,1 1,1,2 | 1,1,1 | Total Reserve
ECL | 1285.86 | 1918.66 | 5951.24 | 0.00 | 2633.77 | 894.37 | 12683.90 | 0.00 | 1056.374 | 1056.37
BCCL | 271.85 | 1914.07 | 6138.38 | 0.00 | 2585.67 | 1035.54 | 11945.50 | 0.00 | 1031.25 | 1031.25
CCL | 14.48 | 3439.92 | 5552.91 | 0.00 | 2046.22 | 311.41 | 11364.94 | 0.00 | 3630.29 | 3630.29
WCL | 184.94 | 1018.93 | 1545.71 | 227.09 | 2240.10 | 204.23 | 5420.99 | 0.00 | 1494.94 | 1494.94
SECL | 217.52 | 6122.94 | 4649.37 | 0.00 | 1615.03 | 291.47 | 12896.32 | 0.00 | 3759.63 | 3759.63
MCL | 780.61 | 2252.79 | 4417.58 | 17.58 | 2235.02 | 38.63 | 9742.20 | 0.00 | 6969.93 | 6969.93
NCL | 0.00 | 2354.85 | 1206.51 | 0.00 | 472.02 | 227.02 | 4260.40 | 0.00 | 1767.95 | 1767.95
NEC | 0.00 | 26.86 | 204.69 | 0.00 | 60.76 | 5.19 | 297.49 | 0.00 | 94.63 | 94.63
CIL | 2755.26 | 19049.01 | 29666.38 | 244.67 | 13888.57 | 3007.86 | 68611.75 | 0.00 | 19805.01 | 19805.01
 | 68611.75 |  |  |  |  |  |  | 19805.01 |  | 

## Slide 17
Coal Resources & Reserves for Some of the Captive Blocks as per UNFC Classification
Captive Block | Coal Resources (Mt) |  |  |  |  |  |  | Coal Reserves (Mt) |  |  | 
 | 3,3,3 | 3,3,2 | 3,3,1 | 2,2,2 | 2,2,1 | 2,1,1 | Total | 1,2,2 & 1,2,1 | 1,1,2 | 1,1,1 | Total
Durgapur-II/Sariya | 0 | 0 | 0 | 0 | 24.708 | 0 | 24.708 | 0 | 0 | 66.962 | 66.962
Mandla North | 0 | 0 | 0 | 0 | 111.253 | 0 | 111.253 | 0 | 0 | 84.125 | 84.125
Utkal-E | 0 | 0 | 51.5644 | 0 | 3.400 | 0 | 54.9644 | 0 | 0 | 67.49 | 67.49
Rajgamar Dip Side | 0 | 0 | 0 | 0 | 42.697 | 0 | 42.697 | 0 | 0 | 19.00 | 19.00
Utkal B2 | 0 | 0 | 0 | 0 | 44.167 | 0 | 44.167 | 0 | 0 | 70.17 | 70.17
Gare Pelma IV/5 | 0 | 0 | 0 | 0 | 49.615 | 0 | 49.615 | 0 | 0 | 42.4295 | 42.4295
Radhikapur East | 0 | 0 | 0 | 31.07 | 41.57 | 0 | 72.64 | 0 | 4.49 | 106.3 | 110.79
Kathautia | 0 | 0 | 0 | 0 | 3.282 | 0 | 3.282 | 0 | 0.16 | 23.803 | 23.963
Mandakini-A | 0 | 0 | 0 | 2.634 | 0 | 0 | 2.634 | 0 | 1.206 | 286.68 | 287.886
Kerendari-A | 0 | 95.718 | 0 | 0 | 49.057 | 0 | 144.775 | 0 | 0 | 139.74 | 139.74
Chatti-Bariatu | 0 | 0 | 0 | 0 | 41.887 | 0 | 41.887 | 0 | 0 | 151.8 | 151.8
Dulunga | 0 | 0 | 48.94 | 0 | 44.139 | 0 | 93.093 | 0 | 0 | 152.05 | 152.05
Pakri Barwadih | 0 | 619.699 | 108.37 | 88.68 | 115.75 | 0 | 932.499 | 0 | 24.82 | 478.58 | 503.4
Chatti-Bariatu South | 0 | 90.86 | 262.99 | 0 | 0 | 0 | 353.85 | 0 | 0 | 0 | 0
Talaipalli | 0 | 0 | 0 | 40.278 | 365.607 | 0 | 405.885 | 0 | 0 | 861.26 | 861.26
TOTAL | 0 | 806.277 | 471.8644 | 162.662 | 937.132 | 0 | 2377.9494 | 0 | 30.676 | 2550.3895 | 2581.066
Total Resource + Reserve for the above 15 Captive Blocks = 2.581 + 2.378 = 4.959 Billion Tonnes. |  |  |  |  |  |  |  |  |  |  | 

## Slide 18
Coal Resources & Reserves for Singareni Blocks as per UNFC
 | SCCL – UNFC CATEGORISATION OF COAL RESERVES / RESOURCES AS ON 01-4-2013 (COAL (MT)) |  |  |  |  |  |  |  |  |  |  | 
Sl No | Block/GR | Coal Resource |  |  |  |  |  | Coal Reserve |  |  |  | Total
 |  | 3,3,3 | 3,3,2 | 3,3,1 | 2,2,2 | 2,2,1 | 2,1,1 | 1,2,2 | 1,2,1 | 1,1,2 | 1,1,1 | 
1 | KHAGAZNAGAR CB | 0.00 | 0.00 | 110.79 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 110.79
2 | DORLI BELLAMPALLI | 0.00 | 0.00 | 676.99 | 0.00 | 655.23 | 73.15 | 0.00 | 0.00 | 0.00 | 75.38 | 1572.88
3 | SOMAGUDEM-INDARAM | 0.00 | 0.00 | 958.41 | 0.00 | 535.22 | 71.35 | 0.00 | 0.00 | 0.00 | 113.90 | 1851.59
4 | CHINNUR CB | 0.00 | 0.00 | 298.97 | 0.00 | 48.09 | 11.70 | 0.00 | 0.00 | 0.00 | 0.00 | 360.57
5 | RAMAGUNDAM | 0.00 | 157.12 | 229.21 | 0.00 | 885.53 | 442.15 | 0.00 | 0.00 | 0.00 | 87.47 | 2185.34
6 | MULUG CB | 0.00 | 0.00 | 802.91 | 0.00 | 262.75 | 77.67 | 0.00 | 0.00 | 0.00 | 36.46 | 1197.47
7 | CHDU-MAHD | 0.00 | 0.00 | 147.17 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 147.17
8 | SOUTH OF KOTHAGUDEM | 0.00 | 0.00 | 237.43 | 0.00 | 44.41 | 0.00 | 0.00 | 0.00 | 0.00 | 247.11 | 550.55
9 | LINGALA KOYAGUDEM | 0.00 | 0.00 | 443.83 | 0.00 | 6.57 | 0.00 | 0.00 | 0.00 | 0.00 | 26.82 | 500.46
10 | ANS-MABU | 0.00 | 0.00 | 92.08 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 92.08
11 | YELLANDU | 0.00 | 0.00 | 22.34 | 0.00 | 208.29 | 6.01 | 0.00 | 0.00 | 0.00 | 17.74 | 357.94
12 | KOTHAGUDEM AREA | 0.00 | 0.00 | 563.87 | 0.00 | 432.85 | 54.84 | 0.00 | 0.00 | 0.00 | 0.00 | 1167.22
13 | MANUGURU CB | 0.00 | 0.00 | 264.47 | 0.00 | 231.11 | 9.14 | 0.00 | 0.00 | 0.00 | 368.07 | 1026.87
 | Total | 0.00 | 157.12 | 4848.46 | 0.00 | 3310.04 | 746.00 | 0.00 | 0.00 | 0.00 | 972.94 | 11120.93