| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/MP.PP/AC.1/2005/9 2 March 2005 Original: ENGLISH |

### ECONOMIC COMMISSION FOR EUROPE

Meeting of the Parties to the

Convention on Access to Information,

Public Participation in Decision-making and

Access to Justice in Environmental Matters

Working Group on Pollutant Release and Transfer Registers

(Second meeting, Geneva, 13-15 April 2005)

# Releases to land, reporting and release determination techniques

# III.	PRTR data

### Facility-level data

### Selection of pollutants to report for facilities

#### Releases to land

- Releases to land of any pollutant specified in annex II in quantities exceeding the applicable threshold are specified in annex II, column 2 for Parties that have opted for pollutant-specific reporting of transfers pursuant to paragraph 5 (d).

- Table 1 reproduces the list of pollutants and thresholds for direct releases to land from annex II of the PRTR Protocol.

| No. | CAS number | Pollutant | Threshold for releases to land (column 1c) | Manufacture, process or use threshold (column 3) |
| --- | --- | --- | --- | --- |
|  |  |  | kg/year | kg/year |
| 1 | 74-82-8 | Methane (CH4) | - | * |
| 2 | 630-08-0 | Carbon monoxide (CO) | - | * |
| 3 | 124-38-9 | Carbon dioxide (CO2) | - | * |
| 4 |  | Hydro-fluorocarbons (HFCs) | - | * |
| 5 | 10024-97-2 | Nitrous oxide (N2O) | - | * |
| 6 | 7664-41-7 | Ammonia (NH3) | - | 10 000 |
| 7 |  | Non-methane volatile organic compounds (NMVOC) | - | * |
| 8 |  | Nitrogen oxides (NOx/NO2) | - | * |
| 9 |  | Perfluorocarbons (PFCs) | - | * |
| 10 | 2551-62-4 | Sulphur hexafluoride (SF6) | - | * |
| 11 |  | Sulphur oxides (SOx/SO2) | - | * |
| 12 |  | Total nitrogen | 50 000 | 10 000 |
| 13 |  | Total phosphorus | 5 000 | 10 000 |
| 14 |  | Hydrochlorofluorocarbons (HCFCs) | - | 10 000 |
| 15 |  | Chlorofluorocarbons (CFCs) | - | 10 000 |
| 16 |  | Halons | - | 10 000 |
| 17 | 7440-38-2 | Arsenic and compounds (as As) | 5 | 50 |
| 18 | 7440-43-9 | Cadmium and compounds (as Cd) | 5 | 5 |
| 19 | 7440-47-3 | Chromium and compounds (as Cr) | 50 | 10 000 |
| 20 | 7440-50-8 | Copper and compounds (as Cu) | 50 | 10 000 |
| 21 | 7439-97-6 | Mercury and compounds (as Hg) | 1 | 5 |
| 22 | 7440-02-0 | Nickel and compounds (as Ni) | 20 | 10 000 |
| 23 | 7439-92-1 | Lead and compounds (as Pb) | 20 | 50 |
| 24 | 7440-66-6 | Zinc and compounds (as Zn) | 100 | 10 000 |
| 25 | 15972-60-8 | Alachlor | - | 10 000 |
| 26 | 309-00-2 | Aldrin | 1 | 1 |
| 27 | 1912-24-9 | Atrazine | 1 | 10 000 |
| 28 | 57-74-9 | Chlordane | 1 | 1 |
| 29 | 143-50-0 | Chlordecone | 1 | 1 |
| 30 | 470-90-6 | Chlorfenvinphos | 1 | 10 000 |
| 31 | 85535-84-8 | Chloro-alkanes, C10-C13 | 1 | 10 000 |
| 32 | 2921-88-2 | Chlorpyrifos | 1 | 10 000 |
| 33 | 50-29-3 | DDT | 1 | 1 |
| 34 | 107-06-2 | 1,2-dichloroethane | 10 | 10 000 |
| 35 | 75-09-2 | Dichloromethane | 10 | 10 000 |
| 36 | 60-57-1 | Dieldrin | 1 | 1 |
| 37 | 330-54-1 | Diuron | 1 | 10 000 |
| 38 | 115-29-7 | Endosulphan | 1 | 10 000 |
| 39 | 72-20-8 | Endrin | 1 | 1 |
| 40 |  | Halogenated organic compounds (as AOX) | 1 000 | 10 000 |
| 41 | 76-44-8 | Heptachlor | 1 | 1 |
| 42 | 118-74-1 | Hexachlorobenzene (HCB) | 1 | 5 |
| 43 | 87-68-3 | Hexachlorobutadiene (HCBD) | 1 | 10 000 |
| 44 | 608-73-1 | 1,2,3,4,5,6-hexachlorocyclohexane (HCH) | 1 | 10 |
| 45 | 58-89-9 | Lindane | 1 | 1 |
| 46 | 2385-85-5 | Mirex | 1 | 1 |
| 47 |  | PCDD + PCDF (dioxins + furans) as Teq | 0.001 | 0.001 |
| 48 | 608-93-5 | Pentachlorobenzene | 1 | 50 |
| 49 | 87-86-5 | Pentachlorophenol (PCP) | 1 | 10 000 |
| 50 | 1336-36-3 | Polychlorinated biphenyls (PCBs) | 0.1 | 50 |
| 51 | 122-34-9 | Simazine | 1 | 10 000 |
| 52 | 127-18-4 | Tetrachloroethylene (PER) | - | 10 000 |
| 53 | 56-23-5 | Tetrachloromethane (TCM) | - | 10 000 |
| 54 | 12002-48-1 | Trichlorobenzenes (TCBs) | - | 10 000 |
| 55 | 71-55-6 | 1,1,1-trichloroethane | - | 10 000 |
| 56 | 79-34-5 | 1,1,2,2-tetrachloroethane | - | 10 000 |
| 57 | 79-01-6 | Trichloroethylene | - | 10 000 |
| 58 | 67-66-3 | Trichloromethane | - | 10 000 |
| 59 | 8001-35-2 | Toxaphene | 1 | 1 |
| 60 | 75-01-4 | Vinyl chloride | 10 | 10 000 |
| 61 | 120-12-7 | Anthracene | 1 | 50 |
| 62 | 71-43-2 | Benzene | 200 (as BTEX) a/ | 10 000 |
| 63 |  | Brominated diphenylethers (PBDE) | 1 | 10 000 |
| 64 |  | Nonylphenol ethoxylates (NP/NPEs) and related substances | 1 | 10 000 |
| 65 | 100-41-4 | Ethyl benzene | 200 (as BTEX) | 10 000 |
| 66 | 75-21-8 | Ethylene oxide | 10 | 10 000 |
| 67 | 34123-59-6 | Isoproturon | 1 | 10 000 |
| 68 | 91-20-3 | Naphthalene | 10 | 10 000 |
| 69 |  | Organotin compounds (as total Sn) | 50 | 10 000 |
| 70 | 117-81-7 | Di-(2-ethyl hexyl) phthalate (DEHP) | 1 | 10 000 |
| 71 | 108-95-2 | Phenols (as total C) | 20 | 10 000 |
| 72 |  | Polycyclic aromatic hydrocarbons (PAHs) b/ | 5 | 50 |
| 73 | 108-88-3 | Toluene | 200 (as BTEX) a/ | 10 000 |
| 74 |  | Tributyltin and compounds | 1 | 10 000 |
| 75 |  | Triphenyltin and compounds | 1 | 10 000 |
| 76 |  | Total organic carbon (TOC) (as total C or COD/3) | - | ** |
| 77 | 1582-09-8 | Trifluralin | 1 | 10 000 |
| 78 | 1330-20-7 | Xylenes | 200 (as BTEX) a/ | 10 000 |
| 79 |  | Chlorides (as total Cl) | 2 million | 10 000 c/ |
| 80 |  | Chlorine and inorganic compounds (as HCl) | - | 10 000 |
| 81 | 1332-21-4 | Asbestos | 1 | 10 000 |
| 82 |  | Cyanides (as total CN) | 50 | 10 000 |
| 83 |  | Fluorides (as total F) | 2 000 | 10 000 c/ |
| 84 |  | Fluorine and inorganic compounds (as HF) | - | 10 000 |
| 85 | 74-90-8 | Hydrogencyanide (HCN) | - | 10 000 |
| 86 |  | Particulate matter (PM10) | - | * |

Table 1:  Identification and thresholds of releases to land from annex II of the PRTR Protocol

### Off-site transfers of pollutants

- Off-site transfers of pollutants can either be waste or waste water fed into a (public) sewer system. The PRTR Protocol text allows for waste two possibilities:

##### pollutant specific reporting; and

##### waste specific reporting.

- Pollutant specific reporting can be generated by analyzing the various wastes on their chemical composition. With the chemical composition the annual mass flow for each pollutant can be calculated.

- For waste-specific reporting Parties should define by means of national law what waste is designated as hazardous waste. The threshold is 2 tons for hazardous waste and 2000 tons for other waste.

- Hazardous wastes and other wastes destined for recovery or disposal transferred off site including transboundary movements shall be indicated respectively with the ‘R’ or ‘D’ operation pursuant to annex III.

- Table 2 reproduces the list of pollutants for off site transfers from annex II of the PRTR Protocol.

| No. | CAS number | Pollutant | Threshold for off-site transfers of pollutants (column 2) | Manufacture, process or use threshold (column 3) |
| --- | --- | --- | --- | --- |
|  |  |  | kg/year | kg/year |
| 1 | 74-82-8 | Methane (CH4) | - | * |
| 2 | 630-08-0 | Carbon monoxide (CO) | - | * |
| 3 | 124-38-9 | Carbon dioxide (CO2) | - | * |
| 4 |  | Hydro-fluorocarbons (HFCs) | - | * |
| 5 | 10024-97-2 | Nitrous oxide (N2O) | - | * |
| 6 | 7664-41-7 | Ammonia (NH3) | - | 10 000 |
| 7 |  | Non-methane volatile organic compounds (NMVOC) | - | * |
| 8 |  | Nitrogen oxides (NOx/NO2) | - | * |
| 9 |  | Perfluorocarbons (PFCs) | - | * |
| 10 | 2551-62-4 | Sulphur hexafluoride (SF6) | - | * |
| 11 |  | Sulphur oxides (SOx/SO2) | - | * |
| 12 |  | Total nitrogen | 10 000 | 10 000 |
| 13 |  | Total phosphorus | 10 000 | 10 000 |
| 14 |  | Hydrochlorofluorocarbons (HCFCs) | 100 | 10 000 |
| 15 |  | Chlorofluorocarbons (CFCs) | 100 | 10 000 |
| 16 |  | Halons | 100 | 10 000 |
| 17 | 7440-38-2 | Arsenic and compounds (as As) | 50 | 50 |
| 18 | 7440-43-9 | Cadmium and compounds (as Cd) | 5 | 5 |
| 19 | 7440-47-3 | Chromium and compounds (as Cr) | 200 | 10 000 |
| 20 | 7440-50-8 | Copper and compounds (as Cu) | 500 | 10 000 |
| 21 | 7439-97-6 | Mercury and compounds (as Hg) | 5 | 5 |
| 22 | 7440-02-0 | Nickel and compounds (as Ni) | 500 | 10 000 |
| 23 | 7439-92-1 | Lead and compounds (as Pb) | 50 | 50 |
| 24 | 7440-66-6 | Zinc and compounds (as Zn) | 1 000 | 10 000 |
| 25 | 15972-60-8 | Alachlor | 5 | 10 000 |
| 26 | 309-00-2 | Aldrin | 1 | 1 |
| 27 | 1912-24-9 | Atrazine | 5 | 10 000 |
| 28 | 57-74-9 | Chlordane | 1 | 1 |
| 29 | 143-50-0 | Chlordecone | 1 | 1 |
| 30 | 470-90-6 | Chlorfenvinphos | 5 | 10 000 |
| 31 | 85535-84-8 | Chloro -alkanes, C10-C13 | 10 | 10 000 |
| 32 | 2921-88-2 | Chlorpyrifos | 5 | 10 000 |
| 33 | 50-29-3 | DDT | 1 | 1 |
| 34 | 107-06-2 | 1,2-dichloroethane | 100 | 10 000 |
| 35 | 75-09-2 | Dichloromethane | 100 | 10 000 |
| 36 | 60-57-1 | Dieldrin | 1 | 1 |
| 37 | 330-54-1 | Diuron | 5 | 10 000 |
| 38 | 115-29-7 | Endosulphan | 5 | 10 000 |
| 39 | 72-20-8 | Endrin | 1 | 1 |
| 40 |  | Halogenated organic compounds (as AOX) | 1 000 | 10 000 |
| 41 | 76-44-8 | Heptachlor | 1 | 1 |
| 42 | 118-74-1 | Hexachlorobenzene (HCB) | 1 | 5 |
| 43 | 87-68-3 | Hexachlorobutadiene (HCBD) | 5 | 10 000 |
| 44 | 608-73-1 | 1,2,3,4,5,6-hexachlorocyclohexane (HCH) | 1 | 10 |
| 45 | 58-89-9 | Lindane | 1 | 1 |
| 46 | 2385-85-5 | Mirex | 1 | 1 |
| 47 |  | PCDD + PCDF (dioxins + furans) as Teq | 0.001 | 0.001 |
| 48 | 608-93-5 | Pentachlorobenzene | 5 | 50 |
| 49 | 87-86-5 | Pentachlorophenol (PCP) | 5 | 10 000 |
| 50 | 1336-36-3 | Polychlorinated biphenyls (PCBs) | 1 | 50 |
| 51 | 122-34-9 | Simazine | 5 | 10 000 |
| 52 | 127-18-4 | Tetrachloroethylene (PER) | 1 000 | 10 000 |
| 53 | 56-23-5 | Tetrachloromethane (TCM) | 1 000 | 10 000 |
| 54 | 12002-48-1 | Trichlorobenzenes (TCBs) | 1 000 | 10 000 |
| 55 | 71-55-6 | 1,1,1-trichloroethane | 1 000 | 10 000 |
| 56 | 79-34-5 | 1,1,2,2-tetrachloroethane | 1 000 | 10 000 |
| 57 | 79-01-6 | Trichloroethylene | 1 000 | 10 000 |
| 58 | 67-66-3 | Trichloromethane | 1 000 | 10 000 |
| 59 | 8001-35-2 | Toxaphene | 1 | 1 |
| 60 | 75-01-4 | Vinyl chloride | 100 | 10 000 |
| 61 | 120-12-7 | Anthracene | 50 | 50 |
| 62 | 71-43-2 | Benzene | 2000 (as BTEX) a/ | 10 000 |
| 63 |  | Brominated diphenylethers (PBDE) | 5 | 10 000 |
| 64 |  | Nonylphenol ethoxylates (NP/NPEs) and related substances | 5 | 10 000 |
| 65 | 100-41-4 | Ethyl benzene | 2000 (as BTEX) | 10 000 |
| 66 | 75-21-8 | Ethylene oxide | 100 | 10 000 |
| 67 | 34123-59-6 | Isoproturon | 5 | 10 000 |
| 68 | 91-20-3 | Naphthalene | 100 | 10 000 |
| 69 |  | Organotin compounds (as total Sn) | 50 | 10 000 |
| 70 | 117-81-7 | Di-(2-ethyl hexyl) phthalate (DEHP) | 100 | 10 000 |
| 71 | 108-95-2 | Phenols (as total C) | 200 | 10 000 |
| 72 |  | Polycyclic aromatic hydrocarbons (PAHs) b/ | 50 | 50 |
| 73 | 108-88-3 | Toluene | 2000 (as BTEX) a/ | 10 000 |
| 74 |  | Tributyltin and compounds | 5 | 10 000 |
| 75 |  | Triphenyltin and compounds | 5 | 10 000 |
| 76 |  | Total organic carbon (TOC) (as total C or COD/3) | - | ** |
| 77 | 1582-09-8 | Trifluralin | 5 | 10 000 |
| 78 | 1330-20-7 | Xylenes | 2000 (as BTEX) a/ | 10 000 |
| 79 |  | Chlorides (as total Cl) | 2 million | 10 000 c/ |
| 80 |  | Chlorine and inorganic compounds (as HCl) |  | 10 000 |
| 81 | 1332-21-4 | Asbestos | 10 | 10 000 |
| 82 |  | Cyanides (as total CN) | 500 | 10 000 |
| 83 |  | Fluorides (as total F) | 10 000 | 10 000 c/ |
| 84 |  | Fluorine and inorganic compounds (as HF) |  | 10 000 |
| 85 | 74-90-8 | Hydrogencyanide (HCN) |  | 10 000 |
| 86 |  | Particulate matter (PM10) |  | * |

Table 2:  Thresholds for off-site transfers from annex II of the PRTR Protocol

Box 1:  Annex III

### Expected releases and transfers

- Each individual source category as listed in annex I releases or transfers a different set of pollutants. In table 3 an indicative list is given of the pollutants for which releases or transfers can be expected that might be above the reporting thresholds for each of the annex I activities.

- The pollutants are indicated in release to air (a) and water (w) and for off-site transfer (o), respectively. This indicative list is presented to assist Parties in identifying the pollutants that are likely to be emitted by a specific source category of annex I of the PRTR Protocol and can be used as a checklist for reporting. Whether or not a pollutant is released or transferred above the threshold value depends on the specific characteristics of the facility.

Table 3: Sector-specific checklist for pollutants likely to be released or transferred by source categories of annex 1activities (a = release to air, w = release to water, o = off-site transfer).

| No. |  | Activity | 1 | 2. | 3. | 4. | 5. | 6. | 7. | 8. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Pollutant | Energy sector | Production and processing of metals | Mineral industry | Chemical industry | Waste and waste -water management | Paper and wood production and processing | Intensive livestock production and aquaculture | Animal and vegetable products from the food and beverage sector |
| 1 | 74-82-8 | Methane (CH4) | A |  |  | a | a |  | a | a |
| 2 | 630-08-0 | Carbon monoxide (CO) | A | a | a | a |  |  |  |  |
| 3 | 124-38-9 | Carbon dioxide (CO2) | a | a | a | a | a | a | a | a |
| 4 |  | Hydro-fluorocarbons (HFCs) |  | a | a |  | a |  |  |  |
| 5 | 10024-97-2 | Nitrous oxide (N2O) | a |  |  | a |  |  |  |  |
| 6 | 7664-41-7 | Ammonia (NH3) |  | a |  | a | a |  | awo |  |
| 7 |  | Non-methane volatile organic compounds (NMVOC) | a | a | a | a | a | a |  |  |
| 8 |  | Nitrogen oxides (NOx/NO2) | a | a | a | a | a | a | a | a |
| 9 |  | Perfluorocarbons (PFCs) |  | a |  | a | a |  |  |  |
| 10 | 2551-62-4 | Sulphur hexafluoride (SF6) |  |  |  |  |  |  |  |  |
| 11 |  | Sulphur oxides (SOx/SO2) | a | a | a | a | a | a | a |  |
| 12 |  | Total nitrogen |  |  | wo | wo | wo | wo | wo | wo |
| 13 |  | Total phosphorus |  |  | wo | wo | wo | wo | wo | wo |
| 14 |  | Hydrochlorofluorocarbons (HCFCs) |  | a | a | a | a | a | a | a |
| 15 |  | Chlorofluorocarbons (CFCs) |  |  |  |  |  |  |  |  |
| 16 |  | Halons |  | a | a | a | a | a | a | a |
| 17 | 7440-38-2 | Arsenic and compounds (as As) | aw | awo | awo | awo | awo |  |  |  |
| 18 | 7440-43-9 | Cadmium and compounds (as Cd) | aw | awo | awo | awo | awo |  |  |  |
| 19 | 7440-47-3 | Chromium and compounds (as Cr) | aw | awo | awo | awo | awo |  |  |  |
| 20 | 7440-50-8 | Copper and compounds (as Cu) | aw | awo | awo | awo | awo |  |  |  |
| 21 | 7439-97-6 | Mercury and compounds (as Hg) | aw | awo | awo | awo | awo |  |  |  |
| 22 | 7440-02-0 | Nickel and compounds (as Ni) | aw | awo | awo | awo | awo |  |  |  |
| 23 | 7439-92-1 | Lead and compounds (as Pb) | aw | awo | awo | awo | awo |  |  |  |
| 24 | 7440-66-6 | Zinc and compounds (as Zn) | aw | awo | awo | awo | awo |  |  |  |
| 25 | 15972-60-8 | Alachlor |  |  |  | awo | awo |  |  |  |
| 26 | 309-00-2 | Aldrin |  |  |  | awo | awo |  |  |  |
| 27 | 1912-24-9 | Atrazine |  |  |  | awo | awo |  |  |  |
| 28 | 57-74-9 | Chlordane |  |  |  | awo | awo |  |  |  |
| 29 | 143-50-0 | Chlordecone |  |  |  | awo | awo |  |  |  |
| 30 | 470-90-6 | Chlorfenvinphos |  |  |  | awo | awo |  |  |  |
| 31 | 85535-84-8 | Chloro-alkanes, C10-C13 |  |  |  | awo | awo |  |  |  |
| 32 | 2921-88-2 | Chlorpyrifos |  |  |  | awo | awo |  |  |  |
| 33 | 50-29-3 | DDT |  |  |  | awo | awo |  |  |  |
| 34 | 107-06-2 | 1,2-dichloroethane |  |  |  | awo | awo |  |  |  |
| 35 | 75-09-2 | Dichloromethane |  |  |  | awo | awo |  |  |  |
| 36 | 60-57-1 | Dieldrin |  |  |  | awo | awo |  |  |  |
| 37 | 330-54-1 | Diuron |  |  |  | awo | awo |  |  |  |
| 38 | 115-29-7 | Endosulphan |  |  |  | awo | awo |  |  |  |
| 39 | 72-20-8 | Endrin |  |  |  | awo | awo |  |  |  |
| 40 |  | Halogenated organic compounds (as AOX) |  |  |  | awo | awo |  |  |  |
| 41 | 76-44-8 | Heptachlor |  |  |  | awo | awo |  |  |  |
| 42 | 118-74-1 | Hexachlorobenzene (HCB) |  |  |  | awo | awo |  |  |  |
| 43 | 87-68-3 | Hexachlorobutadiene (HCBD) |  |  |  | awo | awo |  |  |  |
| 44 | 608-73-1 | 1,2,3,4,5,6-hexachlorocyclohexane (HCH) |  |  |  | awo | awo |  |  |  |
| 45 | 58-89-9 | Lindane |  |  |  | awo | awo |  |  |  |
| 46 | 2385-85-5 | Mirex |  |  |  | awo | awo |  |  |  |
| 47 |  | PCDD + PCDF (dioxins + furans) as Teq | a | a | a | awo | awo | a |  |  |
| 48 | 608-93-5 | Pentachlorobenzene |  |  |  | awo | awo |  |  |  |
| 49 | 87-86-5 | Pentachlorophenol (PCP) |  |  |  | awo | awo |  |  |  |
| 50 | 1336-36-3 | Polychlorinated biphenyls (PCBs) |  |  |  | awo | awo |  |  |  |
| 51 | 122-34-9 | Simazine |  |  |  | awo | awo |  |  |  |
| 52 | 127-18-4 | Tetrachloroethylene (PER) |  |  |  | awo | awo |  |  |  |
| 53 | 56-23-5 | Tetrachloromethane (TCM) |  |  |  | awo | awo |  |  |  |
| 54 | 12002-48-1 | Trichlorobenzenes (TCBs) |  |  |  | awo | awo |  |  |  |
| 55 | 71-55-6 | 1,1,1-trichloroethane |  |  |  | awo | awo |  |  |  |
| 56 | 79-34-5 | 1,1,2,2-tetrachloroethane |  |  |  | awo | awo |  |  |  |
| 57 | 79-01-6 | Trichloroethylene |  |  |  | awo | awo |  |  |  |
| 58 | 67-66-3 | Trichloromethane |  |  |  | awo | awo |  |  |  |
| 59 | 8001-35-2 | Toxaphene |  |  |  | awo | awo |  |  |  |
| 60 | 75-01-4 | Vinyl chloride |  |  |  | awo | awo |  |  |  |
| 61 | 120-12-7 | Anthracene |  |  |  | awo | awo |  |  |  |
| 62 | 71-43-2 | Benzene |  |  |  | awo | awo |  |  |  |
| 63 |  | Brominated diphenylethers (PBDE) |  |  |  | awo | awo |  |  |  |
| 64 |  | Nonylphenol ethoxylates (NP/NPEs) and related substances |  |  |  | awo | awo |  |  |  |
| 65 | 100-41-4 | Ethyl benzene |  |  |  | awo | awo |  |  |  |
| 66 | 75-21-8 | Ethylene oxide |  |  |  | awo | awo |  |  |  |
| 67 | 34123-59-6 | Isoproturon |  |  |  | awo | awo |  |  |  |
| 68 | 91-20-3 | Naphthalene |  |  |  | awo | awo |  |  |  |
| 69 |  | Organotin compounds (as total Sn) |  |  |  | awo | awo |  |  |  |
| 70 | 117-81-7 | Di-(2-ethyl hexyl) phthalate (DEHP) |  |  |  | awo | awo |  |  |  |
| 71 | 108-95-2 | Phenols (as total C) |  |  |  | awo | awo |  |  |  |
| 72 |  | Polycyclic aromatic hydrocarbons (PAHs) b/ |  |  |  | awo | awo |  |  |  |
| 73 | 108-88-3 | Toluene |  |  |  | awo | awo |  |  |  |
| 74 |  | Tributyltin and compounds |  |  |  | awo | awo |  |  |  |
| 75 |  | Triphenyltin and compounds |  |  |  | awo | awo |  |  |  |
| 76 |  | Total organic carbon (TOC) (as total C or COD/3) | wo | wo | wo | awo | awo | wo | wo | wo |
| 77 | 1582-09-8 | Trifluralin |  |  |  | awo | Awo |  |  |  |
| 78 | 1330-20-7 | Xylenes |  |  |  | awo | awo |  |  |  |
| 79 |  | Chlorides (as total Cl) |  |  |  | awo | awo |  |  |  |
| 80 |  | Chlorine and inorganic compounds (as HCl) |  |  |  | awo | awo |  |  |  |
| 81 | 1332-21-4 | Asbestos |  |  |  | awo | awo |  |  |  |
| 82 |  | Cyanides (as total CN) |  |  |  | awo | awo |  |  |  |
| 83 |  | Fluorides (as total F) |  |  |  | awo | awo |  |  |  |
| 84 |  | Fluorine and inorganic compounds (as HF) |  |  |  | awo | awo |  |  |  |
| 85 | 74-90-8 | Hydrogencyanide (HCN) |  |  |  | a | a |  |  |  |
| 86 |  | Particulate matter (PM10) | a | a | a | a | a | a | a | a |

### Reporting

- The requirements for facility-specific reporting are shown in Box 2 (art. 7, para. 5).

Box 2:  Article 7, paragraph 5

#### Release determination methods

- Many facilities already collect data suitable for determining releases and transfers to air, water and land. The release and transfer data on pollutants reported per facility can be based on three different principal determination methods:

##### Measurements using standardized or accepted methods; often additional calculations are needed to convert the results of measurements into annual emission data.

##### Calculations using nationally or internationally agreed estimation methods and emission factors, which are representative for the industrial sectors.

##### Estimations (non-standardized) derived from best assumptions or expert guesses.

- Measurements are derived from the direct monitoring of the releases and transfers of pollutants for specific processes at the facility, based on actual measurements of pollutant concentrations for its media. The term “measurements” refers to the results of standardized or accepted measurement methods (see appendix 3 of the guidance).

- Types of measurements that can be used are government compliance monitoring or prescribed self monitoring, process control measurements, worker exposure measurements or government permit or compliance measurements. These measurements can often directly be used to determine releases. Monitoring data needs to be taken frequently enough to account for normal variations in operating conditions throughout the year. An average concentration can be used with an average flow rate to calculate the yearly emission.

- Calculations determine releases and transfers of pollutants based on activity data (fuel used, production rate, etc.) and emission factors. In some cases more complicated calculation methods can be applied, using variables like temperature, global radiance etc. These cases should also be marked as calculations. Also, calculations based on a mass balance approach should be marked as calculations. Furthermore, the indication “calculation” is used whenever the emission calculation method is obtained from published references.

- Estimations refer to releases and transfers of pollutants that are determined by expert judgment and not based on publicly available references. The indication “estimation” applies also for guesses of the emissions wherever internationally approved emission determination methodologies or good practice guidelines are lacking.

- An overview of different types of determination methods for estimating releases and transfers of pollutants from facilities is given in table 4.

Table 4. Different types of determination methods for estimating releases and transfers of pollutants from facilities and classification as measurement (M), calculation (C) or estimation (E) [Unitar 1997]

| Type of measurtement | Classification for PRTR |
| --- | --- |
| I. Direct Measurement | M |
| - Fugitive Air Emissions | M |
| - Measuring Point Source Air Emissions | M |
| - Measuring Surface Water Discharges | M |
| - Measuring Releases to Land | M |
| II. Materials Accounting and Mass Balance | C |
| - Estimating Fugitive Air Emissions by Materials Accounting | C |
| - Estimating Point Source Air Emissions by Materials Accounting | C |
| - Estimating Surface Water Discharges by Materials Accounting | C |
| - Estimating Releases to Land by Materials Accounting | C |
| III - Emission Factors | C |
| - Estimating Fugitive Air Emissions with Emission Factors | C |
| - Estimating Point Source Air Emissions with Emission Factors | C |
| - Estimating Surface Water Discharges and Releases to Land with Emission Factors | C |
| IV. Engineering Calculation | C / E |
| - Estimating Fugitive Air Emissions by Engineering Calculation | C / E |
| - Estimating Point Source Air Emissions by Engineering Calculation | C / E |
| - Estimating Surface Water Discharges by Engineering Calculation | C / E |
| - Estimating Releases to Land by Engineering Calculation | C / E |

- Measurements are not always considered as more reliable or accurate than calculations.  For example, when determining the amount of CO2 from fuel use released to the atmosphere from a point-source, the direct measurement of the CO2 emission load from stacks relies on the determination of a set of parameters as CO2 concentration and the total flow off flue gas. Each of these introduces a new uncertainty and adds to the total uncertainty of the measurement.

- A more thorough and extensive overview and description of methods can be found in the following documents:

(a)	“Estimating Environmental Releases for Facility PRTR Reporting, Introduction and Guide to Methods” (United Nations Institute for Training and Research
(UNITAR), January 1997);

      - IPPC Bref Monitoring.

19.	In annex III of the guidance, “Analytical Procedures for 86 Substances,” an indicative list is given of:

- Release estimation techniques and the parameters (emission factors) needed for these;

- Measurement methods for relevant pollutants covered by CEN or ISO standards. This list is presented as guidance to the Parties regarding the availability of existing standardised measurement methods.

Box 3:  Organisation for Economic Co-operation and Development (OECD) Resource Centre for PRTR Release Estimation Techniques

- Table 6 gives an example format for reporting of releases and transfers of individual facilities.

| Identification of the facility |
| --- |
| Name of parent company Name of the facility Address / City of the facility ZIP Code / Country Co-ordinates of the location NACE-code (4 digits) Main economic activity Capacity / production volume (for capacity selection approach) Number of employees (for employee selection approach) Regulatory bodies (optional) Number of installations (optional) Number of operating hours in year (optional) |
| Annex I activities/processes (according to annex I) | Activity codes (according to annex I) |
| Activity 1 (main annex I activity) “ Activity N | Code 1 “ Code N |
| Air |  |
| Releases to AIR for the facility for ¦each pollutant exceeding threshold value (according to annex II, column 1a or column 3) |
| Pollutant 1, name and numerical identifier “ Pollutant N | M: measured C : calculated E : estimated | in kg/year |
| Water |  |
| Emission data to WATER (direct or indirect) for the facility for each pollutant exceeding threshold value (according to annex II, column 1b or column 3) |
| Pollutant 1, name and numerical identifier “ Pollutant N | M: measured C : calculated E : estimated | in kg/year |
| Land |  |
| Transfers of pollutant / waste for the facility for each pollutant or waste exceeding threshold value (according to annex II, column 1c or column 3) |
| Pollutant 1 name and numerical identifier “ Pollutant N | M: measured C : calculated E : estimated | in kg/year |
| Off-site transfers |  |
| Off-site transfers of pollutant / waste for the facility for each pollutant or waste exceeding threshold value (according to annex II, column 2 or column 3) |
| Pollutant / waste1 name and numerical identifier “ Pollutant / waste1 | M: measured C : calculated E : estimated | Indication of: hazardous waste (hw) or other waste (ow), recovery (R) or disposal (D) and transboundary movements hazardous waste. | in kg/year |
|  | Name and address of recoverer or disposer of each pollutant / waste |
|  | Name and address of the actual recovery or disposal site of each pollutant / waste |

Table 6 Example format for reporting of releases and transfers of individual facilities

# Footnotes

*/ This document was submitted late due to the need to hold in-depth consultations over the text with a number of leading experts on the topic of pollution registers.

GE.05- 30439

# Endnotes

a/ Single pollutants are to be reported if the threshold for BTEX (the sum parameter of benzene, toluene, ethyl benzene, xylene) is exceeded.

b/ Polycyclic aromatic hydrocarbons (PAHs) are to be measured as benzo(a)pyrene (50-32-8), benzo(b)fluoranthene (205-99-2), benzo(k)fluoranthene (207-08-9), indeno(1,2,3-cd)pyrene (193-39-5) (derived from the Protocol on Persistent Organic Pollutants to the Convention on Long-range Transboundary Air Pollution).

c/ As inorganic compounds.

See http://www.unitar.org/cwm/prtr/pdf/cat5/estimating_rels.pdf

See http://eippcb.jrc.es/cgi-bin/locatemr?ref_final_0203.pdf.  The Integrated Pollution Prevention and Control (IPPC) Directive reference document on the general principles of monitoring is intended to provide information to guide IPPC permit writers and operators of IPPC installations in meeting their obligations under the IPPC Directive with regards to the monitoring requirements of industrial emissions.

# Text boxes

Article 7, paragraph 5

Each Party shall require the owners or operators of the facilities required to report under paragraph 2 to complete and submit to its competent authority, the following inf ormation on a facility-specific basis:

(a) The name, street address, geographical location and the activity or activities of the reporting facility, and the name of the owner or operator, and, as appropriate, company;

(b) The name and numerical identifier of each pollutant required to be reported pursuant to paragraph 2;

(c) The amount of each pollutant required to be reported pursuant to paragraph 2 released from the facility to the environment in the reporting year, both in aggregate and according to whether the release is to air, to water or to land, including by underground injection;

(d) Either:

(i) The amount of each pollutant required to be reported pursuant to paragraph 2 that is transferred off-site in the reporting year, distinguishing between the amounts transferred for disposal and for recovery, and the name and address of the facility receiving the transfer; or

(ii) The amount of waste required to be reported pursuant to paragraph 2 transferred off-site in the reporting year, distinguishing between hazardous waste and other waste, for any operations of recovery or disposal, indicating respectively with ‘R’ or ‘D’ whether the waste is destined for recovery or disposal pursuant to annex III and, for transboundary movements of hazardous waste, the name and address of the recoverer or disposer of the waste and the actual recovery or disposal site receiving the transfer;

(e) The amount of each pollutant in waste water required to be reported pursuant to paragraph 2 transferred off-site in t he reporting year; and

(f) The type of methodology used to derive the information referred to in subparagraphs (c) to (e), according to article 9, paragraph 2, indicating whether the information is based on measurement, calculation or estimation.

Resource Centre for PRTR Release Estimation Techniques (RETs)

The Resource Centre is an Internet site that has been developed by the Task Force on PRTRs (Pollutant Release and Transfer Registers) of the OECD's Environment, Health and Safety Programme under the lead of Environment Canada. The purpose of the site is to provide a clearinghouse of guidance manuals/documents of release estimation techniques for the principal pollutant release and transfer registries developed by OECD member countries. The manuals and documents include descriptive information on the sources of pollution and the pollutants that are released, as well as information on emission factors, mass balance methods, engineering calculations, and monitoring information. The Resource Centre will be updated on a regular basis to include additional and new documents available.

See http://206.191.48.253/

.

Annex III

PART A DISPOSAL OPERATIONS (‘D’)

- Deposit into or onto land (e.g. landfill)

- Land treatment (e.g. biodegradation of liquid or sludgy discards in soils)

- Deep injection (e.g. injection of pumpable discards into wells, salt domes or naturally occurring repositories)

- Surface impoundment (e.g. placement of liquid or sludge discards into pits, ponds or lagoons)

- Specially engineered landfill (e.g. placement into lined discrete cells which are capped and isolated from one another and the environment)

- Release into a water body except seas/oceans

- Release into seas/oceans including sea-bed insertion

- Biological treatment not specified elsewhere in this annex which results in final compounds or mixtures which are discarded by means of any of the operations specified in this part

- Physico-chemical treatment not specified elsewhere in this annex which results in final compounds or mixtures which are discarded by means of any of the operations specified in this part (e.g. evaporation, drying, calcination, neutralization, precipitation)

- Incineration on land

- Incineration at sea

- Permanent storage (e.g. emplacement of containers in a mine)

- Blending or mixing prior to submission to any of the operations specified in this part

- Repackaging prior to submission to any of the operations specified in this part

- Storage pending any of the operations specified in this part

PART B RECOVERY OPERATIONS (‘R’)

- Use as a fuel (other than in direct incineration) or other means to generate energy

- Solvent reclamation/regeneration

- Recycling/reclamation of organic substances which are not used as solvents

- Recycling/reclamation of metals and metal compounds

- Recycling/reclamation of other inorganic materials

- Regeneration of acids or bases

- Recovery of components used for pollution abatement

- Recovery of components from catalysts

- Used oil re-refining or other reuses of previously used oil

- Land treatment resulting in benefit to agriculture or ecological improvement

- Uses of residual materials obtained from any of the recovery operations specified above in this part

- Exchange of wastes for submission to any of the recovery operations specified above in this part

- Accumulation of material intended for any operation specified in this part