Guidance for Parties Making Adjustment Applications and Guidance for the Expert Review of Adjustment Applications

Appendices to the Main Report

A Report of the TFEIP

November 2014

| Report Title | Guidance on the Adjustments Process for Parties and Expert Reviewers – Appendices |
| --- | --- |
| Customer | Submitted to the CLRTAP EB for consideration |
| Recipient | CLRTAP Secretariat |
| Report Reference | TFEIP/11K14/CD |
| Report Status | DRAFT VERSION4 |
| Revisions |  |

| Author(s) | Chris Dore (TFEIP Co-Chair), Yvonne Pang (UK), Leon Ntziachristos (Greece) Morten Winther (Denmark) |
| --- | --- |
| Reviewed by |  |
| Signature |  |
| Date | 26/11/2014 |

| Aether Ltd Oxford Centre for Innovation New Road Oxford OX1 1BY | chris.dore@aether-uk.com +44 (0) 1865 261466 |
| --- | --- |

Contents

Appendices	5

Appendix A1: Non-Road Mobile Machinery: Revisions to EFs	6

Introduction	6

Changes to EFs	6

Quantifying the Adjustment	11

Appendix A2: Road Transport: Revisions to Methodologies, and revisions to EFs	16

Introduction	16

Changes to EFs and Methodologies	16

Quantifying the Adjustment	19

A Summary of What the ERT Will Be Looking For	20

References	21

Appendix A3: Agriculture: New Sources and Revisions to EFs	22

Introduction	22

Changes to EFs	22

Quantifying the Adjustment	22

A Summary of What the ERT Will Be Looking For	22

Appendix B1: Party Template for Reporting a Quantified Adjustment	23

Appendix C1: Expert Reviewers Checklist	23

Appendix C2: Template for Summary Status Report (for the EMEP SB)	24

Appendix C3: Template for Country Report	27

COMMENT: We ask that the TFEIP/CEIP or EMEP SB be given the remit to revise/update any of these Appendices without the need to refer back to the CLRTAP EB.

Appendix A1: Non-Road Mobile Machinery: Revisions to EFs

Introduction

In 1999 when the emission ceilings for the Gothenburg Protocol were set, the Third Edition of the EMEP/EEA Emissions Inventory Guidebook (EMEP/EEA, technical report 30) was available for countries setting up national emission inventories. For Non-road mobile machinery (NRMM) sources the methodology chapter remained unchanged from the previous Second Edition of the guidebook.

The 1999 NRMM methodology chapter proposed a simple and a detailed inventory methodology. The simple methodology has later been replaced by a Tier 1 and a Tier 2 methodology as one of the outcomes of the guidebook revision project carried out in 2008. However, due to project resource limitations, the 1999 detailed methodology remained unchanged and is still in today’s version of the Guidebook (EMEP/EEA Emissions Inventory Guidebook, 2013 Edition)

This section explains the changes in emission factors that arise from changing from the 1999 simple method towards the current Tier 1 method for diesel and gasoline 2-stroke/4-stroke engines. The following sections also explain the impact on emission factors for diesel machinery that arise from changing from the 1999 detailed methodology to a more modern detailed methodology (which includes updated data for the entire range of NRMM technology stages defined by the EU emission legislation, and several pre EU NRMM emission technology as well). As previously mentioned this latter method is not currently described in the 2013 Edition of the EMEP/EEA Emissions Inventory Guidebook - it is derived from the German TREMOD NRMM model (IFEU, 2004; 2009; 2014).

Emission assessment calculations are also made using country specific NRMM inventory data. This case study demonstrates the impact on emissions from Denmark which arise as a consequences of updating the 1999 Guidebook emission factors to those available in 2012.

Changes to EFs

Simple methodology - emission factors and emission factor changes between 1999 Guidebook and 2013 Guidebook factors

Tables A1.1 and A1.2 shows the fuel related Simple (Guidebook 1999) and Tier 1 (2013 Guidebook) emission factors and emission factor ratios for NRMM diesel, and 2-stroke/4-stroke gasoline, respectively.

Table A1.1 Fuel related Simple (Guidebook 1999) and Tier 1 (2013 Guidebook) emission factors and emission factor ratios for NRMM diesel machinery

|  |  | NOx | NMVOC | CH4 | CO | N2O | NH3 | TSP |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Diesel |  | g/kg fuel | g/kg fuel | g/kg fuel | g/kg fuel | g/kg fuel | g/kg fuel | g/kg fuel |
| 1999 Guidebook | Agriculture | 50,30 | 7,27 | 0,17 | 16,00 | 1,29 | 0,007 | 5,87 |
|  | Forestry | 50,30 | 6,50 | 0,17 | 14,50 | 1,32 | 0,007 | 5,31 |
|  | Industry | 48,80 | 7,08 | 0,17 | 15,80 | 1,30 | 0,007 | 5,73 |
| 2013 Guidebook | Agriculture | 35,04 | 3,37 | 0,055 | 10,94 | 0,14 | 0,008 | 1,74 |
|  | Forestry | 29,09 | 2,02 | 0,033 | 7,83 | 0,14 | 0,008 | 0,98 |
|  | Industry | 32,79 | 3,38 | 0,055 | 10,72 | 0,14 | 0,008 | 2,09 |
| 1999:2013 Guidebook | Agriculture | 1,44 | 2,16 | 3,11 | 1,46 | 9,52 | 0,90 | 3,38 |
|  | Forestry | 1,73 | 3,22 | 5,18 | 1,85 | 9,55 | 0,89 | 5,44 |
|  | Industry | 1,49 | 2,09 | 3,09 | 1,47 | 9,61 | 0,91 | 2,75 |

Table A1.2 Fuel related Simple (Guidebook 1999) and Tier 1 (2013 Guidebook) emission factors and emission factor ratios for NRMM gasoline 2-stroke and 4-stroke machinery

|  |  |  | NOx | NMVOC | CH4 | CO | N2O | NH3 | TSP |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | g/kg fuel | g/kg fuel | g/kg fuel | g/kg fuel | g/kg fuel | g/kg fuel | g/kg fuel |
| 1999 Guidebook | Gasoline 2-stroke | Agriculture | 1,70 | 617 | 6,17 | 1070 | 0,02 | 0,004 | no data |
|  |  | Forestry | 1,55 | 762 | 7,67 | 1407 | 0,02 | 0,004 | no data |
|  |  | Industry | 2,10 | 602 | 6,00 | 1103 | 0,02 | 0,004 | no data |
|  |  | Household | 1,77 | 813 | 8,13 | 1572 | 0,02 | 0,004 | no data |
| 1999 Guidebook | Gasoline 4-stroke | Agriculture | 7,56 | 73,6 | 3,68 | 1486 | 0,07 | 0,005 | no data |
|  |  | Forestry | no data | no data | no data | no data | no data | no data | no data |
|  |  | Industry | 9,61 | 43,4 | 2,17 | 1193 | 0,08 | 0,005 | no data |
|  |  | Household | 8,00 | 110 | 5,50 | 2193 | 0,07 | 0,005 | no data |
| 2013 Guidebook | 2-stroke | All | 2,77 | 242,20 | 2,20 | 620,79 | 0,02 | 0,003 | 3,76 |
|  | 4-stroke | All | 7,12 | 17,60 | 1,96 | 770,37 | 0,06 | 0,004 | 0,16 |
| 1999:2013 Guidebook | Gasoline 2-stroke | Agriculture | 0,61 | 2,55 | 2,80 | 1,72 | 1,18 | 1,33 | - |
| - |  | Forestry | 0,56 | 3,15 | 3,49 | 2,27 | 1,18 | 1,33 | - |
|  |  | Industry | 0,76 | 2,49 | 2,73 | 1,78 | 1,18 | 1,33 | - |
|  |  | Household | 0,64 | 3,36 | 3,70 | 2,53 | 1,18 | 1,33 | - |
|  | Gasoline 4-stroke | Agriculture | 1,06 | 4,18 | 1,88 | 1,93 | 1,19 | 1,25 | - |
|  |  | Forestry |  |  |  |  |  |  | - |
|  |  | Industry | 1,35 | 2,47 | 1,11 | 1,55 | 1,36 | 1,25 | - |
|  |  | Household | 1,12 | 6,25 | 2,81 | 2,85 | 1,19 | 1,25 | - |

Detailed methodology - emission factors and emission factor changes between 1999 Guidebook and factors representing today’s state of the art emission knowledge

The Tables A1.3 and A1.4 show the kW based emission factors for Guidebook 1999, and updated emission factors representing todays best available emission factor knowledge. A direct comparison between the two emission factor tables tells that the 1999 Guidebook emission factor are missing data for the newest Stage IIIA and IIIB engine technologies and the future Stage IV standard as well. Further, pre EU emission stages are covered by only one technology stage (Uncontrolled) in Guidebook 1999, whereas emission data allows for distinguishing between three conventional < 1981, 1981–1990, 1991–Stage I emission levels in the updated case.

Table A1.3 kW based detailed Guidebook 1999 emission factors for NRMM diesel machinery

| kW size | Emission Level | NOx | NMVOC | CH4 | CO | N2O | NH3 | PM | Fuel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| kW |  | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh |
| 0-20 | Uncontrolled | 14,4 | 3,82 | 0,05 | 8,38 | 0,35 | 0,002 | 2,22 | 271 |
| 0-20 | Stage I | 14,4 | 3,82 | 0,05 | 8,38 | 0,35 | 0,002 | 2,22 | 271 |
| 0-20 | Stage II | 14,4 | 3,82 | 0,05 | 8,38 | 0,35 | 0,002 | 2,22 | 271 |
| 20-37 | Uncontrolled | 14,4 | 2,91 | 0,05 | 6,43 | 0,35 | 0,002 | 1,81 | 269 |
| 20-37 | Stage I | 14,4 | 2,91 | 0,05 | 6,43 | 0,35 | 0,002 | 1,81 | 269 |
| 20-37 | Stage II | 8,5 | 1,5 | 0,05 | 5,5 | 0,35 | 0,002 | 0,8 | 269 |
| 37-75 | Uncontrolled | 14,4 | 2,28 | 0,05 | 5,06 | 0,35 | 0,002 | 1,51 | 265 |
| 37-75 | Stage I | 9,2 | 1,3 | 0,05 | 6,5 | 0,35 | 0,002 | 0,85 | 265 |
| 37-75 | Stage II | 8 | 1,3 | 0,05 | 5 | 0,35 | 0,002 | 0,4 | 265 |
| 75-130 | Uncontrolled | 14,4 | 1,67 | 0,05 | 3,76 | 0,35 | 0,002 | 1,23 | 260 |
| 75-130 | Stage I | 9,2 | 1,3 | 0,05 | 5 | 0,35 | 0,002 | 0,7 | 260 |
| 75-130 | Stage II | 7 | 1 | 0,05 | 5 | 0,35 | 0,002 | 0,3 | 260 |
| 130-300 | Uncontrolled | 14,4 | 1,3 | 0,05 | 3 | 0,35 | 0,002 | 1,1 | 254 |
| 130-300 | Stage I | 9,2 | 1,3 | 0,05 | 5 | 0,35 | 0,002 | 0,54 | 254 |
| 130-300 | Stage II | 7 | 1 | 0,05 | 3,5 | 0,35 | 0,002 | 0,2 | 254 |
| 300-560 | Uncontrolled | 14,4 | 1,3 | 0,05 | 3 | 0,35 | 0,002 | 1,1 | 254 |
| 300-560 | Stage I | 9,2 | 1,3 | 0,05 | 5 | 0,35 | 0,002 | 0,54 | 254 |
| 300-560 | Stage II | 7 | 1 | 0,05 | 3,5 | 0,35 | 0,002 | 0,2 | 254 |
| 560-1000 | Uncontrolled | 14,4 | 1,3 | 0,05 | 3 | 0,35 | 0,002 | 1,1 | 254 |
| 560-1000 | Stage I | 14,4 | 1,3 | 0,05 | 3 | 0,35 | 0,002 | 1,1 | 254 |
| 560-1000 | Stage II | 14,4 | 1,3 | 0,05 | 3 | 0,35 | 0,002 | 1,1 | 254 |
| >1000 | Uncontrolled | 14,4 | 1,3 | 0,05 | 3 | 0,35 | 0,002 | 1,1 | 254 |
| >1000 | Stage I | 14,4 | 1,3 | 0,05 | 3 | 0,35 | 0,002 | 1,1 | 254 |
| >1000 | Stage II | 14,4 | 1,3 | 0,05 | 3 | 0,35 | 0,002 | 1,1 | 254 |

Table A1.4 Modern kW based detailed emission factors for NRMM diesel machinery

| kW size | Emission Level | NOx | NMVOC | CH4 | CO | N2O | NH3 | PM | Fuel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| kW |  | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh |
| P<19 | <1981 | 12 | 4,92 | 0,080 | 7 | 0,035 | 0,002 | 2,8 | 300 |
| P<19 | 1981-1990 | 11,5 | 3,74 | 0,061 | 6 | 0,035 | 0,002 | 2,3 | 285 |
| P<19 | 1991-Stage I | 11,2 | 2,46 | 0,040 | 5 | 0,035 | 0,002 | 1,6 | 270 |
| P<19 | Stage I | 11,2 | 2,46 | 0,040 | 5 | 0,035 | 0,002 | 1,6 | 270 |
| P<19 | Stage II | 11,2 | 2,46 | 0,040 | 5 | 0,035 | 0,002 | 1,6 | 270 |
| P<19 | Stage IIIA | 11,2 | 2,46 | 0,040 | 5 | 0,035 | 0,002 | 1,6 | 270 |
| P<19 | Stage IIIB | 11,2 | 2,46 | 0,040 | 5 | 0,035 | 0,002 | 1,6 | 270 |
| P<19 | Stage IV | 11,2 | 2,46 | 0,040 | 5 | 0,035 | 0,002 | 1,6 | 270 |
| 19<=P<37 | <1981 | 18 | 2,46 | 0,040 | 6,5 | 0,035 | 0,002 | 2 | 300 |
| 19<=P<37 | 1981-1990 | 18 | 2,16 | 0,035 | 5,5 | 0,035 | 0,002 | 1,4 | 281 |
| 19<=P<37 | 1991-Stage I | 9,8 | 1,77 | 0,029 | 4,5 | 0,035 | 0,002 | 1,4 | 262 |
| 19<=P<37 | Stage I | 9,8 | 1,77 | 0,029 | 4,5 | 0,035 | 0,002 | 1,4 | 262 |
| 19<=P<37 | Stage II | 6,5 | 0,59 | 0,010 | 2,2 | 0,035 | 0,002 | 0,4 | 262 |
| 19<=P<37 | Stage IIIA | 6,18 | 0,56 | 0,009 | 2,2 | 0,035 | 0,002 | 0,4 | 262 |
| 19<=P<37 | Stage IIIB | 6,18 | 0,56 | 0,009 | 2,2 | 0,035 | 0,002 | 0,4 | 262 |
| 19<=P<37 | Stage IV | 6,18 | 0,56 | 0,009 | 2,2 | 0,035 | 0,002 | 0,4 | 262 |
| 37<=P<56 | <1981 | 7,7 | 2,36 | 0,038 | 6 | 0,035 | 0,002 | 1,8 | 290 |
| 37<=P<56 | 1981-1990 | 8,6 | 1,97 | 0,032 | 5,3 | 0,035 | 0,002 | 1,2 | 275 |
| 37<=P<56 | 1991-Stage I | 11,5 | 1,48 | 0,024 | 4,5 | 0,035 | 0,002 | 0,8 | 260 |
| 37<=P<56 | Stage I | 7,7 | 0,59 | 0,010 | 2,2 | 0,035 | 0,002 | 0,4 | 260 |
| 37<=P<56 | Stage II | 5,5 | 0,39 | 0,006 | 2,2 | 0,035 | 0,002 | 0,2 | 260 |
| 37<=P<56 | Stage IIIA | 3,94 | 0,29 | 0,005 | 2,2 | 0,035 | 0,002 | 0,2 | 260 |
| 37<=P<56 | Stage IIIB | 3,94 | 0,29 | 0,005 | 2,2 | 0,035 | 0,002 | 0,0225 | 260 |
| 37<=P<56 | Stage IV | 3,94 | 0,29 | 0,005 | 2,2 | 0,035 | 0,002 | 0,0225 | 260 |
| 56<=P<75 | <1981 | 7,7 | 1,97 | 0,032 | 5 | 0,035 | 0,002 | 1,4 | 290 |
| 56<=P<75 | 1981-1990 | 8,6 | 1,57 | 0,026 | 4,3 | 0,035 | 0,002 | 1 | 275 |
| 56<=P<75 | 1991-Stage I | 11,5 | 1,18 | 0,019 | 3,5 | 0,035 | 0,002 | 0,4 | 260 |
| 56<=P<75 | Stage I | 7,7 | 0,39 | 0,006 | 1,5 | 0,035 | 0,002 | 0,2 | 260 |
| 56<=P<75 | Stage II | 5,5 | 0,30 | 0,005 | 1,5 | 0,035 | 0,002 | 0,2 | 260 |
| 56<=P<75 | Stage IIIA | 4,01 | 0,22 | 0,004 | 1,5 | 0,035 | 0,002 | 0,2 | 260 |
| 56<=P<75 | Stage IIIB | 2,97 | 0,17 | 0,003 | 1,5 | 0,035 | 0,002 | 0,0225 | 260 |
| 56<=P<75 | Stage IV | 0,36 | 0,17 | 0,003 | 1,5 | 0,035 | 0,002 | 0,0225 | 260 |
| 75<=P<130 | <1981 | 10,5 | 1,97 | 0,032 | 5 | 0,035 | 0,002 | 1,4 | 280 |
| 75<=P<130 | 1981-1990 | 11,8 | 1,57 | 0,026 | 4,3 | 0,035 | 0,002 | 1 | 268 |
| 75<=P<130 | 1991-Stage I | 13,3 | 1,18 | 0,019 | 3,5 | 0,035 | 0,002 | 0,4 | 255 |
| 75<=P<130 | Stage I | 8,1 | 0,39 | 0,006 | 1,5 | 0,035 | 0,002 | 0,2 | 255 |
| 75<=P<130 | Stage II | 5,2 | 0,30 | 0,005 | 1,5 | 0,035 | 0,002 | 0,2 | 255 |
| 75<=P<130 | Stage IIIA | 3,40 | 0,20 | 0,003 | 1,5 | 0,035 | 0,002 | 0,2 | 255 |
| 75<=P<130 | Stage IIIB | 2,97 | 0,17 | 0,003 | 1,5 | 0,035 | 0,002 | 0,0225 | 255 |
| 75<=P<130 | Stage IV | 0,36 | 0,17 | 0,003 | 1,5 | 0,035 | 0,002 | 0,0225 | 255 |
| 130<=P<560 | <1981 | 17,8 | 1,48 | 0,024 | 2,5 | 0,035 | 0,002 | 0,9 | 270 |
| 130<=P<560 | 1981-1990 | 12,4 | 0,98 | 0,016 | 2,5 | 0,035 | 0,002 | 0,8 | 260 |
| 130<=P<560 | 1991-Stage I | 11,2 | 0,49 | 0,008 | 2,5 | 0,035 | 0,002 | 0,4 | 250 |
| 130<=P<560 | Stage I | 7,6 | 0,30 | 0,005 | 1,5 | 0,035 | 0,002 | 0,2 | 250 |
| 130<=P<560 | Stage II | 5,2 | 0,30 | 0,005 | 1,5 | 0,035 | 0,002 | 0,1 | 250 |
| 130<=P<560 | Stage IIIA | 3,40 | 0,20 | 0,003 | 1,5 | 0,035 | 0,002 | 0,1 | 250 |
| 130<=P<560 | Stage IIIB | 1,8 | 0,17 | 0,003 | 1,5 | 0,035 | 0,002 | 0,0225 | 250 |
| 130<=P<560 | Stage IV | 0,36 | 0,17 | 0,003 | 1,5 | 0,035 | 0,002 | 0,0225 | 250 |

Table A1.5 shows the ratios between detailed Guidebook 1999 and detailed modern emission factors for NRMM diesel machinery. In the table, the 1999 Guidebook emission stage “Uncontrolled” is compared with the three conventional < 1981, 1981–1990, 1991–Stage I emission levels from the modern emission factor set. The factors for the newest emission technology level Stage II in the 1999 Guidebook is compared with the newer EU Stage IIIA, IIIB and IV emission stages from the modern emission factor base.

The “missing 1999 Guidebook data” comparison in Table A1.5 particularly highlights the emission factor consequences of filling the 1999 Guidebook data gap in the most simple way for countries that during the recent years have continued to use the detailed 1999 Guidebook methodology after Stage IIIA and IIIB technologies have entered into the fleet.

Table A1.5 Ratios between detailed Guidebook 1999 and detailed modern emission factors for NRMM diesel machinery

| Size class | kW size | Emission Level | NOx | NMVOC | CH4 | CO | N2O | NH3 | PM | Fuel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | kW |  | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh | g/kWh |
| A | P<19 | <1981 | 1,20 | 0,78 | 0,63 | 1,20 | 10,00 | 1,00 | 0,79 | 0,90 |
| A | P<19 | 1981-1990 | 1,25 | 1,02 | 0,82 | 1,40 | 10,00 | 1,00 | 0,97 | 0,95 |
| A | P<19 | 1991-Stage I | 1,29 | 1,55 | 1,25 | 1,68 | 10,00 | 1,00 | 1,39 | 1,00 |
| A | P<19 | Stage I | 1,29 | 1,55 | 1,25 | 1,68 | 10,00 | 1,00 | 1,39 | 1,00 |
| A | P<19 | Stage II | 1,29 | 1,55 | 1,25 | 1,68 | 10,00 | 1,00 | 1,39 | 1,00 |
| A | P<19 | Stage IIIA | 1,29 | 1,55 | 1,25 | 1,68 | 10,00 | 1,00 | 1,39 | 1,00 |
| A | P<19 | Stage IIIB | 1,29 | 1,55 | 1,25 | 1,68 | 10,00 | 1,00 | 1,39 | 1,00 |
| A | P<19 | Stage IV | 1,29 | 1,55 | 1,25 | 1,68 | 10,00 | 1,00 | 1,39 | 1,00 |
| B | 19<=P<37 | <1981 | 0,80 | 1,18 | 1,25 | 0,99 | 10,00 | 1,00 | 0,91 | 0,90 |
| B | 19<=P<37 | 1981-1990 | 0,80 | 1,34 | 1,42 | 1,17 | 10,00 | 1,00 | 1,29 | 0,96 |
| B | 19<=P<37 | 1991-Stage I | 1,47 | 1,64 | 1,74 | 1,43 | 10,00 | 1,00 | 1,29 | 1,03 |
| B | 19<=P<37 | Stage I | 1,47 | 1,64 | 1,74 | 1,43 | 10,00 | 1,00 | 1,29 | 1,03 |
| B | 19<=P<37 | Stage II | 1,31 | 2,54 | 5,21 | 2,50 | 10,00 | 1,00 | 2,00 | 1,03 |
| B | 19<=P<37 | Stage IIIA | 1,38 | 2,67 | 5,48 | 2,50 | 10,00 | 1,00 | 2,00 | 1,03 |
| B | 19<=P<37 | Stage IIIB | 1,38 | 2,67 | 5,48 | 2,50 | 10,00 | 1,00 | 2,00 | 1,03 |
| B | 19<=P<37 | Stage IV | 1,38 | 2,67 | 5,48 | 2,50 | 10,00 | 1,00 | 2,00 | 1,03 |
| C | 37<=P<56 | <1981 | 1,87 | 0,97 | 1,30 | 0,84 | 10,00 | 1,00 | 0,84 | 0,91 |
| C | 37<=P<56 | 1981-1990 | 1,67 | 1,16 | 1,56 | 0,95 | 10,00 | 1,00 | 1,26 | 0,96 |
| C | 37<=P<56 | 1991-Stage I | 1,25 | 1,54 | 2,08 | 1,12 | 10,00 | 1,00 | 1,89 | 1,02 |
| C | 37<=P<56 | Stage I | 1,19 | 2,20 | 5,21 | 2,95 | 10,00 | 1,00 | 2,13 | 1,02 |
| C | 37<=P<56 | Stage II | 1,45 | 3,30 | 7,81 | 2,27 | 10,00 | 1,00 | 2,00 | 1,02 |
| C | 37<=P<56 | Stage IIIA | 2,03 | 4,56 | 10,78 | 2,27 | 10,00 | 1,00 | 2,00 | 1,02 |
| C | 37<=P<56 | Stage IIIB | 2,03 | 4,56 | 10,78 | 2,27 | 10,00 | 1,00 | 17,78 | 1,02 |
| C | 37<=P<56 | Stage IV | 2,03 | 4,56 | 10,78 | 2,27 | 10,00 | 1,00 | 17,78 | 1,02 |
| D | 56<=P<75 | <1981 | 1,87 | 1,16 | 1,56 | 1,01 | 10,00 | 1,00 | 1,08 | 0,91 |
| D | 56<=P<75 | 1981-1990 | 1,67 | 1,45 | 1,95 | 1,18 | 10,00 | 1,00 | 1,51 | 0,96 |
| D | 56<=P<75 | 1991-Stage I | 1,25 | 1,93 | 2,60 | 1,45 | 10,00 | 1,00 | 3,78 | 1,02 |
| D | 56<=P<75 | Stage I | 1,19 | 3,30 | 7,81 | 4,33 | 10,00 | 1,00 | 4,25 | 1,02 |
| D | 56<=P<75 | Stage II | 1,45 | 4,40 | 10,42 | 3,33 | 10,00 | 1,00 | 2,00 | 1,02 |
| D | 56<=P<75 | Stage IIIA | 1,99 | 6,01 | 14,20 | 3,33 | 10,00 | 1,00 | 2,00 | 1,02 |
| D | 56<=P<75 | Stage IIIB | 2,69 | 7,73 | 18,27 | 3,33 | 10,00 | 1,00 | 17,78 | 1,02 |
| D | 56<=P<75 | Stage IV | 22,22 | 7,73 | 18,27 | 3,33 | 10,00 | 1,00 | 17,78 | 1,02 |
| E | 75<=P<130 | <1981 | 1,37 | 0,85 | 1,56 | 0,75 | 10,00 | 1,00 | 0,88 | 0,93 |
| E | 75<=P<130 | 1981-1990 | 1,22 | 1,06 | 1,95 | 0,87 | 10,00 | 1,00 | 1,23 | 0,97 |
| E | 75<=P<130 | 1991-Stage I | 1,08 | 1,41 | 2,60 | 1,07 | 10,00 | 1,00 | 3,08 | 1,02 |
| E | 75<=P<130 | Stage I | 1,14 | 3,30 | 7,81 | 3,33 | 10,00 | 1,00 | 3,50 | 1,02 |
| E | 75<=P<130 | Stage II | 1,35 | 3,39 | 10,42 | 3,33 | 10,00 | 1,00 | 1,50 | 1,02 |
| E | 75<=P<130 | Stage IIIA | 2,70 | 6,61 | 15,63 | 3,33 | 10,00 | 1,00 | 3,50 | 1,02 |
| E | 75<=P<130 | Stage IIIB | 3,10 | 7,73 | 18,27 | 3,33 | 10,00 | 1,00 | 31,11 | 1,02 |
| E | 75<=P<130 | Stage IV | 25,56 | 7,73 | 18,27 | 3,33 | 10,00 | 1,00 | 31,11 | 1,02 |
| F | 130<=P<560 | <1981 | 0,81 | 0,88 | 2,08 | 1,20 | 10,00 | 1,00 | 1,22 | 0,94 |
| F | 130<=P<560 | 1981-1990 | 1,16 | 1,32 | 3,13 | 1,20 | 10,00 | 1,00 | 1,38 | 0,98 |
| F | 130<=P<560 | 1991-Stage I | 1,29 | 2,64 | 6,25 | 1,20 | 10,00 | 1,00 | 2,75 | 1,02 |
| F | 130<=P<560 | Stage I | 1,21 | 4,40 | 10,42 | 3,33 | 10,00 | 1,00 | 2,70 | 1,02 |
| F | 130<=P<560 | Stage II | 1,35 | 3,39 | 10,42 | 2,33 | 10,00 | 1,00 | 2,00 | 1,02 |
| F | 130<=P<560 | Stage IIIA | 2,06 | 5,08 | 15,63 | 2,33 | 10,00 | 1,00 | 2,00 | 1,02 |
| F | 130<=P<560 | Stage IIIB | 3,89 | 5,94 | 18,27 | 2,33 | 10,00 | 1,00 | 8,89 | 1,02 |
| F | 130<=P<560 | Stage IV | 19,44 | 5,94 | 18,27 | 2,33 | 10,00 | 1,00 | 8,89 | 1,02 |

Quantifying the Adjustment

Danish NRMM inventory fleet and activity data for 2012 (Nielsen et al., 2014) is used to calculate the fuel consumption for diesel and gasoline 2-stroke/4-stroke engines for the simple methodology case, and further stratified into engine size and emission technology stage for the detailed methodology case.

Simple methodology - emission impact of using 1999 Guidebook instead of 2013 Guidebook factors

Table A1.6 NRMM emissions calculated with the Simple (Guidebook 1999) and Tier 1 (2013 Guidebook) methods for diesel machinery

|  |  | NOx | NMVOC | CH4 | CO | N2O | NH3 | TSP | Fuel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Tons | Tons | Tons | Tons | Tons | Tons | Tons | Tons |
| 1999 Guidebook | Agriculture | 20784 | 3004 | 70 | 6611 | 533 | 3 | 2425 | 413196 |
|  | Forestry | 187 | 24 | 1 | 54 | 5 | 0,03 | 20 | 3718 |
|  | Industry | 14649 | 2125 | 51 | 4743 | 390 | 2 | 1720 | 300186 |
|  | Total | 35620 | 5153 | 122 | 11408 | 928 | 5 | 4165 | 717101 |
| 2013 Guidebook | Agriculture | 14480 | 1391 | 23 | 4520 | 56 | 3 | 718 | 413196 |
|  | Forestry | 108 | 8 | 0 | 29 | 1 | 0 | 4 | 3718 |
|  | Industry | 9844 | 1016 | 17 | 3218 | 41 | 2 | 626 | 300186 |
|  | Total | 24431 | 2414 | 39 | 7767 | 97 | 6 | 1348 | 717101 |
| 1999:2013 Guidebook | Agriculture | 1,44 | 2,16 | 3,11 | 1,46 | 9,52 | 0,90 | 3,38 | 1,00 |
|  | Forestry | 1,73 | 3,22 | 5,18 | 1,85 | 9,55 | 0,89 | 5,44 | 1,00 |
|  | Industry | 1,49 | 2,09 | 3,09 | 1,47 | 9,61 | 0,91 | 2,75 | 1,00 |
|  | Total | 1,46 | 2,13 | 3,11 | 1,47 | 9,55 | 0,90 | 3,09 | 1,00 |

Important for diesel, Table A1.6 shows that close to 50 % more NOx and more than 200 % more PM is estimated for Denmark as an example by using 1999 Guidebook factors instead of 2013 Guidebook factors as the basis for the simple inventory.

Table A1.7 NRMM emissions calculated with the Simple (Guidebook 1999) and Tier 1 (2013 Guidebook) methods for gasoline 2-stroke and 4-stroke machinery

|  |  |  | NOx | NMVOC | CH4 | CO | N2O | NH3 | TSP | Fuel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Tons | Tons | Tons | Tons | Tons | Tons | Tons | Tons |
| 1999 Guidebook | Gasoline 2-stroke | Agriculture | 1 | 494 | 5 | 856 | 0,016 | 0,003 | no data | 800 |
|  |  | Forestry | 1 | 610 | 6 | 1126 | 0,016 | 0,003 | no data | 800 |
|  |  | Industry | 0 | 136 | 1 | 249 | 0,005 | 0,001 | no data | 226 |
|  |  | Household | 25 | 11692 | 117 | 22607 | 0,288 | 0,058 | no data | 14381 |
|  |  | Total | 29 | 12931 | 129 | 24837 | 0,324 | 0,065 | - | 16207 |
| 1999 Guidebook | Gasoline 4-stroke | Agriculture | 7 | 66 | 3 | 1332 | 0,063 | 0,004 | no data | 896 |
|  |  | Forestry | no data | no data | no data | no data | no data | no data | no data | 896 |
|  |  | Industry | 32 | 145 | 7 | 3988 | 0,267 | 0,017 | no data | 3343 |
|  |  | Household | 470 | 6463 | 323 | 128845 | 4,113 | 0,294 | no data | 58753 |
|  |  | Total | 509 | 6674 | 334 | 134165 | 4,443 | 0,315 | - | 63888 |
| 2013 Guidebook | Gasoline 2-stroke | All | 45 | 3925 | 36 | 10061 | 0,28 | 0,05 | 61 | 16207 |
|  | Gasoline 4-stroke | All | 455 | 1125 | 125 | 49217 | 3,77 | 0,26 | 10 | 63888 |
| 1999:2013 Guidebook | Gasoline 2-stroke | All | 0,64 | 3,29 | 3,63 | 2,47 | 1,18 | 1,33 | - | 1,00 |
|  | Gasoline 4-stroke | All | 1,12 | 5,93 | 2,67 | 2,73 | 1,18 | 1,23 | - | 1,00 |

Important for gasoline, Table A1.7 shows that for 2-stroke engines the 1999 Guidebook emissions of NMVOC and CO become 229 % and 147 % higher, compared with 2013 Guidebook based estimates for the simple inventory. For 4-stroke engines the emission differences become even higher; 493 % and 173 % in the corresponding cases.

Detailed methodology - emission impact of using 1999 Guidebook instead of using today’s state of the art emission factors

Table A1.8 NRMM emissions calculated with the detailed Guidebook 1999 method for diesel machinery

| kW size | Emission Level | Nox | NMVOC | CH4 | CO | N2O | NH3 | PM | Fuel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| kW |  | Tons | Tons | Tons | Tons | Tons | Tons | Tons | Tons |
| P<19 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | 1981-1990 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | 1991-Stage I | 269 | 59 | 1 | 120 | 1 | 0 | 38 | 6488 |
| P<19 | Stage I | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | Stage II | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | Stage IIIA | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | Stage IIIB | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | 1981-1990 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | 1991-Stage I | 260 | 47 | 1 | 119 | 1 | 0 | 37 | 6939 |
| 19<=P<37 | Stage I | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | Stage II | 673 | 61 | 1 | 228 | 4 | 0 | 41 | 27123 |
| 19<=P<37 | Stage IIIA | 810 | 74 | 1 | 288 | 5 | 0 | 52 | 34345 |
| 19<=P<37 | Stage IIIB | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 37<=P<56 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 37<=P<56 | 1981-1990 | 236 | 54 | 1 | 145 | 1 | 0 | 33 | 7536 |
| 37<=P<56 | 1991-Stage I | 988 | 127 | 2 | 386 | 3 | 0 | 69 | 22330 |
| 37<=P<56 | Stage I | 253 | 19 | 0 | 72 | 1 | 0 | 13 | 8549 |
| 37<=P<56 | Stage II | 493 | 35 | 1 | 197 | 3 | 0 | 18 | 23283 |
| 37<=P<56 | Stage IIIA | 259 | 19 | 0 | 145 | 2 | 0 | 13 | 17107 |
| 37<=P<56 | Stage IIIB | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 37<=P<56 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 56<=P<75 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 56<=P<75 | 1981-1990 | 521 | 95 | 2 | 260 | 2 | 0 | 61 | 16654 |
| 56<=P<75 | 1991-Stage I | 520 | 53 | 1 | 158 | 2 | 0 | 18 | 11754 |
| 56<=P<75 | Stage I | 160 | 8 | 0 | 31 | 1 | 0 | 4 | 5417 |
| 56<=P<75 | Stage II | 243 | 13 | 0 | 66 | 2 | 0 | 9 | 11471 |
| 56<=P<75 | Stage IIIA | 123 | 7 | 0 | 46 | 1 | 0 | 6 | 7969 |
| 56<=P<75 | Stage IIIB | 19 | 1 | 0 | 10 | 0 | 0 | 0 | 1675 |
| 56<=P<75 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 75<=P<130 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 75<=P<130 | 1981-1990 | 929 | 124 | 2 | 338 | 3 | 0 | 79 | 21092 |
| 75<=P<130 | 1991-Stage I | 1924 | 171 | 3 | 506 | 5 | 0 | 58 | 36886 |
| 75<=P<130 | Stage I | 313 | 15 | 0 | 58 | 1 | 0 | 8 | 9848 |
| 75<=P<130 | Stage II | 1949 | 111 | 2 | 562 | 13 | 1 | 75 | 95561 |
| 75<=P<130 | Stage IIIA | 1757 | 102 | 2 | 774 | 18 | 1 | 103 | 131637 |
| 75<=P<130 | Stage IIIB | 288 | 16 | 0 | 145 | 3 | 0 | 2 | 24734 |
| 75<=P<130 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 130<=P<560 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 130<=P<560 | 1981-1990 | 85 | 7 | 0 | 17 | 0 | 0 | 5 | 1777 |
| 130<=P<560 | 1991-Stage I | 1032 | 45 | 1 | 230 | 3 | 0 | 37 | 23043 |
| 130<=P<560 | Stage I | 31 | 1 | 0 | 6 | 0 | 0 | 1 | 1036 |
| 130<=P<560 | Stage II | 783 | 44 | 1 | 226 | 5 | 0 | 15 | 37668 |
| 130<=P<560 | Stage IIIA | 1285 | 74 | 1 | 566 | 13 | 1 | 38 | 94381 |
| 130<=P<560 | Stage IIIB | 222 | 21 | 0 | 185 | 4 | 0 | 3 | 30796 |
| 130<=P<560 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| All | All | 16424 | 1404 | 23 | 5888 | 98 | 6 | 837 | 717101 |

Table A1.9 NRMM emissions calculated with the detailed modern emission factors for diesel machinery

| kW size | Emission Level | Nox | NMVOC | CH4 | CO | N2O | NH3 | PM | Fuel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| kW |  | Tons | Tons | Tons | Tons | Tons | Tons | Tons | Tons |
| P<19 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | 1981-1990 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | 1991-Stage I | 345 | 91 | 1 | 201 | 8 | 0 | 53 | 6488 |
| P<19 | Stage I | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | Stage II | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | Stage IIIA | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | Stage IIIB | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| P<19 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | 1981-1990 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | 1991-Stage I | 371 | 75 | 1 | 166 | 9 | 0 | 47 | 6939 |
| 19<=P<37 | Stage I | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | Stage II | 857 | 151 | 5 | 555 | 35 | 0 | 81 | 27123 |
| 19<=P<37 | Stage IIIA | 1085 | 192 | 6 | 702 | 45 | 0 | 102 | 34345 |
| 19<=P<37 | Stage IIIB | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 19<=P<37 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 37<=P<56 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 37<=P<56 | 1981-1990 | 410 | 65 | 1 | 144 | 10 | 0 | 43 | 7536 |
| 37<=P<56 | 1991-Stage I | 1213 | 192 | 4 | 426 | 29 | 0 | 127 | 22330 |
| 37<=P<56 | Stage I | 297 | 42 | 2 | 210 | 11 | 0 | 27 | 8549 |
| 37<=P<56 | Stage II | 703 | 114 | 4 | 439 | 31 | 0 | 35 | 23283 |
| 37<=P<56 | Stage IIIA | 516 | 84 | 3 | 323 | 23 | 0 | 26 | 17107 |
| 37<=P<56 | Stage IIIB | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 37<=P<56 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 56<=P<75 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 56<=P<75 | 1981-1990 | 905 | 143 | 3 | 318 | 22 | 0 | 95 | 16654 |
| 56<=P<75 | 1991-Stage I | 639 | 101 | 2 | 224 | 16 | 0 | 67 | 11754 |
| 56<=P<75 | Stage I | 188 | 27 | 1 | 133 | 7 | 0 | 17 | 5417 |
| 56<=P<75 | Stage II | 346 | 56 | 2 | 216 | 15 | 0 | 17 | 11471 |
| 56<=P<75 | Stage IIIA | 241 | 39 | 2 | 150 | 11 | 0 | 12 | 7969 |
| 56<=P<75 | Stage IIIB | 51 | 8 | 0 | 32 | 2 | 0 | 3 | 1675 |
| 56<=P<75 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 75<=P<130 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 75<=P<130 | 1981-1990 | 1168 | 135 | 4 | 305 | 28 | 0 | 100 | 21092 |
| 75<=P<130 | 1991-Stage I | 2043 | 237 | 7 | 533 | 50 | 0 | 174 | 36886 |
| 75<=P<130 | Stage I | 348 | 49 | 2 | 189 | 13 | 0 | 27 | 9848 |
| 75<=P<130 | Stage II | 2573 | 368 | 18 | 1838 | 129 | 1 | 110 | 95561 |
| 75<=P<130 | Stage IIIA | 4658 | 658 | 25 | 2531 | 177 | 1 | 354 | 131637 |
| 75<=P<130 | Stage IIIB | 875 | 124 | 5 | 476 | 33 | 0 | 67 | 24734 |
| 75<=P<130 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 130<=P<560 | <1981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| 130<=P<560 | 1981-1990 | 101 | 9 | 0 | 21 | 2 | 0 | 8 | 1777 |
| 130<=P<560 | 1991-Stage I | 1306 | 118 | 5 | 272 | 32 | 0 | 100 | 23043 |
| 130<=P<560 | Stage I | 38 | 5 | 0 | 20 | 1 | 0 | 2 | 1036 |
| 130<=P<560 | Stage II | 1038 | 148 | 7 | 519 | 52 | 0 | 30 | 37668 |
| 130<=P<560 | Stage IIIA | 2601 | 372 | 19 | 1301 | 130 | 1 | 74 | 94381 |
| 130<=P<560 | Stage IIIB | 849 | 121 | 6 | 424 | 42 | 0 | 24 | 30796 |
| 130<=P<560 | Stage IV | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| All | All | 25765 | 3725 | 138 | 12669 | 964 | 6 | 1822 | 717101 |

The results from the Tables A1.8 and A1.9 show that in total 57 % more NOx and 118 % more PM is estimated for diesel NRMM with the detailed 1999 Guidebook method compared with the results based on modern emission factors.

References

Nielsen, O-K., Winther, M., Mikkelsen, M. H., Hoffmann, L., Nielsen, M., Gyldenkærne, S., Bruun, H. G. (2014). Annual Danish Informative Inventory Report to UNECE: Emission inventories from the base year of the protocols to year 2012. Aarhus University, DCE - Danish Centre for Environment and Energy. (Scientific Report from DCE - Danish Centre for Environment and Energy; Nr. 94).

IFEU 2004: Entwicklung eines Modells zur Berechnung der Luftschadstoffemissionen und des Kraftstoffverbrauchs von Verbrennungsmotoren in mobilen Geräten und Maschinen - Endbericht, UFOPLAN Nr. 299 45 113, pp. 122, Heidelberg.

IFEU 2009: Aktualisierung des Modells TREMOD - Mobile Machinery (TREMOD-MM), Endbericht; Institut für Energie- und Umweltforschung, pp. 48, Heidelberg.

IFEU 2014: Erarbeitung eines Konzepts zur Minderung der Umweltbelastung aus NRMM (non road mobile machinery) unter Berücksichtigung aktueller Emissionsfaktoren und Emissionsverminderungsoptionen für den Bestand, ISSN 1862-4804, Texte 24/2014, pp. 99, Heidelberg.

Appendix A2: Road Transport: Revisions to Methodologies, and revisions to EFs

Introduction

It is not anticipated that there will be new emissions sources (vehicle types or processes) from the road transport sector that have not been considered in the Guidebook when the ceilings were set in 1999.   Methodologies for different emission processes (hot exhaust, cold start, evaporative and non-exhaust emissions) were included for the relevant main vehicle types and fuels in the Guidebook (cars, light duty commercial vehicles, heavy goods vehicles, buses, coaches, mopeds and motorcycles). New technologies such as hybrid electric vehicles are not considered to be new sources.  Therefore, adjustment applications for the road transport sector are expected to be made for the following two circumstances:

Significant changes in emission factors – at the time when the ceilings were set, emission factors for (then) future vehicle emission technologies were based on emission reductions (relative to current vehicles) anticipated at the time.  These reductions were expected mainly on the basis of the relative change in the regulatory emission limit values (the Euro standards).  Therefore, it is natural to expect that emission factors for (then) future emission technologies would be reviewed (and revised if appropriate) as real-world emission measurements were made for these vehicles as they entered the fleet.  In particular, recent evidence on the real-world emission performance of diesel vehicles has indicated that some Euro standards have failed to introduce the reductions for NOx that were estimated prior to and during introduction into vehicle fleets, and thus emission factors have been increased since this to reflect the change in the scientific understanding.

Significant changes in methodology – many Parties use models to estimate road transport emissions and the methodology which underpins these models might have been updated over time to improve the accuracy of emission estimations.  One of the commonly used models is COPERT (COmputer Programme to Calculate Emissions from Road Transport) which uses the methodology adopted by the EMEP/EEA Emission Inventory Guidebook.  Since 1997, COPERT has evolved from COPERT II to COPERT 4 version 11.0 (September 2014 – the latest version to date).  The types of changes include extended vehicle classification, accounting for the effect of the use of improved fuel quality, the effect of vehicle age (mileage) on emissions, alternative approach for modelling evaporative emissions etc.  Moreover, these changes are often coupled by revision of the emission factors.  It should be noted that fixing errors or “bugs” in a model (which leads to any changes in emission results) is not a valid case for adjustment application as it does not represent changes in the scientific understanding of the emission source.

Changes to EFs and Methodologies

The COPERT methodology for the road transport sector, adopted by the EMEP/EEA Emission Inventory Guidebook, has evolved over time.  These changes include updates of emission factors for various pollutants and other changes such as an extension of vehicle classification (and thus inclusion of emission factors associated with these new vehicle sub-categories) to improve the accuracy of emission estimations for road transport.

The principal underlying approaches in COPERT have not changed since emission ceilings were set.  The main changes that have occurred have been to the emission factors for those vehicles in the vehicle fleet in 2010.  Modifications to details in the emission calculation methodologies (e.g. the procedure for cold start emissions) have not led to fundamental changes to the approach and are likely to have led to less significant changes to emission estimations.  Such method changes for road transport would be difficult to separate out from the changes in emission factors in an adjustment procedure.

So far as road transport is concerned, the ability of a Party to attain the emission ceiling is most likely to have been affected by a combination of emission factor changes and differences in activity data to that which had been anticipated when the ceilings were set.  In particular, the failure to attain ceilings for NOx will have been affected by changes to the emission factors for diesel vehicles combined with greater than originally expected dieselisation of the fleet.  This was demonstrated in an ETC/ACC technical paper (Ntziachristos and Papageorgiou, 2011) which showed the impacts of changing COPERT model versions (COPERT II to COPERT 4 version 8.0) and activity data in the context of meeting the EU NEC Directive ceiling commitments.  This study modelled fuel consumption and NOx emissions for four selected countries (Germany, France, Netherlands and Belgium) and found higher NOx emissions were estimated for the road transport sector than originally modelled by the RAINS model of IIASA (which underpinned the setting of 2010 ceilings).  This was mainly due to:

- NOx emission factors that did not follow the reductions as set by the emission standards for diesel passenger cars;

- Diesel fuel consumption (which is important for NOx) exceeding what was foreseen by RAINS.

The results of this study showed that it is the combination of different parameters which might affect the ability (to different extents) of a Party to attain the emission ceilings. For road transport, the exceedances in the past and the expected exceedances in the future are due to the underperforming diesel light duty vehicles with respect to NOx emissions. In such case, an adjustment approach should be based on the changes to the emission factors.

An increase in the dieselisation of the vehicle fleet (in this case a revision to the activity data) is not a valid case for adjustment because it represents an inability to predict future trends accurately, and does not represent a change in the understanding of the science.

Original EFs and methodologies

The RAINS model of IIASA was used as a basis for setting the 2010 ceilings for the 1999 Gothenburg Protocol.  Emission factors from COPERT II were used by RAINS to calculate road transport emissions and the references are as follows:

- RAINS Scenarios developed on Acidification and Ground-Level Ozone Control (Amann et al., 1998)

- COPERT II Computer Programme to calculate Emissions from Road Transport (Ahlvik et al., 1997)

- EMEP/CORINAIR Atmospheric emission inventory guidebook. Road Transport Chapter Version 3.1 – February 1999

Similarly, the GAINS model of IIASA was used a basis of setting the 2020 emission reduction targets and the following version of COPERT underpinned IIASA’s analysis:

- The Gains Baseline Emission Projections with a 2010 perspective (Wagner at el., 2010).

- COPERT 4 version 8.0

- EMEP/EEA Emission Inventory Guidebook, 2011 Update

If Parties use the COPERT methodology for their national emission inventories, these references will provide the starting point for an adjustment calculation. As an example, Table A2.1 shows relative NOx emissions levels used for key vehicle categories in the different projection activities. Relative emissions levels may slightly vary for each party due to national particularities (vehicle sizes, road patterns, ambient conditions, etc.).

Table A2.1: Relative emission levels (Euro 1/I assigned a value of 100) used in the original and revised NEC projections for key vehicle categories, and comparison with emission standards.

| Vehicle Type | Euro Standard | Original NECD | Revised NECD | Emission Standard |
| --- | --- | --- | --- | --- |
| Diesel HDV | Conventional | 149 | 146 |  |
|  | Euro I | 100 | 100 | 100 |
|  | Euro II | 85 | 109 | 87 |
|  | Euro III | 60 | 95 | 63 |
|  | Euro IV | 24 | 56 | 44 |
|  | Euro V | 24 | 32 | 25 |
|  | Euro VI |  | 6 | 5 |
| Vehicle Type | Euro Standard | Original NECD | Revised NECD | Emission Standard |
| Gasoline LDV | Conventional | 400 | 400 |  |
|  | Euro 1 | 100 | 100 | 100 |
|  | Euro 2 | 50 | 48 | 52 |
|  | Euro 3 | 26 | 20 | 36 |
|  | Euro 4 | 13 | 12 | 19 |
|  | Euro 5 | 13 | 10 | 16 |
|  | Euro 6 |  | 10 | 16 |
| Vehicle Type | Euro Standard | Original NECD | Revised NECD | Emission Standard |
| Diesel LDV | Conventional | 145 | 93 |  |
|  | Euro 1 | 100 | 100 | 100 |
|  | Euro 2 | 73 | 105 | 70 |
|  | Euro 3 | 59 | 116 | 38 |
|  | Euro 4 | 29 | 87 | 29 |
|  | Euro 5 | 29 | 63 | 29 |
|  | Euro 6 |  | 28 | 21 |

There are other sources of emissions factors used by Parties such as the Handbook of Emission Factors for Road Transport (HBEFA).  If other sources of EFs (and/or methodology) are used, Parties should provide the relevant information in their supporting document in accordance to Decision 2012/12, annex, para. 2(ii)(a)-(c), i.e.

- A description of the original emission factors, including a detailed description of the scientific basis upon which the emission factor was derived

- Evidence that the original emission factors were used for determining the emission reductions at the time when they were set

- A description of the updated emission factors, including detailed information on the scientific basis upon which the emission factor was derived

In fulfilling the requirement as laid out in Decision 2012/12, annex, para. 2(ii)(b), an example of such a circumstance in an adjustment application can be drawn from that made by Germany in 2014: the Party uses TREMOD (Transport Emission Estimation Model) to calculate emissions from the road transport sector.  The Party attempted to reproduce the NOx emission estimates as calculated by the RAINS model in 1999 (the original NECD scenarios) – this was done by using activity data and emission factors from the TREMOD 3.1 model (2002), which is the oldest version that is still available to the Party.  The difference in NOx results for 2010 were 4% compared to the values from the NCED original scenarios, which could be attributed to different aggregation and modelling system between RAINS and TREMOD.  Given this good agreement with the original NEC scenarios, the ERT considered this step had provided evidence that the emission factors and activity data used in TREMOD 3.1 were in line with the original emission factors (and activity data) that were used for determining the emission reductions at the time when they were set.

Quantifying the Adjustment

As the adjustment applications for road transport are essentially related to changes in emission factors, the following principle is used for quantifying the adjustments:

AY  =  ADY Current  x  (EFcurrent - EFOriginal)

AY is the value for the adjustment for inventory year Y

EFCurrent is the current EF used

EFOriginal is the original EF used when the ceilings were set

ADY Current is the current activity data for inventory year Y

Table A2.2 below provides a simple work template in applying the above principle in practice.  This can also be applied to the following scenarios:

- Scenario 1: Changes in model version underpinned by changes in EFs (e.g. from COPERT II to COPERT 4 or from original and current country own model)

- Scenario 2: Changes in methodology underpinned by changes in EFs (e.g. from COPERT II/4 to other source of emission factors such as HBEFA)

- Scenario 3: Moving to higher Tier of methodology underpinned by changes in EFs (e.g. from Tier 1 to Tier 3 COPERT 4).

Table A2.2: Adjustment Calculation Template for Road Transport

| A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- |
| Vehicle category (vehicle type, fuel type, Euro Standard) | ADY Current | EFOriginal | EFCurrent | Emissions based on current EF for Year Y (B x D) | Emissions based on original EF for Year Y (B x C) | AY (E – F) |
| e.g. Diesel car Pre-Euro 1 |  |  |  |  |  |  |
| e.g. Diesel car Euro 1 |  |  |  |  |  |  |
| and so on… |  |  |  |  |  |  |
| ∑ Total |  |  |  |  |  |  |

Column A will reflect the vehicle categorisation used by the Party, but a detailed categorisation for a Tier 3 methodological approach is shown here.  It can be further disaggregated by engine size or vehicle weight associated with the relevant vehicle and fuel type.  Columns C and D are implied emission factors (IEFs), i.e. weighted by activity over a range of speeds/engine size/vehicle weight.  The table can be expanded to show IEFs for different main road types (urban, rural and motorway) if appropriate.  The current EFs might have different or extended vehicle classifications compared to the original EFs.  In such case, emission factors should be weighted by the common (or current) disaggregation level.

Column B represents the current activity data assigned to each Euro Standard for inventory year Y.  This should correspond to the level of disaggregation chosen for Columns A, C and D.

Columns E, F and G combine the data collected to give the emissions results based on current and original emission factors, and the subsequent adjustment value for inventory year Y.   The overall adjustment for road transport will be the sum of the adjustments for the individual vehicle categories.

It is recommended that the Party provides such a table of information in their supporting document, in order to allow the expert reviewers to check that:

- The original and current (implied) emission factors by Euro standard used by the Party are broadly in line with the original and current Guidebook factors;

- The adjustments are accurate and correctly calculated.

It is important to specify the sources of emission factors and how the implied emission factors have been derived in the supporting document.  The units used for each column should be clearly stated.

If the application is made for more than one inventory year, the same calculations should be repeated following the same principle as outlined above; otherwise the Party need to state clearly how they have derived the adjustments for other inventory years.  For example, this might be done in a form of scaling factors to adjust the results for other inventory years.  The methodology (and any assumptions) used by the Party to calculate the final adjustments should be clearly stated in the supporting document to allow the expert reviewers to understand the rationales and approaches used.

A Summary of What the ERT Will Be Looking For

In accordance with the checklist, the expert reviewers will check whether documentation provided by the Party is complete and transparent and that the adjustments are accurate, correctly calculated and properly documented.  Thus, the following items will be required:

- A description of the original and updated emission factors (or methodology), including a detailed description of the scientific basis upon which the emission factor (or methodology) was derived.  The Party should clearly state the version and year of the Guidebook or any other source when referring to information from taken from the literature.

- Evidence that the original emission factors were used for determining the emission reductions at the time when they were set.

- A comparison of emission estimates made using the original and the updated emission factors (or methodologies), demonstrating that the change in emission factors (or methodologies) contributes to a Party being unable to meet its emission ceilings under the Gothenburg Protocol.

- A description of the approach used in quantifying the adjustments for the concerned years.

- In order for the expert reviewers to validate the quantification of the adjustments for the road transport sector, the Party should provide a table of both the original and current EFs (by Euro standards) and the corresponding current activity data for the concerned year(s).  Table A2.1 provides a working template.

- The rationale for deciding whether the changes in emission factors (or methodology) are significant.  This can be demonstrated by expressing the percentage changes in emissions of total road transport emissions as well as the changes in the national total for the concerned year(s).

References

Ahlvik, P., Eggleston, S., Gorissen, N., Hassel, D., Hickman, A.-J., Joumard, R., Ntziachristos, L., Rijkeboer, R., Samaras, Z., Zierock, K.-H., 1997. COPERT II Computer Programme to calculate Emissions from Road Transport. Methodology and Emission Factors. Technical Report No. 6. European Environment Agency, Copenhagen, Denmark, p. 55.

Amann, M., Bertok, I., Cofala, J., Gyarfas, F., Heyes, Ch., Klimont, Z., Makowski, M., Schöpp, W.,

Syri, S. (1998). Cost‐effective Control of Acidification and Ground‐Level Ozone. Part A:

Methodology and Databases. Sixth Interim Report, IIASA, Austria, p.111.

Wagner, F., Amann, M., Bertok, I., Cofala, J., Heyes, C., Klimont, Z., Rafaj, P., Schoepp, W. 2010. Baseline Emission Projections and Further cost-effective reductions of Air Pollution Impacts in Europe – A 2010 perspective

Appendix A3: Agriculture: New Sources and Revisions to EFs

Introduction

The methodologies for estimating emissions from the agriculture sector have undergone significant development since 1999. This can be observed from the changes to the agriculture chapters of the EMEP/EEA Emissions Inventory Guidebook - emission factors have been revised for some sources, new methodologies have been developed, and new pollutants have been added.

The following summarises the main changes that have been made between the versions of the Guidebook available at the time the ceilings were set, and currently.

New Sources/Pollutants

NH3 from Growing Crops: NH3 emissions from growing (or standing) crops is not included as a source in the EMEP/CORINAIR Guidebook that was available when the ceilings were set for the Gothenburg Protocol in 1999. The current version of the EMEP/EEA Emissions Inventory Guidebook refers to NH3 emissions from this source, but does not include default emission factors for estimating emissions, or provide a clearly defined methodology. Despite this, some countries do include this source in their emission inventories, by using country specific methodologies.

Where countries do include emissions from this source in their emissions inventory, it would be, in principle, a valid case for an emissions adjustment as a “new” source.

NMVOC: In 1999 the available guidance material for the agriculture sector provided methodologies for estimating NMVOC from crops only. Methodologies for estimating NMVOC emissions from animal manure and waste management systems were not available.

The current guidance recognises that there is still a high degree of uncertainty regarding NMVOC emissions from animal waste, and that available information requires review and improvement. As a result, few countries currently include NMVOC emissions from this source in their national emission inventory totals. But where this is the case, emissions from this source can in principle be considered a valid case for an adjustment application as a “new” source.

Particulate Matter: Methodologies for estimating emissions of PM10, PM2.5 and TSP have been added to the Guidebook since 1999. Consequently all sources of these pollutants may be considered new sources (although none of these pollutants are relevant for the 2010 emission ceilings under the Gothenburg Protocol).

Changes to EFs

NH3 Emissions from Synthetic Fertiliser: There have been a number of revisions to EFs for NH3 emissions arising from the application of synthetic fertilisers. The emission factors available in 1999 are presented in the following table (EMEP/CORINAIR, 2nd Edition, Group10, Table 5.1):

Table 5.1: Total NH3 emissions from cultures due to N fertiliser volatilisation, foliar emissions and decomposing vegetation. Values are kg NH3-N volatilised per kg fertiliser-N applied.

| Fertiliser type | Simpler Methodology | Group I | Group II | Group III |
| --- | --- | --- | --- | --- |
| Ammonium sulphate | 0.08 | 0.15 | 0.10 | 0.05 |
| Ammonium nitrate | 0.02 | 0.03 | 0.02 | 0.01 |
| Calcium ammonium nitrate | 0.02 | 0.03 | 0.02 | 0.01 |
| Anhydrous ammonia | 0.04 | 0.04 | 0.04 | 0.04 |
| Urea | 0.15 | 0.20 | 0.15 | 0.15 |
| Combined ammonium phosphates (generally di-ammonium phosphate) | 0.02 – 0.05 | 0.05 | 0.05 | 0.05 |
| Other complex NK, NPK fertilisers | 0.02 | 0.03 | 0.02 | 0.01 |
| Nitrogen solutions (mixed urea and ammonium nitrate) | 0.08 | 0.08 | 0.08 | 0.08 |

Groups I-III are defined as:

- Group I: Warm temperate countries with a large proportion of calcareous soils (e.g. Greece, Spain).

- Group II: Temperate and warm-temperate countries with some calcareous soils (or managed with soil pH >7), but with large areas of acidic soils (e.g. Italy, France, UK, Eire, Portugal, Belgium, Netherlands, Luxembourg).

- Group III Temperate and cool-temperate countries with largely acidic soils (e.g. Nordic countries, Germany, Switzerland, Austria).

The current version of the EMEP/EEA Emissions Inventory Guidebook explains that emission factors are likely to have some temperature dependence, but that more review of the literature is needed before anything definitive can be included in the Guidance. However, the emission factors are presented according to pH of the soil.

Table 3-2 Emission factors for total NH3 emissions from soils due to N fertiliser volatilisation and foliar emissions. Tier 2 EFi (kg NH3 kg N-1)

| Fertiliser type | Simpler Methodology | Low soil pH (=<7) | High soil pH (>7) |
| --- | --- | --- | --- |
| Ammonium nitrate (AN) | 0.081 | 0.037 | 0.037 |
| Anhydrous ammonia |  | 0.011 | 0.011 |
| Ammonium phosphate (MAP and DAP) |  | 0.113 | 0.293 |
| Ammonium sulphate (AS) |  | 0.013 | 0.270 |
| Calcium ammonium nitrate (CAN) |  | 0.022 | 0.022 |
| Calcium nitrate (CN) |  | 0.009 | 0.009 |
| Ammonium solutions (AN) |  | 0.037 | 0.037 |
| Ammonium solutions (Urea AN) |  | 0.125 | 0.125 |
| Urea ammonium sulphate (UAS) |  | 0.195 | 0.195 |
| Urea |  | 0.243 | 0.243 |
| Other NK and NPK |  | 0.037 | 0.037 |

These tables provide data with different stratification (and also in different units - kg NH3-N and kg NH3 respectively). But it is still evident that there are potential revisions both in an upward and downward direction should a Party be updating EFs from the original to the most recently available information.

Furthermore, it is possible that Parties have developed more sophisticated country specific methodologies for estimating emissions, which may take other parameters into account (such as temperature). If this is the case, then Parties will need to present transparent information to demonstrate that the EF (or implied EF) has increased from values originally used in the emissions inventory in 1999.

Quantifying the Adjustment

There are no sector specific requirements in quantifying adjustment values, and Parties should refer to the guidance provided in the main body of this report. However, it will be important that Parties focus on clearly presenting the quantified impacts of any revisions to EFs. This may not be straightforward if the resolution of the calculations, or the stratification of source sectors, has changed between the different versions of the inventory.

A Summary of What the ERT Will Be Looking For

In accordance with the guidance for Parties and Expert Reviewers, the expert reviewers will check whether documentation provided by the Party is complete and transparent and that the quantified adjustments are accurate, correctly calculated and properly documented.

For the agriculture sector, care must be taken to present information on NH3 emission factors in as transparent a way as possible. This is because there have been some fundamental changes in the methodologies that are in use now, compared to those available in 1999.

There are no other specific sector specific requirements for adjustments in the agriculture sector beyond the general guidance provided in the main body of this report. So the following will be required:

For new sources:

- Demonstration of the fact that the source was not included in the inventory in 1999, and that a methodology was not available to quantify the emission.

- Demonstration that emissions from this source are now included in the inventory, due to changes in the understanding of the science.

- Quantification of the adjustment, expected to be the value of the new source, and the rationale for deciding that this change is significant.

For revisions to EFs or methodologies:

- A description of the original and updated emission factors (or methodology), including a detailed description of the scientific basis upon which the emission factor (or methodology) was derived.  The Party should clearly state the version and year of the Guidebook or any other source when referring to information from taken from the literature.

- Evidence that the original emission factors were used for determining the emission reductions at the time when they were set.

- A comparison of emission estimates made using the original and the updated emission factors (or methodologies), demonstrating that the change in emission factors (or methodologies) contributes to a Party being unable to meet its emission ceilings under the Gothenburg Protocol.

- A description of the approach used in quantifying the adjustments for the concerned years.

- The rationale for deciding whether the changes in emission factors (or methodology) are significant.

Appendix B1: Party Template for Reporting a Quantified Adjustment

This is an Excel file, which is provided with this Guidance document.

Appendix C1: Expert Reviewers Checklist

This is an Excel file, which is provided with this Guidance document.

Appendix C2: Template for Summary Status Report (for the EMEP SB)

Review of adjustment applications (Year)

Report by the Centre on Emission Inventories and Projections

Summary The present report was prepared by the Centre on Emission Inventories and Projections in line with its mandate under the 2014–2015 workplan for the implementation of the Convention on Long-range Transboundary Air Pollution (ECE/EB.AIR/122/Add.2, item 1.7.1). The report provides a summary of the XXXX review of applications for adjustments to emission reduction commitments or inventories submitted by the following Parties to the Convention — XXX— in accordance with Executive Body decisions 2012/3, 2012/4 and 2012/12 (see ECE/EB.AIR/111/Add.1 and ECE/EB.AIR/113/Add.1).

Contents

Paragraphs	Page

Introduction		1–4	3

Etc.

Tables

1.	Applications for adjustments to emission reduction commitments or inventories in 2014	4

Etc.

Introduction

1.	The present report was prepared by the Centre on Emission Inventories and Projections (CEIP) of the Cooperative Programme for Monitoring and Evaluation of the Long-range Transmission of Air Pollutants in Europe (EMEP), in line with its mandate under the 2014–2015 workplan for implementation of the Convention on Long-range Transboundary Air Pollution (ECE/EB.AIR/122/Add.2, item 1.7.1). The report provides a summary of the XXXX review of applications for adjustments to emission reduction commitments or inventories submitted by Parties — in accordance with Executive Body decisions 2012/3, 2012/4 and 2012/12 (see ECE/EB.AIR/111/Add.1 and ECE/EB.AIR/113/Add.1).

2.	Parties applied for adjustments to their national emission inventories. The details of the applications are given in table YYY.

II.	Organization of the review

3.	As mandated by Executive Body decision 2012/12, applications for adjustments submitted by Parties are subject to an expert review. Technical coordination and support for the 2014 review was provided by CEIP, led by Ms. Katarina Mareckova (Slovakia). The members of the review team were selected from the review experts nominated by Parties to the CEIP roster of experts.

4.	The expert review team (ERT) was composed of a lead reviewer, Name (Country) and the following sectoral experts: Names (Countries), Sectors. ERT assessed the applications for adjustments and elaborated the relevant documentation.

5.	Each sector was reviewed by two independent sectorial experts. The findings were discussed with the lead reviewer and CEIP, and are summarized in the sections below.

III.	Assessment of applications for adjustments

A.	[Rejection Recommended] Country — Sector (NFR)

6.	ERT undertook a full and thorough assessment of Country application for an adjustment to its Pollutant emissions inventory for year-year for the Sector sector (Nomenclature for Reporting (NFR) source category NFR).

7.	ERT concluded that Country application for an adjustment to emissions from the Energy sector does not meet all the requirements laid out in Executive Body decision 2012/12. In particular, ERT notes that this application is not based on one of the three circumstances listed in paragraph 6 of decision 2012/3.

8.	Summary justification. Therefore, ERT recommends that the EMEP Steering Body reject this adjustment application.

B.	[Acceptance Recommended] Country — Sector (NFR)

9.	ERT undertook a full and thorough assessment of Country application for an adjustment to its Pollutant emissions inventory for year-year for the Sector sector (NFR source categories NFR).

10.	Source category NFR (Sector name): Summary of Party application/explanation.

11.	ERT concluded that the application does meet all of the requirements laid out in decision 2012/12, and therefore recommends that the EMEP Steering Body accept this adjustment application. The impact of the adjustment is summarized in table XXX below.

Table XXX
Impact of adjustment to Party Pollutant emissions inventory for the Sector sector for year-year

|  | Thousands of tonnes (ktonnes) of Pollutant |
| --- | --- |
| NFR source category(ies) | Year | Year | Year |
| NFR | Value | Value | Value |

12.	Country national total emissions will be below its ceilings in accordance with the Gothenburg Protocol from year onwards, if the proposed adjustments are accepted.

IV.	Conclusions and recommendations

13.	Table YYY provides a summary of the adjustment applications received, and the subsequent ERT recommendations to the EMEP Steering Body.

Table YYY
Adjustment applications received and expert review team recommendations

| Country | Sector | NFR | Pollutant | Years/Emissions reduction commitment | ERT recommendation |
| --- | --- | --- | --- | --- | --- |
| Country | Sector | NFR | Pollutant | Year-year | Accept/Reject |

14.	ERT has prepared country-specific reports containing detailed explanations of the findings. These explanations will be made available to the Parties and will also be published on the CEIP website before the XXXX session of the EMEP Steering Body in September XXXX. The country-specific reports will be available as informal documents for this meeting.

Appendix C3: Template for Country Report

Distr. GENERAL

CEIP/Adjustment RR/YYYY/country

DD/MM/YYYY

English ONLY

Review of the YYYY Adjustment Application 
by Country

Expert Review Team Report for the EMEP Steering Body

| Report title | Review of the YYYY Adjustment Application by Country |
| --- | --- |
| Country | Country |
| Report reference | CEIP/Adjustment RR/2014/Country |
| Date | DD/MM/YYYY |
| Version no | Final |

Expert Review Team

| Role | Sectors | Name |
| --- | --- | --- |
| Adjustment lead reviewer | All | Name |
| Primary expert reviewer | Sector1 | Name |
| Secondary expert reviewer | Sector 1 | Name |
| Primary expert reviewer | Sector 2 | Name |
| Secondary expert reviewer | Sector 2 | Name |
| Basic checks (Step 1 and 2) | N/A | Name (CEIP) |

Executive Summary

As mandated by Decision 2012/3 (ECE/EB.AIR/111/Add.1) of the Executive Body of the CLRTAP the nominated Expert Review Team undertook a detailed review of the adjustment application submitted by Country. The review was undertaken on behalf of the EMEP Steering Body and following the guidance published in the Annex to decision 2012/12 (ECE/EB.AIR/113/Add.1). COMMENT: May need to add reference to updated Guidance.

Each sector of the application was reviewed by two independent sectoral experts during MMM YYYY. The findings were discussed at the Review Team Meeting held DD/MMM/YYYY. The conclusions and recommendations for the EMEP SB are documented in this country report.

Table ES1 Summary Information on the Submitted Application

| Reasons for adjustment application (Decision 2012/3, para 6) | e.g. Road Transport 1.A.3.b: Significantly different EFs |
| --- | --- |
| Pollutants for which adjustment is applied for | e.g. NOx |
| Year(s) for which inventory adjustment is applied | e.g. 2010, 2011, 2012 |
| Date of notification of adjustment to the Secretariat | 15 February 2014 |
| Date of submission of supporting documentation | 15 March 2014 |

The Expert Review Team reviewed and evaluated the documents submitted by Country.

Example Text for recommending accept/reject from new sources and revised EFs etc.

Source X (NFR), NOx: The Expert Review Team conclude that emissions from Source X is a “new” source, because no methodology for quantifying emissions is included in the EMEP CORINAIR Emissions Inventory Guidebook, 1999 Edition. The Expert Review Team therefore recommends that the EMEP Steering Body ACCEPT this adjustment application from Country.

Source X (NFR), NOx: The Expert Review Team conclude that emissions from Source X cannot be considered as a “new” source, because an emission factor is included in the EMEP CORINAIR Emissions Inventory Guidebook, 1999 Edition. The Expert Review Team therefore recommends that the EMEP Steering Body REJECT this adjustment application from Country.

Road Transport (1.A.3.b), NOx: Country provided information that transparently presented “extraordinary” revisions to emission factors for NOx, and also clearly quantified the impact of the revisions to the emissions arising from the changes in EFs alone. The Expert Review Team has concluded that the application does meet all of the requirements laid out in Decision 2012/12 of the Executive Body of the CLRTAP, and therefore recommends that the EMEP Steering Body ACCEPT this adjustment application.

Road Transport (1.A.3.b), NOx: Country provided information that did not transparently presented “extraordinary” revisions to NOx emissions arising from the changes in EFs alone. The Expert Review Team has concluded that the application does therefore not meet all of the requirements laid out in Decision 2012/12 of the Executive Body of the CLRTAP, and recommends that the EMEP Steering Body REJECT this adjustment application.

- The following table provides a summary of the inventory adjustments that are accepted by the ERT.

Table ES2 Aggregated Sum of Accepted Inventory Adjustments (ktonnes)

| Pollutant |  | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| NOx | kt |  |  |  |  |  |  |  |  |

Table ES2 Impact of the Accepted Inventory Adjustments on National Emissions

| Poll. | GP Emission Commitment (kt) | 2010 Emission reported in 2014 (kt) | 2010 Emission (adjusted) (kt) | Difference (%) | 2012 Emission reported in 2014(kt) | 2012 Emissions (adjusted) (kt) | Difference (%) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| NOx |  |  |  |  |  |  |  |

- Country’s national total emissions will be below the Gothenburg Protocol ceilings from YYYY onwards, if the proposed adjustments are accepted.

Content

1	Introduction and Context	30

Figure 1: Flow Diagram/Decision Tree for the Review of Adjustment Applications	31

2	Review of Submitted Adjustments	32

2.1	Assessment of Formal Criteria	32

2.2	Road Transport  1.A.3.bi-iv   (NOx)	32

2.2.1	Assessment of Consistency with Requirements of Decision 2012/3	32

2.2.2	Assessment of the Quantification of the Impact of the Revision	33

3	Conclusions and Recommendations	34

Appendix A: Information Provided by the Party	34

Appendix B: References	35

Introduction and Context

Parties may apply to adjust their inventory data or emission reduction commitments if they are (or expect to be) in non-compliance with their emission reduction targets. However, in making an adjustment application, they must demonstrate that extraordinary circumstances have given rise to revisions to their emissions estimates. These extraordinary circumstances fall into three broad categories:

- Emission source categories are identified that were not accounted for at the time when the emission reduction commitments were set; or

- For a particular source, the emission factors used to estimate emissions for the year in which emissions reduction commitments are to be attained are significantly different to those used when the emission reduction commitments were set; or

- The methodologies used for determining emissions from specific source categories have undergone significant changes between the time when emission reduction commitments were set and the year they are to be attained.

Any Party submitting an application for an adjustment to its inventory is required to notify the Convention Secretariat through the Executive Secretary by 15 February at the latest. The supporting information detailed in Decision 2012/12 must be provided (either as part of the Informative Inventory Report, or in a separate report) by 15 March of the same year.

As mandated by Decision 2012/12 of the Executive Body of the CLRTAP, applications for adjustments that are submitted by Parties are subject to an expert review. Technical coordination and support to the review is provided by EMEP’s Centre on Emission Inventories and Projections (CEIP). The members of the review team are selected from the available review experts that Parties have nominated to the CEIP roster of experts. COMMENT: Update according to Updated Guidance being adopted by the EB.

The Expert Review Team (ERT) undertakes a detailed technical review of the adjustment application in cooperation with the EMEP technical bodies and makes a recommendation to the EMEP Steering Body on the acceptance or rejection of the application. The EMEP Steering Body then takes its decision on any adjustment application based on the outcome of the technical assessment completed by ERT.

The flow diagram below outlines the different stages of the technical review. The following sections of this report are structured in the same way, and describe in detail the findings of the ERT at each of the decision gates in the process.

# Figure 1: Flow Diagram/Decision Tree for the Review of Adjustment Applications

Review of Submitted Adjustments

Assessment of Formal Criteria

Country notified the Convention Secretariat through the Executive Secretary of its intention to apply for a new adjustment on 15/02/2014 and thus before the legal deadline of 15 February. All supporting information requested by Decision 2012/12 was provided as part of the Informative Inventory Report before the legal deadline of the 15 March of the same year that it is being submitted for review by the EMEP Steering Body (Decision 2012/12, annex, para 1). Additional documentation was provided during the review in response to requests from the ERT. Section 4 lists the documentation provided by the Party.

Country submitted an application for emissions adjustments to Pollutants for Years for the following sectors:

  - Sector name (NFR)

Country does not comply with its emission reduction commitments listed in Annex II of the Gothenburg Protocol (paragraph 1 of Decision 2012/3).

Country did not/provide information on the impact of the adjustment to its emission inventory, and the extent to which it would reduce the current exceedance and possibly bring the Party in compliance with emission reduction commitments.

Country did not/did include any information on when it will meet its emission ceiling for Pollutant in the supporting documentation.

EXAMPLE TEXT FOR ROAD TRANPORT

Road Transport  1.A.3.bi-iv   (NOx)

Assessment of Consistency with Requirements of Decision 2012/3

The Party made an application based on significant revisions to emission factors (EFs) and methodology.

The adjustment application requires the provision of specific supporting information to demonstrate compliance with specific criteria (Decision 2012/3, para. 6a-c). The ERT reviewed the supporting documentation (see section 4) with regard to these criteria and concluded that emission factors used to determine emission levels for the road transport source categories 1.A.3.bi-iv for the year in which emissions reduction commitments are to be attained are significantly different than the emission factors applied to these categories when emission reduction commitments were set.

The changes in EFs highlighted in the adjustment application arise because XXX add in a few words of technical explanation – in this case revisions to the Euro standards caused by the mismatch between test cycles and real world performanceXXX. The ERT therefore conclude that these changes were driven by a change in the understanding of the science relating to this source.

The ERT concludes that the provided supporting evidence does comply with the criteria presented in Decision 2012/3, and that the circumstances on which the adjustment is based relates to a change in the understanding of the science relating to this source.

The ERT reviewed the documentation that was provided to support the application (listed in section 4).

The supporting information provided by the Party on the revisions made to emission factors was considered to be complete. The ERT found that the information provided by the Party on the impact on NOx emissions from the revisions made to the emission estimates was fully transparent.

COMMENT: Paragraph for use if/when information was not transparent and they did not provide answers to questions with enough clarity:

The ERT found that the information provided was not fully transparent/complete, and asked the Party to provide further supporting information. The Party did provide clarifications on these issues (explain which “issues”). However the ERT concluded that this additional information did not fully explain the impact on the Pollutant emissions from the different revisions that had been made to the calculation methodology that resulted in the exceedance of the 2010 ceiling.

Assessment of the Quantification of the Impact of the Revision

The adjustment application process requires that the Party submit a quantification of the impact of the adjustment for which an application has been submitted. Table 1 provides an overview of the NOx adjustment applications of Country in the Road Transport sector.

Table 2.2a: Country’s NOx Adjustment Applications for Road Transport

| Reference number | Pollutant | NFR09 | unit | 2010 | 2011 | 2012 |
| --- | --- | --- | --- | --- | --- | --- |
| Country/YYYY/1a | NOx | 1.A.3.b i | kt |  |  |  |
| Country/YYYY/1b | NOx | 1.A.3.b ii | kt |  |  |  |
| Country/YYYY/1c | NOx | 1.A.3.b ii | kt |  |  |  |
|  | NOx | Total 1.A.3.b | kt |  |  |  |

The ERT reviewed the quantification of the emissions adjustments provided by the Country. The ERT concluded that the information provided was/was not accurate and error free, and is/is not consistent with the most up-to-date available EMEP/EEA Emissions Inventory Guidebook and scientific literature.

Conclusions and Recommendations

The ERT has undertaken a full and thorough assessment of the application for an  adjustment of Pollutant emissions inventory that was submitted by Country for the following source sectors:

  - Sector name (NFR)

The review of the submitted application followed the guidance provided in the Annex to Decision 2012/12 of the Executive Body of the CLRTAP (and updated Guidance reference if needed). The findings of the ERT are described in detail in Section 2 of this report.

Table 3a below provides a summary of the adjustment applications received from Country, and the subsequent recommendations made by the ERT to the EMEP SB.

Table 3a: Recommendations from the ERT to the EMEP SB

| Country | Sector | NFRs | Pollutant | Years | ERT Recommendation |
| --- | --- | --- | --- | --- | --- |
| Country | Sector Name | NFR | Pollutant | Years | Accept/Reject |
|  | Sector Name | NFR | Pollutant | Years | Accept/Reject |
|  | Sector Name | NFR | Pollutant | Years | Accept/Reject |

Country did/did not provide information on when it will meet its emission ceiling for NOx in the supporting documentation (add year here if provided).

Appendix A: Information Provided by the Party

Table A1a lists the information provided by the Party in its adjustment application. The information provided by Party can be downloaded from the CEIP website.

Table A1a: Information Provided by the Party

| Filename | Short description of content |
| --- | --- |

Optional: The ERT found it necessary to ask the Party for further information. The information provided is described in Table A1b below.

Table A1b: Additional Information Provided by the Party

| Filename | Short description of content |
| --- | --- |

Appendix B: References

Decision 2012/3 (ECE/EB.AIR/111/Add.1): Adjustments under the Gothenburg Protocol to emission reduction commitments or to inventories for the purposes of comparing total national emissions with them

Decision 2012/12 (ECE/EB.AIR/113/Add.1): Guidance for adjustments under the 1999 Protocol to Abate Acidification, Eutrophication and Ground-level Ozone to emission reduction commitments or to inventories for the purposes of comparing total national emissions with them

Data submitted by Parties applying for an adjustment: http://www.ceip.at/ms/ceip_home1/ceip_home/adjustments_gp/

EMEP/EEA Air Pollutant Emission Inventory Guidebook 2013
http://www.eea.europa.eu/publications/emep-eea-guidebook-2013

2009 Reporting Guidelines (ECE/EB.AIR/97) for Estimating and Reporting Emission Data under CLRTAP

The 1999 Gothenburg Protocol to Abate Acidification, Eutrophication and Ground-level Ozone
http://www.unece.org/env/lrtap/multi_h1.html

TFEIP

c/o Aether Ltd

Oxford Centre for Innovation

New Road

Oxford

OX1 1BY

01865 261466

www.aether-uk.com

# Footnotes

At a later stage the 1999 GB factors for N2O was regarded as unrealistical high, and was reduced by a factor of 10 in the 2013 GB

At a later stage 1999 GB factors for N2O was regarded as unrealistical high, and was reduced by a factor of 10 in the 2013 GB

2010 emission ceilings were set in 1999, and whilst the second Edition of the EMEP/CORINAIR Atmospheric Emissions Inventory Guidebook was published in 2000, the methodologies were available in 1999.

See www.ceip.at/fileadmin/inhalte/emep/pdf/2014/0_Roster_2014.pdf.

Throughout this report the term “emission reduction commitments” is used. However, the term “emission ceilings” is equally applicable.

The EMEP Steering Body, in conjunction with other appropriate technical bodies under EMEP, shall review the supporting documentation and assess whether the adjustment is consistent with the circumstances described in paragraph 6 of decision 2012/3 and the further guidance in decision 2012/12.

http://www.ceip.at/fileadmin/inhalte/emep/pdf/2014/0_Roster_2014.pdf

http://www.ceip.at/ms/ceip_home1/ceip_home/adjustments_gp/