## Slide 1
Transport-related Air Pollution in Germany
Nadja Richter
Umweltbundesamt (UBA)
Federal Environment Agency
Germany
Section I 3.1 Environment and Transport
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan

## Slide 2: FACT: air pollutants = health risk
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
 improving health protection means reducing traffic related emissions

## Slide 3: PM10 Emissions in Germany 2010 Share of Transport
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Chart: 
| Energy Industries | Manufacturing Industries and Construction | Commercial/Institutional | Residential | Other | Road | Rail | Inland Waterways | Air
2010 | 11.3526 | 3.2641 | 1.9917 | 32.0516 | 0.15297 | 12.966 | 0.23008 | 0.42845 | 0.11876
Source: National Trend Tables for the German Atmospheric Emission Reporting 1990-2010; TREMOD 5.25

## Slide 4: NOx Emissions in Germany 2010 Share of Transport
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Chart: 
| Energy Industries | Manufacturing Industries and Construction | Commercial/Institutional | Residential | Other | Road | Rail | Inland Waterways | Air
2010 | 300.0683 | 83.3043 | 21.4445 | 70.1838 | 6.0966 | 472.8206 | 12.4239 | 13.4081 | 7.5618
Source: National Trend Tables for the German Atmospheric Emission Reporting 1990-2010; TREMOD 5.25

## Slide 5: PM10 Emissions from Transport Germany 1960-2030
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Chart: 

## Slide 6: NOx Emissions from Transport Germany 1960-2030
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Chart: 

## Slide 7: EU Air Quality Targets Limit Values for the protection of human health
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Pollutant | Averaging period | Limit value* | Date by which value is to be met
NO2 | 1-hour | 200 µg/m3 not to be exceeded > 18 times a calendar year | 1 January 2010
NO2 | Calendar year | 40 µg/m3 (21 ppb) | 1 January 2010
PM10 | 24-hour | 50 µg/m3, not to be exceeded > 35 times a calendar year | 1 January 2005
PM10 | Calendar year | 40 µg/m3 | 1 January 2005
PM2.5 | Calendar year | 25 µg/m3 | 1 January 2015
* Limit Value is legally binding for member states.

## Slide 8: Air quality in Germany
  European air quality limit values for sulphur dioxide, carbon monoxide, benzene and lead no longer exceeded in Germany
  2011: excessive levels of particulate matter (PM10) and nitrogen dioxide (NO2) pollution
     daily averages for PM10 above the allowable limit at 42 % of stations near urban roads
     NO2 levels above the allowable yearly average at 57 % of stations near urban roads
Many German cities record significant instances of exceeding the tolerated limit!
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Source: http://www.umweltbundesamt.de/uba-info-presse-e/2012/pe12-006_how_good_is_air_quality_in_germany.htm

## Slide 9: Air quality in Germany - PM10
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
rural background | 0.028571 | 0.036364 | 0.054795 | 0.057471 | 0 | 0 | 0 | 0 | 0 | 0 | 0.015 | 0.015625
urban background | 0.03871 | 0.034091 | 0.16265 | 0.26 | 0.011173 | 0.015873 | 0.052083 | 0 | 0 | 0.0050761 | 0.025773 | 0.033784
urban traffic | 0.17347 | 0.27723 | 0.51351 | 0.67692 | 0.29104 | 0.37267 | 0.49738 | 0.18483 | 0.087379 | 0.17327 | 0.32 | 0.41875
Percentage share of measuring stations with concentration values exceeding the
PM10- daily mean values of 50 µg/m3, 2000 - 2011

## Slide 10: What can cities and municipalities do?
     set up clean air and action plans
  mix of individual measures (e.g. in transport):
-- promotion of cycling, walking and public transport,
-- appropriate town planning to reduce need of travel,
-- speed limits of 30 km/h on urban roads,
-- parking space cost management,
-- ban on heavy duty vehicles,
-- designate low emission zones (LEZs)
 47 designated LEZs in Germany
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan

## Slide 11: What are Low Emission Zones?
  restricted areas/roads
  often the most effective measure
  mainly fine particles, nitrogen dioxide and indirect ozone
  http://www.lowemissionzones.eu
Countries in Europe designating LEZs:
Austria, Czech Republic, Denmark, Hungary, Germany, Italy, Netherlands, Norway, Portugal, Sweden, United Kingdom
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan

## Slide 12: Low Emission Zones in Germany
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Emissions class | 1 | 2 | 3 | 4
badge | No badge |  |  | 
Requirement for diesel vehicles | Euro 1 or worse | Euro 2 or Euro 1 particulate filter | Euro 3 or Euro 2 particulate filter | Euro 4 or Euro 3 particulate filter
Requirement for petrol vehicles | Without a catalytic converter |  |  | Euro 1 with catalytic converter or better
(35. Federal Immission Control Ordinance – Marking Ordinance)

## Slide 13: LEZ road sign according to national framework
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
DE Euro 2 LEZ DE Euro 3 LEZ DE Euro 4 LEZ
Source: http://www.lowemissionzones.eu/countries-mainmenu-147/germany-mainmenu-61

## Slide 14: Low Emission Zones in Germany
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
LEZ scheduled
LEZ stage 1
ban on vehicles emission class 1
LEZ stage 2
ban on vehicles emission class 1+2
LEZ stage 3
ban on vehicles emission class 1+2+3

## Slide 15: Low Emission Zone in Berlin
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
source: http://www.lowemissionzones.eu/countries-mainmenu-147/germany-mainmenu-61
Abstract:
introduced in two stages (2008, 2010),
comprehending the central city area,
dimension: 88 km2,
more than 1,1 Mio. residents,
delimited by the local, railway loop
01.01.2008, first stage: all vehicles without badge are restricted from entering
01.01.2010, second stage: only vehicles with green badge are admitted

## Slide 16: Impact of LEZ in Berlin
Impact on vehicle fleet
    accelerated modernisation of vehicle fleet
    a high number of cars retrofitted with particulate filters
    Impact on air pollution
    -58 % or 173 t/yr Diesel particle emission reduction
    -20 % or 1517 t/yr NOX emission reduction
    PM10: annual mean -7 %, 10 excess days prevented
    NO2: annual mean -5 %
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan

## Slide 17: Problems?
Problems with measuring the effects of an LEZ
    traffic is only one source of PM and NOX
    measured data is weather-dependent
    additional dependence of the emissions on local traffic situation:
    traffic increase/decrease + congestion
     continued measurements are necessary
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan

## Slide 18: Combining measures!
Transport-related Air Pollution in Germany
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan

## Slide 19
THANK YOU FOR
YOUR ATTENTION
Nadja Richter nadja.richter@uba.de www.umweltbundesamt.de
THE PEP Workshop: Focus on Urban Central Asia – Almaty, Kazakhstan
Transport-related Air Pollution in Germany