|  | United Nations | ECE/TRADE/C/WP.7/GE.1/2010/14 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 12 July 2010 Original: English |

Economic Commission for Europe

Committee on Trade

# Working Party on Agricultural Quality Standards

Specialized Section on Standardization

of Fresh Fruit and Vegetables

Fifty-eighth session

Geneva, 1-3 November 2010

Item 5 of the provisional agenda

Review of the texts of the standards

aligned with the 2009 Standard Layout

UNECE Standard FFV-25 concerning the marketing and commercial quality control
of onions

Submitted by the secretariat

I.	Definition of produce

This standard applies to onions of varieties (cultivars) grown from Allium cepa Cepa group to be supplied to the consumer in the natural state, green onions with full leaves and onions for industrial processing being excluded.

II.	Provisions concerning quality

The purpose of the standard is to define the quality requirements for onions at the export-control stage after preparation and packaging.

However, if applied at stages following export, products may show in relation to the requirements of the standard:

a slight lack of freshness and turgidity

a slight deterioration due to their development and their tendency to perish.

The holder/seller of products may not display such products or offer them for sale, or deliver or market them in any manner other than in conformity with this standard. The holder shall be responsible for observing such conformity.

A.	Minimum requirements

In all classes, subject to the special provisions for each class and the tolerances allowed, the bulbs must be:

intact

sound; produce affected by rotting or deterioration such as to make it unfit for consumption is excluded

clean, practically free of any visible foreign matter

free from damage due to frost

sufficiently dry for the intended use (in the case of onions for storing, at least the first two outer skins and the stem must be fully dried)

without hollow or tough stems

practically free from pests

free from damage caused by pests affecting the flesh

free of abnormal external moisture

free of any foreign smell and/or taste.

In addition, the stems must be twisted or clean cut and must not exceed 6 cm in length (except for stringed onions).

The development and condition of the onions must be such as to enable them:

to withstand transportation and handling

to arrive in satisfactory condition at the place of destination.

B.	Classification

The onions are classified in two classes, as defined below:

(i)	Class I

Onions in this class must be of good quality.  They must be characteristic of the variety and/or commercial type.

The bulbs must be:

firm and compact

free from externally visible shoots

free from swelling caused by abnormal vegetative development

practically free of root tufts; however, for onions harvested before complete maturity, root tufts are allowed.

The following slight defects, however, may be allowed, provided these do not affect the general appearance of the produce, the quality, the keeping quality and presentation in the package:

a slight defect in shape

slight defects in colouring

light staining that does not affect the outer skin, provided it does not cover more than one fifth of the bulb’s surface

superficial cracks in and partial absence of the outer skins, provided the flesh is protected.

(ii)	Class II

This class includes onions that do not qualify for inclusion in Class I, but satisfy the minimum requirements specified above.

The bulbs must be reasonably firm.

The following defects may be allowed, provided the onions retain their essential characteristics as regards the quality, the keeping quality and presentation:

defects in shape

defects in colouring

traces due to rubbing

slight marking caused by parasites or disease

small healed cracks

slight healed bruising

root tufts

stains that do not affect the outer skin, provided they do not cover more than half the bulb’s surface

cracks in the outer skins and partial absence of over a maximum of one third of the bulb’s surface, provided the flesh is not damaged.

III.	Provisions concerning sizing

Size is determined by the maximum diameter of the equatorial section.

The minimum diameter is fixed at 10 mm.

To ensure uniformity in size, the range in size between produce in the same package shall not exceed:

5 mm where the diameter of the smallest onion is 10 mm and over but under 20 mm.  However, where the diameter of the onion is 15 mm and over but under 25 mm, the difference may be 10 mm

15 mm where the diameter of the smallest onion is 20 mm and over but under 40 mm

20 mm where the diameter of the smallest onion is 40 mm and over but under 70 mm

30 mm where the diameter of the smallest onion is 70 mm or over.

IV.	Provisions concerning tolerances

At all marketing stages, tolerances in respect of quality and size shall be allowed in each lot for produce not satisfying the requirements of the class indicated.

A.	Quality tolerances

(i)	Class I

A total tolerance of 10 per cent, by number or weight, of onions not satisfying the requirements of the class but meeting those of Class II is allowed. Within this tolerance not more than 1 per cent in total may consist of produce satisfying neither the requirements of Class II quality nor the minimum requirements, or of produce affected by decay.

(ii)	Class II

A total tolerance of 10 per cent, by number or weight, of onions satisfying neither the requirements of the class nor the minimum requirements is allowed. Within this tolerance not more than 2 per cent in total may consist of produce affected by decay.

In addition, a maximum tolerance of 10 per cent, by number or weight, of bulbs showing early evidence of externally visible shoot growth is allowed.

B.	Size tolerances

For all classes: a total tolerance of 10 per cent, by number or weight, of onions not satisfying the size identified, but with a diameter of no more than 20 per cent below or above it.

V.	Provisions concerning presentation

A.	Uniformity

The contents of each package (or lot for produce presented in bulk in the transport vehicle) must be uniform and contain only onions of the same origin, variety or commercial type, quality and size.

However, a mixture of onions of distinctly different colours and/or commercial types may be packed together in a sales package, provided they are uniform in quality and, for each colour and/or commercial type concerned, in origin.

The visible part of the contents of the package (or lot for produce presented in bulk in the transport vehicle) must be representative of the entire contents.

B.	Packaging

Onions must be packed in such a way as to protect the produce properly.

The materials used inside the package must be clean and of a quality such as to avoid causing any external or internal damage to the produce.  The use of materials, particularly of paper or stamps bearing trade specifications, is allowed, provided the printing or labelling has been done with non-toxic ink or glue.

Stickers individually affixed to the produce shall be such that, when removed, they neither leave visible traces of glue, nor lead to skin defects.

Packages (or lots for produce presented in bulk in the transport vehicle) must be free of all foreign matter.

VI.	Provisions concerning marking

Each package must bear the following particulars, in letters grouped on the same side, legibly and indelibly marked, and visible from the outside.

For onions transported in bulk (direct loading into a transport vehicle) these particulars must appear on a document accompanying the goods, and attached in a visible position inside the transport vehicle.

A.	Identification

Packer and/or dispatcher/shipper:

Name and physical address (e.g. street/city/region/postal code and, if different from the country of origin, the country) or a code mark officially recognized by the national authority.

B.	Nature of produce

"Onions" if the contents are not visible from the outside.

“Mixture of onions”, or equivalent denomination, in the case of a mixture of distinctly different colours and/or commercial types of onions. If the produce is not visible from the outside, the colours or commercial types and the quantity of each in the package must be indicated.

C.	Origin of produce

Country of origin and, optionally, district where grown, or national, regional or local place name.

In the case of a mixture of distinctly different colours and/or commercial types of onions of different origins, the indication of each country of origin shall appear next to the name of the colour and/or commercial type concerned.

D.	Commercial specifications

Class

Size expressed by minimum and maximum diameters

E.	Official control mark (optional)

Adopted 1961

Last revised 2010

# Footnotes

The sales unit should be designed to be purchased in its entirety.

According to the Geneva Protocol, footnote 2, “Package units of produce prepacked for direct sale to the consumer shall not be subject to these marking provisions but shall conform to the national requirements.  However, the markings referred to shall in any event be shown on the transport packaging containing such package units”.

The national legislation of a number of countries requires the explicit declaration of the name and address. However, in the case where a code mark is used, the reference “packer and/or dispatcher (or equivalent abbreviations)” has to be indicated in close connection with the code mark, and the code mark should be preceded by the ISO 3166 (alpha) country/area code of the recognizing country, if not the country of origin.