agenda item 5 (a)			UN/SCETDG/18/INF.25

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Reference document ST/SG/AC.10/C.3/2000/48

UN 1153 Ethylene glycol diethyl ether

Transmitted by the expert from Germany

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions – if necessary state "not known" or "not applicable" –  If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

# Section 1.	SUBSTANCE IDENTITY

1.1	Chemical name	Ethylene glycol diethyl ether

1.2	Chemical formula	C6H14O2

1.3	Other names/synonyms	1,2-Diethoxyethane, Diethylcellosolve, Diethylglycol

1.4.1	UN Number    1153

1.4.2	CAS number	629-14-1

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2() 	Ethylene glycol diethyl ether

1.5.2	class/division	   3		subsidiary risk(s)   no

packing group	   II

1.5.3	proposed special provisions, if any		 no

1.5.4	proposed packing instruction(s)		 no

# Section 2.	PHYSICAL PROPERTIES

2.1	Melting point or range	-74 °C

2.2	Boiling point or range	 120-122 °C

2.3	Relative density at:

2.3.1	15 °C	not known

2.3.2	20 °C	0.84

2.3.3	50 °C	not known

2.4	Vapour pressure at:

2.4.1	50 °C	  6.5 kPa

2.4.2	65 °C	12.8 kPa

2.5	Viscosity at 20 °C		0.77 mm2/s

2.6	Solubility in water at 20 °C	slightly	g/100 ml

2.7	Physical state at 20 °C (2.2.1.1()	solid / liquid / gas

  - Appearance at normal carriage temperatures, including colour and odour

colourless liquid, ether-like odour

2.9	Other relevant physical properties	not known

# Section 3.	FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.3()	19 °C closed cup (ISO 3679)

3.1.2	Is combustion sustained? (2.3.1.2()	yes / no

3.2	Autoignition temperature 	175 °C

3.3	Flammability range (LEL/UEL) 	1.2 / 11.9 % by volume (estimated)

3.4	Is the substance a flammable solid? (2.4.2)	yes / no

3.4.1	If yes, give details ...

# Section 4.	CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity?		yes / no

If yes, state

4.1.1	Inhibitor/stabilizer used ...

4.1.2	Alternative method ...

4.1.3	Time effective at 55 °C ...

4.1.4	Conditions rendering it ineffective ...

4.2	Is the substance an explosive according to paragraph 2.1.1(? 	yes / no

4.2.1	If yes, give details ...

4.3	Is the substance a desensitized explosive? (2.4.2.4()	yes / no

4.3.1	If yes, give details ...

4.4	Is the substance a self-reactive substance? (2.4.1()	yes / no

If yes, state

4.4.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.4.2.3.4()		yes / no

4.4.2	proposed control temperature for a 50 kg package ... °C

4.4.3	proposed emergency temperature for a 50 kg package ... °C

4.5	Is the substance pyrophoric? (2.4.3()				yes / no

4.5.1	If yes, give details ...

4.6	Is the substance liable to self-heating? (2.4.3()		yes / no

4.6.1	If yes, give details ...

4.7	Is the substance an organic peroxide (2.5.1()		yes / no

If yes state

4.7.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.5.3.4.1()		yes / no

4.7.2	proposed control temperature for a 50 kg package ... °C

4.7.3	proposed emergency temperature for a 50 kg package ... °C

4.8	Does the substance in contact with water emit flammable

gases (2.4.4()					yes / no

4.8.1	If yes, give details ...

4.9	Does the substance have oxidizing properties (2.5.1)	yes / no

4.9.1	If yes, give details ...

4.10	Corrosivity (2.8() to:

4.10.1	mild steel 		less than 6.25 mm/year at 55 °C

4.10.2	aluminium 		less than 6.25 mm/year at 55 °C

4.10.3	other packing materials

(specify) no		... mm/year at ...

...		... mm/year at ...

  - Other relevant chemical properties 	not known

# Section 5.	HARMFUL BIOLOGICAL EFFECTS

5.1	LD 50, oral (2.6.2.1.1()               4390	mg/kg	Animal species:  rat

5.2	LD 50, dermal (2.6.2.1.2()          no relevant toxicity expected

5.3	LC 50, inhalation (2.6.2.1.3()      38.64 mg/litre	Exposure time 4 hours

or         8000 ml/m3	Animal species:  rat

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.3()    12 500 ml/m3

5.5	Skin exposure (2.8() results	not appreciably irritating

Exposure time ...				hours/minutes

Animal species	guinea pigs, rabbits, dogs

5.6	Other data ...

5.7	Human experience	no reported instances of any adverse effects

(Petty´s Industrial Hygiene & Toxicology, vol 2C, 1982)

# Section 6.	SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents)

suitable are dry chemical powder, carbon dioxide, water spray and appropriate foam

    - Spillage

Absorb on sand or vermiculit and place in closed containers for disposal; ventilate area and wash spill site after material pickup is complete

6.2	Is it proposed to transport the substance in:

6.2.1	Intermediate Bulk Containers (6.5()		yes / no

6.2.2	Portable tanks (6.7()				yes / no

If yes, give details in Sections 7. and/or 8.

Section 7.	INTERMEDIATE BULK CONTAINERS (IBCs)

(only complete if yes in 6.2.1)

7.1	Proposed type(s)   IBC02

Section 8.	MULTIMODAL TANK TRANSPORT

(only complete if yes in 6.2.2)

  - Description of proposed tank (including IMO tank type if known)   T4

T2 (Amdt. 29-98)     [ T4 (Amdt. 30-2000) ]

8.2.	Minimum test pressure 		2.65 bar

8.3	Minimum shell thickness  	see 6.7.2.4.2 ( (nothing special)

8.4	Details of bottom openings, if any 	see 6.7.2.6.3 ( (with 3 closures)

8.5	Pressure relief arrangements 	normal

8.6	Degree of filling 		97 %

8.7	Unsuitable construction materials 	no

____________