#### UNITED

# NATIONS

Distr.

# GENERAL

# TRANS/WP.15/AC.1/80/Add.4

# 5 April 2000

# ENGLISH

Original: ENGLISH AND FRENCH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

REPORT OF THE SESSION

Held in Geneva from 13 to 24 March 2000

Addendum 4

Chapter 4.2 of the draft restructured ADR

USE OF PORTABLE TANKS

Text adopted by the Joint Meeting

The secretariat reproduces hereunder the text adopted by the Joint Meeting for Chapter 4.2 of the restructured ADR. The corresponding text of Chapter 4.2 of RID will be reproduced by the Central Office for International Carriage by Rail (OCTI) under the symbol OCTI/RID/GT/III/2000-A/Add.4.

GE.00-

CHAPTER 4.2

USE OF PORTABLE TANKS

4.2.1	General provisions for the use of portable tanks for the carriage of substances of Classes 3 to 9

4.2.1.1	This section provides general requirements applicable to the use of portable tanks for the carriage of substances of Classes 3, 4.1, 4.2, 4.3, 5.1, 5.2, 6.1, 6.2, 7, 8 and 9.  In addition to these general requirements, portable tanks shall conform to the design, construction, inspection and testing requirements detailed in 6.7.2.  Substances shall be carried in portable tanks conforming to the applicable portable tank instruction identified in Column 10 of the table A of Chapter 3.2 and described in 4.2.4.2.6  (T1 to T23) and the portable tank special provisions assigned to each substance in Column 11 of table A of Chapter 3.2.

4.2.1.2	During carriage, portable tanks shall be adequately protected against damage to the shell and service equipment resulting from lateral and longitudinal impact and overturning.  If the shell and service equipment are so constructed as to withstand impact or overturning it need not be protected in this way.  Examples of such protection are given in 6.7.2.17.5.

4.2.1.3	Certain substances are chemically unstable. They are accepted for carriage only when the necessary steps have been taken to prevent their dangerous decomposition, transformation or polymerization during carriage.  To this end, care shall in particular be taken to ensure that shells do not contain any substances liable to promote these reactions.

4.2.1.4	The temperature of the outer surface of the shell excluding openings and their closures or of the thermal insulation shall not exceed 70 °C during carriage.  When dangerous goods are carried at elevated temperatures in either liquid or solid state, the shell shall be thermally insulated to meet this condition.

4.2.1.5	Empty portable tanks not cleaned and not gas-free shall comply with the same requirements as portable tanks filled with the previous substance.

4.2.1.6	Substances shall not be carried in adjoining compartments of shells when they may react dangerously with each other and cause:

(a)	Combustion and/or evolution of considerable heat;

(b) 	Evolution of flammable, toxic or asphyxiant gases;

(c) 	The formation of corrosive substances;

(d) 	The formation of unstable substances;

(e) 	Dangerous rise in pressure.

4.2.1.7	The design approval certificate, the test report and the certificate showing the results of the initial inspection and test for each portable tank issued by the competent authority or its authorized body shall be retained by the authority or body and the owner.  Owners shall be able to provide this documentation upon the request of any competent authority.

4.2.1.8	Unless the name of the substance(s) being carried appears on the metal plate described in 6.7.2.20.2, a copy of the certificate specified in 6.7.2.18.1 shall be made available upon the request of a competent authority or its authorized body and readily provided by the consignor, consignee or agent, as appropriate.

4.2.1.9	Filling ratios

4.2.1.9.1	Prior to filling, the consignor shall ensure that the appropriate portable tank is used and that the portable tank is not loaded with substances which in contact with the materials of the shell, gaskets, service equipment and any protective linings, are likely to react dangerously with them to form dangerous products or appreciably weaken the material.  The consignor may need to consult the manufacturer of the substance in conjunction with the competent authority for guidance on the compatibility of the substance with the portable tank materials.

4.2.1.9.1.1	Portable tanks shall not be filled above the extent provided in 4.2.1.9.2 to 4.2.1.9.6. The applicability of 4.2.1.9.2, 4.2.1.9.3 or 4.2.1.9.5.1 to individual substances is specified in the applicable portable tank special provisions in 4.2.4.3 and Column 11 of the table A of Chapter 3.2.

4.2.1.9.2	The maximum degree of filling (in %) for general use is determined by the formula:

4.2.1.9.3	The maximum degree of filling (in %) for liquids of Class 6.1 and Class 8, in packing groups I and II, and liquids with an absolute vapour pressure of more than 175 kPa (1.75 bar) at 65 °C, is determined by the formula:

4.2.1.9.4	In these formulae, (  is the mean coefficient of cubical expansion of the liquid between the mean temperature of the liquid during filling (tf) and the maximum mean bulk temperature during carriage (tr) (both in  °C). For liquids carried under ambient conditions ( could be calculated by the formula:

in which d15 and d50 are the densities of the liquid at 15 °C and 50 °C, respectively.

4.2.1.9.4.1	The maximum mean bulk temperature (tr) shall be taken as 50 °C except that, for journeys under temperate or extreme climatic conditions, the competent authorities concerned may agree to a lower or require a higher temperature, as appropriate.

4.2.1.9.5	The requirements of 4.2.1.9.2 to 4.2.1.9.4.1 do not apply to portable tanks which contain substances maintained at a temperature above 50 °C during carriage (e.g. by means of a heating device).  For portable tanks equipped with a heating device, a temperature regulator shall be used to ensure the maximum degree of filling is not more than 95% full at any time during carriage.

4.2.1.9.5.1	The maximum degree of filling (in %) for liquids carried under elevated temperature conditions is determined by the formula:

in which df and dr are the densities of the liquid at the mean temperature of the liquid during filling and the maximum mean bulk temperature during carriage respectively.

4.2.1.9.6	Portable tanks shall not be offered for carriage:

(a)	With a degree of filling, for liquids having a viscosity less than 2680 mm2/s at 20 °C or maximum temperature of the substance during carriage in the case of the heated substance, of more than 20% but less than 80% unless the shells of portable tanks are divided, by partitions or surge plates, into sections of not more than 7500 litres capacity;

(b) 	With residue of goods previously carried adhering to the outside of the shell or service equipment;

(c) 	When leaking or damaged to such an extent that the integrity of the portable tank or its lifting or securing arrangements may be affected; and

(d) 	Unless the service equipment has been examined and found to be in good working order.

4.2.1.9.7	Forklift pockets of portable tanks shall be closed off when the tank is filled. This provision does not apply to portable tanks which according to 6.7.3.13.4 need not be provided with a means of closing off the forklift pockets.

4.2.1.10		Additional provisions applicable to the carriage of Class 3 substances in portable tanks

4.2.1.10.1	 All portable tanks intended for the carriage of flammable liquids shall be closed and be fitted with relief devices in accordance with 6.7.2.8 to 6.7.2.15.

4.2.1.10.1.1 For portable tanks intended for use only on land, the pertinent regulations governing transport by land may allow open venting systems.

4.2.1.11	Additional provisions applicable to the carriage of Classes 4.1, 4.2 or 4.3 substances (other than Class 4.1 self-reactive substances) in portable tanks

[reserved]

Note: For Class 4.1 self-reactive substances, see 4.2.1.13.1.

4.2.1.12		Additional provisions applicable to the carriage of Class 5.1 substances in portable tanks

[reserved]

4.2.1.13		Additional provisions applicable to the carriage of Class 5.2 substances and Class 4.1 self-reactive substances in portable tanks

4.2.1.13.1	Each substance shall have been tested and a report submitted to the competent authority of the country of origin for approval.  Notification thereof shall be sent to the competent authority of the country of destination.  The notification shall contain relevant transport information and the report with test results.  The tests undertaken shall include those necessary:

(a)	To prove the compatibility of all materials normally in contact with the substance during carriage;

(b)	To provide data for the design of the pressure and emergency relief devices taking into account the design characteristics of the portable tank.

Any special requirement necessary for safe transport of the substance shall be clearly described in the report.

4.2.1.13.2	The following requirements apply to portable tanks intended for the carriage of Type F organic peroxides or Type F self-reactive substances with a Self-Accelerating Decomposition Temperature (SADT) of 55 °C or more.  In case of conflict these requirements prevail over those specified in section  6.7.2.  Emergencies to be taken into account are self-accelerating decomposition of the substance and fire-engulfment as described in 4.2.1.13.8.

4.2.1.13.3	The additional requirements for carriage of organic peroxides or self-reactive substances with a SADT less than 55 °C in portable tanks shall be specified by the competent authority of the country of origin.  Notification thereof shall be sent to the competent authority of the country of destination.

4.2.1.13.4	The portable tank shall be designed for a test pressure of at least 0.4 MPa (4 bar).

4.2.1.13.5	Portable tanks shall be fitted with temperature sensing devices.

4.2.1.13.6	Portable tanks shall be fitted with pressure-relief devices and emergency-relief devices.  Vacuum-relief devices may also be used.  Pressure-relief devices shall operate at pressures determined according to both the properties of the peroxide and the construction characteristics of the portable tank. Fusible elements are not allowed in the shell.

4.2.1.13.7	The pressure-relief devices shall consist of spring-loaded valves fitted to prevent significant build-up within the portable tank of the decomposition products and vapours released at a temperature of 50 °C. The capacity and start-to-discharge pressure of the relief valves shall be based on the results of the tests specified in 4.2.1.13.1.  The start-to-discharge pressure shall, however, in no case be such that liquid would escape from the valve(s) if the portable tank were overturned.

4.2.1.13.8	The emergency-relief devices may be of the spring-loaded or frangible types, or a combination of the two, designed to vent all the decomposition products and vapours evolved during a period of not less than one hour of complete fire-engulfment as calculated by the following formula:

where:

q	=	heat absorption (W)

A	=	wetted area [m2]

F	= 	insulation factor [-]

F 	= 	1 for non-insulated vessels, or

where:

K	= 	heat conductivity of insulation layer			[W(m-1(K-1]

L	= 	thickness of insulation layer 				[m]

U	= 	K/L = heat transfer coefficient of the insulation 	[W(m-2 (K-1]

TPO	= 	temperature of peroxide at relieving conditions 	[K]

The start-to-discharge pressure of the emergency-relief device(s) shall be higher than that specified in 4.2.1.13.7 and based on the results of the tests referred to in 4.2.1.13.1. The emergency-relief devices shall be dimensioned in such a way that the maximum pressure in the tank never exceeds the test pressure of the tank.

NOTE:  An example of a method to determine the size of emergency-relief devices is given in Appendix 5 of the Manual of Tests and Criteria.

4.2.1.13.9	For insulated portable tanks the capacity and setting of emergency-relief device(s) shall be determined assuming a loss of insulation from 1% of the surface area.

4.2.1.13.10  Vacuum-relief devices and spring-loaded valves shall be provided with flame arresters. Due attention shall be paid to the reduction of the relief capacity caused by the flame arrester.

4.2.1.13.11  Service equipment such as valves and external piping shall be so arranged that no substance remains in them after filling the portable tank.

4.2.1.13.12  Portable tanks may be either insulated or protected by a sun-shield.  If the SADT of the substance in the portable tank is 55 °C or less, or the portable tank is constructed of aluminium, the portable tank shall be completely insulated.  The outer surface shall be finished in white or bright metal.

4.2.1.13.13 The degree of filling shall not exceed 90% at 15 oC.

4.2.1.13.14 The marking as required in 6.7.2.20.2 shall include the UN number and the technical name with the approved concentration of the substance concerned.

4.2.1.13.15 Organic peroxides and self-reactive substances specifically listed in portable tank instruction T23 in 4.2.4.2.6 may be carried in portable tanks.

4.2.1.14		Additional provisions applicable to the carriage of Class 6.1 substances in portable tanks

[reserved]

4.2.1.15	Additional provisions applicable to the carriage of Class 7 substances in portable tanks

4.2.1.15.1	Portable tanks used for the carriage of radioactive material shall not be used for the carriage of other goods.

4.2.1.15.2	The degree of filling for portable tanks shall not exceed 90% or, alternatively, any other value approved by the competent authority.

4.2.1.16		Additional provisions applicable to the carriage of Class 8 substances in portable tanks

4.2.1.16.1	Pressure-relief devices of portable tanks used for the carriage of Class 8 substances shall be inspected at intervals not exceeding one year.

4.2.1.17		Additional provisions applicable to the carriage of Class 9 substances in portable tanks

[reserved]

4.2.2	General provisions for the use of portable tanks for the carriage of non-refrigerated liquefied gases

4.2.2.1	This section provides general provisions applicable to the use of portable tanks for the carriage of non-refrigerated liquefied gases.

4.2.2.2	Portable tanks shall conform to the design, construction, inspection and testing requirements detailed in 6.7.3.  Non-refrigerated liquefied gases shall be carried in portable tanks conforming to portable tank instruction T50 as described in 4.2.4.2.6 and any portable tank special provisions assigned to specific non-refrigerated liquefied gases in Column 11 of table A of Chapter 3.2 and described in 4.2.4.3.

4.2.2.3	During carriage, portable tanks shall be adequately protected against damage to the shell and service equipment resulting from lateral and longitudinal impact and overturning.  If the shell and service equipment are so constructed as to withstand impact or overturning it need not be protected in this way.  Examples of such protection are given in 6.7.3.13.5.

4.2.2.4	Certain  non-refrigerated liquefied gases are chemically unstable.  They are accepted for carriage only when the necessary steps have been taken to prevent their dangerous decomposition, transformation or polymerization during carriage.  To this end, care shall in particular be taken to ensure that portable tanks do not contain any non-refrigerated liquefied gases liable to promote these reactions.

4.2.2.5	Unless the name of the dangerous goods being carried appears on the metal plate described in 6.7.3.16.2, a copy of the certificate specified in 6.7.3.14.1 shall be made available upon a competent authority request and readily provided by the consignor, consignee or agent, as appropriate.

4.2.2.6	Empty portable tanks not cleaned and not gas-free shall comply with the same requirements as portable tanks filled with the previous non-refrigerated liquefied gas.

4.2.2.7	Filling

4.2.2.7.1	Prior to filling the consignor shall ensure that the portable tank is approved for the non-refrigerated liquefied gas to be carried and that the portable tank is not loaded with non-refrigerated liquefied gases which in contact with the materials of the shell, gaskets and service equipment, are likely to react dangerously with them to form dangerous products or appreciably weaken the material. During filling, the temperature of the non-refrigerated liquefied gas shall fall within the limits of the design temperature range.

4.2.2.7.2	The maximum mass of non-refrigerated liquefied gas per litre of shell capacity (kg/l) shall not exceed the density of the non-refrigerated liquefied gas at 50 °C multiplied by 0.95. Furthermore, the shell shall not be liquid-full at 60 °C.

4.2.2.7.3	Portable tanks shall not be filled above their maximum permissible gross mass and the maximum permissible load mass specified for each gas to be carried.

4.2.2.8 	Portable tanks shall not be offered for carriage:

(a) 	In an ullage condition liable to produce an unacceptable hydraulic force due to surge within the portable tank;

(b) 	When leaking;

(c) 	When damaged to such an extent that the integrity of the tank or its lifting or securing arrangements may be affected; and

(d) 	Unless the service equipment has been examined and found to be in good working order.

4.2.2.9	Forklift pockets of portable tanks shall be closed off when the tank is filled. This provision does not apply to portable tanks which according to 6.7.4.12.4 need not be provided with a means of closing off the forklift pockets.

4.2.3	General provisions for the use of portable tanks for the carriage of refrigerated liquefied gases

4.2.3.1	This section provides general requirements applicable to the use of portable tanks for the carriage of refrigerated liquefied gases.

4.2.3.2	Portable tanks shall conform to the design, construction, inspection and testing requirements detailed in 6.7.4. Refrigerated liquefied gases shall be carried in portable tanks conforming to portable tank instruction T75 as described in 4.2.4.2.6 and the portable tank special provisions assigned to each substance in the table A of Chapter 3.2.

4.2.3.3	During carriage, portable tanks shall be adequately protected against damage to the shell and service equipment resulting from lateral and longitudinal impact and overturning.  If the shell and service equipment are so constructed as to withstand impact or overturning it need not be protected in this way.  Examples of such protection are provided in 6.7.4.12.5.

4.2.3.4	Unless the name of the dangerous goods being carried appears on the metal plate described in 6.7.4.15.2, a copy of the certificate specified in 6.7.4.13.1 shall be made available upon a competent authority request and readily provided by the consignor, consignee or agent, as appropriate.

4.2.3.5	Empty portable tanks not cleaned and not gas-free shall comply with the same requirements as portable tanks filled with the previous substance.

4.2.3.6	Filling

4.2.3.6.1	Prior to filling the consignor shall ensure that the portable tank is approved for the refrigerated liquefied gas to be carried and that the portable tank is not loaded with refrigerated liquefied gases which in contact with the materials of the shell, gaskets and service equipment, are likely to react dangerously with them to form dangerous products or appreciably weaken the material.  During filling, the temperature of the refrigerated liquefied gas shall be within the limits of the design temperature range.

4.2.3.6.2	In estimating the initial degree of filling the necessary holding time for the intended journey including any delays which might be encountered shall be taken into consideration.  The initial degree of filling of the shell, except as provided for in 4.2.3.6.3 and 4.2.3.6.4, shall be such that if the contents, except helium,  were to be raised to a temperature at which the vapour pressure is equal to the maximum allowable working pressure (MAWP) the volume occupied by liquid would not exceed 98%.

4.2.3.6.3  	Shells intended for the carriage of helium can be filled up to but not above the inlet of the pressure-relief device.

4.2.3.6.4  	A higher initial degree of filling may be allowed, subject to approval by the competent authority, when the intended duration of carriage is considerably shorter than the holding time.

4.2.3.7	Actual holding time

The actual holding time shall be calculated for each journey in accordance with a procedure recognized by the competent authority, on the basis of the following:

(a)	The reference holding time for the refrigerated liquefied gas to be carried (see 6.7.4.2.8.1) (as indicated on the plate referred to in 6.7.4.15.1);

(b)	The actual filling density;

(c)	The actual filling pressure;

(d)	The lowest set pressure of the pressure limiting device(s).

4.2.3.7.1	The actual holding time shall be marked either on the portable tank itself or on a metal plate firmly secured to the portable tank, in accordance with 6.7.4.15.2.

4.2.3.8	Portable tanks shall not be offered for carriage:

(a) 	In an ullage condition liable to produce an unacceptable hydraulic force due to surge within the shell;

(b) 	When leaking;

(c) 	When damaged to such an extent that the integrity of the portable tank or its lifting or securing arrangements may be affected;

(d) 	Unless the service equipment has been examined and found to be in good working order;

(e) 	Unless the actual holding time for the refrigerated liquefied gas being carried has been determined in accordance with 4.2.3.7 and the portable tank is marked in accordance with 6.7.4.15.2; and

(f) 	Unless the duration of carriage, after taking into consideration any delays which might be encountered, does not exceed the actual holding time.

4.2.3.9	Forklift pockets of portable tanks shall be closed off when the tank is filled. This provision does not apply to portable tanks which according to 6.7.4.12.4, as appropriate, need not be provided with a means of closing off the forklift pockets.

4.2.4	Portable tank instructions and special provisions

4.2.4.1	General

4.2.4.1.1	This section includes the portable tank instructions and special provisions applicable to dangerous goods authorized to be carried in portable tanks.  Each portable tank instruction is identified by an alpha-numeric designation (e.g. T1).  Column 10 of table A of Chapter 3.2 indicates the portable tank instruction that shall be used for each substance permitted for carriage in a portable tank.  When no portable tank instruction appears in Column 10 for a specific dangerous goods entry then carriage of the substance in portable tanks is not permitted unless a competent authority approval is granted as detailed in 6.7.1.3. Portable tank special provisions are assigned to specific dangerous goods in Column 11 of table A of Chapter 3.2.  Each portable tank special provision is identified by an alpha-numeric designation (e.g. TP1). A listing of the portable tank special provisions is provided in 4.2.4.3.

4.2.4.2	Portable tank instructions

4.2.4.2.1	Portable tank instructions apply to dangerous goods of Classes 2 to 9. Portable tank instructions provide specific information relevant to portable tanks requirements applicable to specific substances. These requirements shall be met in addition to the general requirements in this Chapter and Chapter 6.7.

4.2.4.2.2	For substances of Classes 3 to 9, the portable tank instructions indicate the applicable minimum test pressure, the minimum shell thickness (in reference steel), bottom opening requirements and pressure relief requirements.  In T23, self-reactive substances of Class 4.1 and Class 5.2 organic peroxides permitted to be carried in portable tanks are listed along with the applicable control and emergency temperatures.

4.2.4.2.3	Non-refrigerated liquefied gases are assigned to portable tank instruction T50. T50 provides the maximum allowable working pressures, bottom opening requirements, pressure relief requirements and degree of filling requirements for non-refrigerated liquefied gases permitted for carriage in portable tanks.

4.2.4.2.4	Refrigerated liquefied gases are assigned to portable tank instruction T75.

4.2.4.2.5	Determination of the appropriate portable tank instructions

When a specific portable tank instruction is specified in Column 10 for a specific dangerous goods entry additional portable tanks which possess higher test pressures, greater wall thicknesses, more stringent bottom opening and pressure-relief device arrangements may be used.  The following guidelines apply to determining the appropriate portable tanks which may be used for carriage of particular substances:

| Portable tank instruction specified | Portable tank instructions also permitted |
| --- | --- |
| T1 | T2, T3, T4, T5, T6, T7, T8, T9, T10, T11, T12, T13, T14, T15, T16, T17, T18, T19, T20, T21, T22 |
| T2 | T4, T5, T6, T7, T8, T9, T10, T11, T12, T13, T14, T15, T16, T17, T18, T19, T20, T21, T22 |
| T3 | T4, T5, T6, T7, T8, T9, T10, T11, T12, T13, T14, T15, T16, T17, T18, T19, T20, T21, T22 |
| T4 | T5, T6, T7, T8, T9, T10, T11, T12, T13, T14, T15, T16, T17, T18, T19, T20, T21, T22 |
| T5 | T10, T12, T14, T16, T18, T19, T20, T22 |
| T6 | T7, T8, T9, T10, T11, T12, T13, T14, T15, T16, T17, T18, T19, T20, T21, T22 |
| T7 | T8, T9, T10, T11, T12, T13, T14, T15, T16, T17, T18, T19, T20, T21, T22 |
| T8 | T9, T10, T13, T14, T19, T20, T21, T22 |
| T9 | T10, T13, T14, T19, T20, T21, T22 |
| T10 | T14, T19, T20, T22 |
| T11 | T12, T13, T14, T15, T16, T17, T18, T19, T20, T21, T22 |
| T12 | T14, T16, T18, T19, T20, T22 |
| T13 | T14, T19, T20, T21, T22 |
| T14 | T19, T20, T22 |
| T15 | T16, T17, T18, T19, T20, T21, T22 |
| T16 | T18, T19, T20, T22 |
| T17 | T18, T19, T20, T21, T22 |
| T18 | T19, T20, T22 |
| T19 | T20, T22 |
| T20 | T22 |
| T21 | T22 |
| T22 | None |
| T23 | None |

4.2.4.2.6	Portable tank instructions

| T1 - T22 PORTABLE TANK INSTRUCTIONS T1 -T22 These portable tank instructions apply to liquid and solid substances of Classes 3 to 9. The general provisions of section 4.2.1 and the requirements of section 6.7.2 shall be met. |  |  |  |  |
| --- | --- | --- | --- | --- |
| Portable tank instruction | Minimum test pressure (bar) | Minimum shell thickness (in mm-reference steel) (see 6.7.2.4) | Pressure-relief requirements (see 6.7.2.8) | Bottom opening requirements (see 6.7.2.6) |
| T1 | 1.5 | See 6.7.2.4.2 | Normal | See 6.7.2.6.2 |
| T2 | 1.5 | See 6.7.2.4.2 | Normal | See 6.7.2.6.3 |
| T3 | 2.65 | See 6.7.2.4.2 | Normal | See 6.7.2.6.2 |
| T4 | 2.65 | See 6.7.2.4.2 | Normal | See 6.7.2.6.3 |
| T5 | 2.65 | See 6.7.2.4.2 | See 6.7.2.8.3 | Not Allowed |
| T6 | 4 | See 6.7.2.4.2 | Normal | See 6.7.2.6.2 |
| T7 | 4 | See 6.7.2.4.2 | Normal | See 6.7.2.6.3 |
| T8 | 4 | See 6.7.2.4.2 | Normal | Not allowed |
| T9 | 4 | 6mm | Normal | Not allowed |
| T10 | 4 | 6mm | See 6.7.2.8.3 | Not allowed |
| T11 | 6 | See 6.7.2.4.2 | Normal | See 6.7.2.6.3 |
| T12 | 6 | See 6.7.2.4.2 | See 6.7.2.8.3 | See 6.7.2.6.3 |
| T13 | 6 | 6mm | Normal | Not allowed |
| T14 | 6 | 6mm | See 6.7.2.8.3 | Not allowed |
| T15 | 10 | See 6.7.2.4.2 | Normal | See 6.7.2.6.3 |
| T16 | 10 | See 6.7.2.4.2 | See 6.7.2.8.3 | See 6.7.2.6.3 |
| T17 | 10 | 6mm | Normal | See 6.7.2.6.3 |
| T18 | 10 | 6mm | See 6.7.2.8.3 | See 6.7.2.6.3 |
| T19 | 10 | 6mm | See 6.7.2.8.3 | Not allowed |
| T20 | 10 | 8mm | See 6.7.2.8.3 | Not allowed |
| T21 | 10 | 10mm | Normal | Not allowed |
| T22 | 10 | 10mm | See 6.7.2.8.3 | Not allowed |

| T23 PORTABLE TANK INSTRUCTION T23 This portable tank instruction applies to self-reactive substances of Class 4.1 and organic peroxides of Class 5.2. The general provisions of section 4.2.1 and the requirements of section 6.7.2 shall be met. The provisions specific to self-reactive substances of Class 4.1 and organic peroxides of Class 5.2 in 4.2.1.13 shall also be met. |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UN No. | Substance | Minimum test pressure (bar) | Minimum shell thickness (mm-reference steel) | Bottom opening requir-ements | Pressure- relief requir-ements | Filling limits | Control temper-ature | Emergency temper-ature |
| 3109 | ORGANIC PEROXIDE, TYPE F, LIQUID tert-Butyl hydro-peroxide*, not more than 72% with water Cumyl hydro-peroxide, not more than 90% in diluent type A Di-tert-butyl peroxide, not more than 32% in diluent type A Isopropyl cumyl hydro-peroxide, not more than 72% in diluent type A p-Menthyl hydro-peroxide, not more than 72% in diluent type A Pinanyl hydro- peroxide, not more than 50% in diluent type A | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 |  |  |
| 3110 | ORGANIC PEROXIDE TYPE F, SOLID Dicumyl peroxide ** | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 |  |  |

__________________________

*	Provided that steps have been taken to achieve the safety equivalence of 65% tert-Butyl hydroperoxide and 35% water.

**	Maximum quantity per receptacle 2000 kg.

| T23 PORTABLE TANK INSTRUCTION (cont'd) T23 This portable tank instruction applies to self-reactive substances of Class 4.1 and organic peroxides of Class 5.2. The general provisions of section 4.2.1 and the requirements of section 6.7.2 shall be met. The provisions specific to self-reactive substances of Class 4.1 and organic peroxides of Class 5.2 in 4.2.1.13 shall also be met. |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UN No. | Substance | Minimum test pressure (bar) | Minimum shell thickness (mm-reference steel) | Bottom opening requir-ements | Pressure- relief requir-ements | Filling limits | Control temper-ature | Emergency temper-ature |
| 3119 | ORGANIC PEROXIDE, TYPE F, LIQUID, TEMPERATURE CONTROLLED tert-Butyl peroxyacetate, not more than 32% in diluent type B tert-Butyl peroxy-2-ethylhexanoate, not more than 32% in diluent type B tert-Butyl peroxypivalate, not more than 27% in diluent type B tert-Butyl peroxy-3,5,5-trimethyl-hexanoate, not more than 32% in diluent type B Di-(3,5,5-trimethyl-hexanoyl) peroxide, not more than 38% in diluent type A | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 | * +30 °C +15 °C +5 °C +35 °C 0 °C | * +35 °C +20 °C +10 °C +40 °C +5 °C |
| 3120 | ORGANIC PEROXIDE, TYPE F, SOLID, TEMPERATURE CONTROLLED | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 | * | * |
| 3229 | SELF-REACTIVE LIQUID TYPE F | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 |  |  |
| 3230 | SELF-REACTIVE SOLID TYPE F | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 |  |  |
| 3239 | SELF-REACTIVE LIQUID TYPE F, TEMPERATURE CONTROLLED | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 | * | * |
| 3240 | SELF-REACTIVE SOLID TYPE F, TEMPERATURE CONTROLLED | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 | * | * |

| T50 PORTABLE TANK INSTRUCTION T50 This portable tank instruction applies to non-refrigerated liquefied gases. The general provisions of section 4.2.2 and the requirements of section 6.7.3 shall be met. |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| UN No. | Non-refrigerated liquefied gases | Max. allowable working pressure (bar) Small; Bare; Sunshield; Insulated | Openings below liquid level | Pressure- relief requirements (see 6.7.3.7) | Maximum filling ratio (kg/l) |
| 1005 | Ammonia, anhydrous | 29.0 25.7 22.0 19.7 | Allowed | See 6.7.3.7.3 | 0.53 |
| 1009 | Bromotrifluoromethane (Refrigerant gas R 13B1) | 38.0 34.0 30.0 27.5 | Allowed | Normal | 1.13 |
| 1010 | Butadienes, stabilized | 7.5 7.0 7.0 7.0 | Allowed | Normal | 0.55 |
| 1011 | Butane | 7.0 7.0 7.0 7.0 | Allowed | Normal | 0.51 |
| 1012 | Butylene | 8.0 7.0 7.0 7.0 | Allowed | Normal | 0.53 |
| 1017 | Chlorine | 19.0 17.0 15.0 13.5 | Not Allowed | See 6.7.3.7.3 | 1.25 |

| T50 PORTABLE TANK INSTRUCTION (cont'd) T50 This portable tank instruction applies to non-refrigerated liquefied gases. The general provisions of section 4.2.2 and the requirements of section 6.7.3 shall be met. |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 1018 | Chlorodifluoromethane (Refrigerant gas R 22) | 26.0 24.0 21.0 19.0 | Allowed | Normal | 1.03 |
| 1020 | Chloropentafluoroethane (Refrigerant gas R 115) | 23.0 20.0 18.0 16.0 | Allowed | Normal | 1.06 |
| 1021 | 1-Chloro-1,2,2,2-tetrafluoroethane (Refrigerant gas R 124) | 10.3 9.8 7.9 7.0 | Allowed | Normal | 1.20 |
| 1027 | Cyclopropane | 18.0 16.0 14.5 13.0 | Allowed | Normal | 0.53 |
| 1028 | Dichlorodifluoromethane (Refrigerant gas R 12) | 16.0 15.0 13.0 11.5 | Allowed | Normal | 1.15 |
| 1029 | Dichlorofluoromethane (Refrigerant gas R 21) | 7.0 7.0 7.0 7.0 | Allowed | Normal | 1.23 |
| 1030 | 1,1-Difluoroethane (Refrigerant gas R 152a) | 16.0 14.0 12.4 11.0 | Allowed | Normal | 0.79 |
| 1032 | Dimethylamine, anhydrous | 7.0 7.0 7.0 7.0 | Allowed | Normal | 0.59 |
| 1033 | Dimethyl ether | 15.5 13.8 12.0 10.6 | Allowed | Normal | 0.58 |
| 1036 | Ethylamine | 7.0 7.0 7.0 7.0 | Allowed | Normal | 0.61 |
| 1037 | Ethyl chloride | 7.0 7.0 7.0 7.0 | Allowed | Normal | 0.80 |
| 1040 | Ethylene oxide with nitrogen up to a total pressure of 1MPa (10 bar) at 50 °C | - - - 10.0 | Not Allowed | See 6.7.3.7.3 | 0.78 |
| 1041 | Ethylene oxide and carbon dioxide mixture with more than 9% but not more than 87% ethylene oxide | See MAWP definition in 6.7.3.1 | Allowed | Normal | See 4.2.2.7 |
| 1055 | Isobutylene | 8.1 7.0 7.0 7.0 | Allowed | Normal | 0.52 |
| 1060 | Methyllacetylene and propadiene mixture, stabilized | 28.0 24.5 22.0 20.0 | Allowed | Normal | 0.43 |
| 1061 | Methylamine, anhydrous | 10.8 9.6 7.8 7.0 | Allowed | Normal | 0.58 |
| 1062 | Methyl bromide | 7.0 7.0 7.0 7.0 | Not Allowed | See 6.7.3.7.3 | 1.51 |
| 1063 | Methyl chloride (Refrigerant gas R 40) | 14.5 12.7 11.3 10.0 | Allowed | Normal | 0.81 |
| 1064 | Methyl mercaptan | 7.0 7.0 7.0 7.0 | Not Allowed | See 6.7.3.7.3 | 0.78 |
| 1067 | Dinitrogen tetroxide | 7.0 7.0 7.0 7.0 | Not Allowed | See 6.7.3.7.3 | 1.30 |
| 1075 | Petroleum gas, liquefied | See MAWP definition in 6.7.3.1 | Allowed | Normal | See 4.2.2.7 |
| 1077 | Propylene | 28.0 24.5 22.0 20.0 | Allowed | Normal | 0.43 |
| 1078 | Refrigerant gas, n.o.s. | See MAWP definition in 6.7.3.1 | Allowed | Normal | See 4.2.2.7 |
| 1079 | Sulphur dioxide | 11.6 10.3 8.5 7.6 | Not Allowed | See 6.7.3.7.3 | 1.23 |
| 1082 | Trifluorochloroethylene, stabilized (Refrigerant gas R 1113) | 17.0 15.0 13.1 11.6 | Not Allowed | See 6.7.3.7.3 | 1.13 |
| 1083 | Trimethylamine, anhydrous | 7.0 7.0 7.0 7.0 | Allowed | Normal | 0.56 |
| 1085 | Vinyl bromide, stabilized | 7.0 7.0 7.0 7.0 | Allowed | Normal | 1.37 |
| 1086 | Vinyl chloride, stabilized | 10.6 9.3 8.0 7.0 | Allowed | Normal | 0.81 |
| 1087 | Vinyl methyl ether, stabilized | 7.0 7.0 7.0 7.0 | Allowed | Normal | 0.67 |
| 1581 | Chloropicrin and methyl bromide mixture | 7.0 7.0 7.0 7.0 | Not Allowed | See 6.7.3.7.3 | 1.51 |
| 1582 | Chloropicrin and methyl chloride mixture | 19.2 16.9 15.1 13.1 | Not Allowed | See 6.7.3.7.3 | 0.81 |
| 1858 | Hexafluoropropylene (Refrigerant gas R 1216) | 19.2 16.9 15.1 13.1 | Allowed | Normal | 1.11 |
| 1912 | Methyl chloride and methylene chloride mixture | 15.2 13.0 11.6 10.1 | Allowed | Normal | 0.81 |
| 1958 | 1,2-Dichloro-1,1,2,2-tetrafluoroethane (Refrigerant gas R 114) | 7.0 7.0 7.0 7.0 | Allowed | Normal | 1.30 |
| 1965 | Hydrocarbon gas, mixture liquefied, n.o.s. | See MAWP definition in 6.7.3.1 | Allowed | Normal | See 4.2.2.7 |
| 1969 | Isobutane | 8.5 7.5 7.0 7.0 | Allowed | Normal | 0.49 |
| 1973 | Chlorodifluoromethane and chloropentafluoroethane mixture with fixed boiling point, with approximately 49% chlorodifluoromethane (Refrigerant gas R 502) | 28.3 25.3 22.8 20.3 | Allowed | Normal | 1.05 |
| 1974 | Chlorodifluorobromomethane (Refrigerant gas R 12B1) | 7.4 7.0 7.0 7.0 | Allowed | Normal | 1.61 |
| 1976 | Octafluorocyclobutane (Refrigerant gas RC 318) | 8.8 7.8 7.0 7.0 | Allowed | Normal | 1.34 |
| 1978 | Propane | 22.5 20.4 18.0 16.5 | Allowed | Normal | 0.42 |
| 1983 | 1-Chloro-2,2,2-trifluoroethane (Refrigerant gas R 133a) | 7.0 7.0 7.0 7.0 | Allowed | Normal | 1.18 |
| 2035 | 1,1,1-Trifluoroethane (Refrigerant gas R 143a) | 31.0 27.5 24.2 21.8 | Allowed | Normal | 0.76 |
| 2424 | Octafluoropropane (Refrigerant gas R 218) | 23.1 20.8 18.6 16.6 | Allowed | Normal | 1.07 |
| 2517 | 1-Chloro-1,1-difluoroethane (Refrigerant gas R 142b) | 8.9 7.8 7.0 7.0 | Allowed | Normal | 0.99 |
| 2602 | Dichlorodifluoromethane and difluoroethane azeotropic mixture with approximately 74% dichlorodifluoromethane (Refrigerant gas R 500) | 20.0 18.0 16.0 14.5 | Allowed | Normal | 1.01 |
| 3057 | Trifluoroacetyl chloride | 14.6 12.9 11.3 9.9 | Not allowed | 6.7.3.7.3 | 1.17 |
| 3070 | Ethylene oxide and dichlorodifluoromethane mixture with not more than 12.5% ethylene oxide | 14.0 12.0 11.0 9.0 | Allowed | 6.7.3.7.3 | 1.09 |
| 3153 | Perfluoro (methyl vinyl ether) | 14.3 13.4 11.2 10.2 | Allowed | Normal | 1.14 |
| 3159 | 1,1,1,2-Tetrafluoroethane (Refrigerant gas R 134a) | 17.7 15.7 13.8 12.1 | Allowed | Normal | 1.04 |
| 3161 | Liquefied gas, flammable, n.o.s. | See MAWP definition in 6.7.3.1 | Allowed | Normal | See 4.2.2.7 |
| 3163 | Liquefied gas, n.o.s. | See MAWP definition in 6.7.3.1 | Allowed | Normal | See 4.2.2.7 |
| 3220 | Pentafluoroethane (Refrigerant gas R 125) | 34.4 30.8 27.5 24.5 | Allowed | Normal | 0.95 |
| 3252 | Difluoromethane (Refrigerant gas R 32) | 43.0 39.0 34.4 30.5 | Allowed | Normal | 0.78 |
| 3296 | Heptafluoropropane (Refrigerant gas R 227) | 16.0 14.0 12.5 11.0 | Allowed | Normal | 1.20 |
| 3297 | Ethylene oxide and chlorotetrafluoroethane mixture, with not more than 8.8% ethylene oxide | 8.1 7.0 7.0 7.0 | Allowed | Normal | 1.16 |
| 3298 | Ethylene oxide and pentafluoroethane mixture, with not more than 7.9% ethylene oxide | 25.9 23.4 20.9 18.6 | Allowed | Normal | 1.02 |
| 3299 | Ethylene oxide and tetrafluoroethane mixture, with not more than 5.6% ethylene oxide | 16.7 14.7 12.9 11.2 | Allowed | Normal | 1.03 |
| 3318 | Ammonia solution, relative density less than 0.880 at 15 °C in water, with more than 50% ammonia | See MAWP definition in 6.7.3.1 | Allowed | See 6.7.3.7.3 | See 4.2.2.7 |
| 3337 | Refrigerant gas R 404A | 31.6 28.2 25.2 22.1 | Allowed | Normal | 0.82 |
| 3338 | Refrigerant gas R 407A | 32.3 29.0 25.7 22.4 | Allowed | Normal | 0.94 |
| 3339 | Refrigerant gas R 407B | 34.0 30.5 27.0 23.6 | Allowed | Normal | 0.93 |
| 3340 | Refrigerant gas R 407C | 30.2 27.0 24.1 21.4 | Allowed | Normal | 0.95 |

T75 PORTABLE TANK INSTRUCTION T75 This portable tank instruction applies to refrigerated liquefied gases. The general provisions of section 4.2.3 and the requirements of section 6.7.4 shall be met.

4.2.4.3	Portable tank special provisions

Portable tank special provisions are assigned to certain substances to indicate requirements which  are in addition to or in lieu of those provided by the portable tank instructions or the requirements in Chapter 6.7.  Portable tank special provisions are designated using the abbreviation TP (tank provision) and are assigned to specific substances in Column 11 of table A of Chapter 3.2.  The following is a list of the portable tank special provisions:

TP3	-	For liquids carried under elevated temperature conditions the filling limits prescribed

TP4 	- 	The degree of filling for portable tanks shall not exceed 90% or, alternatively, any other value approved by the competent authority (see 4.2.1.15.2).

TP5 	- 	Reserved.

TP6 	- 	To prevent the tank bursting in any event, including fire engulfment, it shall be provided with pressure-relief devices which are adequate in relation to the capacity of the tank and to the nature of the substance carried.  The device shall also be compatible with the substance.

TP7 	-	Air shall be eliminated from the vapour space by nitrogen or other means.

TP8 	-	The test pressure for the portable tank may be reduced to 1.5 bar when the flash point of the substances carried is greater than 0 °C.

TP9 	- 	A substance under this description shall only be carried in a portable tank under an approval granted by the competent authority.

TP10 	- 	A lead lining, not less than 5 mm thick, which shall be tested annually, or another suitable lining material approved by the competent authority is required.

TP12 	- 	Highly corrosive to steel.

TP13 	- 	Self-contained breathing apparatus shall be provided when this substance is carried.

TP16 	- 	The tank shall be fitted with a special device to prevent under-pressure and excess pressure during normal carriage conditions. This device shall be approved by the competent authority.

Pressure-relief requirements are as indicated in 6.7.2.8.3 to prevent crystallization of the product in the pressure-relief valve.

TP17 	- 	Only inorganic non-combustible materials shall be used for thermal insulation of the tank.

TP18 	- 	Temperature shall be maintained between 18 °C and 40 °C. Portable tanks containing solidified methacrylic acid shall not be reheated during carriage.

TP19 	- 	The calculated wall thickness shall be increased by 3 mm. Wall thickness shall be verified ultrasonically at intervals midway between periodic hydraulic tests.

TP20 	- 	This substance shall only be carried in insulated tanks under a nitrogen blanket.

TP21 	- 	The wall thickness shall be not less than 8 mm. Tanks shall be hydraulically tested and internally inspected at intervals not exceeding 2.5 years.

TP22 	- 	Lubricant for joints or other devices shall be oxygen compatible.

TP23 	- 	Carriage permitted under special conditions prescribed by the competent authorities.

TP24	- 	The portable tank may be fitted with a device located under maximum filling conditions in the vapour space of the shell to prevent the build up of excess pressure due to the slow decomposition of the substance carried. This device shall also prevent an unacceptable amount of leakage of liquid in the case of overturning or entry of foreign matter into the tank. This device shall be approved by the competent authority or its authorized body.

TP25	-	Sulphur trioxide 99.95% pure and above may be carried in tanks without an inhibitor provided that it is maintained at a temperature equal to or above 32.5 °C.

TP26	-	When carried under heated conditions, the heating device shall be fitted outside the shell. For UN 3176 this requirement only applies when the substance reacts dangerously with water.

TP27	-	A portable tank having a minimum test pressure of 4 bar may be used if it is shown that a test pressure of 4 bar or less is acceptable according to the test pressure definition in 6.7.2.1.

TP28	-	A portable tank having a minimum test pressure of 2.65 bar may be used if it is shown that a test pressure of 2.65 bar or less is acceptable according to the test pressure definition in 6.7.2.1.

TP29 	-	A portable tank having a minimum test pressure of 1.5 bar may be used if it is shown that a test pressure of 1.5 bar or less is acceptable according to the test pressure definition in 6.7.2.1.

___________

# Footnotes

*	As approved by the competent authority.

# Text boxes

E

Economic and Social

Council