#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2001/14

17 April 2001

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Nineteenth session, 2-6 July 2001,

# agenda item 7(b))

# LISTING AND CLASSIFICATION

Assignment of substances and solutions to the correct UN number

in relation to the physical state (liquid/solid)

Transmitted by the experts from the Netherlands and Germany

In its twenty-first session of the Committee of December 2000, the Netherlands submitted a paper  (ST/SG/AC.10/2000/29) concerning the correct assignment of UN Numbers to substances, mixtures and solutions especially related to the physical state.

During the reformatting/restructuring process several discrepancies within the UN Recommendations were identified and the proposal by the Netherlands to discuss these problems in the coming biennium and give guiding principles in the UN Recommendations was adopted.

Intersessionally, the matter has been discussed between several experts and the result is presented in this paper.

The principle of the lay-out of the Dangerous Goods List, is to indicate unambiguously transport requirements related to the substance listed. The cases discussed in this paper, concern substances which may appear in liquid or solid form. Since for liquids and solids different transport requirements apply, separate lines are needed.

It is proposed to have a discussion on the general principle whether separate UN numbers are needed or whether different lines under the same UN number should be used.

GE.01-

To facilitate the discussion, different situations are identified:

A  	Solid substances and their solutions

B 	Substances, having a melting point around the borderline of the definition solid/liquid

including  isomers and  mixtures thereof

C  	 Molten substances

D	Discrepancies in the dangerous goods list.

A. 	Solid substances and their solutions

The first situation deals with the classification of the solution of a solid substance.

Should such a solution be assigned to the same UN number as the solid substance or should the solution have a separate UN number whereby the most specific collective liquid entry is assigned?

These two options are discussed below together with the consequences.

Option A1. Separate UN numbers in the DGL for solids and solutions thereof.

A basic point in the discussion is the principle as laid down in 2.0.2.5 and 2.0.2.6 to have separate UN numbers  to differentiate in physical state liquid/solid. In other words: if the physical state changes, the UN number should change as well.  This means that a solution of a solid substance should not be classified under the UN number for the solid substance but under the most appropriate collective entry available.

As a consequence a solution of UN 1689 SODIUM CYANIDE should not be assigned to UN 1689, but to the most specific liquid entry, in this case UN 1935 CYANIDE SOLUTIONS N.O.S.

In most cases however the most specific entry is a general N.O.S entry with no direct relation to the substance, for example: UN 2810 TOXIC LIQUID, ORGANIC, N.O.S.

In these cases however the chemical or technical name should be added to the proper shipping name.

The general principle as laid down in 2.0.2.5 and 2.0.2.6 is followed, for example, in Class 5.1 where the solid substance has a different UN-number than its related solution:

UN 1485 POTASSIUM CHLORATE

UN 2427 POTASSIUM CHLORATE, AQUEOUS SOLUTION

Within the GHS discussion on labelling and hazard communication and especially from the point of view of emergency response, it has been argued that such a differentiation is relevant.

However in most emergency response systems there is no different indication for solids or liquids, although the action to be taken might be quite different.

In other cases however, this principle has not been followed in the UN model regulations, for example:

UN 1658 NICOTINE SULPHATE, SOLID

UN 1658 NICOTINE SULPHATE, SOLUTIONS

If the principle of 2.0.2.5 and 2.0.2.6 is followed, entries like UN 1658 should be divided as follows:

UN 1658 NICOTINE SULPHATE, SOLID

UN 9999 NICOTINE SULPHATE, SOLUTIONS

In the Dangerous Goods List there will be separate entries for solids and liquids, clearly indicating their applicable transport conditions.

However, only where there is a real need for transport, a new UN number should be assigned to the solutions. This should be considered on a case by case basis.

Consequently, it should be made very clear that in case of a solution, the most specific liquid entry should be used.

Other entries which might be effected by following this option, are listed in Annex 1 of this proposal.  These entries are taken from the present UN Recommendation and from the proposal by IMO (ST/SG/AC.10/C.3/2000/5).

Annex 1 also includes specific N.O.S. entries, for which it appeared necessary to assign new UN numbers for the entries for solutions.

Option A2. The solution of a solid is assigned to the same UN number as the solid itself.

In this option the general rule is that the UN number for the solid substance should also be used for its solution. In this case the word SOLUTION should be added as part of the proper shipping name as has been done for molten substances.

Consequences for this option are:

- The principle to have separate UN numbers to differentiate in physical state liquid/solid, as laid down in 2.0.2.5 and 2.0.2.6 should be amended.

- The information solid/liquid is no longer linked to the UN number.

- For each solid, which can be carried as a solution, the UN entry in the dangerous goods list should be associated with two lines: one for the solid (existing line) and another one for its solution together with the corresponding conditions of transport.

Within this option the following question should be answered. Should the word solution or liquid be in upper case, becoming a part of the Proper Shipping Name (PSN), or should it be in lower case.

UN 1658 NICOTINE SULPHATE, SOLID*

UN 1658 NICOTINE SULPHATE, SOLUTIONS

or

UN 1658  NICOTINE SULPHATE, solid

UN 1658  NICOTINE SULPHATE, solution

* The word SOLID, could be in lower case if this is regarded as the default possibility.

When using the words solid or solution in lower case, the combination UN number/proper shipping name is associated with different conditions of transport.

In this case it is not clear from the proper shipping name on the transport document which situation applies during transport. From an enforcement point of view this is a difficult situation

- Substances, having a melting point around the borderline of the definition solid/liquid including  isomers and  mixtures thereof

It is always difficult to deal with borderline cases. In this discussion these are the substances, isomers, mixtures and mixtures of isomers having a melting point of appr. 20 °C.

Depending on amongst others, the temperature, degree of purity or the composition of the mixture of isomers, these substances are solids or liquids.

Therefore, it is felt necessary to have two lines in the Dangerous Goods List, showing the applicable transport provisions

The present UN Recommendations cover this in 3.1.2.4:

“Unless it is already included in capital letters in the name indicated  in the Dangerous Goods List, the qualifying words LIQUID or SOLID, as appropriate, shall be added as part of the proper shipping name, when a substance specifically listed by name may, due to the differing physical states of the various isomers of the substance, be either liquid or solid (e.g. DINITROTOLUENES, LIQUID; DINITROTOLUENES, SOLID). ”

It is the responsibility of the shipper to apply the transport condition depending on the properties of the substance or mixture of substances and the temperature which might be encountered in the particular transport involved. See also 4.1.3.4 which indicates the types of packagings allowed for substances which are liable to become liquid during transport.

Substances involved are contained in Annex 2.

In principle there are three options:

Option B1

follow the principles as set out in 2.0.2.5 and 2.0.2.6 in full, that is to say two different UN numbers, different proper shipping names and separate entries associated with the liquid and the solid entry in the Dangerous Goods List.

e.g. 	UN 2038 DINITROTOLUENES, LIQUID

UN 9999 DINITROTOLUENES, SOLID

It should be noted that depending on the circumstances, inherent to borderline cases, the substance might be a liquid or a solid.

Option B2

follow the general principle as set out in 3.1.2.4 of the UN Recommendations, as is done for the IMDG Code, which results in the use of one UN number, associated with two different descriptions, one for the liquid and one for the solid and two lines in the Dangerous Goods List.

e.g. 	UN 2038 DINITROTOLUENES, LIQUID

UN 2038 DINITROTOLUENES, SOLID

In options B1 and B2 it is clear which decision the consignor has taken in order to fulfil the conditions of transport. In case of a liquid, a special provision might be appropriate to indicate that the substance might be liquid or solid depending on the circumstances. If shipped as a solid, this indicates that the consignor declares implicitly that the substance does not become liquid during transport.

Option B3

one UN number associated with one PSN and two lines in the DGL. This situation can be found in some cases in the existing UN Recommendations,

e.g. 	UN 2038  DINITROTOLUENES, liquid

UN 2038  DINITROTOLUENES, solid

In this case it is not clear from the proper shipping name on the transport document which situation applies during transport. From an enforcement point of view this is a difficult situation.

C.	Molten substances

As a general rule molten substances may be carried under the same UN number as the solid substance with the addition to the proper shipping name: MOLTEN, unless there is a specific entry for the molten substance (see 3.1.2.5).

As indicated under A and B the same can be discussed for molten substances

e.g. 	2448 SULPHER, MOLTEN and  1350 SULPHER  or

2215 MALEIC ANHYDRIDE, MOLTEN and 2215 MALEIC ANHYDRIDE.

A problem concerns the question whether or not the substance is allowed to be transported in the molten state and which transport conditions should apply. This is not specifically indicated in the Dangerous Goods List.

In RID/ADR many more solid substances in the molten state are allowed in tanks as compared with the UN Recommendations. In order to cope with the problem of molten substances it was argued that the problems arise primarily in tank transport. For molten substances a tank for liquids is required, contrary to the associated solid (powder, granules).

In the cases where a substance may be transported in the molten state this should be clear from the dangerous goods list.  After consultation of the industry it was decided to foresee in RID/ADR the possibility of transport in the molten state for substances with a melting point of not more than 180 °C.

In those cases two tank codes are indicated in the column for the RID/ADR tanks, one for the solid and one for the molten substance.

In order to tackle this problem it is necessary to have a discussion on the questions in which case the transport in the molten form is allowed and under which conditions of transport. However this is beyond the scope of this proposal.

D.	Discrepancies in the dangerous goods list

Some discrepancies have been discovered in comparing the dangerous goods lists for the different modes of transport. It appears that in some cases the UN Recommendations indicate a packing instruction for liquid where the IMDG Code states in the column “ properties and observations” that the substance involved is a solid. Or the other way around, a P002 for solids is indicated and the column “ properties and observations” indicates that the substance involved is a liquid.

It concerns the substances in Annex  (in preparation).

Experts are asked to consider these entries on a case by case basis and to remove the discrepancies which are identified.

Annex 1

All entries which appear in one of the regulations mentioned as a solid and as a liquid or solution, under the same UN number

X means entry is listed in the regulation.

N means entry not listed in the regulation.

| Class/UN No. | PSN | UN (12ed) | RID/ADR | IMDG Amdt. 30-00 | CFR 49 |
| --- | --- | --- | --- | --- | --- |
| 1.1C/0497 | PROPELLANT, LIQUID | X | X | X | X |
| 1.1C/0497 | PROPELLANT, SOLID | N | N | X | N |
| 4.3/1389 | ALKALI METAL AMALGAM, LIQUID | X, P402/403 | X, P402 | X | X |
| 4.3/1389 | ALKALI METAL AMALGAM, SOLID | N | N | X | X |
| 4.3/1392 | ALKALINE EARTH METAL AMALGAM, LIQUID | X, P402/403 | X, P402 | X | N |
| 4.3/1392 | ALKALINE EARTH METAL AMALGAM, SOLID | N | N | X | X |
| 5.1/1445 | BARIUM CHLORATE, SOLUTION | N | N | X | N |
| 5.1/1445 | BARIUM CHLORATE, SOLID | X | X | X | X |
| 5.1/1447 | BARIUM PERCHLORATE, SOLUTION | N | N | X | N |
| 5.1/1447 | BARIUM PERCHLORATE, SOLID | X | X | X | X |
| 5.1/1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLUTION | N | N | X | N |
| 5.1/1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLID | X | X | X | X |
| 5.1/1470 | LEAD PERCHLORATE, SOLUTION | N | N | X | X |
| 5.1/1470 | LEAD PERCHLORATE, SOLID | X | X | X | X |
| 6.1/1579 | 4-CHLORO-ortho-TOLUIDINE HYDROCHLORIDE, SOLUTION | N | N | X | ? |
| 6.1/1579 | 4-CHLORO-ortho-TOLUIDINE HYDROCHLORIDE, SOLUTION | X | X | X | ? |
| 6.1/1656 | NICOTINE HYDROCHLORIDE, SOLUTION | X | X | X | X |
| 6.1/1656 | NICOTINE HYDROCHLORIDE, SOLID | X | X | X | N |
| 6.1/1658 | NICOTINE SULPHATE, SOLUTION | X | X | X | X |
| 6.1/1658 | NICOTINE SULPHATE, SOLID | X | X | X | X |
| 6.1/1680 | POTASSIUM CYANIDE, SOLUTION | N | N | X | N |
| 6.1/1680 | POTASSIUM CYANIDE, SOLID | X | X | X | X |
| 6.1/1689 | SODIUM CYANIDE, SOLUTION | N | N | X | N |
| 6.1/1689 | SODIUM CYANIDE, SOLID | X | X | X | X |
| 6.1/1690 | SODIUM FLUORIDE, SOLUTION | N | N | X | N |
| 6.1/1690 | SODIUM FLUORIDE, SOLID | X | X | X | X |
| 6.1/1693 | TEAR GAS SUBSTANCE, LIQUID, N.O.S. | X | X | X | X |
| 6.1/1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | X | X | X | X |
| 6.1/1697 | CHLOROACETOPHENONE, LIQUID | N | N | X | X |
| 6.1/1697 | CHLOROACETOPHENONE, SOLID | X | X | X | X |
| 6.1/1699 | DIPHENYLCHLOROARSINE, LIQUID | X | X | X | X |
| 6.1/1699 | DIPHENYLCHLOROARSINE, SOLID | X | X | X | X |
| 6.1/1709 | 2,4-TOLUYLENEDIAMINE, LIQUID | N | N | X | N |
| 6.1/1709 | 2,4-TOLUYLENEDIAMINE, SOLID | X | X | X | X |
| 8/1729 | ANISOYL CHLORIDE, LIQUID | X | X | X | X |
| 8/1729 | ANISOYL CHLORIDE, SOLID | N | N | X | N |
| 8/1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX, LIQUID | X | X | X | X |
| 8/1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX, SOLID | N | N | X | N |
| 8/1743 | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX, LIQUID | X | X | X | X |
| 8/1743 | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX, SOLID | N | N | X | N |
| 8/1811 | POTASSIUM HYDROGENDIFLUORIDE, LIQUID | N | N | X | X (solution) |
| 8/1811 | POTASSIUM HYDROGENDIFLUORIDE, SOLID | X | X | X | X |
| 8/1812 | POTASSIUM FLUORIDE, LIQUID | N | N | X | N |
| 8/1812 | POTASSIUM FLUORIDE, SOLID | X | X | X | X |
| 8/1938 | BROMOACETIC ACID, SOLUTION | X | X | X | X |
| 8/1938 | BROMOACETIC ACID, SOLID | N | N | X | X |
| 6.1/2074 | ACRYLAMIDE, SOLUTION | N | N | X | N |
| 6.1/2074 | ACRYLAMIDE, SOLID | X | X | X | X |
| 6.1/2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE, LIQUID | X | X | X | X |
| 6.1/2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE, SOLID | N | N | X | N |
| 8/2511 | 2-CHLOROPROPIONIC ACID, SOLUTION | X | X | X | X |
| 8/2511 | 2-CHLOROPROPIONIC ACID, SOLID | X | X | X | N |
| 6.1/2662 | HYDROQUINONE, SOLUTION | N | N | X | N |
| 6.1/2662 | HYDROQUINONE, SOLID | X | X | X | X |
| 4.2/3052 | ALUMINIUM ALKYL HALIDES, LIQUID | X | X | X | X |
| 4.2/3052 | ALUMINIUM ALKYL HALIDES, SOLID | X | X | X | N |
| 6.1/3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | X | X | X | ? |
| 6.1/3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | X | X | X | ? |
| 4.2/3203 | PYROPHORIC ORGANOMETALLIC COMPOUND, LIQUID, WATER-REACTIVE, N.O.S. | X | X | X | N |
| 4.2/3203 | PYROPHORIC ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, N.O.S. | X | X | X | X |
| 6.1/3278 | ORGANOPHOSPHOROUS COMPOUND, TOXIC, N.O.S., LIQUID | X | X | X | X |
| 6.1/3278 | ORGANOPHOSPHOROUS COMPOUND, TOXIC, N.O.S., SOLID | X | X | X | N |
| 6.1/3280 | ORGANOARSENIC COMPOUND, N.O.S., LIQUID | X | X | X | N |
| 6.1/3280 | ORGANOARSENIC COMPOUND, N.O.S., SOLID | X | X | X | X |
| 6.1/3281 | METAL CARBONYLS, N.O.S., LIQUID | X | X | X | X |
| 6.1/3281 | METAL CARBONYLS, N.O.S., SOLID | X | X | X | N |
| 6.1/3282 | ORGANOMETALIC COMPOUND, TOXIC, N.O.S., LIQUID | X | X | X | N |
| 6.1/3282 | ORGANOMETALIC COMPOUND, TOXIC, N.O.S., LIQUID | X | X | X | X |
| 6.1/3315 | CHEMICAL SAMPLE, TOXIC, LIQUID | X | X | X | ? |
| 6.1/3315 | CHEMICAL SAMPLE, TOXIC, SOLID | X | X | X | ? |

Annex 2

List of UN entries having a melting point around the borderline of  the definition solid/liquid, including isomers and mixtures thereof

X means entry is listed in the regulation

N means entry not listed in the regulation.

| Class/UN No. | PSN | UN 12 (12 ed) | RID/ADR | IMDG (30-00) | CFR 49 |
| --- | --- | --- | --- | --- | --- |
| 6.1/1577 | CHLORODINITROBENZENES, LIQUID | X | X | X | N |
| 6.1/1577 | CHLORODINITROBENZENES, SOLID | X | X | X | X |
| 6.1/1578 | CHLORONITROBENZENES, LIQUID | N | N | X | X |
| 6.1/1578 | CHLORONITROBENZENES, SOLID | X | X | X | X |
| 6.1/1590 | DICHLOROANILINES, LIQUID | X | X | X | X |
| 6.1/1590 | DICHLOROANILINES, SOLID | X | X | X | X |
| 6.1/1597 | DINITROBENZENES, LIQUID | X | X | X | X |
| 6.1/1597 | DINITROBENZENES, SOLID | X | X | X | X |
| 6.1/1664 | NITROTOLUENES, LIQUID | X | X | X | X |
| 6.1/1664 | NITROTOLUENES, SOLID | X | X | X | X |
| 6.1/1665 | NITROXYLENES, LIQUID | X | X | X | X |
| 6.1/1665 | NITROXYLENES, SOLID | X | X | X | N |
| 6.1/1694 | BROMOBENZYL CYANIDES, LIQUID | X | X | X | X |
| 6.1/1694 | BROMOBENZYL CYANIDES, SOLID | X | X | X | X |
| 6.1/1708 | TOLUIDINES, LIQUID | X | X | X | X |
| 6.1/1708 | TOLUIDINES, SOLID | X | X | X | X |
| 6.1/1711 | XYLIDINES, LIQUID | X | X | X | X |
| 6.1/1711 | XYLIDINES, SOLID | X | X | X | X |
| 8/1805 | PHOSPHORIC ACID, LIQUID | X | X | X | X |
| 8/1805 | PHOSPHORIC ACID, SOLID | X | X | X | N |
| 6.1/1843 | AMMONIUM DINITRO-ortho-CRESOLATE, LIQUID | N | N | X | N |
| 6.1/1843 | AMMONIUM DINITRO-ortho-CRESOLATE, SOLID | X | X | X | X |
| 6.1/2038 | DINITROTOLUENES, LIQUID | X | X | X | X |
| 6.1/2038 | DINITROTOLUENES, SOLID | X | X | X | X |
| 6.1/2076 | CRESOLS, LIQUID | X | X | X | X |
| 6.1/2076 | CRESOLS, SOLID | X | X | X | N |
| 6.1/2077 | alpha-NAPHTHYLAMINE, LIQUID | N | N | X | N |
| 6.1/2077 | alpha-NAPHTHYLAMINE, SOLID | X | X | X | X |
| 6.1/2235 | para-chlorobenzyl chlorides, liquid | X | X | X | X |
| 6.1/2235 | para-chlorobenzyl chlorides, solid | N | N | X | N |
| 6.1/2239 | CHLOROTOLUIDINES, LIQUID | N | N | X | X |
| 6.1/2239 | CHLOROTOLUIDINES, SOLID | X | X | X | X |
| 6.1/2261 | XYLENOLS, LIQUID | N | N | X | N |
| 6.1/2261 | XYLENOLS, SOLID | X | X | X | X |
| 6.1/2306 | NITROBENZOTRIFLUORIDES, LIQUID | X | X | X | X |
| 6.1/2306 | NITROBENZOTRIFLUORIDES, SOLID | N | N | X | N |
| 8/2308 | NITROSYLSULPHURIC ACID, LIQUID | X | X | X | X |
| 8/2308 | NITROSYLSULPHURIC ACID, SOLID | X | X | X | N |
| 9/2315 | POLYCHLORINATED BIPHENYLS, LIQUID | P906 | P906 | X | X |
| 9/2315 | POLYCHLORINATED BIPHENYLS, SOLID | P906 | P906 | X | X |
| 6.1/2433 | CHLORONITROTOLUENES, LIQUID | X | X | X | X |
| 6.1/2433 | CHLORONITROTOLUENES, SOLID | X | X | X | X |
| 6.1/2669 | CHLOROCRESOLS, SOLUTION | X | X | X | X |
| 6.1/2669 | CHLOROCRESOLS, SOLID | N | N | X | X |
| 6.1/2730 | NITROANISOLES, LIQUID | X | X | X | N |
| 6.1/2730 | NITROANISOLES, SOLID | X | X | X | X |
| 6.1/2732 | NITROBROMOBENZENES, LIQUID | X | X | X | X |
| 6.1/2732 | NITROBROMOBENZENES, SOLID | X | X | X | X |
| 6.1/2753 | N-ETHYLBENZYLTOLUIDINES, LIQUID | X | X | X | X |
| 6.1/2753 | N-ETHYLBENZYLTOLUIDINES, SOLID | X | X | X | X |
| 6.1/2937 | alpha-METHYLBENZYL ALCOHOL, LIQUID | X | X | X | X |
| 6.1/2937 | alpha-METHYLBENZYL ALCOHOL, SOLID | N | N | X | N |

Annex 3

Discrepancies in the Dangerous Goods List

Note:	amendments are for identification purpose, only given in respect to the packing instructions concerning the use of packagings (except IBCs and large packagings).

Experts are invited to consider this list of discrepancies.

| UN Number | Amendment | Reasoning discrepancy |
| --- | --- | --- |
| 1611 | P002 should read P001 | According to the IMDG Amdt. 30-00 HEXAETHYL TETRAPHOSPHATE is a yellow liquid |
| 1704 | P002 should read P001 | According to the IMDG Amdt. 30-00 TETRAETHYL DITHIOPYROPHOSPHATE is a colourless liquid |
| 1792 | P002 should read P001 | According to the IMDG Amdt. 30-00 IODINE MONOCHLORIDE is a brown, heavy, oily liquid |
| 1793 | P002 should read P001 | According to the IMDG Amdt. 30-00 ISOPROPYL ACID PHOSPHATE is an oily liquid |
| 2305 | P001 should read P002 | According to the IMDG Amdt. 30-00 NITROBENZENESULPHONIC ACID are crystals |
| 2729 | P001 should read P002 | According to the IMDG Amdt. 30-00 HEXACHLOROBENZENE are white needle-like crystals |
| 2751 | P002 should read P001 | According to the IMDG Amdt. 30-00 DIETHYLTHIOPHOSPHORYL CHLORIDE is a colourless liquid with a perceptible odour |
| 2851 | P002 should read P001 | According to the IMDG Amdt. 30-00 BORON TRIFLUORIDE DIHYDRATE is a colourless liquid with a perceptible odour |
| 2936 | P002 should read P001 | According to the IMDG Amdt. 30-00 THIOLACTIC ACID is an oily liquid with a foul odour |

# ___________

# Text boxes

STSTE

Secretariat