#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2001/28

18 April 2001

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Nineteenth session, 2-6 July 2001,

# agenda item 5(b))

PACKAGINGS

Miscellaneous proposals

IBC Packing instructions

Transmitted by the expert from the United States of America

Background

1. 	After reviewing the IBC packing instruction assignments in the Dangerous Goods List the expert from the United States of America believes that some minor amendments need to be addressed by the Sub-Committee.  IBC07 applies to Division 4.3, PG II, Division 6.1, PG I and several Class 8 PG I solid substances (see Annex for a list of assigned substances). Currently IBC07 allows all types of rigid IBCs except for fibreboard IBCs.  The expert from the United States of America considers fibreboard IBCs to provide the same level of safety as other rigid IBCs especially when considering that fibreboard IBCs would be required to be transported in closed transport units and that they would be required to have siftproof liners.  Considering that IBC07 currently allows composite IBCs with fibreboard outer bodies (e.g. 11HG2), it does not seem reasonable to prohibit fibreboard IBCs.  Many of the substances that are assigned IBC07 in the UN Recommendations have been authorized to be transported in fibreboard IBCs in the US Hazardous Materials Regulations for many years.  The expert from the United States of America has considered the transport safety implications and has reviewed the US transportation incident data base and has found no justification for excluding fibreboard IBCs in IBC07. The Sub-Committee is requested to consider this proposal.

GE.01-

Proposal

3. 	In IBC07 add the following:

(5) 	Fibreboard (11G)

Under “Additional requirement:” the words “and fibreboard” should be added after the word “wooden”.

Annex

Substances Assigned “IBC07” in the UN 12th edition

UN No Name Class Sub-Risk PG IBC B

2624 MAGNESIUM SILICIDE 4.3 II IBC07 B2

2813 WATER-REACTIVE SOLID, N.O.S. 4.3 II IBC07 B2

2830 LITHIUM FERROSILICON 4.3 II IBC07 B2

1390 ALKALI METAL AMIDES 4.3 II IBC07 B2

3170 ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS 4.3 II IBC07 B2

3208 METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. 4.3 II IBC07 B2

3078 CERIUM, turnings or gritty powder 4.3 II IBC07 B2

1417 LITHIUM SILICON 4.3 II IBC07 B2

1400 BARIUM 4.3 II IBC07 B2

1393 ALKALINE EARTH METAL ALLOY, N.O.S. 4.3 II IBC07 B2

1394 ALUMINIUM CARBIDE 4.3 II IBC07 B2

1402 CALCIUM CARBIDE 4.3 II IBC07 B2

1401 CALCIUM 4.3 II IBC07 B2

1405 CALCIUM SILICIDE 4.3 II IBC07 B2

1396 ALUMINIUM POWDER, UNCOATED 4.3 II IBC07 B2

1436 ZINC POWDER or ZINC DUST 4.3 4.2 II IBC07 B2

1699 DIPHENYLCHLOROARSINE, SOLID 6.1 I IBC07 B1

1713 ZINC CYANIDE 6.1 I IBC07 B1

2025 MERCURY COMPOUND, SOLID, N.O.S. 6.1 I IBC07 B1

2570 CADMIUM COMPOUND 6.1 I IBC07 B1

2316 SODIUM CUPROCYANIDE, SOLID 6.1 I IBC07 B1

2471 OSMIUM TETROXIDE 6.1 I IBC07 B1

1692 STRYCHNINE or STRYCHNINE SALTS 6.1 I IBC07 B1

2628 POTASSIUM FLUOROACETATE 6.1 I IBC07 B1

2629 SODIUM FLUOROACETATE 6.1 I IBC07 B1

2026 PHENYLMERCURIC COMPOUND, N.O.S. 6.1 I IBC07 B1

1689 SODIUM CYANIDE 6.1 I IBC07 B1

1680 POTASSIUM CYANIDE 6.1 I IBC07 B1

1655 NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. 6.1 I IBC07 B1

1601 DISINFECTANT, SOLID, TOXIC, N.O.S. 6.1 I IBC07 B1

2757 CARBAMATE PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

1588 CYANIDES, INORGANIC, SOLID, N.O.S. 6.1 I IBC07 B1

1575 CALCIUM CYANIDE 6.1 I IBC07 B1

1570 BRUCINE 6.1 I IBC07 B1

1565 BARIUM CYANIDE 6.1 I IBC07 B1

1557 ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. 6.1 I IBC07 B1

1544 ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. 6.1 I IBC07 B1

1626 MERCURIC POTASSIUM CYANIDE 6.1 I IBC07 B1

3048 ALUMINIUM PHOSPHIDE PESTICIDE 6.1 I IBC07 B1

3345 PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

3285 VANADIUM COMPOUND, N.O.S. 6.1 I IBC07 B1

3284 TELLURIUM COMPOUND, N.O.S. 6.1 I IBC07 B1

3283 SELENIUM COMPOUND, N.O.S. 6.1 I IBC07 B1

3282 ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid 6.1 I IBC07 B1

3281 METAL CARBONYLS, N.O.S., solid 6.1 I IBC07 B1

3280 ORGANOARSENIC COMPOUND, N.O.S., solid 6.1 I IBC07 B1

3278 ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid 6.1 I IBC07 B1

3172 TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. 6.1 I IBC07 B1

2630 SELENATES or SELENITES 6.1 I IBC07 B1

3143 DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. 6.1 I IBC07 B1

2642 FLUOROACETIC ACID 6.1 I IBC07 B1

3027 COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2783 ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2781 BIPYRIDILIUM PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2779 SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

3349 PYRETHROID PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2759 ARSENICAL PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2761 ORGANOCHLORINE PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2763 TRIAZINE PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2786 ORGANOTIN PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2771 THIOCARBAMATE PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

3146 ORGANOTIN COMPOUND, SOLID, N.O.S. 6.1 I IBC07 B1

2777 MERCURY BASED PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

2775 COPPER BASED PESTICIDE, SOLID, TOXIC 6.1 I IBC07 B1

3261 CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. 8 I IBC07 B1

2430 ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) 8 I IBC07 B1

3262 CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. 8 I IBC07 B1

3260 CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. 8 I IBC07 B1

3259 AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. 8 I IBC07 B1

1905 SELENIC ACID 8 I IBC07 B1

3147 DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. 8 I IBC07 B1

1759 CORROSIVE SOLID, N.O.S. 8 I IBC07 B1

3263 CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. 8 I IBC07 B1

__________

# Text boxes

STSTE

Secretariat