# UN/SCETDG/20/INF.15

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

(Twentieth session, 3-12 December 2001,

agenda item 5 (b))

PACKAGINGS

# Miscellaneous proposals

# Packaging Marks

Transmitted by the Expert from the United Kingdom

- The expert from the United Kingdom notes that the examples of UN marks for packagings, large packagings and IBC's in Part 6 of the 12th Edition of the Recommendations on the Transport of Dangerous Goods show dates which in some cases are nearly 20 years old. As the Recommendations are intended as Model Regulations it is suggested that these examples should be revised to reflect more recent dates especially as the century has now changed.

- The expert from the United Kingdom suggests that the examples for IBCs be given a separate paragraph in the Model Regulations to follow the pattern for packagings and large packagings.

- In order to ensure that examples of marks in future revised editions of the Model Regulations are kept up to date it is proposed that the Secretariat be authorised to revise the examples each biennium. A similar proposal was adopted at the last meeting of the ICAO Dangerous Goods Panel.

- The expert from the United Kingdom invites the Sub-Committee to consider and agree the amendments proposed below.

#### Proposal

##### Packagings

6.1.3.9	Examples of markings for NEW packagings

|  | 4G/Y145/S/02 NL/VL823 | as in 6.1.3.1 (a), (b), (c), (d) and (e) as in 6.1.3.1 (f) and (g) | For a new fibreboard box |
| --- | --- | --- | --- |
|  | lAl/Y1.4/150/98 NL/VL824 | as in 6.1.3.1 (a), (b), (c), (d) and (e) as in 6.1.3.1 (f) and (g) | For a new steel drum to contain liquids |
|  | 1A2/Y150/S/01 NL/VL825 | as in 6.1.3.1 (a), (b), (c), (d) and (e) as in 6.1.3.1 (f) and (g) | For a new steel drum to contain solids, or inner packagings |
|  | 4HW/Y136/S/98 NL/VL826 | as in 6.1.3.1 (a), (b), (c), (d) and (e) as in 6.1.3.1 (f) and (g) | For a new plastics box of equivalent specification |
|  | 1A2/Y/100/01 USA/MM5 | as in 6.1.3.1 (a), (b), (c), (d) and (e) as in 6.1.3.1 (f) and (g) | For a remanufactured steel drum to contain liquids |

6.1.3.10	Examples of markings for RECONDITIONED packagings

|  | 1A1/Y1.4/150/97 NL/RB/01 RL | as in 6.1.3.l (a), (b), (c), (d) and (e) as in 6.1.3.7 (h), (i) and (j) |
| --- | --- | --- |
|  | 1A2/Y150/S/99 USA/RB/00 R | as in 6.1.3.1 (a), (b), (c), (d), and (e) as in 6.1.3.7 (h), (i) and (j) |

6.1.3.11	Example of marking for SALVAGE packagings

|  | 1A2T/Y300/S/01 USA/abc | as in 6.1.3.1 (a), (b), (c), (d) and (e) as in 6.1.3.1 (f) and (g) |
| --- | --- | --- |

# Infectious packagings

6.3.1.2	Example of marking:

|  | 4G/CLASS 6.2/01 | as in 6.3.1.1 (a), (b), (c) and (d) |
| --- | --- | --- |
|  | S/SP-9989-ERIKSSON | as in 6.3.1.1 (e), (f) |

## IBCs

6.5.2.2	Examples of markings for various types of IBC in accordance with (a) to (h) above:

|  | 11A/Y/02 99 NL/Mulder 007 5500/1500 | For a metal IBC for solids discharged for instance by gravity and made from steel/for Packing Groups II and III/ manufactured in February 1999/authorized by the Netherlands/manufactured by Mulder and of a design type to which the competent authority has allocated serial number 007/the stacking test load in kg/the maximum permissible gross mass in kg. |
| --- | --- | --- |
|  | 13H3/Z/03 01 F/Meunier 1713 0/1500 | For a flexible IBC for solids discharged for instance by gravity and made from woven plastics with a liner/not designed to be stacked. |
|  | 31H1/Y/04 99 GB/9099 10800/1200 | For a rigid plastics IBC for liquids made from plastics with structural equipment withstanding the stack load. |
|  | 31HA1/Y/05 01 D/Muller 1683 10800/1200 | For a composite IBC for liquids with a rigid plastics inner receptacle and a steel outer casing. |
|  | 11C/X/01 02 S/Aurigny 9876 3000/910 | For a wooden IBC for solids with an inner liner and authorized for Packing Group I solids. |

Renumber the subsequent paragraphs in 6.5.2.

# Large Packagings

6.6.3.2	Examples of the marking

|  | 50 A/X/05 01/N/PQRS 2500/1000 |  | For a large steel packaging suitable for stacking; stacking load: 2500 kg; maximum gross mass: 1000 kg. |
| --- | --- | --- | --- |
|  | 50 H/Y/04 02/D/ABCD 1002 0/800 |  | For a large plastics packaging not suitable for stacking; maximum gross mass: 800 kg. |
|  | 51H/Z/06 01/S/0902 0/500 |  | For a large flexible packaging not suitable for stacking; maximum gross mass: 500 kg. |

________________