#### UNITED

# NATIONS

Distr.

# GENERAL

# TRANS/WP.15/AC.1/2001/22

# 19 March  2001

Original: ENGLISH and FRENCH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

(Bern, 28 May – 1 June 2001)

PART 3

# Note by the Secretariat */

This document contains proposed amendments to Part 3 of the restructured RID/ADR for harmonization with the 12th revised edition of the United Nations Recommendations on the Transport of Dangerous Goods, Model Regulations, on the basis of the decisions of the Committee of Experts on the Transport of Dangerous Goods at its twenty-first session, (Geneva, 4-13 December 2000) (See ST/SG/AC.10/27 and addenda 1 and 2).

PART 3

Chapter 3.1

3.1.2	Add the following notes under the heading "Proper shipping name":

"NOTE 1: For proper shipping names to be used for dangerous goods carried as limited quantities, see Chapter 3.4.

NOTE 2: For proper shipping names used for the carriage of samples, see 2.1.4.1".

_______

*/	Circulated by the Central Office  for International Carriage by Rail

(OCTI) under the symbol OCTI/RID/GT/III/2001/22.

3.1.2.6 and

3.1.2.7		Insert new paragraphs 3.1.2.6 and 3.1.2.7 to read as follows:

"3.1.2.6 	Except for self-reactive substances and organic peroxides and unless it is already included in capital letters in the name indicated in Column (2) of Table A of Chapter 3.2, the word "STABILIZED" shall be added as part of the proper shipping name of a substance which without stabilization would be forbidden from carriage in accordance with 1.1.3 due to it being liable to dangerously react under conditions normally encountered in carriage (e.g.: "TOXIC LIQUID, ORGANIC, N.O.S., STABILIZED").

When temperature control is used to stabilize such substances to prevent the development of any dangerous excess pressure, then:

(a)	For liquids: where the SADT is less than 50 °C, the provisions of 2.2.41.1.17, the special provision V8 of Chapter 7.2 ,the special provision S4 of Chapter 8.5  and the special provisions of Chapter 9.6  shall apply; for transport in IBCs and tanks, all the provisions applicable to UN No 3239 apply (see in particular 4.1.7.2, IBC520 et 4.2.1.13);

(b)	For gases: the conditions of carriage shall be approved by the competent authority.

3.1.2.7		Hydrates may be included under the proper shipping name for the anhydrous substance."

Renumber sub-section 3.1.2.6 as 3.1.2.8 accordingly.

3.1.2.8.1	(Former 3.1.2.6.1) Amend to read as follows:

"3.1.2.8.1	Generic and "not otherwise specified" proper shipping names that are assigned to special provision 274 in Column (6) of Table A in Chapter 3.2 shall be supplemented with their technical or chemical group names unless a national law or international convention prohibits its disclosure if it is a controlled substance. For explosives of Class 1, the dangerous goods description may be supplemented by additional descriptive text to indicate commercial or military names.  Technical and chemical group names shall be entered in brackets immediately following the proper shipping name. An appropriate modifier, such as "contains" or "containing" or other qualifying words such as "mixture", "solution", etc. and the percentage of the technical constituent may also be used.  For example: "UN 1993 Flammable liquid, n.o.s. (contains xylene and benzene), 3, PG II"."

3.1.2.8.1.1	(Former 3.1.2.6.1.1) Amend to read as follows:

"3.1.2.8.1.1	The technical name shall be a recognized chemical or other name currently used in scientific and technical handbooks, journals and texts. Trade names shall not be used for this purpose. In the case of pesticides, only ISO common name(s), other name(s) in the World Health Organization (WHO) Recommended Classification of Pesticides by Hazard and Guidelines to Classification, or the name(s) of the active substance(s) may be used."

Renumber following paragraphs and sub-paragraphs accordingly.

Chapter 3.2

Table A

In Table A, when the same UN number applies to both the liquid and solid form of a substance, the liquid entry is always to be listed first.

Wherever they appear in Column (6) of Table A, delete special provisions "15", "18", "36", "107", "222", "268", "287", "628", "629", "630" and "631".

Wherever it appears throughout Chapter 3.2:

- 	For all substances assigned to IBC08, packing group III : apply B3;

- 	For all substances assigned to IBC08, packing groups I or II : apply B4;

- 	For all substances assigned to IBC08, packing group III (other than those of Class 4.3): delete B4;

- 	For all substances assigned to IBC08: delete B3 when B4 is also applied.

Insert the following new entries for UN 2030 (packing groups I and III):

| UN No. | Name and description | Class | ClassifCode | Pack. group | Labels | Special prov. | Limited quant. | Packaging | UN Portable tank |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruc-tions | Special packing prov. | Mixed packing prov. | Instruc- tions | Special prov. |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 4.1.4 | 4.1.4 | 4.1.10 | 4.2.4.2 | 4.2.4.3 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 2030 | HYDRAZINE AQUEOUS SOLUTION, with more than 37% hidrazine, by mass | 8 | CT1 | I | 8 +6.1 | 298 | LQ0 | P001 |  | MP2 | T20 | TP2 TP13 |
|  |  | 8 | CT1 | II | 8 +6.1 | 530 | LQ22 | P001 IBC02 |  | MP15 | T15 | TP2 TP13 |
|  |  | 8 | CT1 | III | 8 +6.1 |  | LQ5 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP2 |

| RID/ADR tank |  | Vehicle for tank carriage | Transport category | Special provisions for carriage |  |  |  | Hazard identifi-cation No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Opera-tion |  |  |  |
| 4.3 | 4.3.5, 6.8.4 | 9.1.1.2 | 1.1.3.6 | 7.2.4 | 7.3.3 | 7.5.11 | 8.5 | 5.3.2.3 |  | 3.1.2 |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| L10DH | TE1? TU14 ? | AT | 1 |  |  | CV13 CV28 |  | 886 | 2030 | HYDRAZINE AQUEOUS SOLUTION, with more than 37% hidrazine, by mass |
| L10BH |  | AT | 2 |  |  | CV13 CV28 |  |  |  |  |
| L4BN |  | AT | 3 |  |  | CV13 CV28 |  | 86 |  |  |

Add the following new entries:

| UN No. | Name and description | Class | ClassifCode | Pack. group | Labels | Special prov. | Limited quant. | Packaging | UN Portable tank |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruc-tions | Special packing prov. | Mixed packing prov. | Instruc- tions | Special prov. |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 4.1.4 | 4.1.4 | 4.1.10 | 4.2.4.2 | 4.2.4.3 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) |
| 1153 | ETHYLENE GLYCOL DIETHYL ETHER | 3 | F1 | II | 3 |  | LQ4 | P001 IBC02 R001 |  | MP19 | T4 | TP1 |
| 1372 | FIBRES, ANIMAL or FIBRES, VEGETABLE burnt, wet or damp | 4.2 | S2 | NOT SUBJECT TO RID/ADR |
| 1387 | WOOL WASTE, WET | 4.2 | S2 | NOT SUBJECT TO RID/ADR |
| 1856 | RAGS, OILY | 4.2 | S2 | NOT SUBJECT TO RID/ADR |
| 1857 | TEXTILE WASTE, WET | 4.2 | S2 | NOT SUBJECT TO RID/ADR |
| 3359 | FUMIGATED UNIT | 9 | M11 |  | 9 | 302 | LQ0 |  |  |  |  |  |
| 3360 | FIBRES, VEGETABLE, DRY | 4.1 | F1 | NOT SUBJECT TO RID/ADR |
| 3361 | CHLOROSILANES, TOXIC, CORROSIVE, N.O.S. | 6.1 | TC1 | II | 6.1 +8 | 274 | LQ0 | P001 IBC01 |  | MP15 | T11 | TP2 TP13 TP27 |
| 3362 | CHLOROSILANES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. | 6.1 | TFC | II | 6.1 +3 +8 | 274 | LQ0 | P001 IBC01 |  | MP15 | T11 | TP2 TP13 TP27 |
| 3363 | DANGEROUS GOODS IN MACHINERY or DANGEROUS GOODS IN APPARATUS | 9 | M11 |  | 9 | 301 | LQ0 | P907 |  |  |  |  |
| 3371 | 2 -METHYLBUTANAL | 3 | F1 | II | 3 |  | LQ4 | P001 IBC02 R001 |  | MP19 | T4 | TP1 |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | WF1 | I | 4.3 +4.1 | 274 | LQ0 | P403 IBC04 |  | MP2 |  |  |
|  |  | 4.3 | WFI | II | 4.3 +4.1 | 274 | LQ11 | P410 IBC04 |  | MP14 |  |  |
|  |  | 4.3 | WFI | III | 4.3 +4.1 | 223 274 | LQ12 | P410 IBC06 |  | MP14 |  |  |
| 3373 | DIAGNOSTIC SPECIMENS | 6.2 | I1 |  | 6.2 | 274 634 | LQ0 | P650 |  | MP15 |  |  |
| 3374 | ACETYLENE, SOLVENT FREE | 2 | 1F |  | 2.1 |  | LQ0 | P200 | PP23 | MP9 |  |  |
| 3375 | AMMONIUM NITRATE EMULSION or SUSPENSION or GEL, intermediate for blasting explosives | 5.1 | O2 | II | 5.1 | 306 309 | LQ11 | P099 IBC99 |  | MP10 | T2 | TP9 |
| 3376 | 4 - NITROPHENYLHY-DRAZINE, with not less than 30% water, by mass | 4.1 | D | II | 4.1 | 28 | LQ0 | P406 | PP26 | MP2 |  |  |

| RID/ADR tank |  | Vehicle for tank carriage | Transport category | Special provisions for carriage |  |  |  | Hazard identifi-cation No. | UN No. | Name and description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Opera-tion |  |  |  |
| 4.3 | 4.3.5, 6.8.4 | 9.1.1.2 | 1.1.3.6 | 7.2.4 | 7.3.3 | 7.5.11 | 8.5 | 5.3.2.3 |  | 3.1.2 |
| (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) | (1) | (2) |
| LGBF |  | FL | 2 |  |  |  | S2 S20 | 33 | 1153 | ETHYLENE GLYCOL DIETHYL ETHER |
| NOT SUBJECT TO RID/ADR | 1372 | FIBRES, ANIMAL or FIBRES, VEGETABLE burnt, wet or damp |
| NOT SUBJECT TO RID/ADR | 1387 | WOOL WASTE, WET |
| NOT SUBJECT TO RID/ADR | 1856 | RAGS, OILY |
| NOT SUBJECT TO RID/ADR | 1857 | TEXTILE WASTE, WET |
|  |  | AT | 3?? 4?? |  |  |  |  |  | 3359 | FUMIGATED UNIT |
| NOT SUBJECT TO RID/ADR | 3360 | FIBRES, VEGETABLE, DRY |
| L4BH | TU15 TE1 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 68 | 3361 | CHLOROSILANES, TOXIC, CORROSIVE, N.O.S. |
|  |  |  | 2 |  |  | CV13 CV28 | S2 S9 S19 | 638 | 3362 | CHLOROSILANES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. |
|  |  | AT | 3?? 4?? |  |  |  |  |  | 3363 | DANGEROUS GOODS IN MACHINERY or DANGEROUS GOODS IN APPARATUS |
| LGBF |  | FL | 2 |  |  |  | S2 S20 | 33 | 3371 | 2 -METHYLBUTANAL |
|  |  |  | 0 | V1 |  | CV23 |  | 423 | 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. |
|  |  |  | 0 | V1 |  | CV23 |  | 423 |  |  |
|  |  |  | 0 | V1 |  | CV23 |  | 423 |  |  |
|  |  |  | 2 |  |  | CV13 CV25 CV26 CV28 | S3 |  | 3373 | DIAGNOSTIC SPECIMENS |
| CxBN(M) |  | FL | 2 | V7 |  | CV9 CV10 | S2 | 23 | 3374 | ACETYLENE, SOLVENT FREE |
|  |  | AT | 2 |  |  | CV24 | S9 S14 | 50 | 3375 | AMMONIUM NITRATE EMULSION or SUSPENSION or GEL, intermediate for blasting explosives |
|  |  |  | 1 |  |  | CV13 CV28 | S17 |  | 3376 | 4 - NITROPHENYLHY-DRAZINE, with not less than 30% water, by mass |

Amend the following entries as follows:

UN 0015	Delete "8" in column (5);

UN 0016	Delete "8" in column (5);

UN 0154	This UN number becomes new UN 3364. Add "PP24" in column (9a);

UN 0155	This UN number becomes new UN 3365. Add "PP24" in column (9a);

UN 0209	This UN number becomes new UN 3366. Add "PP24" in column (9a);

UN 0214	This UN number becomes new UN 3367. Add "PP24" in column (9a);

UN 0215	This UN number becomes new UN 3368. Add "PP24" in column (9a);

UN 0220	This UN number becomes new UN 3370. Add "PP78" in column (9a);

UN 0223	Delete this entry;

UN 0234	This UN number becomes new UN 3369. Add "PP24" in column (9a);

UN 0303	Delete "8" in column (5);

UN 0331	Add "(AGENT, BLASTING, TYPE B)" in column (2);

UN 0332	Add "(AGENT, BLASTING, TYPE E)" in column (2);

UN 0503	Delete "PYROTECHNIC" in the name in column (2) (three times) and add "235" in 	column (6).

UN 1008 	Amend the name in column (2) to read: "BORON TRIFLUORIDE"

UN 1040	Amend the name in column (2) to read: "ETHYLENE OXIDE, or ETHYLENE OXIDE WITH NITROGEN up to a total pressure of 1 MPa (10 bar) at 50 ºC";

UN 1057	In column (2), delete "(cigarettes)";

UN 1062	Amend the name in column (2) to read: "METHYL BROMIDE with not more than 2% chloropicrin";

UN 1177 	Amend the name in column (2) to read:  "2-ETHYLBUTYL ACETATE";

UN 1278 	Amend the name in column (2) to read: "1-CHLOROPROPANE";

UN 1374	Insert special provision "300" in column (6);

UN 1381	Insert "TP31" in column (11);

UN 1422	Insert "TP31" in column (11);

UN 1428	Insert "TP31" in column (11);

UN 1556	For packing group I: insert "T14" in column (10) and "TP2", "TP9", "TP13" and "TP27" in column (11);

For packing group II: insert "T11" in column (10) and insert "TP2", "TP13" and "TP27" in column (11);

For packing group III: insert "T7" in column (10) and insert "TP2" and "TP28" in column (11);

UN 1579	Add "T4" and "TP1" in column (10) and (11) respectively;

UN 1581	Amend the name in column (2) to read: "CHLOROPICRIN AND METHYL BROMIDE MIXTURE with more than 2% 	chloropicrin";

UN 1614	Replace "P200" with "P099" in column (8);

UN 1702 	Amend the name in column (2) to read : "1,1,2,2-TETRACHLOROETHANE";

UN 1790	For packing group I: add "PP79" and "PP81" in column (9a);

UN 1859	Amend the name in column (2) to read: "SILICON TETRAFLUORIDE";

UN 1863	For packing group I: Add "TP28" in column (11);

UN 1866	For packing group I: Add "TP28" in column (11);

UN 1906	Add "TP28" in column (11);

UN 1911	Amend the name in column (2) to read: "DIBORANE";

UN 1942	Add "total" before "combustible" and replace "substances" with " "material" in the name in column (2) and add "306" in column (6);

UN 1962	Amend the name in column (2) to read: "ETHYLENE";

UN 1982	Amend the name in column (2) to read: "TETRAFLUOROMETHANE (REFRIGERANT GAS R14);

UN 1993 	For packing group I: Add "TP27" in column (11);

UN 2031	For packing groups I and II: replace "P802" with "P001" in column (8) and add "PP81"  in column (9a);

UN 2036	Amend the name in column (2) to read: "XENON";

UN 2037	Add special provision "303" in column (6);

UN 2067	Delete "628" and add "307" in column (6);

UN 2068	Delete this entry;

UN 2069	Delete this entry;

UN 2070	Delete this entry;

UN 2072	Delete this entry;

UN 2193	Amend the name in column (2) to read: "HEXAFLUOROETHANE (REFRIGERANT GAS R116)";

UN 2198	Amend the name in column (2) to read : "PHOSPHORUS PENTAFLUORIDE";

UN 2203	Amend the name in column (2) to read : "SILANE";

UN 2257	Insert "TP31" in column (11);

UN 2264 	Amend the name in column (2) to read: "N, N-DIMETHYLCYCLOHEXYLAMINE";

UN 2277	Amend the name in column (2) to read: "ETHYL METHACRYLATE, STABILIZED";

UN 2315	Add special provision "305" in column (6);

UN 2417	Amend the name in column (2) to read: "CARBONYL FLUORIDE";

UN 2451	Amend the name in column (2) to read: "NITROGEN TRIFLUORIDE";

UN 2531	Insert "TP30" in column (11);

UN 2571	Add "TP28" in column (11);

UN 2579	Insert "TP30" in column (11);

UN 2672	Add new special provision "B13" in column (9a);

UN 2680	Amend the name in column (2) to read: "LITHIUM HYDROXIDE";

UN 2684 	Amend the name in column (2) to read:  "3-DIETHYLAMINOPROPYLAMINE";

UN 2699	Replace "P802" with "P001" in column (8);

UN 2740	Insert "T20" in column (10) and insert "TP2" and "TP13" in column (11);

UN 2793	Delete special provision "107" in column (6) and add special provision "223";

UN 2797	Add "TP28" in column (11);

UN 2880	Amend the name in column (2) to read:

"CALCIUM HYPOCHLORITE, HYDRATED, or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE, with not less than 5.5% but not more than 16% water";

UN 2907 	Add "B14" and "PP80" in column (9a);

UN 3027 	Delete the portable tank instructions in columns (10) and (11);

UN 3028	Add special provision "304" in column (6);

UN 3052 	For the solid entry, delete the portable tank instructions in columns (10) and (11);

UN 3090	Add special provision "310" in column (6);

UN 3151	Add special provision "305" in column (6);

UN 3152	Add special provision "305" in column (6);

UN 3166	Amend the name in column (2) to read as follows:

"ENGINE, INTERNAL COMBUSTION or VEHICLE, FLAMMABLE GAS, POWERED or VEHICLE, FLAMMABLE LIQUID, POWERED";

UN 3221	Replace "LQ0" with "LQ14" in column (7);

UN 3222	Replace " LQ0" with "LQ15" in column (7);

UN 3223	Replace " LQ0" with " LQ14" in column (7);

UN 3224	Replace " LQ0" with " LQ15" in column (7);

UN 3225	Replace " LQ0" with " LQ16" in column (7);

UN 3227	Replace " LQ0" with " LQ16" in column (7);

UN 3229	Replace " LQ0" with " LQ16" in column (7);

UN 3250	Add "TP28" in column (11);

UN 3268	Delete "pyrotechnic" in the name in column (2) replace "235" with "280" in column (6) and add "LP902" in column (8);

UN 3279 	For packing group I: add TP 27 in column (11);

UN 3295	For packing group I: add "TP28" in column (11);

UN 3344	Add "PP80" in column (9a);

UN 3353	Delete this entry;

Chapter 3.3

SP 15 		Delete.

SP 18 		Delete.

SP 36	Delete.

SP 107 		Delete.

SP 119	Amend the last sentence to read: "Refrigerating machines and refrigerating machine components are not subject to the requirements of RID/ADR if they contain less than 12 kg of gas in Class 2, group A or O according to 2.2.2.1.3, or if they contain less than 12 litres ammonia solution (UN 2672).".

SP 162		Replace "61 °C" with "60.5 °C".

SP 188		Amend to read as follows:

"Lithium cells and batteries offered for carriage are not subject to other provisions of  RID/ADR if they meet the following:

(a) 	For a lithium metal or lithium alloy cell, the lithium content is not more than 1 g, and for a lithium-ion cell, the lithium-equivalent content is not more than 1.5 g;

(b) 	For a lithium metal or lithium alloy battery the aggregate lithium content is not more than 2 g, and for a lithium-ion battery, the aggregate lithium-equivalent content is not more than 8 g;

(c)	Each cell or battery is of the type proved to meet the requirements of each test in the Manual of Tests and Criteria, Part III, sub-section 38.3;

(d) 	Cells and batteries are separated so as to prevent short circuits and are packed in strong packagings, except when installed in equipment; and

(e)	Except when installed in equipment, each package containing more than 24 lithium cells or 12 lithium batteries shall in addition meet the following requirements:

(i)	Each package shall be marked indicating that it contains lithium batteries and that special procedures should be followed in the event that the package is damaged;

(ii)	Each shipment shall be accompanied with a document indicating that packages contain lithium batteries and that special procedures  should be followed in the event a package is damaged;

(iii)	Each package is capable of withstanding a 1.2 m drop test in any orientation without damage to cells or batteries contained therein, without shifting of the contents so as to allow battery to battery (or cell to cell) contact and without release of contents; and

(iv)	Except in the case of lithium batteries packed with equipment, packages may not exceed 30 kg gross mass.

As used above and elsewhere in RID/ADR, "lithium content" means the mass of lithium in the anode of a lithium metal or lithium alloy cell, except in the case of a lithium-ion cell the "lithium-equivalent content" in grams is calculated to be 0.3 times the rated capacity in ampere-hours.".

SP 193		Amend to read as follows:

"This entry may only be used for uniform ammonium nitrate based fertilizer mixtures of the nitrogen, phosphate or potash type, containing not more than 70% ammonium nitrate and not more than 0.4% total combustible/organic material calculated as carbon or with not more than 45% ammonium nitrate and unrestricted combustible material.  Fertilizers within these composition limits are not subject to the provisions of RID/ADR if shown by a Trough Test (see Manual of Tests and Criteria, Part III, sub-section 38.2) not to be liable to self-sustaining decomposition.".

(Consequential amendment: delete SP 624).

SP 196		Amend to read as follows:

"Formulations which in laboratory testing neither detonate in the cavitated state nor deflagrate, which show no effect when heated under confinement and which exhibit no explosive power may be carried under this entry. The formulation must also be thermally stable (i.e. the SADT is 60 °C or higher for a 50 kg package). Formulations not meeting these criteria shall be carried under the provisions of Class 5.2, (see 2.2.52.4).".

SP 216		Add at the end of the paragraph the following text:

"Sealed packets containing less than 10 ml of a packing group II or III flammable liquid absorbed into a solid material are not subject to the requirements of RID/ADR provided there is no free liquid in the packet.".

SP 222 		Delete.

SP 227		Delete the first sentence.

SP 230		Amend (a) to read: "(a) Each cell or battery is of the type proved to meet the requirements of each test of the Manual of Tests and Criteria, Part III, sub-section 38.3;".

SP 235		Amend to read as follows:

"This entry applies to articles which contain Class 1 explosive substances and which may also contain dangerous goods of other classes. These articles are used as life-saving vehicle air bag inflators or air bag modules or seat-belt pretensioners.".

SP 251		Add the following text:

"Chemical kits and first aid kits containing dangerous goods in inner packagings which do not exceed the quantity limits applicable to individual substances as specified in Column (7) of Table A of Chapter 3.2  may be carried in accordance with Chapter 3.4.".

SP 268		Delete.

SP 280		Amend to read as follows:

"This entry applies to articles which are used as life-saving vehicle air bag inflators, or air bag modules or seat-belt pretensioners and which contain dangerous goods of Class 1 or dangerous goods of other classes and when carried as component parts and when these articles as presented for carriage have been tested in accordance with Test series 6 (c) of Part I of the Manual of Tests and Criteria, with no explosion of the device, no fragmentation of device casing or pressure vessel, and no projection hazard nor thermal effect which would significantly hinder fire-fighting or other emergency response efforts in the immediate vicinity.".

SP 287		Delete.

SP 291	Amend the last sentence to read:

"Refrigerating machines and refrigerating-machine components are not subject to the requirements of RID/ADR if they contain less than 12 kg of gas.".

SP 566		Amend to read:

"UN No. 2030 hydrazine aqueous solution, with more than 37% hydrazine, by mass, is a 		substance of Class 8.".

SP 624		Delete. (See also SP 193).

SP 628		Delete (Consequential amendment from new 307).

SP 629		Delete.

SP 630		Delete.

SP 631		Delete.

Add the following new special provisions:

"298	Solutions with a flash point of 60.5 °C or less shall bear a FLAMMABLE LIQUID label.

300	Fish meal or fish scrap shall not be carried if the temperature at the time of loading exceeds 35 °C or 5 °C above the ambient temperature whichever is higher.

301	This entry only applies to machinery or apparatus containing dangerous substances as a residue or an integral element of the machinery or apparatus. It shall not be used for machinery or apparatus for which a proper shipping name already exists in Table A of Chapter 3.2. Machinery and apparatus carried under this entry shall only contain dangerous goods which are authorized to be carried in accordance with the provisions of Chapter 3.4. The quantity of dangerous goods in machinery or apparatus shall not exceed the quantity specified in Column (7) of Table A of Chapter 3.2 for each item of dangerous goods contained. If the machinery or apparatus contains more than one item of dangerous goods, the individual substances shall not be capable of reacting dangerously with one another (see 4.1.1.6). When it is required to ensure liquid dangerous goods remain in their intended orientation, package orientation labels meeting the specifications of ISO 780:1997 shall be affixed on at least two opposite vertical sides with the arrows pointing in the correct direction.

The competent authority may exempt from regulation machinery or apparatus which would otherwise be carried under this entry. The carriage of dangerous goods in machinery or apparatus where the quantity of dangerous goods exceeds the quantity specified in Column (7) of Table A of Chapter 3.2 is authorized when approved by the competent authority.

302		In the proper shipping name, the word "UNIT" means:

a vehicle;

a wagon (RID only);

a container;

a road tank vehicle; or

a tank.

Fumigated containers and vehicles are only subject to the provisions of 5.5.2.

303 		The classification of UN 2037 shall be based on the gases contained therein and in accordance with the provisions of 2.2.2.

304		Batteries, dry, containing corrosive electrolyte which will not flow out of the battery if the battery case is cracked are not subject to the requirements of RID/ADR provided the batteries are securely packed and protected against short-circuits. Examples of such batteries are: alkali-manganese, zinc-carbon, nickel-metal hydride and nickel-cadmium batteries.

305		These substances are not subject to the requirements of RID/ADR when in concentrations of not more than 50 mg/kg.

306		This entry may only be used for substances that do not exhibit explosive properties of Class 1 when tested in accordance to Test Series 1 and 2 of Class 1 (see Manual of Tests and Criteria, Part I).

307		This entry may only be used for uniform mixtures containing ammonium nitrate as the main ingredient within the following composition limits:

(a)	Not less than 90 % ammonium nitrate with not more than 0.2% total combustible/organic  material calculated as carbon and with added matter, if any, which is inorganic and inert towards ammonium nitrate ; or

(b) 	Less than 90% but more than 70% ammonium nitrate with other inorganic materials  or  more than 80% but less than 90% ammonium nitrate mixed with calcium carbonate and/or dolomite and not more than 0.4% total combustible/organic material calculated as carbon; or

(c)	Nitrogen type ammonium nitrate based fertilizers containing mixtures of ammonium nitrate and ammonium sulphate with more than 45% but less than 70% ammonium nitrate and not more than 0.4% total combustible/organic material calculated as carbon such that the sum of the percentage compositions of ammonium nitrate and ammonium sulphate exceeds 70%.

309		This entry applies to non sensitised emulsions, suspensions and gels consisting primarily of a mixture of ammonium nitrate and a fuel phase, intended to produce a Type E blasting explosive only after further processing prior to use. The mixture typically has the following composition: 60 - 85 % ammonium nitrate; 5 - 30% water; 2 - 8% fuel;

0.5  - 4% emulsifier or thickening agent; 0 - 10 % soluble flame supressants and trace additives. Other inorganic nitrate salts may replace part of the ammonium nitrate. These substances shall not be classified and carried unless authorized by the competent authority.

310		The testing requirements in Chapter 38.3 of the Manual of Tests and Criteria do not apply to production runs consisting of not more than 100 lithium cells and batteries, or to pre-production prototypes of lithium cells and batteries when these prototypes are carried for testing, if:

(a)	the cells and batteries are carried in an outer packaging that is a metal, plastics or plywood drum or a metal, plastics or wooden box and that meets the criteria for packing group I packagings; and

(b)	each cell and battery is individually packed in an inner packaging inside an outer packaging and is surrounded by cushioning material that is non-combustible, and non-conductive.".

Chapter 3.4

3.4.4 (c)		Amend the last paragraph to read as follows:

"These markings shall be displayed within a diamond-shaped area. The width of line forming the diamond shall be at least 2 mm; the number shall be at least 6 mm high. Where more than one substance assigned to different UN numbers are included in the package, the diamond shall be large enough to include each relevant UN number.".

_________

# Text boxes

E

Economic and Social

Council