#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2002/24

3 April 2002

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Twenty-first session, 1-10 July 2002,

# agenda item 8 (c))

LISTING AND CLASSIFICATION

Miscellaneous amendment proposals (Parts 2 and 3)

# Requirements for toxic by inhalation substances

## Transmitted by the expert from the United States of America

Introduction

1.	During previous sessions, the Sub-Committee considered amending the Model Regulations to include requirements for substances that are toxic by inhalation (TIH substances). Hazard communication requirements for TIH substances were discussed on the basis of ST/SG/AC.10/C.3/1998/26.  The intention of this proposal was to improve the hazard communication requirements applicable to these substances since it is not readily apparent whether a substance poses an inhalation, oral or dermal toxicity hazard and because the inhalation hazard poses a greater risk in transport if inadvertently released.  Requirements for packaging of TIH substances to reduce the likelihood of release in transport have generally been completed with the adoption of P601, P602, most recently P200 and with the rationalized assignment of the portable tank T codes.

2.	In this proposal the expert from the United States of America is proposing to introduce ten new N.O.S. entries for toxic liquids that meet the PG I criteria for inhalation toxicity. The adoption of generic TIH liquid N.O.S. entries will serve to ensure that shippers apply the appropriate packaging and portable tank provisions to TIH liquids that are not specifically listed in the Dangerous Goods List.

GE.02-

During previous discussions, a majority of the Sub-Committee indicated support for incorporating generic entries for toxic-by-inhalation liquids in the Model Regulations.  A specific decision was not taken on this matter because the US paper had several hazard communication proposals and the expert from the United States of America did not request that the Sub-Committee take individual decisions on each of the hazard communication proposals. A number of experts also indicated that decisions on TIH substances should be deferred pending completion of the GHS classification efforts which have subsequently been completed.  On this basis, the expert from the United States of America believes that the Sub-Committee should consider adopting generic entries for TIH liquid substances to better distinguish between Division 6.1 TIH substances that meet the PG I inhalation toxicity criteria and those that meet the oral or dermal criteria.

Proposal

3.	The following 10 new entries are proposed:

| UN # | PSN | Class/ Division | Sub-risk | PG | SP | LQ | Packaging and IBCs | Portable Tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | PI (8) | PP (9) | T (10) | TP (11) |
| xxxx | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity of 200 ml/m3 or less and saturated vapour concentration > 500 LC50 | 6.1 |  | I | 274 xxx | None | P601 |  | T22 | TP2, TP13 |
| xxxy | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity of 1000 ml/m3 or less and saturated vapour concentration > 10 LC50 | 6.1 |  | I | 274 xxx | None | P602 |  | T20 | TP2, TP13 |
| xxxz | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity of 200 ml/m3 or less and saturated vapour concentration > 500 LC50 | 6.1 | 3 | I | 274 xxx | None | P601 |  | T22 | TP2, TP13 |
| xxyx | TOXIC BY INHALATION LIQUID,FLAMMABLE, N.O.S. with an inhalation toxicity of 1000 ml/m3 or less and saturated vapour concentration > 10 LC50 | 6.1 | 3 | I | 274 xxx | None | P602 |  | T20 | TP2, TP13 |
| xxyy | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity of 200 ml/m3 or less and saturated vapour concentration > 500 LC50 | 6.1 | 4.3 | I | 274 xxx | None | P601 |  | T22 | TP2, TP13 |
| xxzz | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity of 1000 ml/m3 or less and saturated vapour concentration > 10 LC50 | 6.1 | 4.3 | I | 274 xxx | None | P602 |  | T20 | TP2, TP13 |
| xyyy | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity of 200 ml/m3 or less and saturated vapour concentration > 500 LC50 | 6.1 | 5.1 | I | 274 xxx | None | P601 |  | T22 | TP2, TP13 |
| xzzz | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity of 1000 ml/m3 or less and saturated vapour concentration > 10 LC50 | 6.1 | 5.1 | I | 274 xxx | None | P602 |  | T20 | TP2, TP13 |
| yyyy | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity of 200 ml/m3 or less and saturated vapour concentration > 500 LC50 | 6.1 | 8 | I | 274 xxx | None | P601 |  | T22 | TP2, TP13 |
| zzzz | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity of 1000 ml/m3 or less and saturated vapour concentration > 10 LC50 | 6.1 | 8 | I | 274 xxx | None | P602 |  | T20 | TP2, TP13 |

Each of these entries should have the following special provision indicated in column 6 of the Dangerous Goods list:

“XXX This entry shall only be used for Division 6.1 substances that meet the inhalation toxicity criteria for Packing Group I as described in 2.6.2.2.4.3.”

5. 	To prevent existing toxic liquid NOS entries from being used to describe liquids that meet the inhalation toxicity criteria for PG I a special provision should be placed against each such NOS entry.   The new special provision  should read:

“YYY This entry shall not be used for Division 6.1 substances that meet the inhalation toxicity criteria  for Packing Group I described in 2.6.2.2.4.3.”

This special provision should appear in column 6 of the Dangerous Goods List against the following entries:

1583, 2810, 2927, 2929, 3122, 3123,3275, 3276,3278,3279,3280,3281,3287, and 3289.

___________

# Text boxes

STSTE

Secretariat