#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2002/25

5 April 2002

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Twenty-first session, 1-10 July 2002,

# agenda item 6 (b))

DRAFT AMENDMENTS TO THE MODEL REGULATIONS

ON THE TRANSPORT OF DANGEROUS GOODS

Listing and Classification

Proposal for schematic classification of Organometallic Substances

Transmitted by the International Council of Chemical Associations (ICCA)

1.		Introduction

Last December meeting, ICCA submitted an information paper (UN/SCETDG/20/INF.20) on a classification scheme for organometallic substances, in divisions 4.2 and 4.3. A number of comments have been received and as much as possible incorporated in this proposal.

In the UN Model Regulations, organometallic substances are classified in division 4.2 as pyrophoric substances or, in diluted form, in division 4.3 as water reactive substances. These substances can be designated to a number of UN entries, but not in a systematic way. In practice the same product may be transported under different UN numbers which causes confusion. Also some UN entries may be used for both solid and liquid substances. Over the last two years, relevant industries discussed these problems and developed a systematic classification procedure for organometallic substances as submitted in this proposal.

2.		Appropriate UN numbers

The designation of an appropriate UN number to organometallic compounds is not based on a generic entry system. These materials can be assigned to the following available appropriate UN entries:

GE.02-

Division 4.2

- pyrophoric substances; the current UN numbers are based on physical state (solid/liquid) and nature (organic or inorganic) of the substances;

- pyrophoric organometallic compounds n.o.s (one UN number for both solid and liquid);

- n.o.s entries for pyrophoric metal alkyls, on the basis of their general chemical nature (alkyls general, alkyl halides, alkyl hydrides and aryl hydrides);

- n.o.s. entries for pyrophoric metal alkyls with specified metal part;

- metal alkyls listed by chemical name.

Division 4.3

- organometallic compound or compound solution or compound dispersion, water reactive, flammable

- organometallic compound, solid, water reactive, flammable

A table of currently available UN numbers is given in Annex 1. In practice, the number of possibilities result in a non unambiguous UN number assignment. For example, a pyrophoric solution of a metal alkyl compound can be assigned to UN number 2845 (Pyrophoric liquid, n.o.s.) or UN 3203 (Pyrophoric organometallic compounds, n.o.s) or UN 2003, Metal alkyl, n.o.s. In order to classify organometallic substances in a systematic way, ICCA proposes a procedure to achieve consistent classification. Justification is given below.

3.	Justification of proposed classification scheme

In the proposed scheme for classifying organometallic substances the following aspects are incorporated:

- individual UN entries for solid and liquid substances, which is currently not the case;

- clear distinction between pyrophoric and non-pyrophoric organometallic substances and formulations;

- clear distinction between water reactive and non-water reactive organometallic substances and formulations;

- systematic assignment of packagings, IBCs and tanks (if applicable), in line with the current requirements for these substances and air elimination from the packaging in case of a pyrophoric substance.

In the scheme, the non-pyrophoric water reactive substances have to be evaluated on :

a) 	flammability for solids and liquids; and

b) 	self-heating properties for the solids.

On a): the determination of the flash point to assess flammability properties of liquids is not possible due to the reactive properties of organometallic substances in air. Therefore, it is proposed to use the flash point of the solvent used (if any) in the formulation.

On b): for non pyrophoric, water reactive solid organometallic substances the self-heating properties are tested first, because these substances may react with oxygen. In case of negative result, the flammability of 4.1 is tested. This is in line with the precedence of hazards table 2.0.3.3.

At the moment, test N.5 is not applicable to pyrophoric substances. Nevertheless the water reactivity property is an essential part of the classification. In practice, the test is executed under nitrogen atmosphere to determine water reactivity properties. Therefore it is proposed to amend the introductory text (33.4.1.3.1) of test N.5 accordingly.

All the UN entries proposed for deletion are covered by the proposed organometallic substances. Nevertheless it is proposed to keep the old UN entries in the alphabetic list with reference to the relevant new UN number. For the new generic entries proposed, the wording organometallic “substance” which covers the current descriptions: compounds, solutions, dispersions because it is not always obvious which description should be used.

In case an organometallic substance is not classified according to the flow chart in division 4.2 or 4.3, with relevant subsidiary risk, classification in other classes has to be evaluated.

4.		Proposals

4.1	Insert in chapter 2.4., under introductory notes, the following new note:

NOTE 3: Because Organometallic substances can be classified in division 4.2 or 4.3 with additional subsidiary risks, depending on the properties of the substance, a specific classification flow chart for these substances is given in 2.4.5

4.2	Insert the following new flowchart in new 2.4.5

Figure 2.4.2: Flowchart scheme for organometallic substances

4.3	Delete the following UN numbers from Chapter 3.2, Dangerous Goods List:

1366 	Diethylzinc

1370	Dimethylzinc

2003	Metal alkyls water-reactive N.O.S. or Metal aryls water reactive, N.O.S

2005	Magnesium diphenyl

2445	Lithium alkyls

3049	Metal alkyl halides, water-reactive, N.O.S.,  Metal aryl halides, water-reactive, N.O.S

3050	Metal alkyl hydrides, water-reactive, N.O.S.,  Metal aryl hydrides, water-reactive, N.O.S

3051	Aluminium alkyls

3052	Aluminium alkyl halides (liquid + solid)

3053	Magnesium alkyls

3076	Aluminium alkyl hydrides

3203	Pyrophoric organometallic compound, water reactive, N.O.S (solid + liquid)

3207	Organic metallic compound or compound solution or compound dispersion, water reactive,

flammable, N.O.S

3372	Organic metallic compound solid, water reactive, flammable, N.O.S

4.4	Amend the second line of 33.4.1.3.1 of the Manual of Tests and Criteria to read as follows:

"In case a pyrophoric substance is tested, the test should be executed under nitrogen atmosphere."

4.5	Insert a new special packing provision in packing instruction P404:

"PPxx: For UN Nos. xxx1 and xxx3, air shall be eliminated from the vapour space by nitrogen or other means."

Insert a new special packing provision in packing instruction P400:

"PPxx: For UN Nos. xxx2 and xxx4, air shall be eliminated from the vapour space by nitrogen or other means."

Insert a new special packing provision in packing instruction IBC04:

"Bx: For UN Nos. xxx1 and xxx3, air shall be eliminated from the vapour space by nitrogen or other means."

4.6	Insert the following new UN numbers in the Dangerous Goods List of Chapter 3.2:

| UN No. (1) | Name and description (2) | Class or division (3) | Subsid-iary risk (4) | UN packing group (5) | Special provi-sions (6) | Limited quantities (7) | Packagings and IBCs | Portable tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction (8) | Special provisions (9) | Portable tank instruction (10) | Portable tank special provision (11) |
| xxx1 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC | 4.2 |  | I | 274 yyy | NONE | P404 IBC04 |  |  |  |
| xxx2 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC | 4.2 |  | I | 274 yyy | NONE | P400 |  | T21 | TP2 TP7 |
| xxx3 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC, WATER REACTIVE | 4.2 | 4.3 | I | 274 yyy | NONE | P404 IBC04 |  |  |  |
| xxx4 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC, WATER REACTIVE | 4.2 | 4.3 | I | 274 yyy | NONE | P400 |  | T21 | TP2 TP7 |
| xxx5 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE | 4.3 |  | I | 274 | NONE | P403 IBC04 |  |  |  |
|  |  | 4.3 |  | II | 274 | 500 g | P410 IBC04 |  |  |  |
|  |  | 4.3 |  | III | 223 274 | 1 kg | P410 IBC06 |  |  |  |
| xxx6 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE | 4.3 |  | I | 274 | NONE | P402 |  | T13 | TP2 TP7 |
|  |  | 4.3 |  | II | 274 | 500 g | P001 IBC01 |  | T7 | TP2 TP7 |
|  |  | 4.3 |  | III | 223 274 | 1 kg | P001 IBC02 |  | T7 | TP2 TP7 |
| xxx7 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, FLAMMABLE | 4.3 | 4.1 | I | 274 | NONE | P403 IBC04 |  |  |  |
|  |  | 4.3 | 4.1 | II | 274 | 500 g | P410 IBC04 |  |  |  |
|  |  | 4.3 | 4.1 | III | 223 274 | 1 kg | P410 IBC06 |  |  |  |
| xxx8 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, SELF-HEATING | 4.3 | 4.2 | I | 274 | NONE | P403 IBC04 |  |  |  |
|  |  | 4.3 | 4.2 | II | 274 | 500 g | P410 IBC04 |  |  |  |
|  |  | 4.3 | 4.2 | III | 223 274 | 1 kg | P410 IBC06 |  |  |  |
| xxx9 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE, FLAMMABLE | 4.3 | 3 | I | 274 | NONE | P402 |  | T13 | TP2 TP7 |
|  |  | 4.3 | 3 | II | 274 | 500 g | P001 IBC01 |  | T7 | TP2 TP7 |
|  |  | 4.3 | 3 | III | 223 274 | 1 kg | P001 IBC02 |  | T7 | TP2 TP7 |
| xx10 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING | 4.2 |  | II | 274 | 500 g | P410 IBC06 |  |  |  |
|  |  | 4.2 |  | III | 223 274 | 1 kg | P002 IBC08 |  |  |  |

5.	Consequential amendments

5.1	Amend the following entries in the alphabetical index of substances and articles

| Entry | To read as follows: |
| --- | --- |
| DIETHYLZINC, 4.2, 1366 | Diethylzinc, see 4.2, xxx4 |
| DIMETHYLZINC, 4.2, 1370 | Dimethylzinc, 4.2, xxx4 |
| Metal alkyls, water-reactive, N.O.S, 4.2, 2003 | Metal alkyls, water-reactive N.O.S, see 4.2, xxx3 or xxx4 |
| Metal aRYLs, water-reactive, N.O.S, 4.2, 2003 | Metal aryls, water-reactive N.O.S, see 4.2, xxx3 or xxx4 |
| Magnesium diphenyl, 4.2, 2005 | Magnesium diphenyl, see 4.2, xxx1 |
| Lithium alkyls, 4.2, 2445 | Lithium alkyls, see 4.2, xxx4 |
| Metal alkyl halides, water-reactive, N.O.S., 4.2, 3049 | Metal alkyl halides, water-reactive, N.O.S, see 4.2, xxx4 |
| Metal aryl halides, water-reactive, N.O.S, 4.2, 3049 | Metal aryl halides, water-reactive, N.O.S, see 4.2, xxx4 |
| Metal alkyl hydrides, water-reactive, N.O.S., 4.2, 3050 | Metal alkyl hydrides, water-reactive, N.O.S, see 4.2, xxx4 |
| Metal aryl hydrides, water-reactive, N.O.S, 4.2, 3050 | Metal aryl hydrides, water-reactive, N.O.S, see 4.2, xxx4 |
| Aluminium alkyls, 4.2, 3051 | Aluminium alkyls, see 4.2, xxx4 |
| Aluminium alkyl halides, liquid, 4.2, 3052 | Aluminium alkyl halides, liquid see 4.2, xxx4 |
| Aluminium alkyl halides, solid, 4.2, 3052 | Aluminium alkyl halides, solid see 4.2, xxx3 |
| Magnesium alkyls, 4.2, 3053 | Magnesium alkyls, see 4.2, xxx4 |
| Alminium alkyl hydrides, 4.2, 3076 | Aluminium alkyl hydrides, see 4.2, xxx4 |
| Pyrophoric organometallic compound, water reactive, liquid, N.O.S, 4.2, 3203 | Pyrophoric organometallic compound, water reactive, liquid, N.O.S, see 4.2, xxx4 |
| Pyrophoric organometallic compound, water reactive, solid, N.O.S, 4.2, 3203 | Pyrophoric organometallic compound, water reactive, solid, N.O.S, see 4.2, xxx3 |
| Organometallic compound dispersion, water reactive, flammable, N.O.S, 4.3, 3207 | Organometallic compound dispersion, water reactive, flammable, N.O.S, see 4.3, xxx9 |
| Organometallic compound SOLUTION, water reactive, flammable, N.O.S, 4.3, 3207 | Organometallic compound solution, water reactive, flammable, N.O.S, see 4.3, xxx9 |
| Organometallic compound solid, water reactive, flammable, N.O.S, 4.3, 3372 | Organometallic compound solid, water reactive, flammable, N.O.S, see 4.3, xxx6 |

5.2	Insert the new UN numbers, as shown in 4.4, in the alphabetical index of substances and articles

5.3	In 3.1.2.2 select an other example instead of UN 3207

In 3.1.2.8.1.3: select an other example for UN 2003 Metal Alkyl, water reactive, N.O.S. (triethylgallium)

5.4	Change UN numbers in packing instruction P404 (2005 into xxx1, 3203 into xxx3, 3052 into xxx3)

Annex 1

Possible UN numbers for organometallic compounds, division 4.2

Proper shipping name							UN number

Pyrophoric liquid, organic, N.O.S					2845

Pyrophoric solid, organic, N.O.S					2846

Pyrophoric liquid, inorganic, N.O.S					3194

Pyrophoric solid, inorganic, N.O.S					3200

Pyrophoric organometallic comp, water reactive, N.O.S (solid + liquid)	3203

Metal alkyls/aryls, water reactive, N.O.S					2003

Metal alkyl/aryl halides, water reactive, N.O.S				3049

Metal alkyl/aryl hydrides, water reactive, N.O.S.				3050

Aluminium alkyls							3051

Aluminium alkyl halides (solid + liquid)				3052

Aluminium alkyl hydrides						3076

Magnesium alkyls							3053

Lithium alkyls								2445

Magnesium diphenyl							2005

Diethylzinc								1366

Dimethylzinc								1370

Possible UN numbers for organometallic compounds, division 4.3

Organometallic compound or compound solution or

compound dispersion, water reactive, flammable, N.O.S			3207

Organometallic compound solid, water reactive, flammable, N.O.S	3372

───────────

# Text boxes

STSTE

Secretariat

Organometallic substance/formulation/

solution 1/

solid

solid

liquid

liquid

No

Yes

Yes

No

Organometallic substance,  liquid, pyrophoric, water reactive UN XXX4

Organometallic substance,  solid, pyrophoric, water reactive UN XXX3

Organometallic substance,  liquid, pyrophoric

UN XXX2

Organometallic substance,  solid, pyrophoric

UN XXX1

Is the substance water reactive ?

test N.5

Is the substance pyrophoric ?

test N.2 (solid)

test N.3 (liquid)

Organometallic substance,  solid, water reactive

UN XXX5

No

Is the substance a flammable solid ?

test N.1

Organometallic substance,  solid, water reactive, flammable

UN XXX6

Yes

No

Is the substance self heating ?

test N.4

Organometallic substance,  solid, water reactive, self-heating

UN XXX7

Yes

Yes

Division 4.3, PG I or II or III.

Is the substance a

solid ?

Is the substance water reactive ?

test N.5

Organometallic substance,  liquid, water reactive

UN XXX8

Yes

No

No

Does

the substance contain a diluent with a flash point

≤ 60.5 °C ?

Yes

Organometallic substance,  liquid, water reactive, flammable UN XXX9

No

Is the substance a self heating

solid ?

test N.4

Organometallic substance,  solid, self-heating

UN XX10

Yes

1/ If applicable and testing is relevant, taking into account reactivity

properties,  class 6.1 and 8 properties should be considered according

to the precedence of hazard table 2.0.3.3.

No

Substance does not have to be classified in division 4.2 or in division 4.3