#### UNITED

# NATIONS

Distr.

# GENERAL

# TRANS/WP.15/AC.1/2002/14

# 2 January 2002

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

(Bern, 18-22 March 2002)

Proposal regarding the reference to standards in RID/ADR

Transmitted by the European Committee for Standardisation (CEN) */

CEN submitted at previous sessions of the Joint Meeting several proposals for future reference to European Standards that were in the course of being ratified by CEN and published by its members:

- INF.8 to the March 2000 session for EN 12245, EN 12257, EN 12807, EN ISO 11623

- INF.27 to the September 2001 session for EN 12205, EN 1964-2, EN 13152, EN 13153, EN 1968, EN 1802;

_________

*/	Circulated by the Central Office  for International Carriage by Rail (OCTI) under the symbol OCTI/RID/GT/III/2002/14.

GE.02-

The present document requests to make reference to those European Standards that have been published at the date of issuing this proposal.

Proposal: in table of 6.2.2, add the following references

| for cylinders |  |  |
| --- | --- | --- |
| EN 12245:2001 | Transportable gas cylinders - Fully wrapped composite cylinders | 6.2.1.1 and 6.2.1.5 |
| EN 12205:2001 | Transportable gas cylinders - Non refillable metallic gas cylinders | 6.2.1.1 and 6.2.1.5 |
| EN 12257:2001 | Transportable gas cylinders - Seamless, hoop wrapped composite cylinders -Specification | 6.2.1.1 and 6.2.1.5 |
| EN 1964-2:2001 | Transportable gas cylinders - Specification for the design and construction of refillable transportable seamless steel gas cylinders of capacity from 0.5 litre up to 150 litre - Part 2: Tensile strength (Rm max) > 1100 N/mm² | 6.2.1.1 and 6.2.1.5 |
| EN 12807:2001 | Transportable refillable brazed steel cylinders for liquefied petroleum gas (LPG) - Design and construction | 6.2.1.1, 6.2.1.5 and 6.2.1.7 |
| for closures |  |  |
| EN 13152:2001 | Specifications and testing for liquefied petroleum gas (LPG) - cylinder valves-self closing | 6.2.1.1 |
| EN 13153:2001 | Specifications and testing for liquefied petroleum gas (LPG) - cylinder valves-manually operated | 6.2.1.1 |
| for periodic inspection |  |  |
| EN 1968:2001 | Transportable gas cylinders - Periodic inspection and testing of seamless steel gas cylinders (excluding LPG) | 6.2.1.6 |
| EN 1802:2001 | Transportable gas cylinders - Periodic inspection and testing of seamless aluminium gas cylinders | 6.2.1.6 |

__________

# Text boxes

E

Economic and Social

Council