# UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2003/3

11 April 2003

# ENGLISH ONLY

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Twenty-third session,  30 June-4 July 2003,

# agenda item 8)

HARMONIZATION WITH THE INTERNATIONAL ATOMIC AGENCY (IAEA)

REGULATIONS FOR THE SAFE TRANSPORT OF RADIOACTIVE MATERIAL

Proposed changes to the IAEA Transport Regulations as accepted by the September 2002 Review Panel Meeting and endorsed by the February 2003 TRANSSC Meeting

for 120 day review by member states and international organizations

Transmitted by the International Atomic Energy Agency (IAEA)

The secretariat reproduces hereafter a proposal from IAEA for harmonizing the Model Regulations on the Transport of Dangerous Goods with the IAEA Regulations for the Safe Transport of Radioactive Material.

PROPOSED CHANGES TO THE IAEA TRANSPORT REGULATIONS

AS ACCEPTED BY THE SEPTEMBER 2002 REVIEW PANEL MEETING

AND ENDORSED BY THE FEBRUARY 2003 TRANSSC MEETING

FOR 120 DAY REVIEW BY MEMBER STATES

AND INTERNATIONAL ORGANIZATIONS

# SUMMARY

The proposed changes, as accepted by the September 2002 Review Panel meeting and endorsed by the February 2003 TRANSSC meeting for the 120 day review by Member States and International Organizations, are presented in this report in Tables and Appendices.  Table 1 provides details on the accepted changes which are presented according to the paragraph order in the current regulations (TS-R-1).  Table 2 provides a cross reference table where the accepted changes are also listed alphabetically in country order to facilitate checking which proposals have been accepted and what proposed change numbers have been assigned.

Please note that the Review Panel did not fully support proposed changes #9, # 16, #46 and #58.

There are 3 appendices to this report.  The contents of these appendices are outlined following the further information on the tables.

### TABLES

# TABLE 1

The table contains the following 5 columns:

Column 1 provides the proposal number.

In some cases there are related proposals for the same or a similar change to a paragraph.  These related proposals are listed together in column 1.  For example, change #16 concerning paragraph 416. The accepted proposal is identified as UK/02/52.  The related proposals, Canada/02/02, UK/02/48 and UK/02/49 are identified together with UK/02/52.  This was done in order to recognize that they were also considered by the Review Panel and because the justification and explanation provided in these related proposals are also relevant for the review of the accepted text of the proposed change (which may be different from the originally proposed text in any of these proposals).  Related proposals that were rejected by the Review Panel are not included.

In other cases there could be alternate proposals for the same intended change but the Review Panel did not decide on the preferred alternative.  The 120 day review should help to identify the preferred option.  For example, change #24 and #25.

In still other cases there are proposals concerning unrelated changes to the same paragraph.  In those cases the accepted changes are listed as separate changes for the same paragraph.  For example, changes #27, #31, #32 and #33 all concern changes to paragraph 672.  Actually because there were so many proposals for different aspects of this rather lengthy paragraph these four changes were combined in Appendix 2 for easier review of the result if all these changes were eventually approved.

Sometimes a proposal number is split up in different parts.  For example, Canada/02/12 is split up in 6 parts (changes #6, #7, #8, #42, #53 and # 56).  This was done because as a result of accepting change #6 concerning paragraph 230, there are related changes to other paragraphs.  If the changes to these other paragraphs do not involve other relevant proposals for these other paragraphs then the related parts are listed following the original proposal (for example #7 and #8).  If the changes to these other paragraphs should be considered together with other proposals for these other paragraphs then the parts are listed with the other related proposals for these other paragraphs.  For example, change #42 (Canada/02/12 (4 of 6) which relates to paragraph 805 needs to be considered together with changes #43 (UK/02/39 (1 of 4) and change #44 (UK/02/40) which are also concerned with paragraph 805).  The main proposal number of the split proposals is needed to be able to review the related justification and explanation.

Column 2 provides the number of the affected paragraph of the regulations.

Proposed changes to Tables are listed where the Tables occur in the paragraph sequence.  Where the change involves only consequential changes, for example change #5 involving consequential changes to paragraphs 226, 418 etc. provides first a reference to the change (paragraph 222) that is causing the consequential changes.  This is important in case the original change is not accepted or modified during the further review process.

Column 3 provides the existing text in TS-R-1 for the paragraph for which a change is recommended.

If in this column a part of the paragraph is marked in bold then the proposal involves deleting the bold part of the existing text.

Column 4 provides the proposed new text as accepted by the Review Panel.

Any part in bold in this column indicates where the text is new or revised.

Column 5 provides the assigned change number.

The assigned change number is required for the further review process.

## TABLE 2

A cross reference table is provided, first giving the accepted changes in paragraph order and then giving them in country order.  The country order is provided to facilitate checking which proposals have been accepted for further review and to identify the related proposed change numbers.

APPENDICES

# APPENDIX 1

Appendix 1 provides the details of Change #5 which is a substantial number of consequential changes if Change #4 is accepted.

# APPENDIX 2

Appendix 2 provides a consolidated version of changes #27, #31, #32 and #33 to facilitate review of the separate proposed changes for the same lengthy paragraph.  It should be noted that there is another proposed change (#37) related to the same paragraph which could not be merged into the consolidated paragraph and which was not considered complete by the Review Panel.  In addition, Changes #28/30 and #34/36 are related consequential changes.

# APPENDIX 3

Appendix 3 provides in detail proposed change #51 concerning paragraphs 815/818 TRANSITIONAL ARRANGEMENTS (Grandfathering arrangements).  The detail also includes the justification/explanation.  It should be noted that there are some other proposals (# 48/50) on specific aspects of these paragraphs.

NOTE. The use of bold text in the current and new text in Appendix 3 is not as it is in TABLE 1, columns 3 and 4.  Instead it is reflecting the use of bold text in the current regulations.

#### TABLE 1

DETAILS OF ACCEPTED CHANGES

IN PARAGRAPH ORDER

| Proposal | Para | Existing text in TS-R-1 (2003) | Text accepted by Review Panel (Sep. 2002) | # |
| --- | --- | --- | --- | --- |
| UK/02/04 | 204 | 204. Multilateral approval shall mean approval by the relevant competent authority both of the country of origin of the design or shipment and of each country through or into which the consignment is to be transported. The term “through or into” specifically excludes “over”, i.e. the approval and notification requirements shall not apply to a country over which radioactive material is carried in an aircraft, provided that there is no scheduled stop in that country. | 204. Multilateral approval shall mean approval by the relevant competent authority both of the country of origin of the design or shipment and also, where the design or shipment is to be transported through or into any other country, approval by the competent authority of that country. The term “through or into” specifically excludes “over”, i.e. the approval and notification requirements shall not apply to a country over which radioactive material is carried in an aircraft, provided that there is no scheduled stop in that country. | 1 |
| UK/02/05 | 204 | 204. Multilateral approval shall mean approval by the relevant competent authority both of the country of origin of the design or shipment and of each country through or into which the consignment is to be transported. The term “through or into” specifically excludes “over”, i.e. the approval and notification requirements shall not apply to a country over which radioactive material is carried in an aircraft, provided that there is no scheduled stop in that country. | 204. Multilateral approval shall mean approval by the relevant competent authority both of the country of origin of the design or shipment and of each country through or into which the consignment is to be transported. The term “through or into” specifically excludes “over”, i.e. the approval requirements shall not apply to a country over which radioactive material is carried in an aircraft, provided that there is no scheduled stop in that country. | 2 |
| Canada/02/08 | 212 | 212. Consignor shall mean any person, organization or government which prepares a consignment for transport, and is named as consignor in the transport documents. | 212. Consignor shall mean any person, organization or government which prepares a consignment for transport. | 3 |
| Sweden/02/02 (1 of 2) and France/02/06 | 222 | 222. Fissile material shall mean uranium-233, uranium-235, plutonium-239, plutonium-241, or any combination of these radionuclides. Excepted from this definition is: (a) natural uranium or depleted uranium which is unirradiated, and (b) natural uranium or depleted uranium which has been irradiated in thermal reactors only. | 222. Fissile material shall mean the fissile nuclides uranium-233, uranium-235, plutonium-239 or plutonium-241, contained in any material. Excepted from this definition is: (a) natural uranium or depleted uranium which is unirradiated, and (b) natural uranium or depleted uranium which has been irradiated in thermal reactors only. | 4 |
| Sweden/02/02 (2 of 2) | 222 (Sweden/02/02) related consequential changes in paras 226, 418, 543, 549, 559, 672, 831, 832, 833 and Table XII |  | See Appendix 1 | 5 |
| Canada/02/12 (1 of 6) | 230 | 230. Package shall mean the packaging with its radioactive contents as presented for transport. The types of packages covered by these Regulations, which are subject to the activity limits and material restrictions of Section IV and meet the corresponding requirements, are: (a) Excepted package; (b) Industrial package Type 1 (Type IP-1); (c) Industrial package Type 2 (Type IP-2); (d) Industrial package Type 3 (Type IP-3); (e) Type A package; (f) Type B(U) package; (g) Type B(M) package; (h) Type C package. Packages containing fissile material or uranium hexafluoride are subject to additional requirements. | 230. Package shall mean the packaging with its radioactive contents as presented for transport. The types of packages covered by these Regulations, which are subject to the activity limits and material restrictions of Section IV and meet the corresponding requirements, are: (a) Excepted package; (b) Industrial package Type 1 (Type IP-1); (c) Industrial package Type 2 (Type IP-2); (d) Industrial package Type 3 (Type IP-3); (e) Type A package; (f) Type B(U) package; (g) Type B(M) package; (h) Type C package; (i) Type H(U) package; (j) Type H(M)package. Packages containing fissile material or uranium hexafluoride are subject to additional requirements. | 6 |
| Canada/02/12 (2 of 6) | 230 (Canada/02/12) related change in 538 | 538. Each package which conforms to a design approved under paras 805–814 or 816–817 shall be legibly and durably marked on the outside of the packaging with: (a) The identification mark allocated to that design by the competent authority; (b) A serial number to uniquely identify each packaging which conforms to that design; (c) In the case of a Type B(U) or Type B(M) package design, with “TYPE B(U)” or “TYPE B(M)”; and (d) In the case of a Type C package design, with “TYPE C”. | (possibly needed) 538. Each package which conforms to a design approved under paras 805–814 or 816–817 shall be legibly and durably marked on the outside of the packaging with: (a) The identification mark allocated to that design by the competent authority; (b) A serial number to uniquely identify each packaging which conforms to that design; (c) In the case of a Type B(U) or Type B(M) package design, with “TYPE B(U)” or “TYPE B(M)”; In the case of a Type H(U) or Type H(M) design, with “Type H(U)” or “Type H(M)” unless under these regulations another certification type mark is applicable;and (d) In the case of a Type C package design, with “TYPE C”. | 7 |
| Canada/02/12 (3 of 6) | 230 (Canada/02/12) related change in 539 | 539. Each package which conforms to a Type B(U), Type B(M) or Type C package design shall have the outside of the outermost receptacle which is resistant to the effects of fire and water plainly marked by embossing, stamping or other means resistant to the effects of fire and water with the trefoil symbol shown in Fig. 1. | 539. Each package which conforms to a Type H(U), Type H(M), Type B(U), Type B(M) or Type C package design shall have the outside of the outermost receptacle which is resistant to the effects of fire and water plainly marked by embossing, stamping or other means resistant to the effects of fire and water with the trefoil symbol shown in Fig. 1. | 8 |
| UK/02/13 | 246 | 246. Natural uranium shall mean chemically separated uranium containing the naturally occurring distribution of uranium isotopes (approximately 99.28% uranium-238, and 0.72% uranium-235 by mass). Depleted uranium shall mean uranium containing a lesser mass percentage of uranium-235 than in natural uranium. Enriched uranium shall mean uranium containing a greater mass percentage of uranium-235 than 0.72%. In all cases, a very small mass percentage of uranium-234 is present. | 246. Natural uranium shall mean chemically separated uranium containing the naturally occurring distribution of uranium isotopes (approximately 99.28% uranium-238, and 0.72% uranium-235 by mass). Depleted uranium shall mean uranium containing a lesser mass percentage of uranium-235 than in natural uranium. Enriched uranium shall mean uranium containing a greater mass percentage of uranium-235 than 0.72%. NOTE. Deleted sentence moved to TS-G 1.1 | 9 |
| USA/02/07 and UK/02/14 (1 of 2) | 303 | 303. Workers shall receive appropriate training concerning the radiation hazards involved and the precautions to be observed in order to ensure restriction of their exposure and that of other persons who might be affected by their actions. | 303. Workers shall receive appropriate training concerning the radiation hazards involved and the precautions to be observed in order to control their occupational exposure and that of other persons who might be affected by their actions. | 10 |
| USA/02/07 and UK/02/14 (2of 2) | 305 | 305. For occupational exposures arising from transport activities, where it is assessed that the effective dose: (a) is most unlikely to exceed 1 mSv in a year, neither special work patterns nor detailed monitoring nor dose assessment programmes nor individual record keeping shall be required; (b) is likely to be between 1 and 6 mSv in a year, a dose assessment programme via work place monitoring or individual monitoring shall be conducted; (c) is likely to exceed 6 mSv in a year, individual monitoring shall be conducted. When individual monitoring or work place monitoring is conducted, appropriate records shall be kept. | 305. For occupational exposures arising from transport activities, where it is assessed that the effective dose: (a) is likely to be between 1 and 6 mSv in a year, a dose assessment programme via work place monitoring or individual monitoring shall be conducted; (b) is likely to exceed 6 mSv in a year, individual monitoring shall be conducted. When individual monitoring or work place monitoring is conducted, appropriate records shall be kept. | 11 |
| UK/02/18 | Table I footnote (a) | (a) A1 and/or A2 values for these parent radionuclides include contributions from daughter radionuclides with half-lives less than 10 days. | (a) A1 and/or A2 values for these parent radionuclides include contributions from daughter radionuclides with half-lives less than 10 days, as listed in the following: Mg 28 Al 28 Ar 42 K 42 Ca 47 Sc 47 Ti 44 Sc 44 Fe 52 Mn 52m Fe 60 Co 60m Zn 69m Zn 69 Ge 68 Ga 68 Rb 83 Kr 83m Sr 82 Rb 82 Sr 90 Y 90 Sr 91 Y 91m Sr 92 Y 92 Y 87 Sr 87m Zr 95 Nb 95m Zr 97 Nb 97m, Nb 97 Mo 99 Tc 99m Tc 95m Tc 95 Tc 96m Tc 96 Ru 103 Rh 103m Ru 106 Rh 106 Pd 103 Rh 103m Ag 108m Ag 108 Ag 110m Ag 110 Cd 115 In 115m In 114m In 114 Sn 113 In 113m Sn 121m Sn 121 Sn 126 Sb 126m Te 118 Sb 118 Te 127m Te 127 Te 129m Te 129 Te 131m Te 131 Te 132 I 132 I 135 Xe 135m Xe 122 I 122 Cs 137 Ba 137m Ba 131 Cs 131 Ba 140 La 140 Ce 144 Pr 144m, Pr 144 Pm 148m Pm 148 Gd 146 Eu 146 Dy 166 Ho 166 Hf 172 Lu 172 W 178 Ta 178 W 188 Re 188 Re 189 Os 189m Os 194 Ir 194 Ir 189 Os 189m Pt 188 Ir 188 Hg 194 Au 194 Hg 195m Hg 195 Pb 210 Bi 210 Pb 212 Bi 212, Tl 208, Po 212 Bi 210m Tl 206 Bi 212 Tl 208, Po 212 At 211 Po 211 Rn 222 Po 218, Pb 214, At 218, Bi 214, Po 214 Ra 223 Rn 219, Po 215, Pb 211, Bi 211, Po 211, Tl 207 Ra 224 Rn 220, Po 216, Pb 212, Bi 212, Tl 208, Po 212 Ra 225 Ac 225, Fr 221, At 217, Bi 213, Tl 209, Po 213, Pb 209 Ra 226 Rn 222, Po 218, Pb 214, At 218, Bi 214, Po 214 Ra 228 Ac 228 Ac 225 Fr 221, At 217, Bi 213, Tl 209, Po 213, Pb 209 Ac 227 Fr 223 Th 228 Ra 224, Rn 220, Po 216, Pb 212, Bi 212, Tl 208, Po 212 Th 234 Pa 234m, Pa 234 Pa 230 Ac 226, Th 226, Fr 222, Ra 222, Rn 218, Po 214 U 230 Th 226, Ra 222, Rn 218, Po 214 U 235 Th 231 Pu 241 U 237 Pu 244 U 240, Np 240m Am 242m Am 242, Np 238 Am 243 Np 239 Cm 247 Pu 243 Bk 249 Am 245 Cf 253 Cm 249 | 12 |
| Germany/02/06 | Table I footnote (b) | (b) Parent nuclides and their progeny included in secular equilibrium are listed in the following: Sr-90 Y-90 Zr-93 Nb-93m Zr-97 Nb-97 Ru-106 Rh-106 Cs-137 Ba-137m Ce-134 La-134 Ce-144 Pr-144 Ba-140 La-140 Bi-212 Tl-208 (0.36), Po-212 (0.64) Pb-210 Bi-210, Po-210 Pb-212 Bi-212, Tl-208 (0.36), Po-212 (0.64) Rn-220 Po-216 Rn-222 Po-218, Pb-214, Bi-214, Po-214 Ra-223 Rn-219, Po-215, Pb-211, Bi-211, Tl-207 Ra-224 Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Ra-226 Rn-222, Po-218, Pb-214, Bi-214, Po-214, Pb-210, Bi-210, Po-210 Ra-228 Ac-228 Th-226 Ra-222, Rn-218, Po-214 Th-228 Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Th-229 Ra-225, Ac-225, Fr-221, At-217, Bi-213, Po-213, Pb-209 Th-nat Ra-228, Ac-228, Th-228, Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Th-234 Pa-234m U-230 Th-226, Ra-222, Rn-218, Po-214 U-232 Th-228, Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) U-235 Th-231 U-238 Th-234, Pa-234m U-nat Th-234, Pa-234m, U-234, Th-230, Ra-226, Rn-222, Po-218, Pb-214, Bi-214, Po-214, Pb-210, Bi-210, Po-210 U-240 Np-240m Np-237 Pa-233 Am-242m Am-242 Am-243 Np-239 | (b) Parent nuclides and their progeny included in secular equilibrium are listed in the following: Sr-90 Y-90 Zr-93 Nb-93m Zr-97 Nb-97 Ru-106 Rh-106 Ag-108m Ag-108 Cs-137 Ba-137m Ce-144 Pr-144 Ba-140 La-140 Bi-212 Tl-208 (0.36), Po-212 (0.64) Pb-210 Bi-210, Po-210 Pb-212 Bi-212, Tl-208 (0.36), Po-212 (0.64) Rn-222 Po-218, Pb-214, Bi-214, Po-214 Ra-223 Rn-219, Po-215, Pb-211, Bi-211, Tl-207 Ra-224 Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Ra-226 Rn-222, Po-218, Pb-214, Bi-214, Po-214, Pb-210, Bi-210, Po-210 Ra-228 Ac-228 Th-228 Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Th-229 Ra-225, Ac-225, Fr-221, At-217, Bi-213, Po-213, Pb-209 Th-nat Ra-228, Ac-228, Th-228, Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Th-234 Pa-234m U-230 Th-226, Ra-222, Rn-218, Po-214 U-232 Th-228, Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) U-235 Th-231 U-238 Th-234, Pa-234m U-nat Th-234, Pa-234m, U-234, Th-230, Ra-226, Rn-222, Po-218, Pb-214, Bi-214, Po-214, Pb-210, Bi-210, Po-210 Np-237 Pa-233 Am-242m Am-242 Am-243 Np-239 | 13 |
| UK/02/15 | 402 | 402. For individual radionuclides which are not listed in Table I the determination of the basic radionuclide values referred to in para. 401 shall require competent authority approval or, for international transport, multilateral approval. Where the chemical form of each radionuclide is known, it is permissible to use the A2 value related to its solubility class as recommended by the International Commission on Radiological Protection, if the chemical forms under both normal and accident conditions of transport are taken into consideration. Alternatively, the radionuclide values in Table II may be used without obtaining competent authority approval. | 402. For individual radionuclides which are not listed in Table I the determination of the basic radionuclide values referred to in para. 401 shall require multilateral approval. It is permissible to use the A2 value related to the solubility class, as recommended by the International Commission on Radiological Protection, if the chemical forms of each radionuclide under both normal and accident conditions of transport are taken into consideration. Alternatively, the radionuclide values in Table II may be used without obtaining competent authority approval. | 14 |
| Japan/02/02 | TABLE II (first column) | TABLE II (first column) Radioactive contents Only beta or gamma emitting nuclides are known to be present Only alpha emitting nuclides are known to be present No relevant data are available | TABLE II (first column) Radioactive contents Only beta or gamma emitting nuclides are known to be present Alpha emitting nuclides without emitting neutrons in greater than 10-2 of their decays are known to be present No relevant data are available | 15 |
| UK/02/52 (1 of 2) and Canada/02/02, UK/02/48, UK/02/49 | 416 | 416. Type B(U) and Type B(M) packages, if transported by air, shall meet the requirements of para. 415 and shall not contain activities greater than the following: (a) for low dispersible radioactive material — as authorized for the package design as specified in the certificate of approval, (b) for special form radioactive material — 3000 A1 or 100 000 A2, whichever is the lower; or (c) for all other radioactive material — 3000 A2. | 416. Type B(U) and Type B(M) packages, if transported by air, shall meet the requirements of para. 415 and shall not contain activities greater than the following: (a) for low dispersible radioactive material — as authorized for the package design as specified in the certificate of approval, (b) for special form Co-60 – 30000 A1 (c) for other special form radioactive material — 3000 A1 or 100 000 A2, whichever is the lower; or (d) for all other radioactive material — 3000 A2. | 16 |
| UK/02/19 | 419 | 419. The mass of uranium hexafluoride in a package shall not exceed a value that would lead to an ullage smaller than 5% at the maximum temperature of the package as specified for the plant systems where the package shall be used. The uranium hexafluoride shall be in solid form and the internal pressure of the package shall be below atmospheric pressure when presented for transport. | 419. The mass of uranium hexafluoride in a package shall be within limits set in the certificate of approval, and shall not exceed a value that would lead to an ullage smaller than 5% at the maximum temperature of the package as specified for the plant systems where the package shall be used. The uranium hexafluoride shall be in solid form and the internal pressure of the package shall be below atmospheric pressure when presented for transport. | 17 |
| France/02/22 | 502 | 502. Before each shipment of any package, the following requirements shall be fulfilled: (a) For any package it shall be ensured that all the requirements specified in the relevant provisions of these Regulations have been satisfied. (b) It shall be ensured that lifting attachments which do not meet the requirements of para. 607 have been removed or otherwise rendered incapable of being used for lifting the package, in accordance with para. 608. (c) For each Type B(U), Type B(M) and Type C package and for each package containing fissile material, it shall be ensured that all the requirements specified in the approval certificates have been satisfied. (d) Each Type B(U), Type B(M) and Type C package shall be held until equilibrium conditions have been approached closely enough to demonstrate compliance with the requirements for temperature and pressure unless an exemption from these requirements has received unilateral approval. (e) For each Type B(U), Type B(M) and Type C package, it shall be ensured by inspection and/or appropriate tests that all closures, valve and other openings of the containment system through which the radioactive contents might escape are properly closed and, where appropriate, sealed in the manner for which the demonstrations of compliance with the requirements of paras 656 and 669 were made. (f) For each special form radioactive material, it shall be ensured that all the requirements specified in the approval certificate and the relevant provisions of these Regulations have been satisfied. (g) For packages containing fissile material the measurement specified in para. 674(b) and the tests to demonstrate closure of each package as specified in para. 677 shall be performed where applicable. (h) For each low dispersible radioactive material, it shall be ensured that all the requirements specified in the approval certificate and the relevant provisions of these Regulations have been satisfied. | 502. Before each shipment of any package, the following requirements shall be fulfilled: (a) For any package it shall be ensured that all the requirements specified in the relevant provisions of these Regulations have been satisfied. (b) It shall be ensured that lifting attachments which do not meet the requirements of para. 607 have been removed or otherwise rendered incapable of being used for lifting the package, in accordance with para. 608. (c) For each Type B(U), Type B(M) and Type C package and for each package containing fissile material, or 0.1 kg or more of uranium hexafluoride, it shall be ensured that all the requirements specified in the approval certificates have been satisfied. (d) Each Type B(U), Type B(M) and Type C package shall be held until equilibrium conditions have been approached closely enough to demonstrate compliance with the requirements for temperature and pressure unless an exemption from these requirements has received unilateral approval. (e) For each Type B(U), Type B(M) and Type C package, it shall be ensured by inspection and/or appropriate tests that all closures, valve and other openings of the containment system through which the radioactive contents might escape are properly closed and, where appropriate, sealed in the manner for which the demonstrations of compliance with the requirements of paras 656 and 669 were made. (f) For each special form radioactive material, it shall be ensured that all the requirements specified in the approval certificate and the relevant provisions of these Regulations have been satisfied. (g) For packages containing fissile material the measurement specified in para. 674(b) and the tests to demonstrate closure of each package as specified in para. 677 shall be performed where applicable. (h) For each low dispersible radioactive material, it shall be ensured that all the requirements specified in the approval certificate and the relevant provisions of these Regulations have been satisfied. | 18 |
| UK/02/22 | 503 | 503. A package shall not contain any other items except such articles and documents as are necessary for the use of the radioactive material. This requirement shall not preclude the transport of low specific activity material or surface contaminated objects with other items. The transport of such articles and documents in a package, or of low specific activity material or surface contaminated objects with other items may be permitted provided that there is no interaction between them and the packaging or its radioactive contents that would reduce the safety of the package. | 503. A package shall not contain any other items unless there is no interaction between them and the packaging or its radioactive contents, or that would reduce the safety of the package. | 19 |
| Canada/02/04 (1 of 2) and France/02/17 | Table VIII footnote “c” | Table VIII footnote “c” c UN 2977 and UN 2978 are special cases without a unique relationship with the Schedules. | Table VIII footnote “c” c In the case of non-fissile or fissile excepted uranium hexafluoride, the UN 2978 and the proper shipping name and description, “RADIOACTIVE MATERIAL, URANIUM HEXAFLUORIDE, non-fissile or fissile excepted,” takes precedence over other UN numbers applicable to non-fissile and fissile excepted. In the case of uranium hexafluoride that is fissile material the UN 2977 and the proper shipping name, “RADIOACTIVE MATERIAL, URANIUM HEXAFLUORIDE, FISSILE,” takes precedence over other UN numbers applicable to fissile material. | 20 |
| UK/02/25 | 537 | 537. Each package which conforms to: (a) an IP-1, an IP-2 or an IP-3 design shall be legibly and durably marked on the outside of the packaging with “TYPE IP-1”, “TYPE IP-2” or “TYPE IP-3” as appropriate; (b) a Type A package design shall be legibly and durably marked on the outside of the packaging with “TYPE A”; (c) an IP-2, an IP-3 or a Type A package design shall be legibly and durably marked on the outside of the packaging with the international vehicle registration code (VRI Code) of the country of origin of design and the name of the manufacturers, or other identification of the packaging specified by the competent authority. | 537. Each package which conforms to: (a) an IP-1, an IP-2 or an IP-3 design shall be legibly and durably marked on the outside of the packaging with “TYPE IP-1”, “TYPE IP-2” or “TYPE IP-3” as appropriate; (b) a Type A package design shall be legibly and durably marked on the outside of the packaging with “TYPE A”; (c) an IP-1, an IP-2, an IP-3 or a Type A package design shall be legibly and durably marked on the outside of the packaging with the international vehicle registration code (VRI Code) of the country of origin of design and the name of the manufacturers, or other identification of the packaging specified by the competent authority. | 21 |
| UK/02/66 | 537 | 537. Each package which conforms to: (a) an IP-1, an IP-2 or an IP-3 design shall be legibly and durably marked on the outside of the packaging with “TYPE IP-1”, “TYPE IP-2” or “TYPE IP-3” as appropriate; (b) a Type A package design shall be legibly and durably marked on the outside of the packaging with “TYPE A”; (c) an IP-2, an IP-3 or a Type A package design shall be legibly and durably marked on the outside of the packaging with the international vehicle registration code (VRI Code) of the country of origin of design and the name of the manufacturers, or other identification of the packaging specified by the competent authority. | 537. Each package which conforms to: (a) an IP-1, an IP-2 or an IP-3 design shall be legibly and durably marked on the outside of the packaging with “TYPE IP-1”, “TYPE IP-2” or “TYPE IP-3” as appropriate; (b) a Type A package design shall be legibly and durably marked on the outside of the packaging with “TYPE A”; (c) an IP-2, an IP-3 or a Type A package design shall be legibly and durably marked on the outside of the packaging with the international vehicle registration code (VRI Code) of the country of origin of design and the name of the designer of the package, or other identification of the packaging specified by the competent authority. | 22 |
| UK/02/28 | 566 | 566. Loading of freight containers and accumulation of packages, overpacks and freight containers shall be controlled as follows: (a) Except under the condition of exclusive use, the total number of packages, overpacks and freight containers aboard a single conveyance shall be so limited that the total sum of the transport indexes aboard the conveyance does not exceed the values shown in Table IX. For consignments of LSA-I material there shall be no limit on the sum of the transport indexes. (b) Where a consignment is transported under exclusive use, there shall be no limit on the sum of the transport indexes aboard a single conveyance. (c) The radiation level under routine conditions of transport shall not exceed 2 mSv/h at any point on, and 0.1 mSv/h at 2 m from, the external surface of the conveyance, except for consignments transported under exclusive use by road or rail, for which the radiation limits around the vehicle are set forth in para 572(b) and (c). (d) The total sum of the criticality safety indexes in a freight container and aboard a conveyance shall not exceed the values shown in Table X. | 566. Loading of freight containers and accumulation of packages, overpacks and freight containers shall be controlled as follows: (a) Except under the condition of exclusive use, and for consignments of LSA-I material, the total number of packages, overpacks and freight containers aboard a single conveyance shall be so limited that the total sum of the transport indexes aboard the conveyance does not exceed the values shown in Table IX. (b) The radiation level under routine conditions of transport shall not exceed 2 mSv/h at any point on, and 0.1 mSv/h at 2 m from, the external surface of the conveyance, except for consignments transported under exclusive use by road or rail, for which the radiation limits around the vehicle are set forth in para 572(b) and (c). (c) The total sum of the criticality safety indexes in a freight container and aboard a conveyance shall not exceed the values shown in Table X. | 23 |
| EU/02/01 and Germany/02/01, UK/02/73 | 622 and consequential changes in 624, 625, 627, 628 and 646b | 622. A package, to be qualified as a Type IP-2, shall be designed to meet the requirements for Type IP-1 as specified in para. 621 and, in addition, if it were subjected to the tests specified in paras 722 and 723, it would prevent: (a) loss or dispersal of the radioactive contents; and (b) loss of shielding integrity which would result in more than a 20% increase in the radiation level at any external surface of the package. | 622. A package, to be qualified as a Type IP-2, shall be designed to meet the requirements for Type IP-1 as specified in para. 621 and, in addition, if it were subjected to the tests specified in paras 722 and 723, it would prevent: (a) loss or dispersal of the radioactive contents; and (b) loss of shielding integrity which would result in more than a 20% increase in the maximum radiation level at any external surface of the package. | 24 |
| France/02/04 and UK/02/30 | 622 (alternate proposal) and consequential changes in 624, 625, 627, 628 and 646b | 622. A package, to be qualified as a Type IP-2, shall be designed to meet the requirements for Type IP-1 as specified in para. 621 and, in addition, if it were subjected to the tests specified in paras 722 and 723, it would prevent: (a) loss or dispersal of the radioactive contents; and (b) loss of shielding integrity which would result in more than a 20% increase in the radiation level at any external surface of the package. | 622. A package, to be qualified as a Type IP-2, shall be designed to meet the requirements for Type IP-1 as specified in para. 621 and, in addition, if it were subjected to the tests specified in paras 722 and 723, it would prevent: (a) loss or dispersal of the radioactive contents; and (b) loss of shielding integrity which would result in more than a 20% increase in the transport index of the package | 25 |
| France/02/29 | 652 and 662 | 652. Except as required in para. 617 for a package transported by air, a package shall be so designed that, under the ambient condition specified in para. 653, the temperature of the accessible surfaces of a package shall not exceed 50°C, unless the package is transported under exclusive use. 662. Except as required in para. 617 for a package transported by air, the maximum temperature of any surface readily accessible during transport of a package shall not exceed 85°C in the absence of insolation under the ambient conditions specified in para. 653. The package shall be carried under exclusive use, as specified in para. 652, if this maximum temperature exceeds 50°C. Account may be taken of barriers or screens intended to give protection to persons without the need for the barriers or screens being subject to any test. | 652. A package shall be so designed that, under the ambient condition specified in para. 653 and in the absence of insolation, the temperature of the accessible surfaces of a package shall not exceed 50 °C, unless the package is transported under exclusive use. 652 bis. Except as required in para. 617 for a package transported by air, the maximum temperature of any surface readily accessible during transport of a package under exclusive use shall not exceed 85°C in the absence of insolation under the ambient conditions specified in para. 653. Account may be taken of barriers or screens intended to give protection to persons without the need for the barriers or screens being subject to any test. 662 : deleted and replaced with 652bis as above | 26 |
| UK/02/35 (1 of 4) and France/02/44 | 672 | NOTE. Current para 672, as modified, becomes new para 417bis 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | NOTE. Proposed para 417bis is based on current para 672 417bis. Packages containing fissile material, other than packages approved for the carriage of fissile material, shall meet one of the exceptions (a)–(d). Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table IV, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table IV. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | 27 |
| UK/02/35 (2 of 4) | 672 (417 bis) (UK/02/35) related consequential changes in Table numbers and location | TABLE Numbers IV/XII | TABLE XII to be moved (becomes TABLE IV) – TABLES IV – XI to have table numbers increased by one. | 28 |
| UK/02/35 (3 of 4) | 672 (417bis) (UK/02/35) related consequential change in para 671 | 671. Fissile material shall be transported so as to; (a) maintain subcriticality during normal and accident conditions of transport; in particular, the following contingencies shall be considered: (i) water leaking into or out of packages; (ii) the loss of efficiency of built-in neutron absorbers or moderators; (iii) rearrangement of the contents either within the package or as a result of loss from the package; (iv) reduction of spaces within or between packages; (v) packages becoming immersed in water or buried in snow; and (vi) temperature changes; and (b) meet the requirements: (i) of para. 634 for packages containing fissile material; (ii) prescribed elsewhere in these Regulations which pertain to the radio-active properties of the material; and (iii) specified in paras 673–682, unless excepted by para. 672. | 671. Packages designed for the carriage of fissile material shall; (a) maintain subcriticality during normal and accident conditions of transport; in particular, the following contingencies shall be considered: (i) water leaking into or out of packages; (ii) the loss of efficiency of built-in neutron absorbers or moderators; (iii) rearrangement of the contents either within the package or as a result of loss from the package; (iv) reduction of spaces within or between packages; (v) packages becoming immersed in water or buried in snow; and (vi) temperature changes; and (b) meet the requirements: (i) of para. 634 for packages containing fissile material; (ii) prescribed elsewhere in these Regulations which pertain to the radio-active properties of the material; and (iii) specified in paras 673–682. | 29 |
| UK/02/35 (4 of 4) | 672 (417bis) (UK/02/35) related consequential changes in paras 226, 515, TABLE VIII, 541, 549, 802, 812 | Current reference to para 672 in : 226 (a) (iii) and (iv) 515 (c) TABLE VIII footnote 541 549 (i) 802 (a) (iv) 812 | Change 672 to 417bis in: 226 (a) (iii) and (iv) 515 (c) TABLE VIII footnote 541 549 (i) 802 (a) (iv) 812 | 30 |
| France/02/37 | 672 | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII, except for deuterium in natural concentration in hydrogen. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | 31 |
| Sweden/02/03 | 672 | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g)( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material, provided that the smallest external dimension of each package is not less than 10 cm. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | 32 |
| UK/02/37 (1 of 4) | 672 | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: CSI = mass of uranium-235 (g) + mass of other fissile material (g) * 50 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | 33 |
| UK/02/37 (2 of 4) | 672 (UK/02/37) related change in 544 | 544. Each label conforming to the model in Fig. 5 shall be completed with the criticality safety index (CSI) as stated in the certificate of approval for special arrangement or the certificate of approval for the package design issued by the competent authority. | 544. Each label conforming to the model in Fig. 5 shall be completed with the criticality safety index (CSI) as stated in the certificate of approval for special arrangement. the certificate of approval for the package design issued by the competent authority or as calculated in accordance with 672 (a). | 34 |
| UK/02/37 (3 of 4) | 672 (UK/02/37) related change to TABLE X header | TABLE X. CSI LIMITS FOR FREIGHT CONTAINERS AND CONVEYANCES CONTAINING FISSILE MATERIAL | TABLE X. CSI LIMITS FOR FREIGHT CONTAINERS AND CONVEYANCES | 35 |
| UK/02/37 (4 of 4) | 672 (UK/02/37) related consequential changes in paras 541 and 549 | Current reference to para 672 in: 541 and 549(i) | Change references in paras 541 and 549(i) from 672 to 672(b)-(d) | 36 |
| USA/02/02 | 672 | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. | Para 672. Fissile material meeting one of the provisions (a) - (d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673-682 as well as the other requirements of these Regulations that apply to fissile material. The contents of each individual package contain 15 grams or less of the combination of uranium-233, uranium-235, and plutonium-239, provided there are more than 200 grams of non-fissile, non-combustible, insoluble-in-water contents per gram of fissile material; or the contents of each individual package contain 350 grams or less of the combination of uranium-233, uranium-235, and plutonium-239, provided there are more than 2000 grams of non-fissile, non-combustible, insoluble-in-water contents per gram of fissile material. All other radionuclides listed in para 222 shall not be present in quantities exceeding 1% by mass of the fissile material. Beryllium, graphite, and hydrogenous material enriched in deuterium may be present in the package, but shall not be included in determining the mass ratio for the package. The material can be packaged or unpackaged according to para 523. (b) Uranium enriched in uranium-235 to a maximum of 1 percent by mass, and with total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that beryllium, graphite, and hydrogenous material enriched in deuterium constitute less than 1% of the fissile mass. (c) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. The package shall meet the requirements of para 646. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those two radionuclides. | 37 |
| USA/02/01 | 677 | 677. For a package in isolation, it shall be assumed that water can leak into or out of all void spaces of the package, including those within the containment system. However, if the design incorporates special features to prevent such leakage of water into or out of certain void spaces, even as a result of error, absence of leakage may be assumed in respect of those void spaces. Special features shall include the following: (a) Multiple high standard water barriers, each of which would remain watertight if the package were subject to the tests prescribed in para. 682(b), a high degree of quality control in the manufacture, maintenance and repair of packagings and tests to demonstrate the closure of each package before each shipment; or (b) For packages containing uranium hexafluoride only: (i) packages where, following the tests prescribed in para. 682(b), there is no physical contact between the valve and any other component of the packaging other than at its original point of attachment and where, in addition, following the test prescribed in para. 728 the valves remain leaktight; and (ii) a high degree of quality control in the manufacture, maintenance and repair of packagings coupled with tests to demonstrate closure of each package before each shipment. | 677. For a package in isolation, it shall be assumed that water can leak into or out of all void spaces of the package, including those within the containment system. However, if the design incorporates special features to prevent such leakage of water into or out of certain void spaces, even as a result of error, absence of leakage may be assumed in respect of those void spaces. Special features shall include the following: (a) Multiple high standard water barriers, each of which would remain watertight if the package were subject to the tests prescribed in para. 682(b), a high degree of quality control in the manufacture, maintenance and repair of packagings and tests to demonstrate the closure of each package before each shipment; or (b) For packages containing uranium hexafluoride, with enrichmentof 5 mass percent uranium-235 or less: (i) packages where, following the tests prescribed in para. 682(b), there is no physical contact between the valve and any other component of the packaging other than at its original point of attachment and where, in addition, following the test prescribed in para. 728 the valves remain leaktight; and (ii) a high degree of quality control in the manufacture, maintenance and repair of packagings coupled with tests to demonstrate closure of each package before each shipment. | 38 |
| Canada/02/05 | 709 | 709. Specimens that comprise or simulate radioactive material enclosed in a sealed capsule may be excepted from: (a) The tests prescribed in paras 705 and 706 provided the mass of the special form radioactive material is less than 200 g and they are alternatively subjected to the Class 4 impact test prescribed in the International Organization for Standardization document ISO 2919: “Sealed Radioactive Sources —Classification” [11], and (b) The test prescribed in para. 708 provided they are alternatively subjected to the Class 6 temperature test specified in the International Organization for Standardization document ISO 2919: “Sealed radioactive sources —Classification” [11]. | 709. Specimens that comprise or simulate radioactive material enclosed in a sealed capsule may be excepted from: (a) The tests prescribed in paras 705 and 706 provided the mass of the special form radioactive material (i) is less than 200 g and they are alternately subjected to the Class 4 impact test prescribed in the International Organization for Standardization document ISO 2919: “Sealed Radioactive Sources – Classification” [11], or (ii) is less than 500 g and they are alternately subjected to the Class 5 impact test prescribed in the International Organization for Standardization document ISO 2919: “Sealed Radioactive Sources – Classification” [11], and (b) The test prescribed in para. 708 provided they are alternatively subjected to the Class 6 temperature test specified in the International Organization for Standardization document ISO 2919: “Sealed radioactive sources —Classification” [11]. | 39 |
| France/02/34 | 722 | 722. Free drop test: The specimen shall drop onto the target so as to suffer maximum damage in respect of the safety features to be tested. (a) The height of drop measured from the lowest point of the specimen to the upper surface of the target shall be not less than the distance specified in Table XIII for the applicable mass. The target shall be as defined in para. 717. (b) For rectangular fibreboard or wood packages not exceeding a mass of 50 kg, a separate specimen shall be subjected to a free drop onto each corner from a height of 0.3 m. (c) For cylindrical fibreboard packages not exceeding a mass of 100 kg, a separate specimen shall be subjected to a free drop onto each of the quarters of each rim from a height of 0.3 m. | 722. Free drop test: The specimen shall drop onto the target so as to suffer maximum damage in respect of the safety features to be tested. (a) The height of drop measured from the lowest point of the specimen to the upper surface of the target shall be not less than the distance specified in Table XIII for the applicable mass. For packages with a dimension exceeding 1.2 m, the height of drop measured for any point from its theoretical position considering the package laying on the target (with the orientation it has in routine conditions of transport or handling) and its position in the specimen before drop shall not exceed 1.2 m plus the distance specified in Table XIII for the applicable mass. The target shall be as defined in para. 717. (b) For rectangular fibreboard or wood packages not exceeding a mass of 50 kg, a separate specimen shall be subjected to a free drop onto each corner from a height of 0.3 m. (c) For cylindrical fibreboard packages not exceeding a mass of 100 kg, a separate specimen shall be subjected to a free drop onto each of the quarters of each rim from a height of 0.3 m. | 40 |
| UK/02/71 | 803 | 803. The design for special form radioactive material shall require unilateral approval. The design for low dispersible radioactive material shall require multilateral approval. In both cases, an application for approval shall include: (a) a detailed description of the radioactive material or, if a capsule, the contents; particular reference shall be made to both physical and chemical states; (b) a detailed statement of the design of any capsule to be used; (c) a statement of the tests which have been done and their results, or evidence based on calculative methods to show that the radioactive material is capable of meeting the performance standards, or other evidence that the special form radioactive material or low dispersible radioactive material meets the applicable requirements of these Regulations; (d) a specification of the applicable quality assurance programme as required in para. 310; and (e) any proposed pre-shipment actions for use in the consignment of special form radioactive material or low dispersible radioactive material. | 803. The design for special form radioactive material shall require unilateral approval. The design for low dispersible radioactive material shall require multilateral approval. In both cases, an application for approval shall include: (a) a detailed description of the radioactive material or, if a capsule, the contents; particular reference shall be made to both physical and chemical states; (b) a detailed statement of the design of any capsule to be used; (c) a statement of the tests which have been done and their results, or evidence based on calculative methods to show that the radioactive material is capable of meeting the performance standards, or other evidence that the special form radioactive material or low dispersible radioactive material meets the applicable requirements of these Regulations; (d) A quantitative statement of any time-dependent features of a special form design likely to affect its ability to meet the requirements for special form radioactive material in paras 602 to 604. (e) a specification of the applicable quality assurance programme as required in para. 310; and (f) any proposed pre-shipment actions for use in the consignment of special form radioactive material or low dispersible radioactive material. | 41 |
| Canada/02/12 (4 of 6) | 805 | 805. The approval of designs for packages containing 0.1 kg or more of uranium hexafluoride requires that: (a) After 31 December 2000, each design that meets the requirements of para. 632 shall require multilateral approval. After 31 December 2003, each design that meets the requirements of paras 629–631 shall require unilateral approval by the competent authority of the country of origin of the design; (b) The application for approval shall include all information necessary to satisfy the competent authority that the design meets the requirements of para. 629, and a specification of the applicable quality assurance programme as required in para. 310; (c) The competent authority shall establish an approval certificate stating that the approved design meets the requirements of para. 629 and shall attribute to that design an identification mark. | 805. The approval of designs for packages containing 0.1 kg or more of uranium hexafluoride requires that: (a) Each design that meets the requirements of para. 632 shall require multilateral approval. (a bis) Each design that meets the requirement of paras 629-631 shall require unilateral approval by the competent authority of the country of origin of the design, unless multilateral approval is otherwise required by these regulations. (b) The application for approval shall include all information necessary to satisfy the competent authority that the design meets the requirements of para. 629, and a specification of the applicable quality assurance programme as required in para. 310; (c) The competent authority shall establish an approval certificate stating that the approved design meets the requirements of para. 629 and shall attribute to that design an identification mark. | 42 |
| UK/02/39 (1 of 4) | 805 | 805. The approval of designs for packages containing 0.1 kg or more of uranium hexafluoride requires that: (a) After 31 December 2000, each design that meets the requirements of para. 632 shall require multilateral approval. After 31 December 2003, each design that meets the requirements of paras 629–631 shall require unilateral approval by the competent authority of the country of origin of the design; (b) The application for approval shall include all information necessary to satisfy the competent authority that the design meets the requirements of para. 629, and a specification of the applicable quality assurance programme as required in para. 310; (c) The competent authority shall establish an approval certificate stating that the approved design meets the requirements of para. 629 and shall attribute to that design an identification mark. | 805. The approval of designs for packages containing 0.1 kg or more of uranium hexafluoride requires that: (a) Each design that meets the requirements of para. 632 shall require multilateral approval. Each design that meets the requirements of paras 629–631 shall require unilateral approval by the competent authority of the country of origin of the design; (b) The application for approval shall include all information necessary to satisfy the competent authority that the design meets the requirements of para. 629, and a specification of the applicable quality assurance programme as required in para. 310; (c) The competent authority shall establish an approval certificate stating that the approved design meets the requirements of para. 629 and shall attribute to that design an identification mark. | 43 |
| UK/02/40 | 805 | 805. The approval of designs for packages containing 0.1 kg or more of uranium hexafluoride requires that: (a) After 31 December 2000, each design that meets the requirements of para. 632 shall require multilateral approval. After 31 December 2003, each design that meets the requirements of paras 629–631 shall require unilateral approval by the competent authority of the country of origin of the design; (b) The application for approval shall include all information necessary to satisfy the competent authority that the design meets the requirements of para. 629, and a specification of the applicable quality assurance programme as required in para. 310; (c) The competent authority shall establish an approval certificate stating that the approved design meets the requirements of para. 629 and shall attribute to that design an identification mark. | 805. The approval of designs for packages containing 0.1 kg or more of uranium hexafluoride requires that: (a) After 31 December 2000, each design that meets the requirements of para. 632 or contains fissile material shall require multilateral approval. After 31 December 2003, each design that meets the requirements of paras 629–631, except for those containing fissile material, shall require unilateral approval by the competent authority of the country of origin of the design; (b) The application for approval shall include all information necessary to satisfy the competent authority that the design meets the requirements of para. 629, and a specification of the applicable quality assurance programme as required in para. 310; (c) The competent authority shall establish an approval certificate stating that the approved design meets the requirements of para. 629 and shall attribute to that design an identification mark. | 44 |
| UK/02/41 and UK/02/58 | 806 | 806. Each Type B(U) and Type C package design shall require unilateral approval, except that: (a) a package design for fissile material, which is also subject to paras 812–814, shall require multilateral approval; and (b) a Type B(U) package design for low dispersible radioactive material shall require multilateral approval. | 806. Each Type B(U) and Type C package design shall require unilateral approval, except that: (a) a package design for fissile material, which is also subject to paras 812–814, shall require multilateral approval; and (b) a Type B(U) package design for low dispersible radioactive material shall require multilateral approval for carriage by air. | 45 |
| UK/02/52 (2 of 2) and UK/02/58 | 806 | 806. Each Type B(U) and Type C package design shall require unilateral approval, except that: (a) a package design for fissile material, which is also subject to paras 812–814, shall require multilateral approval; and (b) a Type B(U) package design for low dispersible radioactive material shall require multilateral approval. | 806. Each Type B(U) and Type C package design shall require unilateral approval, except that: (a) a package design for fissile material, which is also subject to paras 812–814, shall require multilateral approval | 46 |
| UK/02/38 | 814bis | The proposal involves new text, complete with heading, (currently missing from the regulations) to be incorporated between existing paras 814 and 815 | APPROVAL OF RADIONUCLIDE VALUES 814bis. Each calculation of radionuclide values that are not listed in Table I shall require multilateral approval. 814bis+1. An application for approval shall include: (a) The effective dose rate coefficient for external dose due to photons calculated at 1m (Sv.Bq-1.h-1); (b) the effective dose rate coefficient for external dose due to beta emission calculated at 1m (Sv.Bq-1.h-1); (c) the effective dose coefficient for the inhalation of a 5 µm aerosol of the radionuclide by workers, in the most restrictive lung absorption category (Sv.Bq-1); (d) the skin dose coefficient for skin contamination (Sv.m2.TBq-1.s-1); (e) if the radionuclide is a noble gas, the effective dose coefficient for submersion dose (Sv.Bq-1.s-1.m3); and (f) the calculated values for A1 and A2 in TBq, the activity concentration for exempt material in Bq/g; and the activity limits for exempt consignments in Bq. 814bis+2. The competent authority shall establish an approval stating that the calculated radionuclide values are approved. | 47 |
| UK/02/39 (2 of 4) | 815 | Packages not requiring competent authority approval of design under the 1985 and 1985 (As Amended 1990) Editions of these Regulations 815. Excepted packages, Type IP-1, Type IP-2 and Type IP-3 and Type A packages that did not require approval of design by the competent authority and which meet the requirements of the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310 and the activity limits and material restrictions of Section IV. Any packaging modified, unless to improve safety, or manufactured after 31 December 2003, shall meet this Edition of the Regulations in full. Packages prepared for transport not later than 31 December 2003 under the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue in transport. Packages prepared for transport after this date shall meet this Edition of the Regulations in full. | Packages not requiring competent authority approval of design under the 1985 and 1985 (As Amended 1990) Editions of these Regulations 815. Excepted packages, Type IP-1, Type IP-2 and Type IP-3 and Type A packages that did not require approval of design by the competent authority and which meet the requirements of the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310 and the activity limits and material restrictions of Section IV. Any packaging modified, unless to improve safety, shall meet this Edition of the Regulations in full. Packages prepared for transport not later than 31 December 2003 under the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue in transport. Packages prepared for transport after this date shall meet this Edition of the Regulations in full. | 48 |
| UK/02/39 (3 of 4) | 817 | Packages approved under the 1973, 1973 (As Amended), 1985 and 1985 (As Amended 1990) Editions of these Regulations 817. Packagings manufactured to a package design approved by the competent authority under the provisions of the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used until 31 December 2003, subject to: the mandatory programme of quality assurance in accordance with the requirements of para. 310; the activity limits and material restrictions of Section IV; and, for a package containing fissile material and transported by air, the requirement of para. 680. After this date use may continue subject, additionally, to multilateral approval of package design. Changes in the design of the packaging or in the nature or quantity of the authorized radioactive contents which, as determined by the competent authority, would significantly affect safety shall require that this Edition of the Regulations be met in full. All packagings for which manufacture begins after 31 December 2006 shall meet this Edition of the Regulations in full. | Packages approved under the 1973, 1973 (As Amended), 1985 and 1985 (As Amended 1990) Editions of these Regulations 817. Packagings manufactured to a package design approved by the competent authority under the provisions of the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used, subject to: multilateral approval of package design, the mandatory programme of quality assurance in accordance with the requirements of para. 310; the activity limits and material restrictions of Section IV; and, for a package containing fissile material and transported by air, the requirement of para. 680. Changes in the design of the packaging or in the nature or quantity of the authorized radioactive contents which, as determined by the competent authority, would significantly affect safety shall require that this Edition of the Regulations be met in full. All packagings for which manufacture begins after 31 December 2006 shall meet this Edition of the Regulations in full. | 49 |
| UK/02/39 (4 of 4) | 818 | Special form radioactive material approved under the 1973, 1973 (As Amended), 1985 and 1985 (As Amended 1990) Editions of these Regulations 818. Special form radioactive material manufactured to a design which had received unilateral approval by the competent authority under the 1973, 1973 (As Amended), 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used when in compliance with the mandatory programme of quality assurance in accordance with the applicable requirements of para. 310. All special form radioactive material manufactured after 31 December 2003 shall meet this Edition of the Regulations in full. | Special form radioactive material approved under the 1973, 1973 (As Amended), 1985 and 1985 (As Amended 1990) Editions of these Regulations 818. Special form radioactive material manufactured to a design which had received unilateral approval by the competent authority under the 1973, 1973 (As Amended), 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used when in compliance with the mandatory programme of quality assurance in accordance with the applicable requirements of para. 310. All special form radioactive material manufactured shall meet this Edition of the Regulations in full. | 50 |
| France/02/42 | 815/818 | See Appendix 3 | See Appendix 3 | 51 |
| UK/02/43 | 819 | 819. The competent authority shall be informed of the serial number of each packaging manufactured to a design approved under paras 806, 809, 812, and 816–817. The competent authority should, consistent with para. 311, maintain a register of such serial numbers. | 819. The competent authority shall be informed of the serial number of each packaging manufactured to a design approved under paras 806, 809, 812, and 816–817 | 52 |
| Canada/02/12 (5 of 6) | 819 | 819. The competent authority shall be informed of the serial number of each packaging manufactured to a design approved under paras 806, 809, 812, and 816–817. The competent authority should, consistent with para. 311, maintain a register of such serial numbers. | 819. The competent authority shall be informed of the serial number of each packaging manufactured to a design approved under paras 805, 806, 809, 812, and 816–817. The competent authority should, consistent with para. 311, maintain a register of such serial numbers. | 53 |
| Germany/02/02 | 820 | 820. Multilateral approval shall be required for: (a) the shipment of Type B(M) packages not conforming with the requirements of para. 637 or designed to allow controlled intermittent venting; (b) the shipment of Type B(M) packages containing radioactive material with an activity greater than 3000 A1 or 3000 A2, as appropriate, or 1000 TBq, whichever is the lower; (c) the shipment of packages containing fissile materials if the sum of the criticality safety indexes of the packages exceeds 50; and (d) radiation protection programmes for shipments by special use vessels according to para. 575(a). | 820. Multilateral approval shall be required for: (a) the shipment of Type B(M) packages not conforming with the requirements of para. 637 or designed to allow controlled intermittent venting; (b) the shipment of Type B(M) packages containing radioactive material with an activity greater than 3000 A1 or 3000 A2, as appropriate, or 1000 TBq, whichever is the lower; (c) the shipment of packages containing fissile materials if the sum of the criticality safety indexes of the packages in a freight container or in any group aboard a conveyance exceeds 50 as provided in para 566 (d); and (d) radiation protection programmes for shipments by special use vessels according to para. 575(a). | 54 |
| UK/02/45 | 824 | 824. Each consignment transported internationally under special arrangement shall require multilateral approval. | 824. Each consignment transported under special arrangement shall require multilateral approval. | 55 |
| Canada/02/12 (2 of 6) | 833 | 833. Each approval certificate of the design of a package issued by a competent authority shall include the following information: (a) Type of certificate. (b) The competent authority identification mark. (c) The issue date and an expiry date. (d) Any restriction on the modes of transport, if appropriate. (e) List of applicable national and international regulations, including the edition of the IAEA Regulations for the Safe Transport of Radioactive Material under which the design is approved. (f) The following statement: “This certificate does not relieve the consignor from compliance with any requirement of the government of any country through or into which the package will be transported.” (g) References to certificates for alternative radioactive contents, other competent authority validation, or additional technical data or information, as deemed appropriate by the competent authority. (h) A statement authorizing shipment where shipment approval is required under para. 820, if deemed appropriate. (i) Identification of the packaging. (j) Description of the packaging by a reference to the drawings or specification of the design. If deemed appropriate by the competent authority, a reproducible illustration, not larger than 21 cm by 30 cm, showing the make-up of the package should also be provided, accompanied by a brief description of the packaging, including materials of manufacture, gross mass, general outside dimensions and appearance. (k) Specification of the design by reference to the drawings. (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. (m) Additionally, for packages containing fissile material: (i) a detailed description of the authorized radioactive contents; (ii) the value of the criticality safety index; (iii) reference to the documentation that demonstrates the criticality safety of the contents; (iv) any special features, on the basis of which the absence of water from certain void spaces has been assumed in the criticality assessment; (v) any allowance (based on para. 674(b)) for a change in neutron multiplication assumed in the criticality assessment as a result of actual irradiation experience; and (vi) the ambient temperature range for which the package design has been approved. (n) For Type B(M) packages, a statement specifying those prescriptions of paras 637, 653, 654 and 657–664 with which the package does not conform and any amplifying information which may be useful to other competent authorities. (o) A detailed listing of any supplementary operational controls required for preparation, loading, carriage, unloading and handling of the consignment, including any special stowage provisions for the safe dissipation of heat. (p) Reference to information provided by the applicant relating to the use of the packaging or specific actions to be taken prior to shipment. (q) A statement regarding the ambient conditions assumed for purposes of design if these are not in accordance with those specified in paras 653, 654 and 664, as applicable. (r) A specification of the applicable quality assurance programme as required in para. 310. (s) Any emergency arrangements deemed necessary by the competent authority. (t) If deemed appropriate by the competent authority, reference to the identity of the applicant. (u) Signature and identification of the certifying official. | 833. Each approval certificate of the design of a package issued by a competent authority shall include the following information: (a) Type of certificate. (b) The competent authority identification mark. (c) The issue date and an expiry date. (d) Any restriction on the modes of transport, if appropriate. (e) List of applicable national and international regulations, including the edition of the IAEA Regulations for the Safe Transport of Radioactive Material under which the design is approved. (f) The following statement: “This certificate does not relieve the consignor from compliance with any requirement of the government of any country through or into which the package will be transported.” (g) References to certificates for alternative radioactive contents, other competent authority validation, or additional technical data or information, as deemed appropriate by the competent authority. (h) A statement authorizing shipment where shipment approval is required under para. 820, if deemed appropriate. (i) Identification of the packaging. (j) Description of the packaging by a reference to the drawings or specification of the design. If deemed appropriate by the competent authority, a reproducible illustration, not larger than 21 cm by 30 cm, showing the make-up of the package should also be provided, accompanied by a brief description of the packaging, including materials of manufacture, gross mass, general outside dimensions and appearance. (k) Specification of the design by reference to the drawings. (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. (m) Additionally, for packages containing fissile material: (i) a detailed description of the authorized radioactive contents; (ii) the value of the criticality safety index; (iii) reference to the documentation that demonstrates the criticality safety of the contents; (iv) any special features, on the basis of which the absence of water from certain void spaces has been assumed in the criticality assessment; (v) any allowance (based on para. 674(b)) for a change in neutron multiplication assumed in the criticality assessment as a result of actual irradiation experience; and (vi) the ambient temperature range for which the package design has been approved. (n) For Type B(M) packages, a statement specifying those prescriptions of paras 637, 653, 654 and 657–664 with which the package does not conform and any amplifying information which may be useful to other competent authorities. (n) (bis) For packages containing more than 0.1 kg of uranium hexafluoride, a statement specifying those prescriptions of paras 630 and 631 with which the package does not conform and any amplifying information which may be useful to other competent authorities.” (o) A detailed listing of any supplementary operational controls required for preparation, loading, carriage, unloading and handling of the consignment, including any special stowage provisions for the safe dissipation of heat. (p) Reference to information provided by the applicant relating to the use of the packaging or specific actions to be taken prior to shipment. (q) A statement regarding the ambient conditions assumed for purposes of design if these are not in accordance with those specified in paras 653, 654 and 664, as applicable. (r) A specification of the applicable quality assurance programme as required in para. 310. (s) Any emergency arrangements deemed necessary by the competent authority. (t) If deemed appropriate by the competent authority, reference to the identity of the applicant. (u) Signature and identification of the certifying official. | 56 |
| Sweden/02/07 | 833 | 833. Each approval certificate of the design of a package issued by a competent authority shall include the following information: (a) Type of certificate. (b) The competent authority identification mark. (c) The issue date and an expiry date. (d) Any restriction on the modes of transport, if appropriate. (e) List of applicable national and international regulations, including the edition of the IAEA Regulations for the Safe Transport of Radioactive Material under which the design is approved. (f) The following statement: “This certificate does not relieve the consignor from compliance with any requirement of the government of any country through or into which the package will be transported.” (g) References to certificates for alternative radioactive contents, other competent authority validation, or additional technical data or information, as deemed appropriate by the competent authority. (h) A statement authorizing shipment where shipment approval is required under para. 820, if deemed appropriate. (i) Identification of the packaging. (j) Description of the packaging by a reference to the drawings or specification of the design. If deemed appropriate by the competent authority, a reproducible illustration, not larger than 21 cm by 30 cm, showing the make-up of the package should also be provided, accompanied by a brief description of the packaging, including materials of manufacture, gross mass, general outside dimensions and appearance. (k) Specification of the design by reference to the drawings. (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. (m) Additionally, for packages containing fissile material: (i) a detailed description of the authorized radioactive contents; (ii) the value of the criticality safety index; (iii) reference to the documentation that demonstrates the criticality safety of the contents; (iv) any special features, on the basis of which the absence of water from certain void spaces has been assumed in the criticality assessment; (v) any allowance (based on para. 674(b)) for a change in neutron multiplication assumed in the criticality assessment as a result of actual irradiation experience; and (vi) the ambient temperature range for which the package design has been approved. (n) For Type B(M) packages, a statement specifying those prescriptions of paras 637, 653, 654 and 657–664 with which the package does not conform and any amplifying information which may be useful to other competent authorities. (o) A detailed listing of any supplementary operational controls required for preparation, loading, carriage, unloading and handling of the consignment, including any special stowage provisions for the safe dissipation of heat. (p) Reference to information provided by the applicant relating to the use of the packaging or specific actions to be taken prior to shipment. (q) A statement regarding the ambient conditions assumed for purposes of design if these are not in accordance with those specified in paras 653, 654 and 664, as applicable. (r) A specification of the applicable quality assurance programme as required in para. 310. (s) Any emergency arrangements deemed necessary by the competent authority. (t) If deemed appropriate by the competent authority, reference to the identity of the applicant. (u) Signature and identification of the certifying official. | 833. Each approval certificate of the design of a package issued by a competent authority shall include the following information: (a) Type of certificate. (b) The competent authority identification mark. (c) The issue date and an expiry date. (d) Any restriction on the modes of transport, if appropriate. (e) List of applicable national and international regulations, including the edition of the IAEA Regulations for the Safe Transport of Radioactive Material under which the design is approved. (f) The following statement: “This certificate does not relieve the consignor from compliance with any requirement of the government of any country through or into which the package will be transported.” (g) References to certificates for alternative radioactive contents, other competent authority validation, or additional technical data or information, as deemed appropriate by the competent authority. (h) A statement authorizing shipment where shipment approval is required under para. 820, if deemed appropriate. (i) Identification of the packaging. (j) Description of the packaging by a reference to the drawings or specification of the design. If deemed appropriate by the competent authority, a reproducible illustration, not larger than 21 cm by 30 cm, showing the make-up of the package should also be provided, accompanied by a brief description of the packaging, including materials of manufacture, gross mass, general outside dimensions and appearance. (j bis) Description(s) of the containment system (para. 213) and, for packages containing fissile material that are not excepted by para. 672, the confinement system (para. 209) (k) Specification of the design by reference to the drawings. (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. (m) Additionally, for packages containing fissile material: (i) a detailed description of the authorized radioactive contents; (ii) the value of the criticality safety index; (iii) reference to the documentation that demonstrates the criticality safety of the contents; (iv) any special features, on the basis of which the absence of water from certain void spaces has been assumed in the criticality assessment; (v) any allowance (based on para. 674(b)) for a change in neutron multiplication assumed in the criticality assessment as a result of actual irradiation experience; and (vi) the ambient temperature range for which the package design has been approved. (n) For Type B(M) packages, a statement specifying those prescriptions of paras 637, 653, 654 and 657–664 with which the package does not conform and any amplifying information which may be useful to other competent authorities. (o) A detailed listing of any supplementary operational controls required for preparation, loading, carriage, unloading and handling of the consignment, including any special stowage provisions for the safe dissipation of heat. (p) Reference to information provided by the applicant relating to the use of the packaging or specific actions to be taken prior to shipment. (q) A statement regarding the ambient conditions assumed for purposes of design if these are not in accordance with those specified in paras 653, 654 and 664, as applicable. (r) A specification of the applicable quality assurance programme as required in para. 310. (s) Any emergency arrangements deemed necessary by the competent authority. (t) If deemed appropriate by the competent authority, reference to the identity of the applicant. (u) Signature and identification of the certifying official. | 57 |
| UK/02/64 | 834bis | No existing text | 834bis. Change(s) to a design, as defined in para 802, for which competent authority approval(s) exist may be approved depending upon their effects upon safety without affecting the validity of the existing package approval. Each change shall include a statement as to its effects upon the nuclear safety of the radioactive contents of the package. In the first instance the change(s) shall be submitted to the competent authority of the country of origin of the design for approval. All changes that effect the nuclear safety of the radioactive contents of a package shall require multilateral approval. The relevant competent authority both of the country of origin of the design or shipment and of each country through or into which the consignment is to be transported, as defined in para 204, shall be notified of all changes. | 58 |
| Canada/02/04 (2 of 2) | Schedules |  | Placarding provisions outlined in Part 9 of Schedule 5, 6, 7, and 9 in the case of Uranium Hexafluoride Schedule 5, Part 9(b) bis For unpackaged LSA-1.....shown in the Fig. 7. However, if the packages contain non-fissile or fissile-excepted uranium hexafluoride, "2978" shall be displayed. For the placards shown in Fig. 6, the numbers shall be preceded by the letters"UN". Schedule 6, Part 9(b) bis. Where an exclusive use ....."3324" shall be displayed on the placards. However, if the packages contain non-fissile or fissile-excepted uranium hexafluoride, "2978" shall be displayed. If the packages contain uranium hexafluoride that is fissile material, "2977" shall be displayed. For the placards shown in Fig. 6, the numbers shall be preceded by the letters "UN". Schedule 7, Part 9(b) bis. Where an exclusive use ....."3325" shall be displayed on the placards. However, if the packages contain non-fissile or fissile-excepted uranium hexafluoride, "2978" shall be displayed. If the packages contain uranium hexafluoride that is fissile material, "2977" shall be displayed. For the placards shown in Fig. 6, the numbers shall be preceded by the letters "UN". Schedule 9, Part 9(c) bis. Where an exclusive use ....."3327" shall be displayed on the placards. However, if the Type A packages contain non-fissile or fissile-excepted uranium hexafluoride, "2978" shall be displayed. If the Type A packages contain uranium hexafluoride that is fissile material, "2977" shall be displayed. For the placards shown in Fig. 6, the numbers shall be preceded by the letters "UN". | 59 |

TABLE 2

CROSS REFERENCE TABLE

| Para order |  | Country order |
| --- | --- | --- |
| # | Para | Proposal |  | Proposal | para | # |
| 1 | 204 | UK/02/04 |  | Canada/02/04 (1 of 2) and France/02/17 | Table VIII footnote “c” | 20 |
| 2 | 204 | UK/02/05 |  | Canada/02/04 (2 of 2) | Schedules | 59 |
| 3 | 212 | Canada/02/08 |  | Canada/02/05 | 709 | 39 |
| 4 | 222 | Sweden/02/02 (1 of 2) and France/02/06 |  | Canada/02/08 | 212 | 3 |
| 5 | 222 (Sweden/02/02) related consequential changes in paras 226, 418, 543, 549, 559, 672, 831, 832, 833 and Table XII | Sweden/02/02 (2 of 2) |  | Canada/02/12 (1 of 6) | 230 | 6 |
| 6 | 230 | Canada/02/12 (1 of 6) |  | Canada/02/12 (2 of 6) | 230 (Canada/02/12) related change in 538 | 7 |
| 7 | 230 (Canada/02/12) related change in 538 | Canada/02/12 (2 of 6) |  | Canada/02/12 (3 of 6) | 230 (Canada/02/12) related change in 539 | 8 |
| 8 | 230 (Canada/02/12) related change in 539 | Canada/02/12 (3 of 6) |  | Canada/02/12 (4 of 6) | 805 | 42 |
| 9 | 246 | UK/02/13 |  | Canada/02/12 (5 of 6) | 819 | 53 |
| 10 | 303 | USA/02/07 and UK/02/14 (1 of 2) |  | Canada/02/12 (6 of 6) |  | 56 |
| 11 | 305 | USA/02/07 and UK/02/14 (2of 2) |  | EU/02/01 and Germany/02/01and UK/02/73 | 622 and consequential changes in 624, 625, 627, 628 and 646b | 24 |
| Para order |  | Country order |
| 12 | Table I footnote (a) | UK/02/18 |  | France/02/04 and UK/02/30 | 622 (alternate proposal) and consequential changes in 624, 625, 627, 628 and 646b | 25 |
| 13 | Table I footnote (b) | Germany/02/06 |  | France/02/22 | 502 | 18 |
| 14 | 402 | UK/02/15 |  | France/02/29 | 652 and 662 | 26 |
| 15 | TABLE II (first column) | Japan/02/02 |  | France/02/34 | 722 | 40 |
| 16 | 416 | UK/02/52 (1 of 2) and Canada/02/02, UK/02/48, UK/02/49 |  | France/02/37 | 672 | 31 |
| 17 | 419 | UK/02/19 |  | France/02/42 | 815/818 | 51 |
| 18 | 502 | France/02/22 |  | Germany/02/02 | 820 | 54 |
| 19 | 503 | UK/02/22 |  | Germany/02/06 | Table I footnote (b) | 13 |
| 20 | Table VIII footnote “c” | Canada/02/04 (1 of 2) and France/02/17 |  | Japan/02/02 | TABLE II (first column) | 15 |
| 21 | 537 | UK/02/25 |  | Sweden/02/02 (1 of 2) and France/02/06 | 222 | 4 |
| 22 | 537 | UK/02/66 |  | Sweden/02/02 (2 of 2) | 222 (Sweden/02/02) related consequential changes in paras 226, 418, 543, 549, 559, 672, 831, 832, 833 and Table XII | 5 |
| 23 | 566 | UK/02/28 |  | Sweden/02/03 | 672 | 32 |
| 24 | 622 and consequential changes in 624, 625, 627, 628 and 646b | EU/02/01 and Germany/02/01, UK/02/73 |  | Sweden/02/07 | 833 | 57 |
| Para order |  | Country order |
| 25 | 622 (alternate proposal) and consequential changes in 624, 625, 627, 628 and 646b | France/02/04 and UK/02/30 |  | UK/02/04 | 204 | 1 |
| 26 | 652 and 662 | France/02/29 |  | UK/02/05 | 204 | 2 |
| 27 | 672 | UK/02/35 (1 of 4) and France/02/44 |  | UK/02/13 | 246 | 9 |
| 28 | 672 (417 bis) (UK/02/35) related consequential changes in Table numbers and location | UK/02/35 (2 of 4) |  | UK/02/15 | 402 | 14 |
| 29 | 672 (417bis) (UK/02/35) related consequential change in para 671 | UK/02/35 (3 of 4) |  | UK/02/18 | Table I footnote (a) | 12 |
| 30 | 672 (417bis) (UK/02/35) related consequential changes in paras 226, 515, TABLE VIII, 541, 549, 802, 812 | UK/02/35 (4 of 4) |  | UK/02/19 | 419 | 17 |
| 31 | 672 | France/02/37 |  | UK/02/22 | 503 | 19 |
| 32 | 672 | Sweden/02/03 |  | UK/02/25 | 537 | 21 |
| 33 | 672 | UK/02/37 (1 of 4) |  | UK/02/28 | 566 | 23 |
| 34 | 672 (UK/02/37) related change in 544 | UK/02/37 (2 of 4) |  | UK/02/35 (1 of 4) and France/02/44 | 672 | 27 |
| 35 | 672 (UK/02/37) related change to TABLE X header | UK/02/37 (3 of 4) |  | UK/02/35 (2 of 4) | 672 (417 bis) (UK/02/35) related consequential changes in Table numbers and location | 28 |
| Para order |  | Country order |
| 36 | 672 (UK/02/37) related consequential changes in paras 541 and 549 | UK/02/37 (4 of 4) |  | UK/02/35 (3 of 4) | 672 (417bis) (UK/02/35) related consequential change in para 671 | 29 |
| 37 | 672 | USA/02/02 |  | UK/02/35 (4 of 4) | 672 (417bis) (UK/02/35) related consequential changes in paras 226, 515, TABLE VIII, 541, 549, 802, 812 | 30 |
| 38 | 677 | USA/02/01 |  | UK/02/37 (1 of 4) | 672 | 33 |
| 39 | 709 | Canada/02/05 |  | UK/02/37 (2 of 4) | 672 (UK/02/37) related change in 544 | 34 |
| 40 | 722 | France/02/34 |  | UK/02/37 (3 of 4) | 672 (UK/02/37) related change to TABLE X header | 35 |
| 41 | 803 | UK/02/71 |  | UK/02/37 (4 of 4) | 672 (UK/02/37) related consequential changes in paras 541 and 549 | 36 |
| 42 | 805 | Canada/02/12 (4 of 6) |  | UK/02/38 | 814bis | 47 |
| 43 | 805 | UK/02/39 (1 of 4) |  | UK/02/39 (1 of 4) | 805 | 43 |
| 44 | 805 | UK/02/40 |  | UK/02/39 (2 of 4) | 815 | 48 |
| 45 | 806 | UK/02/41 and UK/02/58 |  | UK/02/39 (3 of 4) | 817 | 49 |
| Para order |  | Country order |
| 46 | 806 | UK/02/52 (2 of 2) and UK/02/58 |  | UK/02/39 (4 of 4) | 818 | 50 |
| 47 | 814bis | UK/02/38 |  | UK/02/40 | 805 | 44 |
| 48 | 815 | UK/02/39 (2 of 4) |  | UK/02/41 and UK/02/58 | 806 | 45 |
| 49 | 817 | UK/02/39 (3 of 4) |  | UK/02/43 | 819 | 52 |
| 50 | 818 | UK/02/39 (4 of 4) |  | UK/02/45 | 824 | 55 |
| 51 | 815/818 | France/02/42 |  | UK/02/52 (1 of 2) and Canada/02/02, UK/02/48, and UK/02/49 | 416 | 16 |
| 52 | 819 | UK/02/43 |  | UK/02/52 (2 of 2) and UK/02/58 | 806 | 46 |
| 53 | 819 | Canada/02/12 (5 of 6) |  | UK/02/64 | 834bis | 58 |
| 54 | 820 | Germany/02/02 |  | UK/02/66 | 537 | 22 |
| 55 | 824 | UK/02/45 |  | UK/02/71 | 803 | 41 |
| 56 | 833 | Canada/02/12 (6 of 6) |  | USA/02/01 | 677 | 38 |
| 57 | 833 | Sweden/02/07 |  | USA/02/02 | 672 | 37 |
| 58 | 834bis | UK/02/64 |  | USA/02/07 and UK/02/14 (1 of 2) | 303 | 10 |
| 59 | Schedules | Canada/02/04 (2 of 2) |  | USA/02/07 and UK/02/14 (2of 2) | 305 | 11 |

##### APPENDIX 1

CHANGE #5 (SWEDEN/02/02, 2 of 2)

CONSEQUENTIAL CHANGES

IF CHANGE #4 (SWEDEN/02/02, 1 of 2) WERE ACCEPTED

Sweden/02/02 – Additional consequential changes due to accepted proposal

Current texts often correspond more to the proposed definition than to the current one. Many of the texts that are changed are identical but refer to different paragraphs or schedules. Both “fissile materials” and “fissile nuclides” are important terms that should be maintained.

| Regulations |
| --- |
| Section, Para. or location (number of occurrences) | Current use of “fissile” | Proposed use of “fissile” (bold type indicates change) | Comment Change without text proposal means “material” is exchanged for “nuclide(s)” |
|  | Material | Nuclide(s) | Material | Nuclide(s) |  |
| Section II |  |  |  |  |  |
| 222. Definition text | Yes | No | Yes | Yes | Major change |
| 226(a)(iii) LSA-I def. ”excluding FM in quantities not excepted…” | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| 226(a)(iv) LSA-I def. ”excluding FM in quantities not excepted…” | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Section IV |  |  |  |  |  |
| 418. Contents (3) | Yes | No | Yes | Yes | Change “(a) quantities of FNs not authorized …” “(b) any radionuclide different from …” |
| Section V |  |  |  |  |  |
| 543(b) Activity (2) | Yes | No | Yes | Yes | Change “For FM, the mass of fissile nuclides …” |
| 549(f) (2) | Yes | No | Yes | Yes | Change “For FM, the mass of fissile nuclides …” |
| 559(e) Notification (2) | Yes | No | Yes | Yes | Change “For FM, the mass of fissile nuclides …” |
| Section VI |  |  |  |  |  |
| 672(a) Formula | Yes | No | No | Yes | Change |
| 672(a)(i) 15 g | Yes | No | No | Yes | Change |
| 672(a)(iii) 5 g/10 l | Yes | No | No | Yes | Change |
| 672(b) 1% enrichm. | Yes | No | No | Yes | Change |
| Table XII body (3) | Yes | No | No | Yes | Change |
| Section VIII |  |  |  |  |  |
| 831(j) Special arr. App. cert. Contents | Yes | No | No | Yes | Change |
| 832(j) Shipm. Appr. | Yes | No | No | Yes | Change |
| 833(l) Package design, Contents | Yes | No | No | Yes | Change |
| Schedules |
| Section, Para. or location (number of occurrences) | Current use of “fissile” | Proposed use of “fissile” (bold type indicates change) | Comment Change without text proposal means “material” is exchanged for “nuclide(s)” |
|  | Material | Nuclide(s) | Material | Nuclide(s) |  |
| Schedule 5. 1.(b)(iii) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 5. 1.(b)(iv) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 6. 2.(f) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 6. 2.(g) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 7. 2.(f) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 7. 2.(g) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 8.2.(d) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 9. 2.(e) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 9. 2.(f) | Yes | No | No | Yes | Changed. “excluding FN quantities not excepted …” |
| Schedule 13. 1. Def. (2) | Yes | No | Yes | Yes | Major change See 222. |

| ADVISORY MATERIAL |
| --- |
| Section, Para. or location | Current use of “fissile” | Proposed use of “fissile” (bold type indicates change) | Comment Change without text proposal means “material” is exchanged for “nuclide(s)” |
|  | Material | Nuclide(s) | Material | Nuclide(s) |  |
| 222.1 | Yes | No | Yes | No | Delete two last sentences: “In the Regulations the term ‘fissile material’ is occasionally used to refer both to fissile radionuclides and to material containing those radionuclides. Users of the Regulations should remain alert to the context in which the term ‘fissile material’ is used. |
| 222.3 | Yes | No | Yes | No | Modify to: “As indicated in the above paragraph, the basis used to select the fissile nuclides in the definition of fissile material for the purposes of the Regulations relies on ...” |
| Advisory text appears to be written with fissile material as a general term that can be used with either definition (specific nuclides or material including such nuclides). Further changes are not necessary |

##### APPENDIX 2

CONSOLIDATED VERSION OF PROPOSED CHANGES

#27 UK/02/35 (1 of 4),

#31 France/02/37,

#32 Sweden/02/03 and

#33 UK/02/37 (1 of 4)

CONCERNING PARAGRAPH 672

| CURRENT TEXT IN TS-R-1 PARA 672 |
| --- |
| 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. |  |
| PROPOSED TEXT TO REPLACE 672, COMBINING PROPOSED CHANGES #27, #31, #32 AND #33 |
| 417bis. Packages containing fissile material, other than packages approved for the carriage of fissile material, and provided that the smallest external dimension of each package is not less than 10 cm, shall meet one of the exceptions (a)–(d). Only one type of exception is allowed per consignment. A mass limit per consignment such that: CSI = mass of uranium-235 (g) + mass of other fissile material (g) * 50 X Y where X and Y are the mass limits defined in Table IV, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table IV , except for deuterium in natural concentration in hydrogen. (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. (c ) Liquid solutions of uranyl nitrate enriched in uranium-235 to a maximum of 2% by mass, with a total plutonium and uranium-233 content not exceeding 0.002% of the mass of uranium, and with a minimum nitrogen to uranium atomic ratio (N/U) of 2. (d) Packages containing, individually, a total plutonium mass not more than 1 kg, of which not more than 20% by mass may consist of plutonium-239, plutonium-241 or any combination of those radionuclides. |  |

APPENDIX 3

CHANGE #51

TRANSITIONAL ARRANGEMENTS

(PARAGRAPHS 815/818)

FRANCE/02/42   TRANSITIONAL ARRANGEMENTS (Paras 815/818)

## CURRENT TEXT IN TS-R-1

TRANSITIONAL ARRANGEMENTS

Packages not requiring competent authority approval of design under the 1985 and 1985 (As Amended 1990) Editions of these Regulations

815.	Excepted packages, Type IP-1, Type IP-2 and Type IP-3 and Type A packages that did not require approval of design by the competent authority and which meet the requirements of the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310 and the activity limits and material restrictions of Section IV. Any packaging modified, unless to improve safety, or manufactured after 31 December 2003, shall meet this Edition of the Regulations in full. Packages prepared for transport not later than 31 December 2003 under the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue in transport. Packages prepared for transport after this date shall meet this Edition of the Regulations in full.

Packages approved under the 1973, 1973 (As Amended), 1985 and 1985 (As Amended 1990) Editions of these Regulations

816.	Packagings manufactured to a package design approved by the competent authority under the provisions of the 1973 or 1973 (As Amended) Editions of these Regulations may continue to be used, subject to: multilateral approval of package design, the mandatory programme of quality assurance in accordance with the applicable requirements of para. 310; the activity limits and material restrictions of Section IV; and, for a package containing fissile material and transported by air, the requirement of para. 680. No new manufacture of such packaging shall be permitted to commence. Changes in the design of the packaging or in the nature or quantity of the authorized radioactive contents which, as determined by the competent authority, would significantly affect safety shall require that this Edition of the Regulations be met in full. A serial number according to the provision of para. 538 shall be assigned to and marked on the outside of each packaging.

817.	Packagings manufactured to a package design approved by the competent authority under the provisions of the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used until 31 December 2003, subject to: the mandatory programme of quality assurance in accordance with the requirements of para. 310; the activity limits and material restrictions of Section IV; and, for a package containing fissile material and transported by air, the requirement of para. 680. After this date use may continue subject, additionally, to multilateral approval of package design. Changes in the design of the packaging or in the nature or quantity of the authorized radioactive contents which, as determined by the competent authority, would significantly affect safety shall require that this Edition of the Regulations be met in full. All packagings for which manufacture begins after 31 December 2006 shall meet this Edition of the Regulations in full.

Special form radioactive material approved under the 1973, 1973 (As Amended), 1985 and 1985 (As Amended 1990) Editions of these Regulations

818.	Special form radioactive material manufactured to a design which had received unilateral approval by the competent authority under the 1973, 1973 (As Amended), 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used when in compliance with the mandatory programme of quality assurance in accordance with the applicable requirements of para. 310. All special form radioactive material manufactured after 31 December 2003 shall meet this Edition of the Regulations in full.

PROPOSED TEXT IN FRANCE/02/42

Paragraphs affected and proposed text change to regulatory text in TS-R-1 (ST-1, Rev.) TRANSITIONAL ARRANGEMENTS Packages not requiring competent authority approval of design under the 1985, 1985 (As Amended 1990) and 1996 (Revised and Amended 2005) Editions of these Regulations 815. Excepted packages, Industrial packages Types IP-1, IP-2 and IP-3 and Type A packages which did not require approval of design by the competent authority and which meet the requirements of an Edition of the Regulations specified in column 1 of Table XIV may continue to be prepared, or such packagings may continue to be manufactured, until the corresponding date specified in column 3 of Table XIV. Packages prepared for transport not later than the date specified in column 3 of Table XIV for the corresponding Edition of the Regulations specified in column 1, may continue in transport until the corresponding date specified in column 4 of Table XIV. Except as allowed in this paragraph, manufacture of packagings and use of packages shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para 310; and the activity limits and material restrictions of Section IV , the requirements and controls for transport of section V; for a package containing fissile material, the requirements of para. 672 and for a package containing fissile material transported by air, the requirements of para. 680. 815bis.Excepted packages, Industrial packages Types IP-1, IP-2 and IP-3 and Type A packages which did not require approval of design by the competent authority may be modified or continued to be designed until the date specified in column 2 of Table XIV in accordance with the requirements of the corresponding Edition of the Regulations specified in column 1 of Table XIV. Except as allowed in this paragraph, modification of packaging and design of packages shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310; and the activity limits and material restrictions of Section IV , the requirements and controls for transport of section V; for a package containing fissile material, the requirements of para. 672 and for a package containing fissile material transported by air, the requirements of para. 680. Table XIV : PACKAGES NOT REQUIRING COMPETENT AUTHORITY APPROVAL OF DESIGN Edition of the regulation* Design or modification until Manufacture and prepare until End of transport 1985 Dec. 31, 2003+ Dec. 31, 2003+ 2028 1996 Dec. 31, 2006 Dec. 31, 2010 2034 * Includes Revised Editions and Amended Editions +dates which are already mandatory according to edition that have been in force (para 815 of the 1996 edition) Packages approved under the 1973, 1973 (As Amended), 1985 and 1985 (As Amended 1990) and 1996 (Revised and Amended 2005) Editions of these Regulations 816. Packagings manufactured to a package design approved by the competent authority as meeting the Edition of the Regulations specified in column 1 of Table XV may continue to be used until the date specified in column 4 of Table XV corresponding with the Edition of the Regulations specified in column 1 of Table XV. After this date use may continue, until the corresponding date specified in column 6 of Table XV, subject, additionally, to multilateral approval of package design. A serial number according to the provision of para. 538 shall be assigned to and marked on the outside of each packaging. Except as allowed in this paragraph, use of packagings shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310; and the activity limits and material restrictions of Section IV , the requirements and controls for transport of section V; for a package containing fissile material, the requirements of para. 672 and for a package containing fissile material transported by air, the requirements of para. 680.

816bis. Packagings, for which the package design was approved by a competent authority, may be manufactured until the date specified in column 5 of Table XV corresponding to the Edition of the Regulations in column 1 of Table XV to which the package design was approved. After this date no new manufacture shall commence. Except as allowed in this paragraph, manufacture of packagings shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310; and the activity limits and material restrictions of Section IV , the requirements and controls for transport of section V; for a package containing fissile material, the requirements of para. 672 and for a package containing fissile material transported by air, the requirements of para. 680. 816bis+1. Packages which require competent authority approval of design may continue to be designed until the date specified in column 3 of Table XV, in accordance with the requirements of the corresponding Edition of the Regulations specified in column 1 of Table XV. The commencing of any new design or modification in design which, as determined by the competent authority, would significantly affect safety, shall require the package design to meet this edition of the Regulations in full. Changes in the design or in the nature or quantity of the authorized radioactive contents which, as determined by the competent authority, would not significantly affect safety, may be made after the date specified in column 3 of Table XV manufactured to a design which had received unilateral approval by the competent authority under an Edition of the Regulations specified in column 1 of Table XV may continue to be used until the corresponding date specified in column 6 of Table XV. Except as allowed in this paragraph, design and modification of packages shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310; and the activity limits and material restrictions of Section IV , the requirements and controls for transport of section V; for a package containing fissile material, the requirements of para. 672 and for a package containing fissile material transported by air, the requirements of para. 680. Special form radioactive material , in accordance with the requirements of the corresponding Edition of the Regulations specified in column 1 of Table XV approved under the 1973, 1973 (As Amended), 1985 and 1985 (As Amended 1990) and 1996 (Revised and As amended 2005) Editions of these Regulations and low dispersible material 818. Special form radioactive material . Except as allowed in this paragraph, use of special form material shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310. 818bis. Special form radioactive material may continue to be designed or modified until the date specified in column 3 of Table XV in accordance with the requirements of the corresponding Edition of the Regulations specified in column 1 of Table XV. Changes in the design which, as determined by the competent authority, would not significantly affect safety, may be made after the date specified in column 3 of Table XV, in accordance with the requirements of the corresponding Edition of the Regulations specified in column 1 of Table XV. Except as allowed in this paragraph, design and modification of special form material shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310. 818bis+1. Special form radioactive material may be manufactured until the date specified in column 5 of Table XV corresponding to the Edition of the Regulations in column 1 of Table XV to which the design is approved. After this date no new manufacture shall commence. Except as allowed in this paragraph, manufacture of special form material shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310.

Low dispersible radioactive material approved under a previous Edition of these Regulations 818bis+2. Low dispersible radioactive material manufactured to a design which had received multilateral approval by the competent authority under the Edition of the Regulations specified in column 1 of Table XV may continue to be used until the corresponding date specified in column 6 of Table XV. Except as allowed in this paragraph, use of low dispersible radioactive material shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310. 818bis+3. Low dispersible radioactive material may be designed or modified until the date specified in column 3 of Table XV in accordance with the requirements of the corresponding Edition of the Regulations specified in column 1 of Table XV. Changes in the design which, as determined by the competent authority, would not significantly affect safety, may be made after the date specified in column 3 of Table XV, in accordance with the requirements of the corresponding Edition of the Regulations specified in column 1 of Table XV. Except as allowed in this paragraph, design and modification of low dispersible radioactive material shall be subject to the mandatory programme of quality assurance in accordance with the requirements of para. 310. 819 reference to 816-817 becomes reference to 816 Amend para 828(d) as follows: REPLACE ALL OCCURRENCES OF “96" BY “05". Amend para 829 as follows: REPLACE ALL OCCURRENCES OF “96" BY “05". Table XV: COMPETENT AUTHORITY APPROVED PACKAGES AND MATERIALS Edition of the regulations * Type Design or Modification until Multilateral approval after Commence manufacture until End of use 1967 All Packages Dec. 31, 2001 Special Form Dec. 31, 2001 1973 All Packages Dec. 31,1995+ Dec. 31,1992+ Dec. 31, 1995+ Dec. 31, 2019 Special Form Dec. 31,1995+ N/A Dec. 31, 2003++ Dec. 31, 2019 1985 All Packages Dec. 31,2001** Dec. 31,2003** Dec. 31, 2006** Dec. 31, 2028 Special Form Dec. 31,2001** N/A Dec. 31,2003++ Dec. 31, 2028 1996 All Packages Dec. 31,2012 Dec. 31,2016 Dec. 31, 2018 Dec. 31, 2034 Special Form Dec. 31,2008 N/A Dec. 31,2012 Dec. 31, 2034 Low Dispersible Dec. 31,2008 N/A Dec. 31,2012 Dec. 31, 2034 * Includes Revised Editions and Amended Editions Nota: dates which are already mandatory according to edition that have been in force: +para 714 of the 1985 edition **para 817 of the 1996 edition ++para 818 of the 1996 edition

RELATED PROPOSED TEXT FOR TS-G-1.1

Paragraphs affected and proposed text change to advisory material in TS-G-1.1 538.3bis In the case where package designs are updated to meet newer standards it may be appropriate to apply the date suffix to the competent authority identification mark as a legible and durable label. This is particularly justified when some of the packagings of the same initial design have not yet been or cannot be modified to the updated design. TRANSITIONAL ARRANGEMENTS Packages not requiring competent authority approval of design under previous editions of these Regulations 815.1. Following from the adoption of the 1985 Editions of the Regulations, packages not requiring approval of design by competent authority based on the 1973 Edition of the Regulations and the 1973 (As Amended) Edition of the Regulations could no longer be used. Continued operational use of such packages required either that the design be reviewed according to the requirements of the 1985 Editions of the Regulations, or that shipments reviewed and approved by the competent authority as special arrangements, although this was not explicitly stated in the Regulations. 815.2. Paragraph 815 was introduced into the 1996 Edition of the Regulations to allow such existing packagings to continue in use for a limited and defined period of time, following publication, during which the designs might be reviewed, and if necessary modified, to ensure they meet the requirements of the current Edition of the Regulations in full. Where such review and/or modification proves impractical, the transition period is intended to allow time for package designs to be phased out and new designs meeting the requirements of the latest Edition of the Regulations to be phased in. 815.3 Such transitional arrangements for packages not requiring competent authority approval were continued in the 2005 Edition of the Regulations, using time intervals based on a broad consensus view on the intervals necassary. The dates were introduced into a table format (Table XIV) to facilitate updating the transitional arrangements for these packages during future revisions of the regulations. 815.4 Packages prepared in accordance with previous Editions of the Regulations are sometimes stored for many years prior to further shipment. This may be particularly applicable in the case of Industrial or Type A packages containing radioactive waste and awaiting shipment to intermediate or final storage repositories. Paragraph 815 allows such packages, prepared during a defined period of time and when properly maintained, to be transported in the future on the basis of compliance with the earlier Editions of the Regulations. 815.5. Paragraph 815 emphasizes the requirement to apply quality assurance measures, according to the latest Edition of the Regulations, to ensure that only such packages remain in use, where they continue to meet the original design intent or regulatory requirements. This can best be achieved by ensuring that the latest quality assurance measures are applied to post-manufacturing activities such as servicing, maintenance, modification and use of such packages.

815.6. The reference to Section IV of the current Regulations is included to ensure that only the most recent radiological data (as reflected in A1 and A2 values) are used to determine package content and other related limits. It should be noted that the scope of the transitional arrangements of the regulations only extends to the requirements for certain packagings and packages. In all other aspects e.g., concerning general provisions; the requirements and controls for transport including consignment and conveyance limits; and approval and administrative requirements, the provisions of the Edition of the Regulations in force apply. 815.7. With the introduction of a new Edition of the Regulations that could be published in 2007, packages that do not require competent authority approval of the design that meet the 2005 Edition of the regulations would similarly be grandparented. The proposed grandparenting periods could be consistent with those intervals established in the 1996 Edition of the Regulations. The end-of-design or-modification date would be December 31, 2008, the end-of- manufacture date would be December 2012 and the end-of- use date would be December 31 2036, assuming publication of the next Edition in 2007 with an implementation date after December 31, 2008. These dates may be modified considering the extent of the changes in the package design standards in the new Regulations. 815bis.1. Any revision to the original package design, or increase in contained activity, or addition of other types of radioactive materials, which would significantly and detrimentally affect safety, as determined by the package owner in consultation with the package designer, will require the design to be reassessed according to the latest Edition of the Regulations. This could include such things as an increase in the mass of the contents, changes to the closure, changes to any impact limiters, changes to the thermal protection and shielding and changes in the form of the contents. Paragraph 815 bis defines the time period during which design and modifications may be made to a package design following the publication of revised Regulations. This paragraph refers to Table XIV which lists the date applicable to designs that meet the specified Editions of the Regulations. By default, modifications to improve safety are allowed until the date in column 3 of Table XIV (end of manufacture and use date). 815bis.2. The most recent radiological data, as reflected in the A1 and A2 values are used to determine package content and other related limits - this concerns the limitations given in paras. 226, 408, 410 to 414, 525, 601. The most recent data relative to fissile exceptions also need to be used. Packages approved under previous Editions of these Regulations 816.1. Previous Editions of the Regulations have included provisions that allow packages requiring approval of design by competent authority (Type B, Type B(U), Type B(M), Type C packages, packages for uranium hexafluoride and package designs for fissile material) based on earlier Editions of the Regulations to be continued in use, subject to certain limitations on new manufacture, additional requirements to mark such packages with serial numbers and multilateral approval of all such designs. This provision, known colloquially as 'grandparenting', was newly introduced into the 1985 Editions of the Regulations to ease the transition to those Regulations. This allowed packages, provided they were properly maintained and continued to meet their original design intent, to continue in use to the end of their useful design lives. It also provided for a period of time, following publication, during which the designs could be reviewed, and, if necessary, modified, to ensure packages met the requirements of the 1985 Edition of the Regulations in full. Where such review and/or modification proved impractical, the transition period allowed time for packages to be phased out and new designs meeting the requirements of the 1985 Edition of the Regulations to be phased in.

816.2. Such transitional arrangements for packages were continued in the 2005 Edition of the Regulations, using time intervals consistent with those in the 1996 Edition. The dates specified in the grandparenting provisions have been included in the Regulations in a tabular format (Table XV). 816.3 When applying para 816, the original competent authority identification mark and design codes, assigned by the competent authority of design, should be retained both on the packages and on the competent authority certificates of design approval, notwithstanding that these packages may become subject to multilateral approval of design. This means that packages originally designated Type B(U)-85 or Type B(U)F-85 under the 1985 Editions of the Regulations should not be redesignated Type B(M)-85 or Type B(M)F-85, nor should they be redesignated Type B(M)-05 or Type B(M)F-05, when used under the provisions of para. 816. This is to ensure that such packages can be clearly identified as packages "grandfathered" under the provisions of paragraph 816, having been originally approved under the 1985 Editions of the Regulations. 816.4. The most recent radiological data, as reflected in the A1 and A2 values are used to determine package content and other related limits - this concerns the limitations given in paras. 416, 558, 657, 730, 820. It is also noted that when the A1 or A2 value is listed as a limit in the package approval (for example, contents may be limited to a certain number of A2's instead of specific radionuclides), the new A1 and A2 values in the new regulations should be used, without a transitional period. It is not expected that the calculations that may have been used to demonstrate compliance with the release criteria in paras. 656 and 669 of these Regulations will be immediately updated to include the most recent A2 values. If the package is evaluated to a more recent edition of the Regulations, the analysis, including the A2 values, should be updated. 816.5. The reference to Section IV and para. 680 of the Edition of the Regulations in force is included to ensure that only the most recent radiological data (as reflected in the A1 and A2 values), and requirements for fissile material by air, may be used to determine package content and other related limits. It should be noted that the scope of the transitional arrangements of the regulations only extends to the requirements for certain packagings and packages. In all other aspects e.g., concerning general provisions, the requirements and controls for transport including consignment and conveyance limits, and approval and administrative requirements, the provisions of the Edition of the Regulations in force apply. 816.6. In the process of developing the 1996 Edition of the Regulations it was determined that there was no need for an immediate change of package designs following the adoption of the Regulations, but that changes aiming at a long term improvement of safety in transport were justified. Therefore it was also decided to accept continued operational use of certain packages designed and approved under the 1973 Editions of the Regulations. The continued use of existing packagings with a 1967 Edition based package design approval was considered to be no longer necessary or justified and was not authorized in the 1985 Edition and subsequent Editions of the Regulations. 816.7. The continued use of packages approved under previous Editions of the Regulations is subject to multilateral approval from the date in column 4 of Table XV, in order to permit the competent authorities to establish a framework within which continued use may be approved. 816.8. The grandparenting provisions collectively allow transport of packages and materials for which the designs were approved to a previous Edition of the Regulations. Transport of grandparented designs will comply with other applicable requirements of the Edition of Regulations in force at the time of transport. The various grandparenting provisions specifically call out provisions in the Edition of the Regulations in force at the time of transport, such as quality assurance requirements of para. 310, the activity limits and materials restrictions of Section IV, and the requirements of para. 680 for packages containing fissile material and transported by air. Other provisions of the Edition of the Regulations in force at the time of transport must also be applied, such as the applicable general provisions in Section III, requirements and controls for transport in Section V, and approval and administrative requirements of Section VIII

816.9. With the excepted publication in 2007 of a new Edition of the Regulations and its implementation after December 31, 2008, competent authority approved packages that meet the 2005 Edition of the Regulations would similarly be grandparented. The proposed grandparenting periods of Table XV could be consistent with those intervals established in the 1985 and 1996 Editions of the Regulations. For packages, the end-of-design or-modification date would be December 31, 2014, the commence-manufacture until date would be December 31, 2020, the use-under-multilateral approval would be until December 31, 2036. These dates may be modified considering the extent of the changes in the package design standards in the future edition of the Regulations. 816bis.1. See para. 538.2. 816bis.2 Specified time intervals are also given for continued fabrication of designs that were approved to previous Editions of the Regulations. After such a period, fabrication is not permitted to commence. 816bis+1.1 To accommodate possible frequent revision of the package design standards in the Regulations, a new transitional period for design and modification is defined. This period allows the design and certification of the package to be performed under a single Revision of the Regulations. It is appropriate to consider the date of application to the competent authority as the relevant date. During this period of changes in the design of the packages or in the nature or quantity of the radioactive contents which would significantly and detrimentally affect safety, as determined by the competent authority, would be assessed under the design standards in effect at the time of the design approval. This could include an increase in the mass of the contents, changes to the closure, changes to any impact limiters, changes to the thermal protection or shielding and changes in the form of the contents. For a two-year revision cycle, it is judged that the period of time needed for package design, testing, approval by the competent authority, and fabrication may last over several revisions of the regulations. Modifications to the package design are commonly needed to allow the transport of new contents, or to include design improvements, particularly those based on operational experience. The specified design interval has been established to allow these activities to be performed under a single set of regulatory requirements. 816bis+1.2 The most recent radiological data, as reflected in the A1 and A2 values are used to determine package content and other related limits - this concerns the limitations given in paras. 416, 558, 657, 730, 820. It is also noted that when the A1 or A2 value is listed as a limit in the package approval (for example, contents may be limited to a certain number of A2's instead of specific radionuclides), the new A1 and A2 values in the new regulations should be used, without a transitional period. It is not expected that the calculations that may have been used to demonstrate compliance with the release criteria in paras. 656 and 669 of these Regulations will be immediately updated to include the most recent A2 values. If the package is evaluated to a more recent edition of the Regulations, the analysis, including the A2 values, should be updated. Special form radioactive material approved under previous Editions of these Regulations

818.1. Paragraph 818 introduces transitional arrangements for special form radioactive material, the design of which is also subject to competent authority approval. It specifies the need to apply quality assurance measures according to the Edition of the Regulations in force to ensure that such special form radioactive material remains in use, only where it continues to meet the original design intent or regulatory requirements. This can best be achieved by ensuring that the latest quality assurance measures are applied to post-manufacturing activities such as servicing, maintenance, modification and use of such special form material. It should be noted that the scope of the transitional arrangements of the regulations only extends to the requirements for certain special form radioactive materials. In all other aspects e.g., concerning general provisions; the requirements and controls for transport including consignment and conveyance limits; and approval and administrative requirements, the provisions of the Edition of the Regulations in force apply. 818.2. In the process of developing the 1996 Edition of the Regulations it was determined that there was no need for an immediate change in the design of special form radioactive material following the adoption of the Regulations, but that changes aiming at a long term improvement of safety in transport were justified. Therefore it was also decided to accept continued operational use of special form radioactive material designed and approved under the 1973 or 1985 Editions of the Regulations. However, no new manufacture of such special form radioactive material is permitted to commence beyond 31 December 2003 as specified in the 1996 edition. The continued use of existing special form radioactive material with a 1967 Edition based design approval was considered to be no longer necessary or justified. 818.3. With the excepted publication in 2007 of a new Edition of the Regulations and its implementation after December 31, 2008, competent authority approved designs for special form radioactive material and low dispersible material that meet the 2005 Edition of the Regulations would similarly be grandparented. The proposed grandparenting periods could be consistent with those intervals established in the 1996 Editions of the Regulations. For these materials the end-of-design-or modification date would be December 31, 2010, and the commence-manufacture-until date would be December 31, 2014. The use would be until December 31, 2036. These dates may be modified considering the extent of the changes in the design standards in the new Regulations. 828.2. It is essential that easy means are available for determining under which edition of the Regulations the original package design approval was issued, preferably in the identification mark. This will be achieved by adding the symbol ‘-05' to the type code. Using this two-digit year designation should be continued through subsequent revisions of the regulations. Example: Edition of Package design Regulations identification mark 1967 Edition A/132/B 1973 Edition A/132B(U), or A/132/B(M) 1985 Edition A/132/B(U)-85, or A/132/B(M)-85 1996 Edition A/132/B(U)-96, or A/132/B(M)-96 2005 Edition A/132/B(U)-05, or A/132/B(M)-05

__________________

# Text boxes

STSTE

Secretariat