Informal document No.   6

(51st GRE, 15-19 September 2003,

agenda item 1.1.2.9.)

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Lighting and Light-Signalling (GRE)

(Fifty-first session, 15 September - 19 September 2003,

agenda item ????.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 48

02 SERIES OF AMENDMENTS

(Installation of lighting and light-signalling devices)

Transmitted by the Experts from Germany

Note:	The text reproduced below was prepared by the experts from Germany, in order to allow the signalling of emergency braking.  This proposal is based on document TRANS/WP.29/GRE/2002/22/Rev.1.  The amended text is marked in bold characters.

_________

_____________

Note:  This document is distributed to the Experts on Lighting and Light-Signalling only.

### A.	PROPOSAL

Insert a new paragraph 2.27., to read:

"2.27.	"Emergency braking" means a braking with a deceleration at the physical limits of tire adhesion to the road surface."

Paragraph 5.9., amend to read:

"5.9.	In the absence of specific instructions, no lamps other than direction-indicator lamps, the vehicle-hazard warning signal, the stop lamps in the case of emergency braking, and amber side-marker lamps complying with paragraph 6.18.7. below, shall be flashing lamps."

Paragraph 6.7.7., amend to read:

"6.7.7.	Electrical connections

6.7.7.1.	Must light up when the service brake is applied. The stop lamps need not function if the device, which starts and/or stops the engine, is in a position, which makes it impossible for the engine to operate.

The stop lamps may be activated by the application of a retarder or a similar device.

      - In the case of an emergency braking the stop lamps may flash. If so the following conditions shall be met:

- the frequency of flashing is 5 Hz ( 2 Hz

- the vehicle speed is higher than 10 km/h

- the signal is activated and deactivated automatically."

*       *       *

##### B.	JUSTIFICATION:

The indication of an emergency braking increases road safety:

Research studies prove that the reaction time of the drivers is reduced.  An earlier reaction time of 0.2 sec at a vehicle speed of 80 km/h results in a reduced stopping distance of 4.4 m which corresponds to 30 km/h residual speed.

The frequency of 5 Hz ( 2 Hz allows the flashing of filament bulbs as well as for LED’s.

The threshold of velocity of 10 km/h ensures that emergency brake indication is only activated during deceleration of the vehicle and a signalisation at standstill is prevented.

Only automatic activation assures the immediate signalisation of emergency braking.  Automatic deactivation avoids false signals and misuse.

____________