# Informal document N° 11

(53rd GRRF, 3-7 February 2003

agenda item 1.4)

###### PROPOSED AMENDMENTS TO ECE REGULATION N° 48

Paragraph 2.7.12., amend to read:

    - “Stop lamp” means a lamp used to indicate to other road users to the rear of the vehicle that the vehicle may be decelerating.

Paragraph 6.7.7., amend to read:

6.7.7.	Electrical Connections

The stop lamp is only allowed to illuminate under the conditions set out in ECE Regulation 13, sections 5.2.1.30 and 5.2.2.21.

The stop lamps need not function if the device that activates the propulsion system of the vehicle is in a position which makes it impossible for the vehicle to operate.

____________