#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2004/12

31 March 2004

# ORIGINAL: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-fifth session, 5-14 July 2004

# Item 6 of the provisional agenda

# LISTING, CLASSIFICATION AND PACKING

Proposal to add new UN Numbers for Formic Acid (UN 1779) and Propionic Acid (UN 1848)

Transmitted by the expert from Germany

## Background

- During the March 2003 session of the International Maritime Organization (IMO)'s Sub-Committee on Dangerous Goods, Solid Cargoes and Containers (DSC), Germany drew attention to a problem concerning a very well known substance which is called propionic acid (UN 1848).

- For this substance in column (17) of the Dangerous Goods List (DGL) of the IMDG Code the following information about properties and observations can be found:

Colourless, flammable liquid with a pungent odour. Miscible with water. Corrosive to lead and most other metals. Burns skin. Vapours irritate mucous membranes.

- Although this substance is described as a flammable liquid there is no subsidiary risk of Class 3 mentioned in column (4) of the DGL of the IMDG Code.

- Germany were asked to solve that problem by proposing a new UN number to the UN Sub-Committee.

- During the work on this document the attention of Germany was drawn by the industry to a substance which shows similar properties as propionic acid. This substance is known as formic acid (UN 1779).

- Germany gathered all necessary data to classify these two substances. These data are given in the data sheets of annexes 1 and 2 and supplementary information in annex 3.

- To transfer the data of the data sheets and to classify formic acid (UN 1779) and propionic acid (UN 1848) correctly Germany proposes the following amendments to the Dangerous Goods List of the UN Model Regulations:

Proposal

- UN 1779 FORMIC ACID

Column (2), amend the name and description to read as follows:

FORMIC ACID with more than 85% acid by mass

- UN 1779 FORMIC ACID

Column (4), add "3"

- Formic acid

Add a new entry to read as follows:

| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| xxxx | FORMIC ACID with not less than 10% but not more than 85 % acid by mass | 8 |  | II |  | 1 L | P001 IBC02 |  | T7 | TP2 |
|  | FORMIC ACID with not less than 5% but less than 10% acid by mass | 8 |  | III |  | 5 L | P001 IBC03 LP01 |  | T7 | TP2 |

- UN 1848 PROPIONIC ACID

Column (2), amend the name and description to read as follows:

PROPIONIC ACID with not less than 10% and less than 90% acid by mass

- Propionic acid

Add a new entry to read as follows:

| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| yyyy | PROPIONIC ACID with not less than 90% acid by mass | 8 | 3 | II |  | 1 L | P001 IBC02 |  | T7 | TP2 |

ANNEXES (ENGLISH ONLY)

Annex 1

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by	 Germany								Date  04-03-29

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions – if necessary state "not known" or "not applicable" – if data is not available in the form requested, provide what is available with details. Delete inappropriate words.

# Section 1.	SUBSTANCES IDENTITY

1.1	Chemical name	Formic acid

1.2	Chemical formula	CH2O2

1.3	Other names/synonyms	none

1.4.1	UN Number    1779		1.4.2	CAS number	64-18-6

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2)	Formic acid

1.5.2	class/division	   8	subsidiary risk(s)   3 for C > 85%

packing group	   II

class/division	   8 	subsidiary risk(s) no for 10%<C≤ 85%

packing group	   II

class/division	   8 	subsidiary risk(s)  no for 5%<C< 10%

packing group	   III

1.5.3	proposed special provisions, if any		none

1.5.4	proposed packing instruction(s)		PG II = P001/IBC02

PG III = P001/IBC03/LP01

# Section 2.	PHYSICAL PROPERTIES

2.1	Melting point or range	    8 °C

2.2	Boiling point or range	101 °C

2.3	Relative density at:

2.3.1	15 °C	not known

2.3.2	20 °C	1.220 g/cm3

2.3.3	50 °C	not known

2.4	Vapour pressure at:

2.4.1	20°C	4.2 kPa

50 °C	17.0 kPa

2.4.2	65 °C	not known

2.5	Viscosity at 20 °C		1.8 mPa*s

2.6	Solubility in water at 20 °C		complete	g/100 ml

2.7	Physical state at 20 °C (2.2.1.1)	solid / liquid / gas

  - Appearance at normal carriage temperatures, including colour and odour

colourless liquid, pungent odour

2.9	Other relevant physical properties	not known

# Section 3.	FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.3)	 	see attachment

3.1.2	Is combustion sustained? (2.3.1.2)	yes / no

3.2	Autoignition temperature 		480 °C

3.3	Flammability range (LEL/UEL) 	12 / 38 % estimated

3.4	Is the substance a flammable solid? (2.4.2)	yes / no

3.4.1	If yes, give details ...

# Section 4.	CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity?	yes / no

If yes, state

4.1.1	Inhibitor/stabilizer used ...

4.1.2	Alternative method ...

4.1.3	Time effective at 55 °C ...

    - Conditions rendering it ineffective ...

4.2	Is the substance an explosive according to paragraph 2.1.1? (2.1)	yes / no

4.2.1	If yes, give details ...

4.3	Is the substance a desensitized explosive? (2.4.2.4)			yes / no

4.3.1	If yes, give details ...

4.4	Is the substance a self-reactive substance? (2.4.1)	yes / no

If yes, state

4.4.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.4.2.3.4)	yes / no

4.4.2	proposed control temperature for a 50 kg package ... °C

4.4.3	proposed emergency temperature for a 50 kg package ... °C

4.5	Is the substance pyrophoric? (2.4.3)	yes / no

4.5.1	If yes, give details ...

4.6	Is the substance liable to self-heating? (2.4.3)	yes / no

4.6.1	If yes, give details ...

4.7	Is the substance an organic peroxide (2.5.1)	yes / no

If yes state

4.7.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.5.3.4.1)		yes / no

4.7.2	proposed control temperature for a 50 kg package ... °C

4.7.3	proposed emergency temperature for a 50 kg package ... °C

4.8	Does the substance in contact with water emit flammable

gases (2.4.4)					yes / no

4.8.1	If yes, give details ...

4.9	Does the substance have oxidizing properties (2.5.1)		yes / no

4.9.1	If yes, give details ...

4.10	Corrosivity (2.8) to:

4.10.1	mild steel ...	C>5%	more than 6.25 mm/year at 55 °C

4.10.2	aluminium ...	C>5%	more than 6.25 mm/year at 55 °C

4.10.3	other packing materials

(specify) no		... mm/year at ...

...		... mm/year at ...

  - Other relevant chemical properties 	...not known...

# Section 5.	HARMFUL BIOLOGICAL EFFECTS

5.1	LD 50, oral (2.6.2.1.1)         730      	mg/kg	Animal species ...rat..

5.2	LD 50, dermal (2.6.2.1.2) .....x..	mg/kg	Animal species ...

x...not published (Patty’s Ind. Hyg. Toxicol. 4, 1994)

5.3	LC 50, inhalation (2.6.2.1.3) ...>14.8....	mg/litre	Exposure time .1.. hours

or  .......	ml/m3	Animal species ...

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.3)	 41.7. ml/m3

5.5	Skin exposure (2.8) results:   corrosive

Exposure time ... x x				hours/minutes

x x...not published (Patty’s Ind. Hyg. Toxicol. 3, 1981)

Animal species ... rabbit

5.6	Other data ...

  - Human experience ...medical reports of acute exposures of workers show severe skin burns (C>90%) and mild to moderate skin burns (10%<C≤ 90%).

# Section 6.	SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents):

suitable are dry chemical powder, carbon dioxide, water spray and appropriate foam

    - Spillage:

Absorb on sand or vermiculite and place in closed containers for disposal; ventilate area and wash spill site after material pickup is complete

6.2	Is it proposed to transport the substance in:

6.2.1	Intermediate Bulk Containers (6.5)		yes / no

6.2.2	Portable tanks (6.7)			yes / no

If yes, give details in Sections 7. and/or 8.

Section 7.	INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.1)

  - Proposed type(s)

PG II = IBC02

PG III = IBC03

Section 8.	MULTIMODAL TANK TRANSPORT(only complete if yes in 6.2.2)

  - Description of proposed tank (including IMO tank type if known)

For 8(3), II  and  8, II and 8, III

T7

8.2.	Minimum test pressure 	4.0 bar

8.3	Minimum shell thickness  		see 6.7.2.4.2

8.4	Details of bottom openings, if any 	see 6.7.2.6.3

8.5	Pressure relief arrangements 		normal

8.6	Degree of filling 		TP2

8.7	Unsuitable construction materials 	no

* * * * *

Annex 2

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by	 Germany								Date  04-03-25

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions – if necessary state "not known" or "not applicable" – if data is not available in the form requested, provide what is available with details. Delete inappropriate words.

# Section 1.	SUBSTANCES IDENTITY

1.1	Chemical name	Propionic acid

1.2	Chemical formula	C3H6O2

1.3	Other names/synonyms	Propanoic acid

1.4.1	UN Number	1848

1.4.2	CAS number	79-09-4

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2)	Propionic acid

1.5.2	class/division	   8	subsidiary risk(s)   3 for C ( 90%

packing group	   II

class/division	   8 	subsidiary risk(s) no for 10%<C< 90%

packing group	   III

1.5.3	proposed special provisions, if any		none

1.5.4	proposed packing instruction(s)		PG II = P001/IBC02

PG III = P001/IBC03/LP01

# Section 2.	PHYSICAL PROPERTIES

2.1	Melting/freezing point or range    -20 °C

2.2	Boiling point or range	 141 °C

2.3	Relative density at:

2.3.1	15 °C	not known

2.3.2	20 °C	0.992 g/cm3

2.3.3	50 °C	not known

2.4	Vapour pressure at:

2.4.1	20 °C	0.5 kPa

50 °C	not known

2.4.2	65 °C	not known

2.5	Viscosity at 20 °C		10    mPas

2.6	Solubility in water at 20 °C		complete	g/100 ml

2.7	Physical state at 20 °C (2.2.1.1)	solid / liquid / gas

  - Appearance at normal carriage temperatures, including colour and odour

colourless liquid, pungent odour

2.9	Other relevant physical properties	not known

# Section 3.	FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.3)	 	see attachment

3.1.2	Is combustion sustained? (2.3.1.2)	yes / no

3.2	Autoignition temperature 		485 °C

3.3	Flammability range (LEL/UEL) 	2.0 / 12.0 % estimated

3.4	Is the substance a flammable solid? (2.4.2)	yes / no

3.4.1	If yes, give details ...

# Section 4.	CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity?	yes / no

If yes, state

4.1.1	Inhibitor/stabilizer used ...

4.1.2	Alternative method ...

4.1.3	Time effective at 55 °C ...

4.1.4	Conditions rendering it ineffective ...

4.2	Is the substance an explosive according to paragraph 2.1.1? (2.1)	yes / no

4.2.1	If yes, give details ...

4.3	Is the substance a desensitized explosive? (2.4.2.4)			yes / no

4.3.1	If yes, give details ...

4.4	Is the substance a self-reactive substance? (2.4.1)			yes / no

If yes, state

4.4.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.4.2.3.4)			yes / no

4.4.2	proposed control temperature for a 50 kg package ... °C

4.4.3	proposed emergency temperature for a 50 kg package ... °C

4.5	Is the substance pyrophoric? (2.4.3)				yes / no

4.5.1	If yes, give details ...

4.6	Is the substance liable to self-heating? (2.4.3)				yes / no

4.6.1	If yes, give details ...

4.7	Is the substance an organic peroxide (2.5.1)				yes / no

If yes state

4.7.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.5.3.4.1)		yes / no

4.7.2	proposed control temperature for a 50 kg package ... °C

4.7.3	proposed emergency temperature for a 50 kg package ... °C

4.8	Does the substance in contact with water emit flammable gases (2.4.4)	yes / no

4.8.1	If yes, give details ...

4.9	Does the substance have oxidizing properties (2.5.1)		yes / no

4.9.1	If yes, give details ...

4.10	Corrosivity (2.8) to:

4.10.1	mild steel ...	C>10%	more than 6.25 mm/year at 55 °C

4.10.2	aluminium ...	C>10%	more than 6.25 mm/year at 55 °C

4.10.3	other packing materials

(specify) no		... mm/year at ...

…		... mm/year at ...

  - Other relevant chemical properties 	... not known...

# Section 5.	HARMFUL BIOLOGICAL EFFECTS

5.1	LD 50, oral (2.6.2.1.1) 	3500-4200   	mg/kg	Animal species 	rat..

5.2	LD 50, dermal (2.6.2.1.2) 	500....	mg/kg	Animal species 	rabbit

5.3	LC 50, inhalation (2.6.2.1.3) 	>19.7....	mg/litre	Exposure time 	1. hours

or  .......	ml/m3	Animal species 	rat..

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.3) 4.96 ml/m3

5.5	Skin exposure (2.8) results: corrosive

Exposure time ...1 + 5 + 15			hours/minutes

Animal species ... rabbit

5.6	Other data ...

5.7	Human experience ... medical reports of acute exposures of workers show moderate skin burns (C>25%).

# Section 6.	SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents):

suitable are dry chemical powder, carbon dioxide, water spray and appropriate foam

    - Spillage:

Absorb on sand or vermiculite and place in closed containers for disposal; ventilate area and wash spill site after material pickup is complete

6.2	Is it proposed to transport the substance in:

6.2.1	Intermediate Bulk Containers (6.5)		yes / no

6.2.2	Portable tanks (6.7)			yes / no

If yes, give details in Sections 7. and/or 8.

Section 7.	INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.1)

7.1	Proposed type(s)

PG II = IBC02

PG III = IBC03

Section 8.	MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.2)

  - Description of proposed tank (including IMO tank type if known)

for 8(3), II	for 8, III

T7	T4

8.2.	Minimum test pressure 		4.0 bar 		2.65 bar

8.3	Minimum shell thickness  		see 6.7.2.4.2 	see 6.7.2.4.2

8.4	Details of bottom openings, if any 	see 6.7.2.6.3 	see 6.7.2.6.3

8.5	Pressure relief arrangements 		normal 	normal

8.6	Degree of filling 		TP2 	TP1

8.7	Unsuitable construction materials 	no	no

* * * * *

Annex 3

UN 1779 Formic acid + UN 1848 Propionic acid

| Flashpoint as a function of the concentration |
| --- |
| Concentration % | Flashpoint of formic acid (UN 1779) | Flashpoint of propionic acid (UN 1848) |
| 100 | 48 | 50 |
| 95 | 51 | 54 |
| 90 | 57 | 61 |
| 85 | 65 | 72 |
| 80 | 82 | 91 |

__________________

# Text boxes

STSTE

Secretariat