#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2004/34

19 April 2004

# ORIGINAL: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-fifth session, 5-14 July 2004

# Item 6 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Liquid and Solid variants in the Dangerous Goods List

Discrepancies between the UN Model Regulations and the ICAO Technical Instructions

### Transmitted by the expert from the United Kingdom

Background

- The expert from the United Kingdom notes that in November 2001 the ICAO Dangerous Goods Panel agreed to review and as far as possible align their Packing Instructions with those in the Model Regulations. The main exercise was completed in September 2003 and the 2002 Dangerous Goods Panel agreed that a changeover would take place in 2007/8 edition of the ICAO Technical Instructions.

- However during the exercise to allocate air Packing Instructions to UN numbers three discrepancies with the UN text concerning solids and liquids were identified. They are listed in the Annex 2 to this document with the comments made to the Panel which provide the justification for the proposals. The substances are shown as being liquid and solid in the Technical Instructions but not in the UN Model Regulations.

- Upon further examination it will be seen that the other modal regulations have not been consistent in their approach and the expert from the United Kingdom has been asked by the ICAO Dangerous Goods Panel to draw this problem to the attention of the Sub-Committee.

- At the December 2003 Sub-Committee meeting the expert from the United Kingdom submitted UN/SCETDG/24/INF.57 inviting comments on suggested changes. Comments were received from the secretariat (see ST/SG/AC.10/C.3/48, par. 93) and the expert from the United Kingdom was invited to prepare an official proposal.

- Having considered the matter further and taking into account the comments made, the expert from the United Kingdom proposes the following amendments to the Dangerous Goods List as indicated below in Annex 1.

Explanation of the proposed changes

- From the melting point of about 73 °C, it is proposed that the entry for UN 1733 Antimony trichloride is changed to the solid entry (use of P002, etc).

- It is proposed that UN 1740 is confirmed as the solid entry for Hydrogendifluorides by addition of "SOLID" to the Proper Shipping Name (PSN). A new entry "XXXX" is created for (aqueous) solutions and to be consistent with other existing solution entries (UN 2817 and UN 3421), a subsidiary risk of 6.1 is indicated.

- Based on the two isomeric forms of crotonic acid it is proposed to confirm UN 2823 as the solid form by adding "SOLID" to the PSN and creating a new entry "YYYY" for the liquid form. It is proposed to refer to the solid and liquid forms in the PSNs rather than the isomer names to allow for commercial products that may be mixtures of the isomers. This was the general approach taken during the review of solid/liquid entries previously at UN level.

# Proposal                                                                                                                                                                                         	ANNEX 1

| UN No. | Name and description | Class or division | Subsi- diary risk | UN packing group | Special provi- sions | Limited quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Instruc- tions | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| Change to solid entry |  |  |  |  |  |  |
| 1733 | ANTIMONY TRICHLORIDE | 8 |  | II |  | 1kg | P002 IBC08 | B2 B4 | T3 | TP33 |
| EXISTING ENTRY -add "SOLID" |  |  |  |  |  |  |
| 1740 | HYDROGEN-DIFLUORIDES, SOLID N.O.S. | 8 |  | II |  | 1kg | P002 |  | T3 | TP33 |
|  |  |  |  |  |  |  | IBC08 | B2 B4 |  |  |
|  |  | 8 |  | III | 223 | 5kg | P002 |  | T1 | TP33 |
|  |  |  |  |  |  |  | IBC08 | B3 |  |  |
|  |  |  |  |  |  |  | LP02 |  |  |  |
| NEW ENTRY |  |  |  |  |  |  |  |  |  |
| XXXX | HYDROGEN-DIFLUORIDES, SOLUTION N.O.S. | 8 | 6.1 | II |  | 1L | P001 |  | T7 | TP2 |
|  |  |  |  |  |  |  | IBC02 |  |  |  |
|  |  | 8 | 6.1 | III | 223 | 5L | P001 |  | T4 | TP1 |
|  |  |  |  |  |  |  | IBC03 |  |  |  |
| 2823 | CROTONIC ACID SOLID | 8 |  | III |  | 5 kg | P002 IBC08 |  | T1 | TP33 |
|  |  |  |  |  |  |  | LP02 |  |  |  |
| YYYY | CROTONIC ACID LIQUID | 8 |  | III |  | 5L | P001 IBC03 LP01 |  | T4 | TP1 |

ANNEX 2

| Packing Instructions: | UN | ICAO TIs | IMDG | RID/ ADR | Comments made for the ICAO Meeting |
| --- | --- | --- | --- | --- | --- |
| 1733 | Antimony trichloride | Solid |  | 814 | P002 | P002 | Antimony trichloride is a colourless, transparent, very hygroscopic, crystalline mass. Its melting point is about 73(C. It is soluble in alcohol, acetone and acids; with water it forms antimony oxychloride. The entry for antimony trichloride, liquid in the Technical Instructions is therefore not clear. |
|  |  | Liquid | P001 | 808 | P001 |  |  |
| 1740 | Hydrogen-difluoride | Solid | P002 | 815 | P002 | P002 | It is reasonable to have separate entries for the solid entry and (aqueous) solution entry here. UN 1811 and UN 3421 provide some justification, though it should be noted that a "SOLUTION" entry does not exist for UN 2439 in the 13th UN Orange Book. |
|  |  | Liquid |  | 825 |  |  |  |
| 2823 | Crotonic acid | Solid | P002 (13th Ed.) | 822 | P002 |  | Crotonic acid exists in two isomeric forms, (cis- and trans-). The trans- isomer has a melting point of about 72 degrees C and is soluble in water. The cis- isomer (otherwise known as isocrotonic acid) is a liquid at room temperature, melting point about 14 degrees C. Both isomers exhibit corrosivity. |
|  |  | Liquid | P001 (12th Ed.) | 818 |  | P001 |  |

# Text boxes

STSTE

Secretariat